CHAPTER 7

CASE STUDY: ECONOMIC ASSESSMENT OF EARTHQUAKE DISASTER MITIGATION

7.0	Overview

The model is developed for assessing the feasibility of retrofitting of brick and mud buildings. Values of parameters are evolved through statistical analysis and other analytical tools. The developed model is validated on case study data. The case study is from Khandwa district of Madhya Pradesh. The methodology for economic assessment of retrofitting of non-engineered buildings is shown in following paragraphs.

7.1	Geographic and Geological Information

(i)	Area

The case study is carried for Pandhana tehsil of Khandwa district. The case study area includes 21 villages for Pandhana Tehsil of Khandwa district.  In principal, two types of houses were mostly found in semi urban to rural area, i.e. mud and brick types. Figure 7.1 shows the location of area, which is considered for case study.

(ii)	Earthquake History

# Khandwa was considered to be a stable region from the seismic point of view. But seismic activity in the Central India is on the ascent over the years. The very recent Jabalpur earthquake (22nd May 1997) and some more earthquakes of moderate and small magnitudes in the region have confirmed that the area once considered to be stable has now become susceptible to earthquake of intensity VI and more.

Earth scientists have studied in detail the seismic activities and are of the view that East Nimar has had a record of minor earthquakes in the past. The Bureau of Indian Standards (1893:2002) has classified the entire country into four zones on the basis of earthquake history. Khandwa district falls in Zone III of Earthquake Hazard Zone Map of India. District falls in the Sone-Narmada-Tapti Lineament, which is seismically considered to be a weak zone. The study has been carried in Madhya Pradesh for Earthquake Resistant Construction by Disaster Management Institute in 2004. Figure 7.2 shows seismic zoning of Madhya Pradesh based on IS 1893:2002. A team of experts have further worked out the seismic zoning of Madhya Pradesh based on past experience of Jabalpur earthquake, their extent of intensity and other seismological factors. The zoning has been further divided into moderate and moderate high seismic zones.  The moderate, high seismic risk zone has been figured out in Figure 7.2. The study area has been circled in Figure 7.2. Figure 7.3 shows active faults in and around study area. This zone is classified into four seismically active areas:

- Sopani fault area of Malwa situated towards north of Balwara fault (North Narmada fault);

- The Narmada area between North and South Narmada fault;

- The Satpura Horst between South Narmada and South Satpura fault (The Burhanpur fault);

- Tapti valley situated south of South Satpura.

In addition to these faults, the Sukta-Barhwani fault is also an identified weak zone. The earthquakes in Khandwa district are mainly attributed to seismic activities along Burhanpur fault and Barwani-Sukta fault. Presence of hot water springs along Burhanpur fault confirms it as a seismically active zone.

Khandwa & its adjoining areas have experienced about 7 earthquakes of magnitude 4 to 6.5 on Richter scale between the years 1847 and 1992.  Out of these, two were of magnitude more than 6. Hence, an earthquake of magnitude between 6 and 6.5 is a likely phenomenon in the area. In addition to earthquakes of moderate to high magnitudes, micro-earthquakes are recorded in Taklikalan (1993-95), Silawal (1992), Kusumari (1986, 1992), Ghanora (1992), Borlai (1992), Ratlam, Sehore (1993) & Ahmedpur Khaigaon (1994).

Geological Survey of India (GSI) and Indian Meteorological Department (IMD) did intensive study of the micro-earthquakes of Taklikalan between 1993-95, according to which a total of 460 such micro-earthquakes were recorded, the highest magnitude being that of 29th November 1993, with focus at a depth of 10 km. The highest frequency of micro shocks was recorded as 29 on 5th January 1994. Recently, Pandhana tehsil is experiencing similar micro-earthquake activities. Maximum of this occurred between December 11, 1998 to April 5, 1999.

Figure 7.1: Map Showing the Location of Study Area in Madhya Pradesh

Figure 7.2: Map of Madhya Pradesh Showing the Seismic Zoning 
(Source: Handbook: Earthquake Resistant Construction For Madhya Pradesh, 2004)

Figure 7.3: Map of Madhya Pradesh Showing Active Faults 
(Source: Handbook: Earthquake Resistant Construction For Madhya Pradesh, 2004)

Pandhana micro-earthquake between September and October '98 was also recorded and reported by GSI.  The above information is extracted from official circulars received from various organizations of Government of India at Disaster Management Institute, Bhopal, India.

(iii)	Earthquake Probabilities

Earthquake probabilities are worked out for this region. Kishor et. al., 2002 has worked out the magnitude with annual frequency. Using the magnitude intensity attenuation relationship (Nevi et. al.1977), the magnitude is deduced to Intensity scale with annual frequency.  The details are given in Table 7.1

Table 7. 1: Annual Earthquake Frequency (Kishor et. al. 2002)

| S.No. | Magnitude | Intensity | Mean Annual Frequency Gumbel’s Type I |
| --- | --- | --- | --- |
|  | 4.0 | V | 0.455 |
|  | 4.5 |  |  |
|  | 5.0 | VI | 0.170 |
|  | 5.5 |  |  |
|  | 6.0 | VII | 0.0755 |
|  | 6.5 | VIII | 0.0313 |
|  | 7.0 |  |  |

  - Data Collection

The questionnaire (Appendix 6.1) is framed out for collecting the data. The data collection requires sound knowledge of earthquake engineering as well as civil engineering with social dimensions. For execution of extensive survey, the District Administration, Khandwa had nominated sub-engineers from various government works department like, Public Works Department (PWD), Rural Engineering Services (RES) and Madhya Pradesh State Housing Board (MPSHB) under the leadership of author of present research work. Sixteen well trained engineers were deployed for this purpose. The engineers were provided three days training orientation program of earthquake disaster management, state of art for seismic evaluation of buildings and the methodology for survey of buildings for pre and post disaster situation. The special on-site field demonstration was also conducted for the trained surveyors. The data collection was done on door-to-door basis. With assistance of Panchayat Secretary, the buildings were surveyed. As the data was voluminous, pace of survey was slow, hence it was realized that additional manpower is required. The government works departments further provided five engineers for carrying out survey. The database was prepared using the FoxPro® software.

7.3	Data Analysis

For retrofitting of buildings, various parameters are studied for evolving low cost retrofitting techniques. These are structural, utility, functional, social, economical, material and other parameters.

# 7.3.1	Building Criteria based on Structural System and Material Used

Foundation

For the study area, the survey states that nearly 92 % buildings have depth of foundation about 60 cm. But still there is little variation in the depth of foundation. Out of 21 villages, study reveals that 83 % houses are having spread footing foundation. Remaining 17 % belongs to either isolated footing or other type of foundation. Nearly 99 % houses exist without plinth band. Most of the foundations are made up of Random Rubble Masonry with mud mortar.

Wall

Based on these datasets, the variation of wall material is worked out. It is found that 69.25 % building stock falls under mud type, 30 % belongs to Brick type and remaining 0.75% holds for thatch, and other non-conventional building material. About 95 % of brick buildings are made up of mud mortar, which requires attention and retrofitting. Void wall ratio is important parameter for seismic safety. The Void wall ratio is ratio of area of opening and total wall area in particular direction. In most of the cases it is found that the void wall ratio is less than 10 %. The level of windows and doors in walls have also been studied and found that more than 91 % buildings do not have doors and windows at same level. Lintel band which is considered to be an earthquake resistant feature was observed in less than 10 % of building stock. However small member of buildings possessing bands. More than 90 % buildings are not having a proper continuous band, thus increasing vulnerability.

# Roof

In study area, more than 97 % buildings have sloping roofs. There is a wide variation in material used for roof supporting component. The percentage of material used for roof support may be referred at Figure 7.4. The study shows that more than 44 % buildings stock is covered with GI Sheet Roofing. It is observed that 64.50 % building’s roofs are not in good status.

About 75 % of houses are having wood or bamboo roof supporting material. Steel section attributes about 22 % of total stock. Clay tiles stands next to GI sheet widely used in the area.

Figure 7.4: Variation in Roof Supporting Material

# Connectivity between Various Elements

Earthquake safety of buildings depends upon continuity of building elements and their integral action. It is very important to study the inter-connectivity of building elements. Aspects for investigation include connection between wall to wall, wall and foundation, wall and roof and vertical and horizontal supporting elements.

The Study reveals that in more than 90 % of buildings, walls are not connected at the corners and junctions. The foundation and wall should be properly connected as it helps in transferring seismic load from foundation to wall and dead and live loads from wall to foundation. Proper connection helps in safe transfer of forces.

## General Configuration

Apart from various parameters stated above, there are other important parameters, which attributes to seismic safety and retrofitting. These are age of buildings, maintenance status, occupation, number of storeys etc.

It is observed that in villages nearly 70 % buildings belong to the mud category. Hence it is very important to assess the performance of such buildings. About 30 % of total buildings stock are more than 40 years old. Among surveyed buildings, 44 % of buildings have vertical/ horizontal or diagonal cracks. This aggravates the seismic risk to buildings. About 58 % of buildings are poorly maintained. The household owners of the study area are mostly farmers. More than 95% buildings are characterized by one storey with attic.

## 7.3.2	Social and Economical Parameters

These parameters are important for assessing the needs and level of retrofitting. There is a need to assess the social and economic status of beneficiaries and their willingness to pay for the same. If the beneficiaries are well off then they can go for higher safety level of retrofitting, but for poor people who are mostly farmers have very limited income, it is difficult to contribute for retrofitting. So, it becomes necessary to assess one’s capacity. There are various aspects, viz., annual / monthly income, housing configuration, ownership etc., which are taken into account for seismic retrofitting

The data from study area states that more than 40 % of families have monthly income less than Rs. 500. About 37.5 % of families earn between Rs. 500 to Rs. 1000 per month. Only about 20 % families have capacity to earn more than Rs. 1000 per month. This influences the willingness to pay for retrofitting of buildings. Most of the families are either from farmer background or labour class; who cannot afford to invest money for seismic safety. The basic need for them is still food, drinking water, housing and employment. Other important issues are education, environment, sanitation, health and immunization. The safety against natural and man made calamity stands secondary.

7.3.3	Performance Objectives

It is important to evaluate the parameters involved in retrofitting. These may be willingness to pay, maintenance of houses, economic status of house owner, seismic risk of the area, provision in construction codes, resources available within area,  typology of houses, earthquake history, government policy and earthquake safety awareness

Retrofitting objective of clients is also important to be known. Depending upon the resources available to house owners, the retrofitting may be suggested. About 84 % of house owner opted for life safety option, which applies low cost means of retrofitting. The damage reduction options are opted by 3% of household and remaining 13% opted for immediate safety.

It is important to know the house owner’s willingness to pay for the retrofitting of their houses. If the maintenance of house is good then the retrofitting cost reduces comparatively. More than half housing stock is poorly maintained in condition. As the seismic risk of area increases, the cost of retrofitting also increases accordingly. In case of study area, the area falls in zone III, which requires low cost retrofitting techniques. It is also important to make sure the material available for retrofitting in the area. Generally in rural area, very few new innovative materials are available. Also, it is not economical and feasible for retrofitting measures. Retrofitting of structures depend upon their configuration and the process of construction.  The techniques will be discussed in coming section for various types of houses under study. It is necessary to review the damage and losses associated with specific type of houses. This helps in understanding the mode of failure and type of treatment required. Government policy and schemes also play important role in motivating the house owners to go for retrofitting. The schemes may include financial incentives, mass insurance etc. The occurrence of earthquake is rare. Human memory is very short and there are number of priorities. Among all priorities, the seismic safety stands secondary. Many times, villagers are unaware of seismic safety. There is requirement of community awareness among the people to go for seismic retrofitting and make their houses safe.

The suggested retrofitting techniques have been derived from guidelines developed by Dr. Svetlana N. Brzev(1998), International  Seismic Consultant, and her team on “Earthquake Resistant Construction and Seismic Strengthening of Non-engineered Buildings in Rural Areas of Maharashtra”, Published by Maharashtra Earthquake Rehabilitation Programme, Revenue and Forest Department, Government of Maharashtra, Mumbai (GOM 1998) . The details of the guidelines may be referred at http://www.eeri.org/lfe/clearinghouse/kashmir/resources.html.

7.3.4	Utility

In study area, most of the buildings are residential types. Therefore the proposed research,  only residential buildings are considered for analysis.

  - Construction Techniques for Buildings under Study

The houses are typically constructed with locally available resources. The details of construction for two main types of buildings are given below:

7.4.1	Brick Buildings

The detail features of brick buildings are given below. The features may be referred with greater details in Figure 7.5.

Foundation

For brick wall construction, generally spread footing foundation is practiced. The depth of foundation confines to about 60 cm. The foundation is made up of random rubble masonry with mud mortar. The thickness of footing varies from 60 to 75 cm. In many cases, the width of foundation continues above plinth level and gradually tapers down to wall thickness.

Wall Construction

The quality of brick is poor in this area. The irregular size, improper burning, lumps of minerals in brick section are serious concern for quality. The bonding at joints and corners are not proper. The poor mud mortar is being used for the masonry work.

Roofing System

Sloping roof with GIS sheet or clay tiles are common practice in the study area. Also, the thin stone slab (100 mm) with steel build up sections is used for roofing. In general, T or I sections are used for supporting stone slabs. The built up sections are placed at regular interval of 0.90 to 1.25mt. The stone slabs are supported on built up section and joints are filled up with lime or cement mortar.

# 7.4.2	Features of Existing Mud Wall Construction

The Traditional mud wall construction practiced in Khandwa region is unique i.e. the construction is partially load bearing and partially framed structure. The details of the mud wall construction may be referred at (Figure-7.6)

# Foundation

The foundation of mud buildings is similar to brick buildings. The mud construction is generally done above plinth level and the foundation is made up of random rubble masonry with mud mortar.

Wall Construction

The mud wall is used for partition and separation. The thickness of mud wall varies from 45 cm to 75 cm. The quality of mud for construction is not satisfactory. The soil behavior is inconsistent with extreme weather. During rainy season, the soil swells extensively and during summer it shrikes and causes cracks. Similar behaviour is observed in old existing mud walls and requires immediate attention.  Sometimes the wall is constructed by mixing mud with field stone pebbles.

# Timber Frame Arrangement

The columns are erected from the foundation. The timber columns of 200 mm dia are provided at the interval of 2 to 2.5 meter. The columns are arranged longitudinally and transversely. Generally houses are of one storey with attics. The timber columns are extended upto roof level. The joineries of the column and beam are found to be satisfactory but require maintenance.

  - Retrofitting Measures For Vernacular Construction

As per 1893: 1984 (New Revision 2002), the study area falls in seismic zone III. The brick buildings are low strength masonry buildings. As per Indian Code 13828, the building belongs to category B for retrofitting purpose. Apart from setting up the criteria for retrofitting by National Standard Codes, the strength and weakness of brick and mud buildings are worked out with respect to Indian Standard codes. The critical study about strength and weakness of brick buildings may be referred at Appendix 7.1. The general retrofitting measures include provision of lintel, Roof, Plinth & gable bands and bracing in plan at tie level of sloping roof. These bands tie the walls together and ensure integral action and ductile behaviour of all the walls of the house in resisting seismic forces. On the basis of critical analysis carried out at Appendix 7.1 for brick and mud buildings for the study area, specific strengthening measures have been suggested, which may be referred at 7.5.1.1 & 7.5.2.1.

7.5.1	Retrofitting Measures adopted for Brick Wall Building

The performance objective of the research study is to provide life safety through cost effective retrofitting measures. Accordingly based on building characteristics, the feasible options of retrofitting measures are horizontal bands at roof level, seismic bandage at lintel level above opening and strengthening of roof elements. In guidelines published by Government of Maharashtra, 1998, the detailed procedure for providing roof band, seismic bandage at various level and many other measures are suggested by the team lead by Dr. Svetlana N. Brzev (International Seismic Consultant), Vancouver, Canada. The guidelines provide laying procedure and specification of RCC seismic band in detail. Figure 7.7 shows the details of proposed retrofitting techniques for brick building.

The laying procedure has also been descried in detail. The same procedure has been adopted to estimate the quantity and cost of material and retrofitting for brick buildings. The guidelines also suggest provision of steel cross tie bars, corner strengthening and installation of seismic bandage. The guidelines also suggest specification and sequence of construction, strengthening of roof elements through bracing purlins and rafter, the same has been adopted in proposed measures. Accordingly as per the configuration and dimensions of the building, estimation of material cost has been worked out. The labour cost has also been worked out using local labour rates provided by Department of Labour, District Administration, Khandwa, Madhya Pradesh.

7.5.1.1 Variation in Brick Building and Proposed Retrofitting Techniques

#### The brick buildings are classified further based on structural and architectural configuration. Accordingly, retrofitting measures are suggested. The details are referred below:

#### (a)	Wall with Gable, Frame Structure

#### The brick building with frame structure is found to be safe from earthquake forces. However it was found that the frame was not properly linked to columns/ beam elements. It is necessary to strengthen the walls and timber frame with roofing elements.

Figure 7.8: Wall with Gable, Frame Structure

#### (b)	Brick Wall with Steel Section Flat Roof

Generally this type of construction is found with the owner having good social and economic background. The roof rests on the steel built-up or rolled T, I or L sections. The thin stone slab is placed above the steel section and filled with the cement mortar. The roof and walls are weak from lateral seismic force, which requires strengthening.

Figure 7.9 (a, b): Brick Wall with Steel Section Flat Roof

(c)	Brick Wall with Attic

Apart from strengthening walls and integrating wall elements, it is also necessary to strengthen the gable ends. The retrofitting technique for gabled brick building is as following:

Figure 7.10: Brick Wall With Attic

(d)	Brick Wall with Low Height

This common type of brick wall building is found in large number. The built up area is found to be comparatively small.

Figure 7.11: Brick Wall with Low Height

7.5.2	Retrofitting Techniques of Mud Wall Building

The performance objective of the research study is to provide life safety through cost effective retrofitting measures. Accordingly based on building characteristics, the feasible options of retrofitting measures are horizontal, diagonal and X bracing of existing columns, Tee bracing and strengthening of roof elements through bracing purlins and rafters. In guidelines published by Government of Maharashtra, 1998, the detailed procedure for providing horizontal and diagonal bracing, roof strengthening and many other measures are suggested by the team lead by Dr. Svetlana N. Brzev (International Seismic Consultant), Vancouver, Canada.

The guidelines provide the details of specification of various bracings. The laying procedure has also been descried in detail. The same procedure has been adopted to estimate the quantity and cost of material and retrofitting for mud buildings. The GOM 1998 guidelines also suggest provision of roof band. The guidelines suggest strengthening of roof elements through bracing purlins and rafter in detail, the same has been adopted in proposed measures. In adopting the same, and as per the configuration and dimensions of the building, estimation of material cost has been worked out. The labour cost has also been worked out using local labour rates provided by Department of Labour, District Administration, Khandwa, Madhya Pradesh. Figure 7.12 shows the general configuration of retrofitting of typical mud building.

7.5.2.1	Variation in Mud Building and Proposed Retrofitting Techniques

The recommendations primarily include introduction of timber frame, strengthening of existing columns, strengthening of various structural components, roof strengthening and repair to the cracked walls.

(a)	High Mud Wall Construction without Timber Frame

This building typology is very unsafe. It is very obvious that the adobe or mud construction is very brittle and even small tensile stress may damage the structure. So it is necessary to give support by introducing frame elements in the form of columns and beams. The following are the measures to be taken for strengthening the buildings.

Figure 7.13(a, b, c) High Mud Wall Construction without Timber Frame

(b)	High Mud Wall with Wooden Frame

Mud wall building with wooden frame may perform better than without frame, but it is necessary to check the connectivity of frame elements. In general, with the time, the wooden elements deteriorate due to water and temperature, so it requires strengthening and repair. Retrofitting measures are as below:

Figure 7.14 : High Mud Wall with Wooden Frame

(c)	Mud Wall with 1½ Frame Storey and Opening at Gable End

The mud wall with 1½ Storey Frame building is usually provided with wooden frame. In this category of building, it is found that the door opens at the gable end. The opening of doors at gable is found to be vulnerable and may get damage at moderate seismic shocks. The retrofitting techniques are described in the following paragraph:

(d)	Mud Wall with Perfect Frame Structure

This type of construction is found to be firm and strong to resist the shock. These types of buildings function as timber frame construction. The mud wall works as partition wall and all loads are transferred though frame structure. The retrofitting cost may be comparatively lesser than other type of buildings.

Figure 7.16: Mud Wall with Perfect Frame Structure

(e) 	Mud Wall with Projection of Timber Frame in façade, Perpendicular to Gable Side

This type of building is 1½ Frame Storey, with timber projection at the façade. These types of projections are used as a storeroom or for other utility. The retrofitting techniques for such buildings are mentioned below:

Figure 7.17: Mud Wall with Projection of Timber 
Frame in Front, Perpendicular to Gable Side

(f)	Mud Wall without Frame

This is typical mud construction where columns and beams are not present. This type of building is very much vulnerable to earthquake shakings. This type of construction is also unsafe for floodwater and may require periodical maintenance.

a                                                        b

Figure 7.18 (a,b): Mud Wall without Frame

(g)	Mud Wall with Projection at Gable Side

This type of construction is rarely found but existing in the pilot study region. This typology is not safe from seismic forces.  It is necessary to retrofit the buildings.

Figure 7.19: Mud Wall with Projection at Gable Side

7.6	Sampling for Cost Estimation

21 villages of Pandhana tehsil have been considered as the study area, having more than 4500 houses comprising of mostly mud and brick types. Generally, mud type of houses is belonging to low economy and socially backward community in villages. The type of construction is more or less similar in built-up area, material of construction and construction techniques. From dataset, 11% of Brick and 6 % of mud buildings are selected for analysis on random basis to avoid biases.

7.7	Estimation of Reconstruction Cost

The proposed methodology describes the process of cost estimation. The algorithm for cost estimation can be referred at Appendix 6.4. The estimation of construction cost and their projection commences with estimation of cost for sample data. It is imperative to analyze parameters which attribute most to overall cost of construction. Based on study, it is found that numbers of parameter are contributing towards the cost of construction. Since the costs of manpower and material has been increased in last three years. The cost escalation factor needs to be incorporated. Based on present rate, it is assumed that manpower cost has increased by 15 % and material cost has gone up by 10%. The rationale has been derived from Schedule of Rates, published by Public Works Department, Government of Madhya Pradesh.

    - Estimation of Cost of Brick Buildings

To establish the relationship between various cost contributing parameters, regression analysis has been conducted. If more parameters are included, the significance of regression is lost. So it is generally advised to include those parameters, which are significantly contributing the overall cost of construction. For analysis of data, included parameters are length of building, width of buildings, depth of foundation, width of foundation, thickness of wall, height of building, height of gable, number of longitudinal walls, number of transverse walls and roof projection. Based on these parameters, All Possible Regression Analysis has been carried out.

# (a)	Identification of Most Contributing Parameters

Finding this subset of regressor (independent) variables involves two opposing objectives. First, the regression model is to be as complete and realistic as possible. It is desired that every regressor which is even remotely related to the dependent variable should be included. Second, it is also desired to include as few variables as possible because each irrelevant regressor decreases the precision of the estimated coefficients and predicted values. Also, the presence of extra variables increases the complexity of data collection and model maintenance. The goal of variable selection becomes one of complexity to achieve a balance between simplicity (as few regressors as possible) and an apt fit (as many regressors as needed). NCSS, 2001© is used for optimizing the variables for cost estimation.

## All Possible Regressions

The All Possible Regressions solution is the target of the popular step-regression procedures. Although it takes longer to run, it guarantees the right answer. Hence, when 15 or fewer independent variables are there, this variable selection procedure is preferred. This algorithm developed in chapter 6 (Appendix 6.4 & 6.5), fits all regressions involving one regressor, two regressors, three regressors, and so on. The selection criterion is recorded for each regression. Once the procedure finishes, the champion for each subset size is determined. It is determined which subset size is optimum for the specific case.

The All Possible Regression was applied and the result shows that out of six, only four parameters are to be considered as their R2 value is maximized. R-Squared is the ratio of the variation explained by the model to the total variation in the dependent variable. In case study, these four variables are height_roof, Length_building, Thickness_wall  and Width_bldg.

Checking For Validity of Result

Figure 7.20: Graph Showing Relationship between R-Square Vs Variable Count 
(Brick Building)

Figure 7.20 displays the values of R-Squared on the vertical axis and the number of independent variables on the horizontal axis for the data displayed in the All Possible Results Section of NCSS 2001. The large disparity in the four-variable models has been noted. This four variable model is most suited than others.

Figure 7.21: Relationship between Root MSE Vs Variable Count 
(Brick Building)

Figure 7.21 displays the values of the square root of the mean square error on the vertical axis and the number of independent variables on the horizontal axis for the data displayed. The large disparity in the four-variable models has been noted. This four variable model is most suited than others.

Root MSE is often considered a better criterion for choosing a best model than R-Squared. The root MSE decreases initially as p (Regressors) increases, stabilizes at some subset size, and eventually begins to increase with further increments of p. It should be chosen a best model based on the minimum MSE or a value of p near the point where the smallest MSE turns upward. The model subset that minimizes MSE will usually maximize R-Squared.

In view of Root MSE and R2, Both satisfy four parameters. Hence, four parameters has been taken for the studies i.e. height_roof, Length_building, Thickness_wall  and Width_bldg

(b)	Regression Model for Reconstruction Cost of Brick Buildings

Now the next step is to find out the regression between various independent parameters to apply on other set of data to find out the cost of all building. The data is apt for multiple regression models. Considering the dataset to be normally distributed, the multiple regression analysis for the cost of reconstruction is performed using NCSS 2001® software. Using all possible regression, out of six independent variable, four have been identified for cost estimation. The total reconstruction cost is the dependent parameters, which is attributed by independent parameters viz. Length_bldg, Width_bldg, Height_roof, and Thickness_wall. For analysis, 147 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Reconstruction Cost (in Rs.)

{-83353 + 10327 × (height_roof)+ 2893 × (Length building)+ 14891 × (Thickness_wall)+ 1582 × (Width_building)}× 1.10	(7.1)

Standard

Variable	Count	Mean	Deviation	Minimum    Maximum

Length_bldg	147	13.11878	8.33208	3	50

Width_bldg	147	3.87898	2.354092	2	30

Thickness_wall	147	0.3721769	0.2293156	0.2	3

height_roof	147	3.873184	1.017499	2.5	6.25

Total_cost	147	56154.84	48043.21	11700	484047

The regression is worked out with coefficient of independent variables and constants. These values are given as:

Regression Coefficient Section

Independent	Regression	Standard	Lower	Upper  	Standardized

Variable	Coefficient	Error	95% C.L.	95% C.L. 	coefficient

Intercept	-83353	3522.41	-90316.14	-76389.86	0.0000

Length_bldg	2892.783	97.06394	2700.906	3084.66	0.5017

Width_bldg	1581.993	334.0595	921.6204	2242.365	0.0775

Thickness_wall	148912.2	3416.895	142157.6	155666.7	0.7108

height_roof	10327.39	785.4436	8774.72	11880.07	0.2187

T-Critical	1.976811

(c)	Validity of Regression Relationship

For checking the validity, following regression check were conducted.

(i)	Check for Linearity

The check for linearity is carried out for all 4 predictors. For this, the Residual vs. Predictor Plots has to be analysed. All four Independent parameters except Length_bldg shows rectangular shape. In Length_bldg parameter, the extreme values are showing deviated trend. This is happening due to uncommon configuration of brick building construction in case study area.

The scatter plot between various independent variables and the total cost is showing near to linear relation.

(ii)	Check for Normality

Referring the normal probability plot, Most of the residuals fall within the confidence band. It has also been observed that few extreme values are falling beyond the confidence band; the reason is explained in the above paragraph.

(iii)  	Non Constant Variances

Referring the residual predictor plot, rectangular plot shows that dataset is apt for the regression analysis

(iv)	Independence or Serial Correlation

For evaluating serial correlation for independent variables, most of the values of standard correlation exhibit values below critical values. Hence indicating the independence of the data.

(v)	Outliers

One dataset has values of cook’s D more than One. Otherwise for all dataset, the Cook’s D values are below 1. This shows that datasets are free from outliers.Looking at the Dfbetas Section, if any Dfbetas beyond the cutoff of ( 2/(n, which comes out to be 0.140 indicate influential observations. There are 7 dataset that shows values exceeding those values. Other than these all dataset have values less than 0.14. Hence showing maximum dataset are non-outliers.

(vi)	Multicollinearity

Looking at the Multicollinearity Section, if any variable has a variance inflation factor greater than 10, it depicts the Multicollinearity problems. Analysis shows all the values are less than 10; hence collinearity is not a problem. Looking at the Eigen values of Centered Correlations Section, Condition numbers greater than 1000 indicate severe collinearity. In analysis all values are falling below 100, thus there is no problem of collinearity.

(vii)	Predictability

Referring analysis of variance section, if the Press R Squared is almost as large as the R Squared, the result is as per expectation. The value of R square is 96.3 % which shows that projected values are 96.3 % closer to Actual Values. The Figure 7.22 shows that projected values are coming very close actual result.

Figure 7.22: Comparison between Actual Reconstruction Cost and Regression Cost (Brick Building)

After applying above check of validity, the actual estimated cost and results though regression is compared and the effectiveness of regression is worked out, it is found that the results are accurate up to 95 % as shown in Figure 7.22.

(d)	Checking Results on Other Data with the Study Area

For checking the validity of regression analysis, another 40 set of data is taken from the study area. The cost of reconstruction is estimated using regression model and compared with actual calculation based on algorithm. The results are checked and it is found that the results obtained from regression are coming closer to 84.30% of the actual data, hence, the calculation is showing accuracy of 83 to 84%.

7.7.2	Estimation of Cost of Mud Buildings

The mud building data is analysed for calculating the cost of construction. The parameters for multiple regressions are selected using All Possible Regression Analysis. Total cost is dependent on various transformed data which is derived from basic data like Length_bldg, Width_bldg, Depth_found, Width_found, Thickness_wall, height_roof, Gable_ht, No__Long_wall, and No__trans_wall. The result shows that three parameters are significant which dominantly influence the cost of construction of Mud buildings. The All Possible Regression Analysis is carried out. R2 value is calculated. It is found that the value of R2 gets maximum value for three variables. Hence, three parameters are taken for further analysis. Figure 7.23 shows the relationship between R2 and  variable count.

Checking for Validity of Result

R-Squared Value

Figure 7.23: Relationship between R-Squares Vs Variable Count (Mud Building)

Root MSE Value

Root MSE value is further considered for analyzing parameters for optimal number of variables most contributing towards the mud construction cost. Figure 7.24 shows the relationship between Root MSE Vs variable count.

Figure 7.24: Relationship between Root MSE Vs Variable Count (Mud Building)

The Root MSE express that at three parameters, the dataset is more deviated. So finally, three parameters are taken for analysis. These are Qty_Tin, Total_mud_wall and Total_manpower. The data is fit to multiple regression model.

(a)	Regression Modeling for Reconstruction Cost of Mud Buildings

Considering the dataset to be normally distributed, the multiple regression analysis for cost of mud buildings reconstruction has been performed using NCSS 2001® software. The total reconstruction cost does not give clear relationship between independent parameters. If applied with those parameters, the relationship is very poorly framed. So, the transformed independent parameters are considered for reconstruction cost of mud building. The problem is arising due to certain reasons. The construction cost for such buildings are very low and most of the cost is attributed due to cost of manpower and overheads. The material is attributing very less for the construction of Mud buildings. Various parameters are considered which attribute to the total cost. Out of all, only three parameters, which significantly attribute to the total cost are considered based on All Possible Regression Analysis. These are Total_mud_wall, Qty_Tin and Total_manpower. For analysis, 138 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software.

Reconstruction Cost (Rs.)

-149.60- (128.25 ×  1.10 × Total_mud_wall)+(98.50 × Qty_Tin × 1.10 ) + (3.207 × Total_manpower × 1.15 )	(7.2)

Standard

Variable	Count	Mean	Deviation	Minimum	Maximum

Total_mud_wall	138	43.17988	34.85694	12.3525	267.435

Qty_Tin	138	54.90977	38.45347	12.40231	218.3909

total_manpower	138	7060.362	4738.622	2365	28735

total_cost	138	22366.67	14705.93	6680.74	84689.58

The regression is worked out with coefficient of independent variables and constants. These values are given as:

Independent	Regression	Standard	Lower	Upper	Standardized

Variable	Coefficient	Error	95% C.L.	95% C.L.	coefficient

Intercept	-149.5966	205.1752		-555.3973	256.2042	0.0000

Total_mud_wall	-128.2533	6.113285		-140.3444	-116.1623	-0.3040

Qty_Tin	98.50106	4.925315		88.75965	108.2425	0.2576

total_manpower	3.207421	4.049562E-02	3.127328	3.287515	1.0335

T-Critical	1.977826

(b)	Validity of Regression Relationship

For checking the validity of the following regression check are required to be conducted.

(i)	Check for Linearity

The check for linearity is carried out for 3 transformed predictors. For this, the Residual vs. Predictor Plots has to be analysed. All three Independent parameters shows point shape. The scatter plot between various independent variables and the total cost is showing near to linear relation.

(ii)	Check for Normality

Referring the normal probability plot, Most of the residuals are falling with in the confidence band for the normal probability plot. It is also observed that few minimum and maximum extreme values are falling beyond the confidence band; the reason is explained in the above paragraph.

(iii) 	Non Constant Variances

Referring the residual predictor plot, rectangular plot shows that dataset is fit for the regression analysis.

(iv) 	Independence or Serial Correlation

For evaluating serial correlation for independent variables, except one all, values of standard correlation are exhibiting values below critical values. Hence indicating the independence of the data and no biasing is associated.

(v) 	Outliers

One dataset has values of cook’s D more than 1. Otherwise for all dataset, the Cook’s D values are below 1. this shows that datasets are free from outliers.

Referring at the Dfbetas Section, if any Dfbetas beyond the cutoff of ( 2/(n, which comes out to be 0.145 indicate influential observations. There are 2 dataset shows the values exceeding those values. Other than these all dataset are having values less than 0.14. Hence showing maximum dataset are non-outliers.

(vi) 	Multicollinearity

Referring at the Multicollinearity Section, If any variable has a variance inflation factor greater than 10 shows the Multicollinearity problems. In analysis shows all the values are less than 10 hence collinearity is not a problem.

Referring the Eigen values of Centered Correlations Section, Condition numbers greater than 1000 indicate severe collinearity. In analysis all values are falling below 100, thus there is no problem of collinearity.

(vii)	Predictability

Looking at the Analysis of Variance Section, if the Press R Squared is almost as large as the R Squared, you have done as well as could be expected. The value of R square is 99 % which shows that projected values are coming 99 % closer to Actual Values. The graph shows that projected values are coming very close actual result.

Figure 7.25: Comparison between Actual Mud Building Reconstruction Cost and Regression Cost

Figure 7.25 shows the comparison between estimated reconstruction cost of mud buildings and regression cost. For assessing the validity of results, the actual estimated cost and results though regression is checked and the effectiveness of regression is calculated. It is found that the results are accurate up to 97.5 %.

(c)	Checking results on other Dataset within the Study Area

For checking the validity of regression analysis, another set of 40 dataset from study area is taken. The same regression analysis is applied. The results are checked and it is found that the results are closer to 98.65 % of the estimated data.

  - Estimation of Cost of Retrofitting of Non-engineered Buildings

7.8.1	Brick Buildings

(a)	Selection of Parameters

For estimating the cost of retrofitting for brick buildings, using all possible regression, four parameters, which significantly contribute to the cost aspects, have been considered. These are Length_bldg, Width_bldg, Gable_ht and Projection. In All Possible Regression analysis, it is found that there is no much difference in R2 and Root MSE for three and four parameters. Since gable height is playing significant role in cost of retrofitting so, four parameters have been considered for cost estimation.

(b)	Multiple Regression Model

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of retrofitting of Brick Buildings is performed using NCSS 2001 software. The Retrofitting cost is worked out based on independent parameters viz. Length_bldg, Width_bldg, Gable_ht and Projection. For analysis, 149 dataset is selected. The multiple regression analysis is carried out to find out the relationship between total cost and Independent parameters. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Cost of Retrofitting for brick Building

{-941.1006+ (390.414 × Length_bldg) + (216.0124 × Width_bldg)+ (196.0521 × Gable_ht)    + (352.1179 × Projection)} × 1.10		             (7.3)

Standard

Variable	Count	Mean	Deviation	Minimum 	Maximum

Length_bldg	149	12.51597	9.338062	3	55

Width_bldg	149	4.438523	3.035693	3	30

Gable_ht	149	1.163826	0.4160392	0.25	2.5

Projection	149	0.5247584	0.1659773	0.1	0.84

total_retrofitting_cost	149	5317.034	3544.366	1429	20498

The regression is worked out with coefficient of independent variables and constants. These values are given as:

Regression Equation Section

Independent	Regression	Standard	T-Value	Prob	Power

Variable	Coefficient	Error	(Ho: B=0)	Level	(5%)

Intercept	-941.1006	129.5383	-7.2650	0.000000	1.000000

Length_bldg	390.414	3.066621	127.3108	0.000000	1.000000

Width_bldg	216.0124	9.33485	23.1404	0.000000	1.000000

Gable_ht	196.0521	65.4346	2.9962	0.003220	0.845221

Projection	352.1179	165.8007	2.1237	0.035401	0.559484

R-Squared	0.991555

(c)	Validity of Regression Relationship

For assessing the validity, the following regression checks have been conducted.

(i)	Check for Linearity

The check for linearity is carried out for all 4 predictors. For this, the Residual vs. Predictor Plots has to be analysed. All four Independent parameters show rectangular shape. The scatter plot between various independent variables and the total cost is showing near to linear relation.

(ii)	Check for Normality

Referring normal probability plot, most of the residuals are falling with in the confidence band for the normal probability plot. It is also observed that few extreme values are falling beyond the confidence band.

(iii)  	Non Constant Variances

Referring residual predictor plot, rectangular plot shows that dataset is apt for the regression analysis.

(iv)  	Independence or Serial Correlation

Evaluating serial correlation for independent variables, All standard correlation exhibit values below critical values. Hence indicating the independence of the data and no biasing is associated.

(v)	Outliers

One dataset has values of cook’s D more than one. Otherwise for all dataset, the Cook’s D values are below 1. This shows that datasets are free from outliers.

Referring the Dfbetas Section, if any Dfbetas beyond the cutoff of ( 2/(n, which comes out to be 0.140 indicate influential observations. There are 4 dataset shows the values exceeding those values. Other than few, all dataset are having values less than 0.14. Hence showing maximum dataset are non-outliers.

(vi)	Multicollinearity

Referring the Multicollinearity Section, if any variable has a variance inflation factor greater than 10, it shows the Multicollinearity problems. The analysis shows that all the values are less than 10, hence collinearity is not a problem.

In the Eigen values of Centered Correlations Section if condition numbers is greater than 1000, it indicates severe collinearity. In analysis all values are falling below 100, thus there is no problem of collinearity.

(vii)	Predictability

If the Press R Squared is almost as large as the R Squared, the result is precise. The value of R square is 99 %, which shows that projected values are 99 % closer to actual values. The graph shows that projected values are coming very close actual result.

The regression equation 7.4 is once again applied to the dataset and analysis is carried out. The result shows that there is an efficiency of 95.25% i.e. result is correct to the extent of 95.25%.

(d)	Checking Results on other Dataset within the Study Area

For checking the validity of regression analysis, another set of 40 houses from study area is considered. The same regression analysis is applied. The results are checked and it is found that the results are coming closer to 92.78 % of the estimated data. The Figure 7.26 shows the results and closeness to the actual data.

Figure 7.26: Figure showing Closeness of Data w.r.t. Estimated and Regressed Data (Brick Building)

7.8.2	Mud Building Retrofitting

(a)	Selection of Parameters

For estimating the cost of retrofitting for mud buildings, four parameters are considered which significantly contribute to the cost aspects. These are Length_bldg, Width_bldg, Gable_ht and Projection. In All Possible Regression analysis, it is found that there is not much difference in R2 and Root MSE for three and four parameters. Since gable height plays significant role in cost of retrofitting so, four parameters are considered for cost estimation.

(b)	Multiple Regression Model

The validity of proposed model is checked and found that the model is acceptable. All the parameters are critically checked which may be referred in following section.

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of retrofitting of Mud Buildings had been performed using NCSS 2001 software. Out of all, only four parameters, which significantly attribute to the total cost are considered based on All Possible Regression Analysis. These are Length_bldg, Width_bldg, Gable_ht and Projection. For analysis, 140 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software.

Cost of Retrofitting for Mud Building

{-45482.49 + 4459.728 × Length_bldg + 3655.026 × Width_bldg - 7398.978 × Gable_ht + 5202.654 × Projection} × 1.10	(7.4)

|  |  |  | Standard |  |  |
| --- | --- | --- | --- | --- | --- |
| Variable | Count | Mean | Deviation | Minimum | Maximum |
| Length_bldg | 140 | 12.05221 | 16.89013 | 3 | 185 |
| Width_bldg | 140 | 3.941 | 1.724537 | 3 | 15 |
| Gable_ht | 140 | 1.049857 | 0.4036916 | 0.25 | 3 |
| Projection | 140 | 0.6946857 | 0.3042166 | 0.145 | 1.8 |
| Total_Retrofitting_ expenditure | 140 | 18517.9 | 79231.41 | 3158.324 | 936466.4 |

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Decision | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% | -5% |
| Intercept | -45482.49 | 11035.41 | -4.1215 | 0.000065 | Reject Ho | 0.983499 |
| Length_bldg | 4459.728 | 137.7424 | 32.3773 | 0 | Reject Ho | 1 |
| Width_bldg | 3655.026 | 1356.591 | 2.6943 | 0.00795 | Reject Ho | 0.762727 |
| Gable_ht | -7398.978 | 5700.817 | -1.2979 | 0.196542 | Accept Ho | 0.251592 |
| Projection | 5202.654 | 7643.885 | 0.6806 | 0.497272 | Accept Ho | 0.103739 |
| R-Squared | 0.88716 |  |  |  |  |  |

(c)	Validity of Regression Relationship

For checking the validity of the following regression check are required to be conducted.

(i)	Check for Linearity

The check for linearity is carried out for all 4 predictors. For this, the Residual vs. Predictor Plots has to be analysed. Three other Independent parameters show rectangular shape than Length_bldg. The scatter plot between various independent variables and the total cost shows near to linear relation.

(ii)	Check for Normality

Referring the normal probability plot, most of the residuals are falling with in the confidence band for the normal probability plot. It has also been observed that few early extreme values fall beyond the confidence band. The reason is explained in previous section.

(iii)  	Non Constant Variances

Referring the residual predictor plot, rectangular plot shows that dataset is fit for the regression analysis

(iv)  	Independence or Serial Correlation

Evaluating serial correlation for independent variables, all standard correlation is exhibit values below critical values. Hence indicating the independence of the data and no biasing is associated.

(v)	Outliers

One dataset has values of cook’s D more than one. Otherwise for all dataset, the Cook’s D values are below 1. This shows that datasets are free from outliers.

Looking at the Dfbetas Section, if any Dfbetas beyond the cutoff of ( 2/(n, which comes out to be 0.140 indicate influential observations. There are 6 dataset that shows the values exceeding those values. Other than these, all dataset are having values less than 0.14. Hence showing maximum dataset are non-outliers.

(vi)	Multicollinearity

Referring the Multicollinearity Section, If any variable has a variance inflation factor greater than 10 if shows the Multicollinearity problems. Analysis shows all the values are less than 10 hence collinearity is not a problem.

Referring the Eigen values of Centered Correlations Section, Condition numbers greater than 1000 indicate severe collinearity. In analysis, one data is reelecting 125, which reflects very slight multicollinearity. Thus collinearity is not a major problem in analysis.

(vii)	Predictability

Looking at the Analysis of Variance Section, if the Press R Squared is almost as large as the R Squared, result is as per the expected value. The value of R square is coming 98 %, which shows that projected values are coming 98 % closer to Actual Values. Hence checks are validating the regression relationship

7.9	Structural Damage Assessment

It is assumed that the damage at various intensities will fit to linear multiple regression models. The damage assessment is based on following facts:

- IS code 1893:2002, Comprehensive Intensity Scale(MSK 64) provides grades of damage for various types of construction. These norms are considered as the key for assessing the damage.

- Past few decades, many earthquakes have taken place in developing and under developing countries like Iran, India, Pakistan, Turkey, Nepal, Afghanistan and South East Asian counties. These countries have experienced colossal losses of non engineered construction. The damage profile of these mega earthquakes spelt out the damageability of such buildings. This gives fare idea about extent of losses to non engineered buildings. The assumption about damage is also drawn, based on past experience of earthquakes in the region.

For establishing the proportion of damage to buildings, a set of data has been considered. Based on above stated criteria, the damage profile is generated for varying earthquake intensities of VI, VII and VIII. Based on damage to typical buildings, the cost of repair at varying intensities has been worked out. The cost of repair is based on material, manpower and man-days. The cost of repair to the damage is treated as damage cost. The ratio of cost of damage to thecost of reconstruction gives the damage ratio. The damage ratio is calculated for set of sample data and average gives the rationale for the value given below.

(a) 	Brick Buildings

- At intensity VI it is expected to have 10 % the damage to Brick walls; which require replacement of construction material

- At intensity VII it is expected to have 20 % the damage to Brick walls; which require replacement of construction material

- At intensity VI it is expected to have 30 % the damage to Brick walls; which require replacement of construction material

(b)	Mud Buildings

- At intensity VI it is expected to have 35 % the damage to mud walls

- At intensity VII it is expected to have 50 % the damage to mud walls

- At intensity VII it is expected to have 65  % the damage to mud walls

7.10	Damage Assessment of Brick Building

(a)	Damage Cost of Brick Buildings

The basis for assessment of damage at various intensities is explained in previous chapter. Broadly, damage is categorized into two types, First is tangible and the other is being intangible. The methodologies are worked out, which is explained as below:

(i)	Damage before Retrofitting at Intensity VI

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of Damage at varying intensities is performed. The total damage cost before retrofitting at Intensity VI is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Width_bldg, Thickness_wall, height_roof, Gable_ht and No__trans_wall. For analysis, 147 dataset from various parts of the case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

The regression is worked out with coefficient of independent variables and constants. These values are given as:

Cost of damage at Intensity VI

{-18579.29+ 492.8791*Length_bldg + 702.8381*Width_bldg + 24971.6* Thickness_wall + 1941.238*height_roof + 754.8861*Gable_ht + 520.0966* No__trans_wall } *1.10				(7.5)

Standard

Variable	Count	Mean	Deviation	Minimum	Maximum

Length_bldg 	147	11.36467	7.88324	3	44

Width_bldg 	147	4.756131	3.206034	3	30

Thickness_wall 	147	0.3754015	0.2365687	0.2	3

height_roof 	147	3.817942	1.001314	2.5	6.25

Gable_ht 	147	1.086715	0.3908778	0.25	1.85

No__trans_wall 	147	3.357664	2.006377	2	22

Total_damage 	147	9717.467	8390.796	2117	83540

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -18579.29 | 667.3647 | -27.8398 | 0 | 1 |
| Length_bldg | 492.8791 | 16.84641 | 29.2572 | 0 | 1 |
| Width_bldg | 702.8381 | 38.76932 | 18.1287 | 0 | 1 |
| Thickness_wall | 24971.6 | 510.5277 | 48.9133 | 0 | 1 |
| height_roof | 1941.238 | 123.4626 | 15.7233 | 0 | 1 |
| Gable_ht | 754.8861 | 303.7707 | 2.4851 | 0.014223 | 0.69382 |
| No__trans_wall | 520.0966 | 62.27648 | 8.3514 | 0 | 1 |
| R-Squared | 0.974232 |  |  |  |  |

Validity of Regression Relationship: All seven checks are performed to establishing the regression relationship between various parameters.  Analysis of Variance Section shows that the value of R square is 97 % which shows that projected values are coming 97 % closer to the actual values. The projected values are close actual result, hence, validating the regression relationship.

(ii)	Damage before Retrofitting at Intensity VII

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of Damage at varying intensities is performed. The total damage cost before retrofitting at Intensity VII is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Width_bldg, Thickness_wall, height_roof, Gable_ht and No__trans_wall. For analysis, 147 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Cost of damage at Intensity VII

{-34811.52+ 912.6431*Length_bldg + 1296.995*Width_bldg + 46102.29* Thickness_wall + 3634.135*height_roof + 1463.865*Gable_ht + 957.7581* No__trans_wall } * 1.10   				(7.6)

Standard

Variable	Count	Mean	Deviation	Minimum	Maximum

Length_bldg 	147	11.78884	8.157075	3	44

Width_bldg 	147	4.636667	3.12813	2	30

Thickness_wall 	147	0.375034	0.2291658	0.2	3

height_roof 	147	3.870122	1.011717	2.5	6.25

Gable_ht 	147	1.102585	0.3928908	0.25	1.85

No__trans_wall 	147	3.29932	1.952922	2	22

Total_damage 	147	18089.67	15309.05	3835	154253

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -34811.52 | 1194.471 | -29.1439 | 0 | 1 |
| Length_bldg | 912.6431 | 28.95891 | 31.5151 | 0 | 1 |
| Width_bldg | 1296.995 | 70.48556 | 18.4009 | 0 | 1 |
| Thickness_wall | 46102.29 | 931.5498 | 49.4899 | 0 | 1 |
| height_roof | 3634.135 | 220.4648 | 16.484 | 0 | 1 |
| Gable_ht | 1463.865 | 538.4359 | 2.7187 | 0.007383 | 0.770375 |
| No__trans_wall | 957.7581 | 112.6715 | 8.5004 | 0 | 1 |
| R-Squared | 0.973854 |  |  |  |  |

Validity of Regression Relationship: All seven checks, is performed to establish the regression relationship between various parameters.  The value of R square is worked out to be 97 % which shows that projected values are coming 97 % closer to Actual Values. The projected values are closer to the actual result, hence validating the regression relationship.

(iii)	Damage before Retrofitting at Intensity VIII

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of Damage at varying intensities is performed using NCSS 2001 software. The total damage cost before retrofitting at Intensity VIII is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Width_bldg, Thickness_wall, height_roof, Gable_ht and No__trans_wall. For analysis, 138 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Cost of damage at Intensity VIII

{-56176.54+1465.079(Length_bldg + 2083.392(Width_bldg + 74350.03( Thickness_wall + 5850.626(height_roof + 2366.006(Gable_ht + 1547.97( No__trans_wall}(1.10	 (7.7)

Standard

Variable	Count	Mean	Deviation	Minimum 	Maximum

Length_bldg 	147	11.78884	8.157075	3	44

Width_bldg 	147	4.636667	3.12813	2	30

Thickness_wall 	147	0.375034	0.2291658	0.2	3

height_roof 	147	3.870122	1.011717	2.5	6.25

Gable_ht 	147	1.102585	0.3928908	0.25	1.85

No__trans_wall 	147	3.29932	1.952922	2	22

Total_damage 	147	28997.44	24653.07	6080	248537

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -56176.54 | 1924.93 | -29.1837 | 0 | 1 |
| Length_bldg | 1465.079 | 46.66824 | 31.3935 | 0 | 1 |
| Width_bldg | 2083.392 | 113.5898 | 18.3414 | 0 | 1 |
| Thickness_wall | 74350.03 | 1501.223 | 49.5263 | 0 | 1 |
| height_roof | 5850.626 | 355.2864 | 16.4674 | 0 | 1 |
| Gable_ht | 2366.006 | 867.7072 | 2.7267 | 0.007215 | 0.772777 |
| No__trans_wall | 1547.97 | 181.5739 | 8.5253 | 0 | 1 |
| R-Squared | 0.973816 |  |  |  |  |

Validity of Regression Relationship: All seven checks, is performed to establishing the regression relationship between various parameters.  The value of R square works out to be 97 % which shows that projected values are 97 % closer to the actual values. The projected values are very close to the actual result, hence validating the regression relationship.

Testing Validity of regression relationship

To check the validity of regression relationship, 50 housing dataset is taken from study area. The relationship is applied to those housing samples. The comparison is made with actual damage cost w.r.t., estimated damage cost through regression. It is found that there is some error between actual and estimated data. Estimates show that at   intensity VI, the average precision of equation is upto 87.11%. As the intensity increases, there is a slight decrease in precision. At intensity VII, the accuracy of the regression is upto 86.75 % and at intensity VIII, the precision is confined to 86%. Therefore, the regression relationship is precise ranging from 86 to 87 %.  The figure 7.27(a, b & c) shows the variation in actual and estimated cost of damage before application of retrofitting for 50 housing dataset.

Figure 7.27(a): Comparison between Actual and Regression Damage Assessment for Brick Buildings before Retrofitting

Figure 7.27(b): Comparison between Actual and Regression Damage Assessment for Brick Buildings before Retrofitting

Figure 7.27(c): Comparison between Actual and Regression Damage Assessment for Brick Buildings before Retrofitting

(iv)	Damage after Retrofitting at Intensity VI

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of Damage at varying intensities is performed using NCSS 2001 software. The total damage cost after retrofitting at Intensity VI is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Width_bldg, Thickness_wall, height_roof, Gable_ht and No__trans_wall. For analysis, 147 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Damage Cost after Retrofitting at Intensity VI(Rs.) =

{-10648.66+ (292.9049 × Length_bldg + 478.0513 × Width_bldg + 14074.47 × Thickness_wall + 1108.614 × height_roof + 535.3107 × Gable_ht + 291.6651 × No__trans_wall)} × 1.10			(7.8)

Standard

Variable	Count	Mean	Deviation	Minimum	Maximum

Length_bldg 	147	11.78884	8.157075	3	44

Width_bldg 	147	4.636667	3.12813	2	30

Thickness_wall 	147	0.375034	0.2291658	0.2	3

height_roof 	147	3.870122	1.011717	2.5	6.25

Gable_ht 	147	1.102585	0.3928908	0.25	1.85

No__trans_wall 	147	3.29932	1.952922	2	22

Total_Damage_cost 	147	6142.313	4760.576	1757	47749

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -10648.66 | 366.1285 | -29.0845 | 0 | 1 |
| Length_bldg | 292.9049 | 8.876467 | 32.9979 | 0 | 1 |
| Width_bldg | 478.0513 | 21.60519 | 22.1267 | 0 | 1 |
| Thickness_wall | 14074.47 | 285.5381 | 49.2911 | 0 | 1 |
| height_roof | 1108.614 | 67.57674 | 16.4053 | 0 | 1 |
| Gable_ht | 535.3107 | 165.041 | 3.2435 | 0.001476 | 0.896383 |
| No__trans_wall | 291.6651 | 34.536 | 8.4452 | 0 | 1 |
| R-Squared | 0.974597 |  |  |  |  |

Validity of Regression Relationship: All seven checks are performed to establishing the regression relationship among various parameters.  The value of R square is worked out which is 97.45 %.  It shows that projected values are 97.45 % closer to actual values. The projected values are close actual result, hence, validating the regression relationship.

(v)	Damage after Retrofitting at Intensity VII

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of damage at intensity VII is performed. The total damage cost after retrofitting at Intensity VII is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Width_bldg, Thickness_wall, height_roof, Gable_ht and No__trans_wall. For analysis, 147 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The regression relationship is as below:

Damage after Retrofitting at Intensity VII

{-21476.29 + (586.1358 × Length_bldg + 959.9459 × Width_bldg + 28187.29 × Thickness_wall + 2224.869 × height_roof + 1063.842 × Gable_ht + 586.9277 × No__trans_wall) }×1.10	(7.9)

Standard

Variable	Count	Mean	Deviation	Minimum	Maximum

Length_bldg 	147	11.78884	8.157075	3	44

Width_bldg 	147	4.636667	3.12813	2	30

Thickness_wall 	147	0.375034	0.2291658	0.2	3

height_roof 	147	3.870122	1.011717	2.5	6.25

Gable_ht 	147	1.102585	0.3928908	0.25	1.85

No__trans_wall 	147	3.29932	1.952922	2	22

Total_Damage_cost 	147	12175.67	9535.535	3302	95497

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -21476.29 | 733.0793 | -29.296 | 0 | 1 |
| Length_bldg | 586.1358 | 17.77287 | 32.9792 | 0 | 1 |
| Width_bldg | 959.9459 | 43.2589 | 22.1907 | 0 | 1 |
| Thickness_wall | 28187.29 | 571.7175 | 49.3028 | 0 | 1 |
| height_roof | 2224.869 | 135.3053 | 16.4433 | 0 | 1 |
| Gable_ht | 1063.842 | 330.4527 | 3.2193 | 0.001597 | 0.891998 |
| No__trans_wall | 586.9277 | 69.14957 | 8.4878 | 0 | 1 |
| R-Squared | 0.974616 |  |  |  |  |

Validity of Regression Relationship: All seven checks are performed to establishing the regression relationship among various parameters.  The value of R square is worked out which is 97.46 %. It shows that projected values are 97.6 % closer to Actual Values. The projected values are close actual result, hence, validating the regression relationship.

(vi)	Damage after Retrofitting at Intensity VIII

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of Damage at intensity VII is performed. The total damage cost after retrofitting at Intensity VIII is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Width_bldg, Thickness_wall, height_roof, Gable_ht and No__trans_wall. For analysis, 147 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The regression relationship is as below:

Damage after Retrofitting at Intensity VIII =

{-37696.24+ (1025.596 × Length_bldg + 1678.627 × Width_bldg + 49354.56 × Thickness_wall + 3898.735 × height_roof + 1865.534 × Gable_ht + 1027.478 × No__trans_wall)} × 1.10 			(7. 10)

Standard

Variable	Count	Mean	Deviation	Minimum 	Maximum

Length_bldg 	147	11.78884	8.157075	3	44

Width_bldg 	147	4.636667	3.12813	2	30

Thickness_wall 	147	0.375034	0.2291658	0.2	3

height_roof 	147	3.870122	1.011717	2.5	6.25

Gable_ht 	147	1.102585	0.3928908	0.25	1.85

No__trans_wall 	147	3.29932	1.952922	2	22

Total_Damage_cost 	147	21222.7	16693.75	5806	167112

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -37696.24 | 1284.417 | -29.3489 | 0 | 1 |
| Length_bldg | 1025.596 | 31.13958 | 32.9355 | 0 | 1 |
| Width_bldg | 1678.627 | 75.79328 | 22.1474 | 0 | 1 |
| Thickness_wall | 49354.56 | 1001.698 | 49.2709 | 0 | 1 |
| height_roof | 3898.735 | 237.0663 | 16.4458 | 0 | 1 |
| Gable_ht | 1865.534 | 578.9813 | 3.2221 | 0.001583 | 0.892504 |
| No__trans_wall | 1027.478 | 121.1559 | 8.4806 | 0 | 1 |
| R-Squared | 0.974576 |  |  |  |  |

Testing Validity of Regression Relationship

To check the validity of regression relationship, the 41 housing dataset is taken from study area. The relationship is applied to those housing samples. The comparison is made with actual damage cost w.r.t., estimated damage cost through regression. It is found that there is some error between actual and estimated data. Estimates show that at   intensity VI, the average precision of equation is upto 88.33 %. As the intensity increases, there is a slight decrease in precision. At intensity VII and VII,  the accuracy of the regression is 88.12 %. Therefore, the regression relationship is precise ranging from 88 %.  The figure 7.28 (a, b & c) shows the variation in actual and estimated cost of damage after application of retrofitting for 41 housing dataset.

Figure 7.28 (a): Comparison between Actual and Estimated Damage Cost through Regression for Brick Buildings after Retrofitting

Figure 7.28 (b): Comparison between Actual and Estimated Damage Cost through Regression for Brick Buildings after Retrofitting

Figure 7.28 (c): Comparison between Actual and Estimated Damage Cost through Regression for Brick Buildings after Retrofitting

(b)	Casualty Estimation for Brick Building

Using the lethality ratio, the human loss is estimated. The monetary valuation of various grade of injury is worked out based on Relief Manual of Government of Madhya Pradesh. The estimation of value of human life is illustrated in following section.

The death and injury is worked out based on Lethality ratio discussed in chapter 6. The parameters for calculation of death and injury are worked out based on following rationale.

Population per Building (M1) is calculated based on field survey. The M1 factor for the study area is 5.378. Occupancy at Time of Earthquake (M2) is calculated during the field data collection. Based on field survey, the occupancy time (Figure 7.29) is plotted for the study area, which is shown below:

M2-1 = Occupancy at day time 40%

M2-2 = Occupancy at night time 95 %

Figure 7.29: Occupancy Rate for Residential Houses

Occupants Trapped by Collapse (M3) is based on studies conducted by Okada & Pomonis (1990). They have carried out the research for people trapped in collapsed buildings caused by earthquake based on data from developing countries. Same parameters have been adopted for the current research, which is given as:

Intensity 	Factor( M3)

VI		Nil

VII		5%

VIII		30%

The causes of death and injury of those trapped inside damaged structures varies considerably. There are some evidences that different types of buildings cause injuries in different ways and different severity when they collapse. In masonry buildings, a primary cause of death is often suffocation from the weight and dust of collapsed wall or roof material, which buries the victims. A number of injury severity scales are proposed (Noji, 1989), one of the simplest and most useful to emergency managers is the four point standard triage categorization of injuries. The same coefficients are adopted in present research work.

Triage Injury Category	Masonry

1.   Dead or Unsaveable (MMas4-1)	20

2.	Life threatening cases needing immediate medical attention (MMas4-2)	30

3.	Injury requiring hospital treatment (MMas4-3)	30

4.	Light injury nor necessary hospitalization (MMas4-4)	20

Triage injury category	Mud

- Dead or Unsaveable (MMud4-1)	10

- Life threatening cases needing immediate medical attention (MMud4-2)	30

- Injury requiring hospital treatment (MMud4-3)	40

- Light injury nor necessary hospitalization (MMud4-4)	 20

Based on the parameters stated above the injury and deaths are calculated for various intensities for mud and brick residential buildings.  The valuation of deaths and injuries has been worked out based on government circulars of Revenue Department of Madhya Pradesh.

The parameters are summarized in Table 7.2

Table 7.2: Coefficients for Casualty Estimation

| Parameters for Mud Buildings | Parameters for Brick Building |
| --- | --- |
| M1Population per Building M1 = 5.378 M2Occupancy at the Time of Earthquake M2-1 = Occupancy at day time 40% M2-2 = Occupancy at night time 95% M3 Occupants Trapped by Collapse VI Nil VII 5% VIII 30% M4 Triage injury category Dead or Unsaveable MMud4-1 10 Life threatening cases needing immediate medical attention MMud4-2 30 Injury requiring hospital treatment MMud4-3 40 Light injury nor necessary hospitalization MMud4-4 20 | M1Population per Building M1 = 5.378 M2Occupancy at the Time of Earthquake M2-1 = Occupancy at day time 40% M2-2 = Occupancy at night time 95% M3 Occupants Trapped by Collapse VI Nil VII 5% VIII 30% M4 Triage injury category Dead or Unsaveable MMas4-1 20 Life threatening cases needing immediate medical attention MMas4-2 30 Injury requiring hospital treatment MMas4-3 30 Light injury nor necessary hospitalization MMas4-4 20 |

Value of various grades of Injury ( Madhya Pradesh Relief Book)

Death value 		Rs. 50,000

Severe Value 		Rs. 40,000

Medium Value	Rs. 25,000

Minor Value 		Rs. 15,000

The Intangible damage includes rental, functional and property losses induced by earthquake. The details are given as follows

(c)	Rental Losses

The rental cost of various types of buildings has been worked out based on locally available data. The rental loss is a function of functionality loss of buildings due to damage and rental charges per day. The functionality losses (LOF) are the function of built-up area and man-days required for repair.

RT = RLoss × LOF	 (7.11)

is the function of percentage of replacement cost per day . For brick buildings, the annual rental charges are calculated at 8 % of replacement cost.

(7.12)

For calculation of loss of function, a set of buildings are considered for analysis. Expected damages at various intensities are worked out for set of buildings. The man-days are calculated for repair such buildings at varying intensities. The regression analysis is performed between built-up area of house and restoration time. The relationship between built-up area and restoration time due to damage at varying earthquake intensities are established, which can be referred at 7.13, 7.14 and 7.15. It is assumed that the relationship is linear.

Total damage restoration time for intensity VI = 1.42+ 6.63E-02 × Area	(7.13)

Total damage restoration for time intensity VII = 2.35+ .132 × Area 	(7.14)

Total damage restoration for time intensity viii = 3.6376+ .221 × Area	 (7.15)

The rental cost for both brick and mud buildings are calculated on the basis of percentage of reconstruction cost. The rental charges are worked out on per day basis for Pandhana region

(d)	Relocation Loss

The relocation cost is same as rental losses in case of earthquake. Therefore, the value of relocation loss is treated equal to rental losses.

(e)	Property Loss

The property losses are calculated based on past experience of earthquake damage.  The values are derived from past earthquakes.

During survey of buildings, household survey was also conducted. Initially, a written questionnaire was circulated, but feedback was not reflected positive. Later other survey tool like passive observation and personal interview was conducted to understand the household items and personal property of inhabitants. Based on survey, it was found that occupants of low income groups are having minimal household items. Mostly houses are having day to day edible items, minimum requirements and some furniture. People are mostly farmers, largely depending upon manual tools and equipments. Due to poor power supply, the electrical accessories were missing. Based on their household items, an average cost of household items was worked out. The household cost is correlated to reconstruction cost. Depending on expected damage, the cost of personal property damage is projected in present work as % of reconstruction cost.

It is assumed that when the building is retrofitted, the building will be safe and will not collapse. Only non-structured damages will be reported. Due to such damages, there are chances that some personal properties will be damaged. The quantum of damage will be less than without retrofitting case. This factor has been worked out. The damage factors before and after retrofitting are given below for reference. Based on these factors, the economic assessment is done. The property loss (%) has been estimated for brick and mud buildings, before and after retrofitting.

Personal Property Loss =  (Cost of Replacement) x Proportion of Damage 	(7.16)

(i)	Brick Buildings	Property loss (% age of Reconstruction cost)

Intensity VI	15 %

Intensity VII	30%

Intensity VIII	50%

(ii)	Mud Buildings	Proportion of Damage (%age of Reconstruction cost)

Intensity VI	50%

Intensity VII	70%

Intensity VIII	90%

After earthquake retrofitting, the proportion of damage is as below:

(i)	Brick Buildings	Proportion of Damage (%age of Reconstruction cost)

Intensity VI	10 %

Intensity VII	20%

Intensity VIII	35%

(ii)	Mud Buildings	Proportion of Damage (%age of Reconstruction cost)

Intensity VI	35%

Intensity VII	50%

Intensity VIII	65%

7.11	Damage Cost of Mud Buildings

(a)	Structural Damage Assessment

The cost of sample mud building dataset is considered and damages are worked out.  The multiple regression analysis is carried out using NCSS® 2001. The validity of the regression equation is performed following the seven checks explained in chapter 6. It is assumed that the damage at various intensities is fitted to linear multiple regression models. The damage at particular intensity is worked out which, is shown in following paragraph.

(i)	Damage before Retrofitting at Intensity VI

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of damage at varying intensities is performed. The total damage cost before retrofitting at Intensity VI is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Thickness_wall and height_roof. These parameters are selected using All Possible Regression Analysis. For analysis, 138 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Cost of Damage at Intensity VI before retrofitting =

{-10460.17+ (447.4066 × Length_bldg+ 12827.73 × Thickness_wall + 2129.542× height_roof)} ×1.10	 (7.17)

Standard

Variable	Count	Mean	Deviation	Minimum 	Maximum

Length_bldg	138	11.28341	8.154883	3	58

Thickness_wall	138	0.4013043	5.974185E-02	0.3	0.7

height_roof	138	3.382609	0.7477375	1.85	7

Total_Damage	138	6939.333	4796.806	2242	30799

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -10460.17 | 733.4457 | -14.2617 | 0 | 1 |
| Length_bldg | 447.4066 | 13.15913 | 33.9997 | 0 | 1 |
| Thickness_wall | 12827.73 | 1739.703 | 7.3735 | 0 | 1 |
| height_roof | 2129.542 | 148.9149 | 14.3004 | 0 | 1 |
| R-Squared | 0.941898 |  |  |  |  |

Validity of Regression Relationship: All seven checks, which is performed to establishing the regression relationship between various parameters.  Analysis of Variance Section shows that the value of R square is 94 % which shows that projected values are 94 % closer to actual values. The projected values are close actual result. Hence, this validates the regression relationship.

(ii)	Damage cost of Mud Buildings before Retrofitting at Intensity VII

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of damage at varying intensities is performed. The total damage cost before retrofitting at Intensity VII is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Thickness_wall and height_roof. These parameters are selected using All Possible Regression analysis. For analysis, 138 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Cost of Damage at Intensity VII before retrofitting =

{-14641.42+ 592.2764 × Length_bldg+ 18032.21 × Thickness_wall + 2922.767 × height_roof}×1.10	(7.18)

Standard

Variable	Count	Mean	Deviation	Minimum 	Maximum

Length_bldg	138	11.28341	8.154883	3	58

Thickness_wall	138	0.4013043	5.974185E-02	0.3	0.7

height_roof	138	3.382609	0.7477375	1.85	7

Total_Damage	138	9164.456	6429.212	2871	41868

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -14641.42 | 995.5121 | -14.7074 | 0 | 1 |
| Length_bldg | 592.2764 | 17.861 | 33.1603 | 0 | 1 |
| Thickness_wall | 18032.21 | 2361.313 | 7.6365 | 0 | 1 |
| height_roof | 2922.767 | 202.1234 | 14.4603 | 0 | 1 |
| R-Squared | 0.940415 |  |  |  |  |

Validity of Regression Relationship: All seven checks, which is performed to establishing the regression relationship between various parameters.  Analysis of Variance Section shows that the value of R square is 94 % which shows that projected values are 94 % closer to Actual Values. The projected values are close actual result. Hence, this validates the regression relationship. The statistical suitability of the model is checked and found to be satisfactory.

(iii)	Damage cost of Mud Buildings before Retrofitting at Intensity VIII

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of damage at varying intensities is performed. The total damage cost before retrofitting at Intensity VIII is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Thickness_wall and height_roof. These parameters are selected using All Possible Regression analysis. For analysis, 138 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Cost of Damage at Intensity VIII before retrofitting =

{-18873.92+ (737.0989 × Length_bldg + 23258 × Thickness_wall + 3729.831 × height_roof)} × 1.10	(7.19)

Standard

Variable	Count	Mean	Deviation	Minimum 	Maximum

Length_bldg	138	11.28341	8.154883	3	58

Thickness_wall	138	0.4013043	5.974185E-02	0.3	0.7

height_roof	138	3.382609	0.7477375	1.85	7

Total_Damage	138	11393.16	8070.753	3486	53012

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -18873.92 | 1261.396 | -14.9627 | 0 | 1 |
| Length_bldg | 737.0989 | 22.63137 | 32.5698 | 0 | 1 |
| Thickness_wall | 23258 | 2991.979 | 7.7734 | 0 | 1 |
| height_roof | 3729.831 | 256.1071 | 14.5636 | 0 | 1 |
| R-Squared | 0.939293 |  |  |  |  |

Validity of Regression Relationship: All seven checks, which is performed to establishing the regression relationship between various parameters.  Analysis of Variance Section shows that the value of R square is 93.9 % which shows that projected values are 93.9 % closer to Actual Values. The projected values are close actual result. Hence, this validates the regression relationship. The statistical suitability of the model is checked and found to be satisfactory.

Testing Validity of Regression Relationship

To check the validity of regression relationship, the 41 housing dataset is taken from study area. The relationship is applied to those housing samples. The comparison is made with actual damage cost w.r.t., estimated damage cost through regression. It is found that there is some error between actual and estimated data. The calculation shows that at   intensity VI, the average precision of equation is upto 88.0 %. As the intensity increases, there is a slight decrease in precision. At intensity VII and VII, the accuracy of the regression are 87 % and 86.5 % respectively. Therefore, the regression relationship is precise ranging from 86 % to 88%.  The figure 7.30 (a, b & c) shows the variation in actual and estimated cost of damage before retrofitting for 41 housing dataset.

Figure 7.30 (a): Comparing Actual VS Estimated Mud Building Damage Cost before Retrofitting for Varying Intensities

Figure 7.30 (b): Comparing Actual VS Estimated Mud Building Damage Cost before Retrofitting for Varying Intensities

Figure 7.30 (c): Comparing Actual VS Estimated Mud Building Damage Cost before Retrofitting for Varying Intensities

(iv)	Damage Assessment after Retrofitting at Intensity VI

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of damage at varying intensities is performed. The total damage cost after retrofitting at Intensity VI is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Thickness_wall, height_roof and Gable_ht. These parameters are selected using All Possible Regression analysis. For analysis, 138 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Cost of Damage at Intensity VI after retrofitting =

{-3313.167+ (216.4862 × Length_bldg + 4122.6 × Thickness_wall + 660.4294 × height_roof + 350.1758 × Gable_ht )} × 1.10	 (7.20)

Standard

Variable	Count	Mean	Deviation	Minimum	Maximum

Length_bldg	138	11.28341	8.154883	3	58

Thickness_wall	138	0.4013043	5.974185E-02	0.3	0.7

height_roof	138	3.382609	0.7477375	1.85	7

Gable_ht	138	1.059638	0.4025202	0.25	3

Total_Damage	138	3388.986	2113.154	1247	12058

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -3313.167 | 314.092 | -10.5484 | 0 | 1 |
| Length_bldg | 216.4862 | 5.230657 | 41.388 | 0 | 1 |
| Thickness_wall | 4122.6 | 704.8749 | 5.8487 | 0 | 0.99994 |
| height_roof | 660.4294 | 60.74666 | 10.8719 | 0 | 1 |
| Gable_ht | 350.1758 | 102.5399 | 3.415 | 0.000846 | 0.923684 |
| R-Squared | 0.953052 |  |  |  |  |

Validity of Regression Relationship: All seven checks, which is performed to establishing the regression relationship between various parameters.  Analysis of Variance Section shows that the value of R square is 95 % which shows that projected values are 95 % closer to Actual Values. The statistical suitability of the model is checked and found to be satisfactory.

(v)	Damage Assessment after Retrofitting at Intensity VII

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of damage at varying intensities is performed. The total damage cost after retrofitting at Intensity VII is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Thickness_wall, height_roof and Gable_ht. These parameters are selected using All Possible Regression analysis. For analysis, 138 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Cost of Damage at Intensity VII after retrofitting =

{-5033.762+ (324.3157 × Length_bldg + 6088.801 × Thickness_wall + 942.0339 × height_roof + 555.192 × Gable_ht)} × 1.10	(7.21)

Standard

Variable	Count	Mean	Deviation	Minimum	Maximum

Length_bldg	138	11.28341	8.154883	3	58

Thickness_wall	138	0.4013043	5.974185E-02	0.3	0.7

height_roof	138	3.382609	0.7477375	1.85	7

Gable_ht	138	1.059638	0.4025202	0.25	3

Total_Damage	138	4843.92	3142.713	1673	17700

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -5033.762 | 459.6355 | -10.9516 | 0 | 1 |
| Length_bldg | 324.3157 | 7.65443 | 42.3697 | 0 | 1 |
| Thickness_wall | 6088.801 | 1031.499 | 5.9029 | 0 | 0.999952 |
| height_roof | 942.0339 | 88.89535 | 10.5971 | 0 | 1 |
| Gable_ht | 555.192 | 150.0546 | 3.6999 | 0.000315 | 0.956655 |
| R-Squared | 0.954545 |  |  |  |  |

Validity of Regression Relationship: All seven checks, which is performed to establishing the regression relationship between various parameters.  Analysis of Variance Section shows that the value of R square is 95.45 % which shows that projected values are 95.45 % closer to actual values. The statistical suitability of the model is checked and found to be satisfactory.

(vi) 	Damage Assessment after Retrofitting at Intensity VIII

Considering the dataset to be normally distributed, the multiple regression analysis for the cost of damage at varying intensities is performed. The total damage cost after retrofitting at Intensity VIII is the dependent parameter which is attributed by independent parameters viz. Length_bldg, Thickness_wall, height_roof and Gable_ht. These parameters are selected using All Possible Regression analysis. For analysis, 138 dataset from various parts of case study area is considered. The maximum and minimum values of these independent variable and respective mean and standard deviation are worked out using the software. The values are as follows:

Cost of Damage at Intensity VIII after retrofitting =

{-6693.968+ (430.5028 × Length_bldg+ 7899.487 × Thickness_wall + 1236.141 × height_roof+ 749.2935 × Gable_ht)} × 1.10	(7.22)

Standard

Variable	Count	Mean	Deviation	Minimum 	Maximum

Length_bldg	138	11.28341	8.154883	3	58

Thickness_wall	138	0.4013043	5.974185E-02	0.3	0.7

height_roof	138	3.382609	0.7477375	1.85	7

Gable_ht	138	1.059638	0.4025202	0.25	3

Total_Damage	138	6309.029	4163.883	2082	23205

The regression is worked out with coefficient of independent variables and constants. These values are given as:

| Regression Equation Section |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Independent | Regression | Standard | T-Value | Prob | Power |
| Variable | Coefficient | Error | (Ho: B=0) | Level | -5% |
| Intercept | -6693.968 | 609.7384 | -10.9784 | 0 | 1 |
| Length_bldg | 430.5028 | 10.15413 | 42.3968 | 0 | 1 |
| Thickness_wall | 7899.487 | 1368.355 | 5.773 | 0 | 0.999919 |
| height_roof | 1236.141 | 117.9258 | 10.4824 | 0 | 1 |
| Gable_ht | 749.2935 | 199.0578 | 3.7642 | 0.00025 | 0.962209 |
| R-Squared | 0.954432 |  |  |  |  |

Validity of Regression Relationship: All seven checks, which is performed to establishing the regression relationship between various parameters.  Analysis of Variance Section shows that the value of R square is worked out to be 95 % which shows that projected values are 95 % closer to Actual Values. The statistical suitability of the model is checked and found to be satisfactory.

Testing Validity of Regression Relationship

To check the validity of regression relationship, the 45 housing dataset is taken from study area. The relationship is applied to those housing samples. The comparison is made with actual damage cost w.r.t., estimated damage cost through regression. It is found that there is some error between actual and estimated data. Estimates show that at   intensity VI, the average precision of equation is upto 87.35 %. As the intensity increases, there is a slight decrease in precision. At intensity VII and VII, the accuracy of the regression are 86.92 % and 86.20 % respectively. Therefore, the regression relationship is precise ranging from 86 % to 87%.  The figure 7.31 shows the variation in actual and estimated cost of damage before application of retrofitting to 45 housing dataset.

Figure 7.31(a): Comparing Actual VS Estimated Mud Building Damage Cost after Retrofitting for Varying Intensities

Figure 7.31(b): Comparing Actual VS Estimated Mud Building Damage Cost after Retrofitting for Varying Intensities

Figure 7.31(c): Comparing Actual VS Estimated Mud Building Damage Cost after Retrofitting for Varying Intensities

(b)	Casualty Estimation for Mud Building

The casualty loss assessment methodology is discussed with parameters in 7.10(b). The coefficients for estimating the values of life affected due to earthquake, is described in Table 7.2.

(c)	Rental Losses

The rental cost of mud buildings has been worked out based on locally available data. The rental loss is a function of functionality loss of buildings due to damage and rental charges per day. The functionality losses are the function of built-up area and man-days required for repair and restoration.

RT = RLoss × LOF

is the function of percentage of replacement cost per day . For Brick buildings, the annual rental charges are calculated at 8 % of replacement cost.

The rental losses are function of damage restoration time, built-up area and rental charges for building.  The restoration time is estimated for mud buildings. The relationship between built-up area and time is assumed linear. The relationship between built-up area and restoration time due to damage at varying earthquake intensities are established, which can be referred at 7.23, 7.24 and 7.25. It is assumed that the relationship is linear.

For varying intensities, the relationship is worked out, which is given below.

Total Damage Restoration Time (RT) at Intensity VI = (10.09) + (1.556E-02) × (Area)		(7.23)

Total Damage Restoration Time (RT)  at Intensity VII = (13.948) + ( .0215)  ×  (Area )		(7.24)

Total Damage Restoration Time (RT) at Intensity VIII = ( 17.819) + ( .0269)  ×  (Area) 	(7.25)

(d)	Relocation Loss

The relocation cost is same as rental losses in case of earthquake. Therefore, the value of relocation loss is treated equal to rental losses.

(e)	Property Loss

The property losses are calculated based on past experience of earthquake damage.  The values are derived from past earthquakes. The coefficients are discussed in section 7.10(e).

7.12	Average Effectiveness of Retrofitting (ERE)

The reductions in losses are calculated based on effectiveness of retrofitting measures which can be treated as profit.  The reduction in rental, functional and property losses are calculated by simply multiplying the average effectiveness of retrofitting for various categories of buildings. The application of average effectiveness of retrofitting can be referred in benefit calculations. For calculation of ERE, Set of brick and mud buildings are taken from study area. Applying the formulae mentioned above, the damage cost has been worked out before and after retrofitting. Applying the equation 7.26, the ERE has been calculated. Figure 7.32 (a, b) shows the variation of damage before and after the retrofitting. Table 7.3 is showing the coefficient of effectiveness of retrofitting for brick and mud buildings. This coefficient has been used for calculation of benefits accrued from retrofitting measures. Average effectiveness may be calculated by formula given below:

(7.26)

Figure 7.32(a): Variation in Brick Building Damage before and after Retrofitting

Figure 7.32(b): Variation in Mud Building Damage before and after Retrofitting

Table 7.3: Effectiveness of Retrofitting

| Type of construction | Effectiveness @ Intensity VI | Effectiveness @ Intensity VII | Effectiveness @ Intensity VIII |
| --- | --- | --- | --- |
| Mud | 28.2 | 20.7 | 15.6 |
| Brick | 36.48 | 31.03 | 24.99 |

7.13	General Economic Appraisal Factors

(i)	Discount Rate

The discount rate is used to calculate the present value of benefits, which occur in the future. Increasing the discount rate lowers the present value of future benefits and thus lowers benefit-cost ratios. Conversely, assuming a lower discount rate raises the present value of future benefits and increases benefit- cost ratios. However, at present, there is no clear directive regarding rate of interest for such social project. It varies from local to national level, so sensitivity analysis is conducted for finding most appropriate rate of discount for such financial planning strategy for disaster management. For present research, the NPV is calculated for varying discount rates viz., 2.5 %, 3%, 4%, 5%, 7.5% and 10 %.

(ii)	Planning Horizon

The planning horizon is the time period over which the economic benefits of strengthening programs are considered. The typical planning horizons are 20 to 30 years. Longer planning horizons compute more future benefits and thus increase benefit / cost ratios. Short planning horizons captures future benefits for fewer years and thus result in lower benefit/ cost ratios. Planning horizons for economic analysis are typically shorter because benefits or costs in the far distant future contribute relatively little to the net present value of a proposed investment.

7.14	Benefit / Cost Analysis for a Single Brick Building

Village:				Babli

Tehsil:					Pandhana

District	:				Khandwa

State:					Madhya Pradesh

Name of Owner: 			Sri. Gangaram Laxman Gujjar

Type of house				Brick

Length_bldg	12 mt.

Width_bldg	3 mt.

Depth_found	0.6 mt.

Width_found	0.3 mt.

Thickness_wall	0.45 mt.

height_roof	3 mt.

Gable_ht	1mt.

No._Long_wall	2

No._trans_wall	4

Projection	1mt.

Number of house	One

(i) 	Cost of Reconstruction (Rs.) (Refer Equation 7.1)

= {-83353 + 10327 × (height_roof)+ 2893 × (Length building)+ 14891 × (Thickness_wall) + 1582 × (Width_building)} × 1.10 = Rs. 59508.9

(ii) 	Cost of Retrofitting (Rs.) (Refer equation 	7.3)

= {-941+390  ×  Length_bldg+216  ×  Width_bldg+196  ×  Gable_ht + 352  ×  Projection} × 1.10  = Rs. 5428.50

(iii)	Damage at Various Intensities before Retrofitting ( In Rs.)

- Intensity VI (Refer equation 7.5)

Building Loss VI  = {-18579.29+ 492.8791 × Length_bldg + 702.8381 × Width_bldg + 24971.6 × Thickness_wall + 1941.238 × height_roof + 754.8861 × Gable_ht + 520.0966 × No__trans_wall} × 1.10 =  Rs. 10274

- Intensity VII (Refer equation 7.6)

Building Loss VII = {-34811.52+ 912.6431 × Length_bldg + 1296.995 × Width_bldg + 46102.29 × Thickness_wall + 3634.135 × height_roof + 1463.865 × Gable_ht + 957.7581 × No__trans_wall} × 1.10 = Rs. 18672.5

- Intensity VIII (Refer equation 7.7)

Building Loss VIII =  {-56176.54+ 1465.079 × Length_bldg + 2083.392 × Width_bldg + 74350.03 × Thickness_wall + 5850.626 × height_roof + 2366.006 × Gable_ht + 1547.97 × No__trans_wall} × 1.1 =  Rs. 29,944.2

(iv)	Damage after Retrofitting ( In Rs.)

- Intensity VI (Refer equation (7.8)

Building Loss VI =  {-10648.66+ 292.9049 × Length_bldg + 478.0513 × Width_bldg + 14074.47 × Thickness_wall + 1108.614 × height_roof + 535.3107 × Gable_ht + 291.6651 × No__trans_wall} × 1.1 =  Rs. 6228.20

- Intensity VII (Refer equation 7.9)

Building Loss VII = {-21476+ 586 × Length_bldg + 960 × Width_bldg + 28187 × Thickness_wall + 2225 × height_roof + 1064 × Gable_ht + 587 × No__trans_wall} × 1.10 =  Rs. 12329

- Intensity VIII (Refer equation 7.10)

Building Loss VIII =  {-37696+ 1026 × Length_bldg + 1679 × Width_bldg + 49355 × Thickness_wall + 3899 × height_roof + 1866 × Gable_ht + 1027 × No__trans_wall} × 1.10 =  Rs. 21480.80

The loss reduction for non-tangible parameters are calculated using ERE coefficient discussed in 7.12. The rental, relocation, personal property and human loss reduction has been calculated using ERE factors. The procedure for such calculation has been discussed in following sections. For assessment of human loss reduction, the lethality ratio has been modified and ERE factor has been multiplied to get reduction in human losses.  Accordingly the notations have been changed. The Lethality ratio (M) has been modified. As the earthquake intensity, time and level of injury change, the human loss reduction changes. The methodology has been described in detail in 7.14 and 7.15.

(v) 	Rental Losses Reduction due to Retrofitting (In Rs.)

Rental Loss Intensity (RT) =  (Replacement Cost) x Percentage of Rental Cost x Functional loss in days x Coefficient of Effectiveness of retrofitting ()

- Rental losses VI  =

Rs. 18.70

- Rental losses VII =

Rs. 29.70

- Rental losses VIII =

Rs. 38.5

(vi)	Relocational Loss Reduction (REL) ( In Rs.)

- Relocational Loss VI = Rental Loss VI = Rs. 18.70

- Relocational Loss VII = Rental Loss VII = Rs. 29.70

- Relocational Loss VII = Rental Loss VIII = Rs. 38.50

(vii) 	Property Loss Reduction (PP) ( In Rs.)

- Property Loss reduction at Intensity VI

= x

= Rs. 5427.40

- Property Loss reduction at Intensity VII

= x

= Rs. 8310.50

- Property Loss reduction at Intensity VIII

= x

= Rs. 11158.40

(viii)	Death and Injury Loss Reduction for Brick buildings (In Rs.)

(a)	Intensity VI

- M Red-Death-Day –VI	= Noh (M1 × M2 × M3 × M4 x (Death Value)

= 1 x 5.378 x 0.40 x nil x 0.10 x 50000 x 0.3648 = 0

- M Red-life threat -Day -VI = 0

- M Red-medium -Day -VI = 0

- M Red-minor-Day -VI = 0

(b) Intensity VII

Day Time Casualties

- M Red-Death-Day –VII	= Noh (M1 × M2 × M3 × M4 x (Death Value)

= 1 x 5.378 x 0.40 x 0.05 x 0.10 x 50000 x 0.3103

= Rs. 166.87  Rs. 167

- M Red-severe-Day -VII 	= Noh (M1 × M2 × M3 × M4 x (Life threat)

= 1 x 5.378 x 0.40 x 0.05 x 0.30 x 40000 x 0.3103

= Rs. 400.51  Rs. 401

- M Red-medium-Day –VII	= Noh (M1 × M2 × M3 × M4 x (Hospitalization)

= 1 x 5.378 x 0.40 x 0.05 x 0.40 x 25000 x 0.3103

= Rs. 333.75 Rs. 334

- M Red-minor-Day -VII 	= Noh (M1 × M2 × M3 × M4 x (Minor)

= 1 x 5.378 x 0.40 x 0.05 x 0.20 x 15000x 0.3103

= Rs. 100.12  Rs.101

Night Time Casualties

- M Red-Death-night -VII 	= Noh (M1 × M2 × M3 × M4 x (Death Value)

= 1 x 5.378 x 0.95 x 0.05 x 0.10 x 50000 x 0.3103

= Rs. 396

- M Red-severe-night -VII 	= Noh (M1 × M2 × M3 × M4 x (Life threat)

= 1 x 5.378 x 0.95 x 0.05 x 0.30 x 40000 x 0.3103

= Rs. 951.21  Rs. 952

- M Red-medium-night –VII = Noh (M1 × M2 × M3 × M4 x (Hospitalization)

= 1 x 5.378 x 0.95 x 0.05 x 0.40 x 25000 x 0.3103

= Rs. 793

- M Red-life minor-night-VII = Noh (M1 × M2 × M3 × M4 x (Minor)

= 1 x 5.378 x 0.95 x 0.05 x 0.20 x 15000x 0.3103

= Rs. 238

Day Time Casualties

- M Red-Death-Day –VIII	= Noh (M1 × M2 × M3 × M4 x (Death Value)

= 1 x 5.378 x 0.40 x 0.30 x 0.10 x 50000 x 0.2499

= Rs. 806.37 Rs.807

- M Red-severe-Day –VIII	= Noh (M1 × M2 × M3 × M4 x (Life threat)

= 1 x 5.378 x 0.40 x 0.30 x 0.30 x 40000 x 0.2499

= Rs. 1935.30  Rs. 1936

- M Red-medium-Day –VII	 = Noh (M1 × M2 × M3 × M4 x (Hospitalization)

= 1 x 5.378 x 0.40 x 0.30x 0.40 x 25000 x 0.2499

= Rs. 1612.75  Rs. 1613

- M Red-minor-Day –VIII = Noh (M1 × M2 × M3 × M4 x (Minor)

= 1 x 5.378 x 0.40 x 0.30x 0.20 x 15000x 0.2499

= Rs. 483.82 Rs.484

Night Time Casualties

- M Red-Death-night -VIII = Noh (M1 × M2 × M3 × M4 x (Death Value)

= 1 x 5.378 x 0.95 x 0.30 x 0.10 x 50000 x 0.2499

= Rs. 1915.14  Rs. 1916

- M Red-severe-night -VIII = Noh (M1 × M2 × M3 × M4 x (Life threat)

= 1 x 5.378 x 0.95 x 0.30x 0.30 x 40000 x 0.2499

= Rs. 4596.35  Rs. 4597

- M Red-medium-night -VIII = Noh (M1 × M2 × M3 × M4 x (Hospitalization)

= 1 x 5.378 x 0.95 x 0.30 x 0.40 x 25000 x 0.2499

= Rs. 3830.29 Rs.3831

- M Red-minor-night-VIII 	= Noh (M1 × M2 × M3 × M4 x (Minor)

= 1 x 5.378 x 0.95 x 0.30 x 0.20 x 15000x 0.2499

= Rs. 1143.087  Rs.1144

Table 7.4: Reduction of Human Losses due to Retrofitting  (in Rs.)

| S. No | Grade of casualties | Intensity VI | Intensity VII | Intensity VIII |
| --- | --- | --- | --- | --- |
|  |  | Day | Night | Day | Night | Day | Night |
| 1 | Death (M4-1) | 0 | 0 | 167 | 396 | 807 | 1916 |
| 2 | Life threat (M4-2) | 0 | 0 | 401 | 952 | 1936 | 4597 |
| 3 | Hospitalization (M4-3) | 0 | 0 | 334 | 793 | 1613 | 3831 |
| 4 | Minor (M4-4) | 0 | 0 | 101 | 238 | 484 | 1144 |
| Total Loss reduction | 0 | 0 | 1003 | 2379 | 4840 | 11488 |

(ix)	Net Present Value at Intensity VI

+

= Damage of building X rehabilitation effectiveness

= 10274  ×  0.3648 = Rs. 3748

Bt = 0.170 x (3748+18.70 +18.70 + 5427) = Rs. 1566.40

Varying discount rate and time the sensitivity analysis is conducted. The calculated amount at various intensities may be referred at figure 7.33(a-e).

The characteristics of  net present value with respect to period for benefit realization, discount rate and damage scenario for brick building has been shown in form of 3D graph at Figure  7.34.

Figure 7.33(a): Net Present Value of Retrofitting of Brick Buildings

Figure 7.33(b): Net Present Value of Retrofitting of Brick Buildings

Figure 7.33(c): Net Present Value of Retrofitting of Brick Buildings

Figure 7.33(d): Net Present Value of Retrofitting of Brick Buildings

Figure 7.33(e): Net Present Value of Retrofitting of Brick Buildings

Figure 7.34: Time Required in Years to Realize the Benefits for Single Brick Building

7.15	Benefit / Cost Analysis for a Sample Mud Building

Village:				Kusumbia

Tehsil:					Pandhana

District	:				Khandwa

State:					Madhya Pradesh

Name of Owner: 			Sri. Dharmendra Singh

Type of house				Mud

Length_bldg	8 m

Width_bldg	4 m

Depth_found	0.6 m

Width_found	1 m

Thickness_wall	0.5 m

height_roof	4 m

Gable_ht	0.75 m

No._Long_wall	2

No._trans_wall	4

Projection	0.56 m

Total Mud Wall (derived from Algorithm)	44.55 cum

Total Quantity of wood roof (derived from Algorithm)	1.50 cum

Quantity of Tin (derived from Algorithm)	38.65 sq.m

Quantity of bean (derived from Algorithm)	0.96 cum

Quantity of column (derived from Algorithm)	1.75 cum

Plank required 		2.71 cum

Number of house							One

(i)	Cost of Replacement	(Refer equation 7.2)

-149.60-(128.25 ×  Total_mud_wall-98.50 ×  Qty_Tin) ×  1.10 + 3.207 ×  1.15 ×  Total_Manpower = Rs. 33580

(ii)	Cost of Retrofitting (Refer equation 7.4)

{-45483+ 4460 × Length_bldg + 3655 × Width_bldg -7399 × Gable_ht + 5203 × Projection}  × 1.10  = Rs. 2662.00

(iii)	Damage at Various Intensities before Retrofitting

- Intensity VI(Refer equation 7.11)

Building Loss VI = {-10460.17+ 447.4066 × Length_bldg+ 12827.73 × Thickness_wall+ 2129.542 × height_roof} × 1.10 =  Rs. 8856.00

- Intensity VII(Refer equation 7.12)

Building Loss VII = -14641.42+ 592.2764 × Length_bldg+ 18032.21 × Thickness_wall+ 2922.767 × height_roof = Rs. 11884.00

- Intensity VIII (Refer equation 7.13)

Building Loss VIII = -18873.92+ 737.0989 × Length_bldg+ 23258 × Thickness_wall+ 3729.831 × height_roof =  Rs. 14928.00

(iv)	Damage Reduction after Retrofitting

- Intensity VI (Refer equation7.14)

Building Loss VI = -3313.167+ 216.4862 × Length_bldg+ 4122.6 × Thickness_wall + 660.4294 × height_roof+ 350.1758 × Gable_ht = Rs. 3722.00

- Intensity VII (Refer equation7.15)

Building Loss VII = -5033.762+ 324.3157 × Length_bldg+ 6088.801 × Thickness_wall+ 942.0339 × height_roof+ 555.192 × Gable_ht =  Rs. 5269.0

- Intensity VIII (Refer equation7.16)

Building Loss VIII = -6693.968+ 430.5028 × Length_bldg+ 7899.487 × Thickness_wall+ 1236.141 × height_roof+ 749.2935 × Gable_ht =  Rs. 6826.0

(v) 	Rental losses reduction due to retrofitting

Rental Loss Intensity = (Replacement Cost) x Percentage of Rental Cost x Functional loss in days x Coefficient of Effectiveness of retrofitting

- Rental losses VI  =

Rs. 10.00

- Rental losses VII =

Rs. 10.00

- Rental losses VIII = Rs. 10.00

(vi)	Relocational Loss Reduction

- Relocational Loss VI = Rental Loss VI = Rs. 10.00

- Relocational Loss VII = Rental Loss VII = Rs. 10.00

- Relocational Loss VII = Rental Loss VIII = Rs. 10.00

(vii) 	Property Loss Reduction

- Property Loss reduction at Intensity VI

= x

= Rs. 2322

- Property Loss reduction at Intensity VII

= x

= Rs. 2436.5

- Property Loss reduction at Intensity VIII

= x

= Rs. 3283.5

(viii)	Death and injury loss reduction for mud buildings

(a)	Intensity VI

- M Red-Death-Day -VI = Noh (M1 × M2 × M3 × M4 x (Death Value)

= 1 x 5.378 x 0.40 x 0.05 x 0.10 x 50000 x 0.282 = 0

- M Red-life threat -Day -VI = 0

- M Red-medium -Day -VI = 0

- M Red-minor-Day -VI = 0

(b)	Intensity VII

Day Time Casualties

- M Red-Death-Day -VII = Noh (M1 × M2 × M3 × M4 x (Death Value)

= 1 x 5.378 x 0.40 x 0.05 x 0.10 x 50000 x .207

= Rs. 111.32 Rs. 112

- M Red-severe-Day -VII = Noh (M1 × M2 × M3 × M4 x (Life threat)

= 1 x 5.378 x 0.40 x 0.05 x 0.30 x 40000 x .207

= Rs. 267.17 Rs. 268

- M Red-medium-Day -VII = Noh (M1 × M2 × M3 × M4 x (Hospitalization)

= 1 x 5.378 x 0.40 x 0.05 x 0.40 x 25000 x .207

= Rs. 222.6492 Rs. 223

- M Red-minor-Day -VII = Noh (M1 × M2 × M3 × M4 x (Minor)

= 1 x 5.378 x 0.40 x 0.05 x 0.20 x 15000x .207

= Rs. 66.79 Rs 67

Night Time Casualties

- M Red-Death-night -VII = Noh (M1 × M2 × M3 × M4 x (Death Value)

= 1 x 5.378 x 0.95 x 0.05 x 0.10 x 50000 x .207

= Rs. 264.39= Rs. 265

- M Red-severe-night -VII = Noh (M1 × M2 × M3 × M4 x (Life threat)

= 1 x 5.378 x 0.95 x 0.05 x 0.30 x 40000 x .207

= Rs. 634.55  Rs.635

- M Red-medium-night -VII = Noh (M1 × M2 × M3 × M4 x (Hospitalization)

= 1 x 5.378 x 0.95 x 0.05 x 0.40 x 25000 x .207

= Rs. 528.79= 529

- M Red-life minor-night-VII = Noh (M1 × M2 × M3 × M4 x (Minor)

= 1 x 5.378 x 0.95 x 0.05 x 0.20 x 15000x .207

= Rs. 158.63= 159

Day Time Casualties

- M Red-Death-Day -VIII = Noh (M1 × M2 × M3 × M4 x (Death Value)

= 1 x 5.378 x 0.40 x 0.30 x 0.10 x 50000 x 0.156

= Rs. 503.38 Rs.504

- M Red-severe-Day -VIII = Noh (M1 × M2 × M3 × M4 x (Life threat)

= 1 x 5.378 x 0.40 x 0.30 x 0.30 x 40000 x 0.156

= Rs. 1208.11 Rs. 1209

- M Red-medium-Day -VIII = Noh (M1 × M2 × M3 × M4 x (Hospitalization)

= 1 x 5.378 x 0.40 x 0.30x 0.40 x 25000 x 0.156

= Rs. 1006.76 Rs. 1007

- M Red-minor-Day -VIII= Noh (M1 × M2 × M3 × M4 x (Minor)

= 1 x 5.378 x 0.40 x 0.30x 0.20 x 15000x 0.156

= Rs. 302.028 Rs.303

Night Time Casualties

- M Red-Death-night -VIII = Noh (M1 × M2 × M3 × M4 x (Death Value)

= 1 x 5.378 x 0.95 x 0.30 x 0.10 x 50000 x 0.156

= Rs. 1195.52 Rs. 1196

- M Red-severe-night -VIII = Noh (M1 × M2 × M3 × M4 x (Life threat)

= 1 x 5.378 x 0.95 x 0.30x 0.30 x 40000 x 0.156

= Rs. 2869.27 Rs.2870

- M Red-medium-night -VIII = Noh (M1 × M2 × M3 × M4 x (Hospitalization)

= 1 x 5.378 x 0.95 x 0.30 x 0.40 x 25000 x 0.156

= Rs. 2391.05 Rs.2392

- M Red-minor-night-VIII = Noh (M1 × M2 × M3 × M4 x (Minor)

= 1 x 5.378 x 0.95 x 0.30 x 0.20 x 15000x 0.156

= Rs. 717.31 Rs.718

Table 7. 5: Reduction of Human Losses due to Retrofitting (in Rs.)

| S. No | Grade of casualties | Intensity VI | Intensity VII | Intensity VIII |
| --- | --- | --- | --- | --- |
|  |  | Day | Night | Day | Night | Day | Night |
| 1 | Death | 0 | 0 | 112 | 265 | 504 | 1196 |
| 2 | Life threat | 0 | 0 | 268 | 635 | 1209 | 2870 |
| 3 | Hospitalization | 0 | 0 | 223 | 529 | 1007 | 2392 |
| 4 | Minor | 0 | 0 | 67 | 159 | 303 | 718 |
| Total loss reduction | 0 | 0 | 670 | 1588 | 3023 | 7176 |

(ix)	Net Present Value at Intensity VI

+

= Damage of building X rehabilitation effectiveness

= 8856x 0.282 = Rs. 2498.0

Bt = 0.170 x (2498+10+10+2322) = Rs. 823.00

Varying discount rate and time the sensitivity analysis is conducted, which may be referred at Figure 7. 35 (a-e).

The characteristics of net present value with respect to period for benefit realization, discount rate and damage scenario for mud building has been shown in form of 3D graph at Figure 7.36.

Figure 7.35(a): Net Present Value of Retrofitting of Mud Buildings

Figure 7.35(b): Net Present Value of Retrofitting of Mud Buildings

Figure 7.35(c): Net Present Value of Retrofitting of Mud Buildings

Figure 7.35(d): Net Present Value of Retrofitting of Mud Buildings

Figure 7.35(e): Net Present Value of Retrofitting of Mud Buildings

Figure 7.36: Time required in years to realize the benefits for Single Mud Building

7.16	Discussion of Results and Conclusion

The clear profile of benefit returns from retrofitting project is given in Figure 7.33(a-e) and Figure 7.35(a-e) for single brick and mud building. The analysis has been carried out for finding the sensitivity of investments with respect to discount rate, planning period and damage scenarios. The comprehensive profile of these parameters is reflected in 3D charts in Figure 7.34 and 7.36. Following situations have been studied to understand the sensitivity of investment.

- Effect of changing the planning period with fixed rate of discount

- Effect of changing the discount rate with fixed planning period

- Assessing the period for profit realization at varying scenarios

- Comparison of NPV for temporal changes in scenarios

7.16.1	Changing the planning period with fixed rate of discount

The analysis has been carried out for single brick and mud building. For understanding the sensitivity of investment returns, the increment factor has been worked out. This factor has been calculated for particular rate of interest as a ratio of NPV at 30 years to NPV at 5 years. The increment factor has been calculated based on figure 7.33(a-e) for brick buildings and Figure 7.35(a-e) for mud buildings. The increment factors reflect the benefits of investments which is summarized in Table 7.6.

Table 7.6: Comparison of Increment Factors for Brick and Mud Buildings with Respect to Change in Discount Rate

| Scenario | Increment Factors for Brick and Mud Building Discount Rate (%) |
| --- | --- |
|  | 2.50 % | 5.00 % | 10.00 % |
|  | Brick Building | Mud Building | Brick Building | Mud Building | Brick Building | Mud Building |
| VIDN | 11.86 | 10.51 | 10.56 | 21.02 | 11.08 | 8.20 |
| VIID | 8.17 | 7.98 | 6.69 | 6.52 | 5.12 | 4.94 |
| VIIN | 6.05 | 5.76 | 4.81 | 4.56 | 3.40 | 3.21 |
| VIIID | 5.35 | 5.18 | 4.22 | 4.09 | 2.96 | 2.86 |
| VIIIN | 4.84 | 4.77 | 3.81 | 3.76 | 2.67 | 2.63 |

(a) 	Brick Building

If the rate of discount is fixed and planning period is changed from 5 years to 30 years, followings are the observations:

- For Intensity VI (D-N), at discount rate of 2.5%, there is an increase in NPV by 11.86 times. If discount rate is changed further to 5 % and 10 %, the corresponding increments are 10.56 and 11.08 times. It shows that increase in NPV at this scenario is almost independent of discount rate. The benefit will be achieved even at lower discount rates if planning period is 30 years.

- For Intensity VII (Day), at discount rate of 2.5%, there is an increase in NPV by 8.16 times. If discount rate is changed further to 5 % and 10 %, the corresponding increment factors are 6.69 times and 5.11. At this scenario, the NPV is continuously decreasing with increase in discount rate.

- For Intensity VII (Night), at discount rate of 2.5%, there is an increase in NPV by 6.05 times If discount rate is changed further to 5 % and 10 %, the corresponding increment factors are 4.80 times and 3.39 times. As the rate of discount is increasing, the increment factor reduces significantly as compared to scenario of intensity VII(day), indicating that benefit realization could be ahieved much earlier.

- Similar trend has been recorded for Intensity VIII (Day) to VIII (Night). Her the reduction in sharper than other intensities.

- Analysis further reveals that as the damage scenario increases, the rate of increment factor decreases. At 2.5 % discount rate, if scenario changes from VI(D-N) to VIII(Night), the increment factor reduces from 11.86 to 4.84 times, thus indicating more benefits.

(b) 	Mud Buildings

In line with application of criteria on brick building, the same criteria have been evaluated for mud building. The finding of the same is described in detail below:

- For Intensity VI (D-N), at discount rate of 2.5%, there is an increase in NPV by 10.51times. If discount rate is changed further to 5 % and 10 %, the corresponding increment factors are 21.02 and 8.20 times.

- For Intensity VII (Day), at discount rate of 2.5%, there is an increase in NPV by 7.98 times. If discount rate is changed further to 5 % and 10 %, the corresponding increment factors are 6.52 times and 4.94 times The same trend as Intensity VI has been recorded. At this scenario, the NPV is continuously decreasing with increase in discount rate.

- For Intensity VII (Night), at discount rate of 2.5%, there is an increase in NPV by 5.76 times If discount rate is changed further to 5 % and 10 %, the corresponding increment factors  are 4.56 times and 3.21 times. As the rate of discount is increasing, the increment factor reduces significantly.

- Similar trend has been recorded for Intensity VIII (Day) VIII(Night).

- Analysis further reveals that as the damage scenario increases, the rate of increment factor decreases. At 2.5 % discount rate, if scenario changes from VI(D-N) to VIII(Night), the increment factor reduces from 10.51 to 4.77 times.

Comparison of increment factors between brick and mud buildings

If the rate of discount is fixed and planning period is changed from 5 years to 30 years for varying disaster scenario, Table 7.7 shows that there is a decline in increment factor. The trends are same for brick and mud buildings. For brick buildings, the increment factors are higher than mud buildings. There is no significant change in rate of decline of increment factors at particular discount rate, irrespective of building class. If the discount rate increases from 2.5 % to 5 and 10 %, the rate of decline of increment factor is steeper for each type of building. However, this decline is more for brick building.

7.16.2	Changing the discount rate with fixed planning period

For analyzing the sensitivity of investment, the planning period is fixed and rate of discount is varied. Two scenarios are taken for understanding the sensitivity of various parameters. The sensitivity of NPV changes are measured for two planning periods i.e. 5 years and 30 years. The summary for analysis may be referred at Table 7.7. For this study increment factors is projected as ratio of NPV at 2.5 % discount rate to NPV 10% discount rate.

Table 7.7: Sensitivity of Increment Factors with Varying Scenario, Fixed Planning Period and Varying Discount Rate ( 2.5% to 10 %)

| Scenario | Planning Period |
| --- | --- |
|  | 5 year | 30 Years |
|  | Brick Building | Mud Building | Brick Building | Mud Building |
| VI | 2.75 | 2.24 | 2.95 | 2.87 |
| VIID | 1.69 | 1.66 | 2.70 | 2.69 |
| VIIN | 1.39 | 1.35 | 2.47 | 2.43 |
| VIIID | 1.31 | 1.29 | 2.37 | 2.34 |
| VIIIN | 1.26 | 1.25 | 2.28 | 2.27 |

If the planning period is fixed and rate of discount is varied from 2.5 % to 10 %, there is decline in NPV increment factors. Table 7.8 shows that same trend is followed in brick and mud buildings. However, it has been observed that as the damage scenario increases from VII (day) to VIII (Night), there is no much variation in decline rate, irrespective of the building type. The decline rate is independent of planning period, i.e. same ratio has been observed for mud and brick buildings for 5 years and 30 years, so benefits will be achieved in both class of buildings.

7.16.3	Assessing the period for profit realization at various scenarios

For checking the effectiveness of rate of discount and planning period, it is necessary to check the span of investment returns, which may be treated as benefits. The Table 7.8 provides the information about time required in months to realize the benefits from executing the retrofitting projects for single brick and mud building.

(a) 	Brick Building

The observations are as below:

- At intensity VI (D-N), the project receives the benefits at 40.1 months. As the discount rate increases, benefit realization is delayed by few months upto a discount rate of 5 %, beyond which it increases by 13 months for discount rate of 10 %.

- At intensity VII (Day) and VII(Night), same trend has been reflected. It is observed that as the severity increases, the span of benefit realization decreases. The same trend is also observed in Intensity VIII (Day) and VIII(Night). At VIII(Night), the benefits are realised from 5th months of execution.

- It is also observed that there is no much variation in benefit returns with respect to discount rate for a particular scenario.

(b) 	Mud Building

In mud construction, at discount rate of 2.5%, as the earthquake scenario increases, the span of benefit return decreases. For instance, At intensity VI(DN) the benefits are accrued at 37.1 months, however if scenario changes to VIII(Night), the benefit is accrued from 4 months. At Intensity VI, if rate of Interest is varied from 2.5 % to 10 %, the rate of benefit realization increases from 37.1 months to 48 months.

For mud building, the period for benefit realization is faster than brick building. Table 7.8 shows comparison of period (Months) of benefit realization for Single brick and mud building from Pandhana Tehsil.

Table 7.8: Comparison of Period (Months) of Benefit Realization for Single Brick and Mud Building from Pandhana Tehsil

| Scenario | Discount Rate |
| --- | --- |
|  | 2.50% | 3% | 4% | 5% | 7.50% | 10% |
|  | Type of Building |
|  | Brick | Mud | Brick | Mud | Brick | Mud | Brick | Mud | Brick | Mud | Brick | Mud |
| VIDN | 40.1 | 37.1 | 40.8 | 37.6 | 42.1 | 38.7 | 43.6 | 47.4 | 47.9 | 43.5 | 53.1 | 48 |
| VIID | 30 | 29.9 | 30.2 | 29.8 | 30.9 | 30.7 | 31.8 | 31.7 | 34.2 | 34.4 | 37.2 | 37.6 |
| VIIN | 17.7 | 15.6 | 17.8 | 15.7 | 18.2 | 16 | 18.5 | 16.4 | 19.6 | 17.5 | 20.8 | 18.8 |
| VIIID | 11.3 | 9.2 | 11.4 | 9.3 | 11.6 | 9.4 | 11.8 | 9.5 | 12.4 | 9.9 | 13.2 | 10.3 |
| VIIIN | 5 | 4 | 5 | 4 | 5 | 4.1 | 5.1 | 4.2 | 5.3 | 4.3 | 5.4 | 4.5 |

7.16.4	Comparison of NPV for temporal changes in scenarios

The analysis has been made for understanding the impact of temporal changes on NPV. It is found that the severity increases at night times because of maximum occupancy. The retrofitting gives better results for increased severity.  The analysis shows that if planning period is fixed and severity is changed, it is observed that there is lesser decline in NPV for night scenario than day time. In both cases, it has been observed that the span benefits realization shortens by 50-60 % irrespective of the building class.

Conclusion

Clause 7.16 discusses the results obtained from the NPV calculation of seismic retrofitting of mud and brick buildings. The observations may be concluded as below:

- Irrespective of types of buildings, the increment factors reduces as the scenario increases.

- At any fixed scenario, as the discount rate increases the span for investment return increases. This is valid for both types of buildings.

- It has been observed that brick buildings are recovering their investment faster than mud buildings.

- It has been observed that irrespective of type of buildings, as the scenario changes from day to night, there is a sharp increase in net present value.

# Footnotes

The map is developed by expert group for “Handbook Earthquake Resistant Construction For Madhya Pradesh, 2004” under the aegis of Disaster Management Institute, Bhopal, India.

# Text boxes

## Retrofitting Measures

- Installation of RCC bands or seismic bandage and cross ties at the eave level

- Corner strengthening

- Pointing of external wall

- Strengthening of roofing elements

Retrofitting Measures

- Seismic bandage and cross ties at the eave level

- Installation of RCC bands

- Gable band

- Bracing of Floor / First floor ceiling

- Roof bracing

- Pointing of external wall

- Strengthening of roofing elements

Retrofitting Measures

- Seismic bandage and cross ties at the eave level

- Bracing of Steel Built up Section

- Installation of RCC bands

- Gable band in inclined roof

- Roof bracing

- Pointing of external wall

- Strengthening of roofing elements

Retrofitting Measures

- Seismic bandage and cross ties at the eave level

- Bracing of Floor / First floor ceiling

- Installation of RCC bands

- Roof and Gable band

- Roof bracing

- Pointing of external wall

- Strengthening of roofing elements

# Retrofitting Measures

- Removal of roofing elements

- Strengthening of timber frame

- Mud wall connection with frame

- Roof strengthening

- Water proofing  of mud all

- GI sheet of tile roof fixing

- Strengthening of opening

Retrofitting Measures

- Removal of roofing elements

- Strengthening of timber frame

- Mud wall connection with frame

- Roof strengthening

- Water proofing  of mud all

- GI sheet of tile roof fixing

Retrofitting Measures

- Removal of roofing elements

- Strengthening of timber frame

- Mud wall connection with frame

- Roof strengthening

- Water proofing  of mud all

- GI sheet of tile roof fixing

Retrofitting Measures

- Strengthening of timber frame

- Mud wall connection with frame

- Roof strengthening

- Water proofing  of mud all

- GI sheet of tile roof fixing

- Removal of roofing elements

- Strengthening of timber frame

- Mud wall connection with frame

- Roof strengthening

- Water proofing  of mud all

- GI sheet of tile roof fixing

- Strengthening of opening

- Removal of roofing elements

- Strengthening of timber frame

- Mud wall connection with frame

- Roof strengthening

- Water proofing of mud wall

- GI sheet of tile roof fixing

- Removal of roofing elements

- Introduction of timber frame

- Strengthening of timber frame

- Mud wall connection with frame

- Roof strengthening

- Water proofing  of mud wall

- GI sheet of tile roof fixing

Figure 7.15a: Mud Wall with 1½ Frame Storey and Opening at Gable End

Figure 7.15 b : Mud Wall with 1½ Frame Storey and Opening at Gable End