BIODIESEL PRODUCTION AND PERFORMANCE TESTING USING TUMBA (CITRULLUS COLOCYNTHIS) OIL

A Major Dissertation submitted

in partial fulfillment of the requirements for the award of the degree of

Master of Engineering

In

Thermal Engineering

By

SNEHLATA GAUTAM

University Roll No.-8558

Under the Supervision of

DR. S. S. KACHHWAHA			                   PROF. A. PAL

Department of Mechanical Engineering

Faculty of Technology, University of Delhi

Delhi-110042, INDIA

# STUDENT DECLARATION

I hereby certify that the work which is being presented in the dissertation entitled “BIODIESEL PRODUCTION AND PERFORMANCE TESTING USING TUMBA (CITRULLUS COLOCYNTHIS) OIL”, in partial fulfillment of the requirements for the award of the Degree of Master of Engineering in Thermal Engineering, submitted in the Department of Mechanical Engineering, Delhi University. This is an authentic record of my own work carried under the supervision of Dr. S.S. Kachhwaha, Asst. Professor and Mr. Amit Pal, Sr. Lecturer of Mechanical Engineering Department, Faculty of technology, University of Delhi, Delhi.

I have not submitted the matter embodied in this dissertation for the award of any other degree.

SNEHLATA GAUTAM

ME (Thermal Engg.)

University Roll No.-8558

CERTIFICATE

Date: ___________

This is certified that the work contained in this dissertation entitled “BIODIESEL PRODUCTION AND PERFORMANCE TESTING USING TUMBA (CITRULLUS COLOCYNTHIS) OIL” by Ms. Snehlata Gautam, 18/THR/07, (University Roll No.8558)  in partial fulfillment of requirements for the award of Degree of Master of Engineering in Thermal Engineering,  is an authentic record of students own work carried by her under our guidance.

This is also certified that this work has not been submitted to any other Institute or University for  the award of any other degree or diploma.

Prof. Amit Pal                                                                                      Dr. S.S. Kachhwaha

Sr. Lecturer                                                                                            Assist. Professor

Department of Mechanical Engineering

Faculty of Technology

University of Delhi, Delhi, India

# ACKNOWLEDGEMENT

It is a great pleasure to have the opportunity to extent my heartiest felt gratitude to everybody who helped me throughout the course of this dissertation.

It is distinct pleasure to express my deep sense of gratitude and indebtedness to my guide    Prof. S. S. Kachhwaha, Department of Mechanical Engineering, and Prof. Amit Pal, Department of Mechanical Engineering, Faculty of Technology, Delhi University, for there invaluable guidance, encouragement and patient reviews. Their continuous inspiration only has made me to complete this major project.

I would like to thanks Sh.Vijay, Sh. Lalit Kumar & Sh. Harjeet Singh of I.C Engine laboratory for extending their kind support and sharing their valuable time for the completion of the project.

I am thankful to my all teachers, classmates and friends for their unconditional support and motivation during this project. It is a great opportunity for me to extend my heartiest felt gratitude to everybody who helped me throughout the course of this dissertation in anyway.

.

SNEHLATA GAUTAM

ME (Thermal Engneering)

University Roll No.-8558

# ABSTRACT

# World is facing severe scarcity of fossil fuels and problem of rising pollution level, among several factors such as industrial pollution and vehicular emissions, splurge in vehicular population is the major factor responsible for it. The increase in CO2, CO, HC, PM and NOx emissions are leading to the problem of global warming, health hazards and depletion in ozone layer etc.. To overcome such problems work is under progress on alternative fuels like non-edible oils, ethanol, CNG, LPG etc. In this report vegetable oils can be converted into biodiesel through transesterification process such as–conventional mechanical stirring method, ultrasonic and hydrodynamic cavitation methods using Tumba (Citrullus Colocynthis) vegetable oil.

An integrated, clean, facile and ecologically friendly approach of biodiesel production from Tumba (Citrullus Colocynthis) oil focused on lab scaling up is reported in this study. Transesterification was catalyzed by KOH with methanol (assay 99.0%) for Tumba biodiesel production, maintaining the temperature of solution within the range of 40oC to 45oC. Through conventional mechanical stirring method the optimum yields obtained by using alcohol to oil ratio 4.5:1 in reaction time of 90 minutes at 1% catalyst is 91.32% whereas at 6:1, 93.42% yield is obtained in the same reaction time  using reduced percentage of catalyst (0.75%). By using ultrasonic method optimum results obtained on the experimentation of alcohol to oil ratio 4.5:1 in 40 minutes using 1% catalyst is 92.11% yield whereas at 6:1, 94% methyl ester conversion is obtained in the same reaction time with reduced catalyst  (0.50%). In this work, an experimental test rig based on hydrodynamic cavitation process was developed for production of Tumba biodiesel. The results show that maximum biodiesel, using the molar ratio of 6:1 and 4.5:1, methyl ester conversion of 95.76% and 92.36% can be achieved respectively, within the reaction time of 30 minute, therefore it is industrially viable. The results illustrate that the use of KOH can be minimized in hydrodynamic cavitation. Among all the processes hydrodynamic cavitation method is most efficient and less time consuming. The relatively mild reaction conditions and high yield of methyl esters using this environment friendly method make it viable for practical use in industry.

An experimental investigation was also conducted to the performance of Tumba oil and its fuel blends with diesel. Performance study was carried out on a single cylinder, direct injection, four stroke, Kirloskar diesel engine connected to eddy current dynamometer unit and data was obtained through the “Engine soft” software whereas controlling of parameters is done by using National Instruments-Data Acquisition Driver (NI-DAQ) software. The experiment covers a wide range of loads at the compression ratio of 17.5 by using pure diesel, B20, B40, B60, B80 and B100 biodiesel blends of Tumba oil to obtain  various parameters such as torque, exhaust temperature, brake thermal efficiency, brake specific energy consumption, mechanical efficiency and  smoke opacity. The maximum brake thermal efficiency achieved with Tumba biodiesel and its blends are in the range of 28% to 29% which are comparable with diesel efficiency. The properties of Tumba biodiesel were comparable to conventional diesel fuel. The comparison of performance parameters show that biodiesel produced from Tumba oil (Citrullus Colcynthis) can be used as an alternative fuel in the automobiles with better performance and lower emissions.

LIST OF TABLES

Table 1.1: Estimated biodiesel requirement in India

Table 1.2: Global productions of the major vegetable oils [53]

Table 1.3: Top 10 countries in terms of biodiesel potential [49]

Table 1.4: Top 10 countries in terms of biodiesel potential [49]

Table 2.1: Comparison of different technologies to produce biodiesel [39]

Table 2.2: Comparison of biodiesel properties with diesel fuel [56]

Table 2.3: Summary of Biodiesel Production Techniques

Table 2.4: Summary of Performance and Emission

Table 4.1: Oil, alcohol and catalyst during the experimentation

Table 4.2: Ultrasonic horn type method at 28 kHz (molar ratio 4.5:1)

Table 4.3: Ultrasonic horn type method at 28 kHz (molar  ratio 6:1)

Table 4.4: Conventional mechanical stirring method (molar  ratio 4.5:1)

Table 4.5: Conventional mechanical stirring method (molar  ratio 6:1)

Table 5.1: Yield observed at various reaction time for molar ratio of 6:1

Table 5.2: Yield observed at various reaction time for molar ratio of 4.5:1

Table 6.1: Specifications of component used

Table 6.2: Description of different blends of biodiesel

Table 6.3: Performance parameters for pure diesel against speed

Table 6.4: Performance parameters for TB20 against speed

Table 6.5: Performance parameters for B40 against speed

Table 6.6: Performance parameters for B60 against speed

Table 6.7: Performance parameters for B80 against speed

Table 6.8: Performance parameters for TB100 against speed

Table 6.9: Observation data of exhaust temperature (Ex. Temp.) and air/fuel(A/F) ratio

Table 6.10: Percentage change of biodiesel with respect to diesel using BThE parameter

Table 6.11: Percentage difference of diesel with respect to diesel using SFC parameter

Table 6.12: Percentage difference of diesel with respect to diesel using BSEC parameter

Table 6.13: Percentage difference of diesel with respect to diesel using A/F Ratio parameter

Table 6.14: Percentage difference of diesel with respect to diesel using Ex. Temp. parameter

Table 6.15: Data of pressure and crank angle

Table 6.16: Percentage difference of biodiesel from diesel in terms of smoke opacity

LIST OF FIGURES

Figure 1.1(a): Citrullus Colocynthis plant

Figure 1.1(b): Tumba fruit and seeds

Figure 3.1: Process Flow Schematic for Biodiesel Production [54]

Figure 3.2: Scheme of the reactor used in the transesterification experiments

Figure 3.3: Flow diagram of cotton oil soapstock biodiesel production process [3]

Figure 3.4: Schematic representation of ultrasonic horn [17]

Figure 3.5: Schematic representation of and ultrasonic bath [17]

Figure 3.6(a): Schematic representation of the experimental setup for hydrodynamic cavitation

reactor [12]

Figure 3.6(b): Schematic diagram of hydrodynamic cavitation system setup [16]

Figure 3.7: Test rig for biodiesel production by hydrodynamic cavitation

Figure 3.8: Amount of biodiesel yield v/s time for 1:4.5 molar ratio of oil to alcohol [21]

Figure 3.9: Effect of the molar ratios of methanol to rapeseed oil in transesterification

reaction on producing methyl esters, as treated at 350oC [22]

Figure 3.10: Effect the reaction temperature on methyl esters formation [22]

Figure 3.11: Unmethyl esters content in rapeseed oil during transesterification reaction

Figure 3.12: Supercritical continuous reaction device

Figure 4.1(a): Schematic diagram of ultrasonic horn type reactor

Figure 4.1(b): Side view of the Horn type Processor

Figure 4.2: Photograph of ultrasonic horn type processor (TU-50)

Figure 4.3(a): Heating of raw vegetable oil

Figure 4.3(b): Methanol and KOH

Figure 4.3(c): Weighing machine

Figure 4.3(d): Transesterification, Separation of Layers, Washing processes

Figure 4.4(a): Yield (%) Vs reaction time in minute for molar ratio of 4.5:1

Figure 4.4(b): Yield (%) Vs reaction time in minute for molar ratio of 6:1

Figure 4.5: Conventional mechanical stirring method

Figure 4.6(a): Yield (%) Vs reaction time in minute for the molar ratio 4.5:1 from the data

Table 4.4

Figure 4.6(b): Yield (%) Vs reaction time in minute for the molar ratio 6:1 from the data Table

4.5

Figure 4.7(a): Comparison of methods through yield percentage Vs Time in minute for catalyst

0.75% at molar ratio 4.5:1

Figure 4.7(b):Comparison of methods through yield percentage Vs Time in minute for catalyst

1% at molar ratio 4.5:1

Figure 4.7(c): Comparison of methods through yield percentage Vs Time in minute for catalyst

0.75% at molar ratio 6:1

Figure 4.7(d): Comparison of methods through    yield percentage Vs Time in minute for

catalyst     1% at molar ratio 6:1

Figure 4.7(e): Comparison of methods through yield (%) Vs reaction time in minute for

catalyst   0.65%  for MS & 0.50% for U at molar ratio 6:1

Figure 4.7(f): Comparison of methods      through yield (%) Vs reaction time in   minute for

catalyst 0.70%  for MS &  0.50% for U at molar ratio 4.5:1

Figure 5.1(a): Hydrodynamic cavitation setup

Figure 5.1(b): Front view of the experimental set up

Figure 5.2: Schematic diagram of hydrodynamic cavitation machine

Figure 5.3: Nozzle spray gun

Figure 5.4: Schematic diagram of Cylindrical Pipe

Figure 5.5(a): Top view of Base supporting frame

Figure 5.5(b): Schematic diagram of Base supporting frame

Figure 5.6(a): Heating of raw vegetable oil

Figure 5.6 (b): Methanol and KOH

Figure 5.6 (c): Weighing machine

Figure 5.7: Thottle valve and plungers

## Figure 5.8: Mixture inlet manifold

Figure 5.9: Pressure gauge and spray gun

Figure 5.10: Rotameter

Figure 5.11: Reciprocating pressure pump

Figure 5.12(a): Yield% Vs Reaction time (min) for 6:1 molar ratio

Figure 5.12(b): Yield% Vs Reaction time (min) for 4.5:1 molar ratio

Figure 5.13: Comparison of molar ratios of hydrodynamic cavitation method

Figure 5.14(a): Comparison of methods for 0.75% catalyst by hydrodynamic, ultrasonic &

stirring method 6:1

Figure 5.14(b): Comparison of methods for 0.75% catalyst by hydrodynamic, ultrasonic &

stirring method 4.5:1

Figure 6.1(a): Experimental set-up of Kirloskar diesel engine

Figure 6.1(b): Rear view of the Kirloskar diesel engine

Figure 6.1(c): Schematic Diagram of the Experimental set-up

Figure 6.2 (a): BThE (%) Vs brake power for B 20

Figure 6.2 (c): BThE (%) Vs brake power for B 40

Figure 6.2 (d): BThE (%) Vs brake power for B 60

Figure 6.2 (e): BThE (%) Vs brake power for B 80

Figure 6.2 (f): BThE (%) Vs brake power for B 100

Figure 6.3: Comparison of BThE (%) Vs brake power for B 20, B40, B60, B80, B100

Figure 6.4: Percentage difference of biodiesel Vs brake power for BThE

Figure 6.5(a): SFC Vs Brake power for B 20

Figure 6.5(b): SFC Vs Brake power for B 40

Figure 6.5(c): SFC Vs Brake power for B 60

Figure 6.5(d): SFC Vs Brake power for B 80

Figure 6.5(e): SFC Vs Brake power for B 100

Figure 6.6: Comparison of SFC Vs Brake power for B 20, B 40, B 60, B 80, B100 from

diesel

Figure 6.7: Percentage difference of biodiesel  Vs brake power for SFC

Figure 6.8(a): BSEC Vs Brake power for B 20

Figure 6.8(b): BSEC Vs Brake power for B 40

Figure 6.8(c): BSEC Vs Brake power for B 60

Figure 6.8(d): BSEC Vs Brake power for B 80

Figure 6.8(e): BSEC Vs Brake power for B 100

Figure 6.9: Comparison of BSEC Vs Brake power for B 20, B 40, B 60, B 80, B100 from

diesel

Figure 6.10: Percentage difference of biodiesel Vs brake power for BSEC

Figure 6.11(a): Air/Fuel Ratio  Vs Brake power for B 20

Figure 6.11(b): Air/Fuel Ratio  Vs Brake power for B 40

Figure 6.11(c): Air/Fuel Ratio  Vs Brake power for B 60

Figure 6.11(d): Air/Fuel Ratio  Vs Brake power for B 80

Figure 6.11(d): Air/Fuel Ratio  Vs Brake power for B 100

Figure 6.12: Comparison of Air/Fuel Ratio Vs Brake power for B 20, B 40, B60, B 80, B 100

from diesel

Figure 6.13: Percentage difference of biodiesel Vs brake power for A/F Ratio

Figure 6.14(a): ExT Vs Brake Power for B20

Figure 6.14(b): ExT Vs Brake Power for B40

Figure 6.14(c): ExT Vs Brake Power for B60

Figure 6.14(d): ExT Vs Brake Power for B80

Figure 6.14(e): ExT Vs Brake Power for B100

Figure 6.15: Comparison of ExT Vs Brake Power for B20, B 40, B 60 ,B 80, B100 from

diesel

Figure 6.16: Percentage difference of biodiesel Vs brake power for ExT

Figure 6.17(a): Pressure Vs Crank Angle for B20

Figure 6.17(b): Pressure Vs Crank Angle for B40

Figure 6.17(c): Pressure Vs Crank angle for B60

Figure 6.17(d): Pressure Vs Crank angle for B80

Figure 6.17(e): Pressure Vs Crank angle for B100

Figure 6.18: Comparison of pressure Vs Crank angle for B20, B40, B60, B100 from diesel

Figure 6.19(a): Smoke Opacity Vs Brake power for B20

Figure 6.19(b): Smoke Opacity Vs Brake power for B40

Figure 6.19(c): Smoke Opacity Vs Brake power for B60

Figure 6.19(d): Smoke Opacity Vs Brake power for B80

Figure 6.19(e): Smoke Opacity Vs Brake power for B100

Figure 6.20: Comparison of Smoke Opacity Vs Brake power for B20,B40,B60,B100 from

diesel

Figure 6.21: Percentage difference Vs brake power for smoke opacity

ABBREVIATIONS AND SYMBOLS

m                      Meter

Ѳ                      Crank Angle

oC                     Degree Celcius

cm                    Centimeter

h                       Hour

g                       Gram

mm                   Millimeter

mg                    Milligram

k                        Kilo

kg                      Kilogram

Hg                     Mercury

J                         Joule

lph                     Liter per hour

M                       Mega

N                       Newton

%                       Percentage

Pa                      Pascal

rpm                    Revolution per minute

s                         Second

W                       Watt

ASTM                American Society for Testing and Materials

B20                     Blend of 20% Tumba biodiesel

B40                     Blend of 40% Tumba biodiesel

B60                     Blend of 60% Tumba biodiesel

B80                     Blend of 80% Tumba biodiesel

B100                   Blend of 100% Tumba biodiesel

BSEC                  Brake specific energy consumption

BSFC                  Brake specific fuel consumption

BTDC                 Bottom top dead centre

BThE                  Brake thermal efficiency

CN                      Cetane number

CP                       Cloud point

CO2                     Carbon dioxide

CO                       Carbon monoxide

CH3OH                Methanol

CR                       Compression ratio

Ex. Temp.            Exhaust Temperature

US                        United State

IC                         Internal Combustion

HC                       Hydrocarbon, Hydrodynamic Cavitation

KOH                    Potassium hydroxide

MS                       Mechanical stirring

NOx                     Nitric oxide

P                           Pressure

PM                        Particulate matter

TOME                  Tumba oil methyl ester

TDC                      Top dead centre

UHC                     Unburnt hydrocarbon

US                        Ultrasonic

# INDEX

TITLE                                                                                                               PAGE NO.

STUDENT DECLARATION

CERTIFICATE

ACKNOWLEDGEMENT                                                                                       (i)

ABSTRACT                                                                                                            (ii)

CONTENTS                                                                                                             (iii)-()

LIST OF TABLES                                                                                                  (iii)                                                                                      LIST OF FIGURES                                                                                                 (iv)

ABBREVIATIONS & SYMBOLS                                                                         (v)

CHAPTER-1

INTRODUCTION                                                                         1-11

1.1   Background and Concept of Biofuel                                        1

1.2   Definition of Biodiesel			                                 2

1.3   Rise of Biodiesel                                                                      2-3

1.4   Indian Energy Scenario of Biofuels                                         3-4

1.5   Resources of  Biodiesel       	4-5

1.6   Chemistry of Biodiesel	6

1.7   Properties of Biodiesel	7-10

1.8   Motivation 	10

1.9   Objective                                                            	10

1.10 Organization of the Report	10-11

CHAPTER-2

LITERATURE OVERVIEW                                                        12-81

2.1  Biodiesel Production Techniques                                              12

2.1.1  Conventional Mechanical Stirring Method                      12-15

2.1.2  Cavitation Method	  15

2.1.2.1  Ultrasonic Cavitation Method	  15-18

2.1.2.2  Hydrodynamic Cavitation Method	  18-20

2.1.3  Supercritical & Co-solvent Method  	 20-24

2.1.4  Miscellaneous Methods                                                  24- 38

2.2   Properties and Characteristics                 	38-42

2.3   Performance and Emission                		                      42-76

2.4   Comparison of Biodiesel Production Techniques	76

2.5   Comparison of Biodiesel Properties with Diesel Fuel	77

2.6   Summary	78-91

CHAPTER-3

BIODIESEL PRODUCTION TECHNIQUES                             82-97

3.1 Process Overview	 82

3.1.1 Direct use and Blending	 82

3.1.2 Microemulsions	 82

3.1.3 Thermal Cracking (Pyrolysis)	 82

3.1.4 Transesterification                                                              82-85

3.2 Conventional Mechanical Stirring Method	85-87

3.2.1 Principle                          	85-86

3.2.2 General Reviews 	86-87

3.3 Cavitation Method 	88-93

3.3.1 Ultrasonic Cavitation Method 	88

3.3.1.1 Principle                              	88-89

3.3.1.2 General Reviews            	89-90

3.3.2 Hydrodynamic Cavitation Method	 90-93

3.3.2.1 Principle                              	 90-91

3.3.2.2 General Reviews                       	 91-93

3.4 Supercritical & Co-solvent Method	 94-97

3.4.1 Principle                              	 94

3.4.2 General Reviews 	 95-97

CHAPTER-4

BIODIESEL PRODUCTION THROUGH ULTRASONIC

HORN TYPE & COVENTIONAL STIRRING METHOD          98-109

4.1 Ultrasonic cavitation	98-104

4.1.1 Experimental Set-up	98-99

## 4.1.2 Reagents and Materials used	100

## 4.1.3 Procedure	100-101

4.1.4 Experiment Data	101-104

4.2 Conventional Mechanical Stirring Method	104-107

4.2.1 Experimental Set-up	104

4.2.2  Reagents and material used	105

4.2.3  Procedure                                                                            105

4.1.4 Experiment Data                                                                  105-107

4.3 Results & Discussion                                                                    107-109

CHAPTER-5

BIODIESEL PRODUCTION THROUGH HYDRODYNAMIC

CAVITATION METHOD                                                              110-121

5.1 Working and Constructions	110-115

5.2 Reagents and Material used   				                 116

## 5.3 Procedure	116-117

## 5.4 Experimental Data				                  	     117-119

5.2 Results & Discussion           		                                         119-121

CHAPTER-6

PERFORMANCE AND EMISSION TESTING                                122-155

6.1 Engine Test Set-up	122-127

6.2 Preparation of biodiesel blends	127

6.3 Performance Evaluation	128

6.4 Performance Data for Load Testing	129

6.4.1 Pure Diesel	129-132

6.4.2 Biodiesel Blends from Tumba oil	129

6.5 Results & Discussion	129-132

6.5.1 Brake thermal efficiency (BThE) V Brake Power 	132-155

6.5.2 Specific fuel consumption (SFC) V Brake Power

6.5.3 Brake Specific Energy Consumption (BSEC) V Brake Power

6.5.4 Air/Fuel Ratio (A/F Ratio) V Brake Power

6.5.5 Exhaust Temperature (Ex. Temp.) V Brake Power

6.5.6 Smoke Opacity V Brake Power

6.5.7 Pressure V Crank Angle (Ѳ)

CHAPTER-7

CONCLUSIONS & FUTURE SCOPE                                             60-47

7.1 Conclusion

7.2 Future scope & Recommendations

REFERENCES                                                                                                           63-64

APPENDIX - I

APPENDIX - II

APPENDIX - III

CHAPTER-1

INTRODUCTION

1.1  Background and Concept of Biofuel

The concept of bio fuel dates back to 1885 when Dr. Rudolf Diesel built the first diesel engine with the full intention of running it on vegetative source [48]. In 1912 he observed, "…the use of vegetable oils for engine fuels may seem insignificant today. But such oils may in the course of time become as important as petroleum and the coal tar products of present time" [25, 35]. Most of the investigations reported in the literature on the usage of vegetable oil as engine fuels have emphasized modifying the oil to work in existing engine designs. The primary problem associated with using straight vegetable oils as a fuel in a compression ignition engine is the high viscosity [23]. Among the methods that have been investigated was transforming the vegetable oils to their corresponding esters. The fuel characteristics of these esters are much closer to those of diesel fuel than those of the fresh vegetable oils. In the 1970s, it was found that the viscosity of vegetable oils could be decreased through a simple chemical process. The process yields a vegetable oil based fuel that works as efficiently as diesel fuel in modern diesel engines [33].Since then the technical developments have come a long way and the plant oil today has been highly established as bio fuel, equivalent to diesel. Increasing pollution levels and the depletion of the petroleum reserves have lead to the search for alternate fuel sources for internal combustion engines. Usage of vegetable oils poses some challenges like poor spray penetration, valve sticking and clogging of injector nozzles. Most of these problems may be solved by partial substitution of diesel with vegetable oil. In view of the fast depletion of fossil fuels and worsening environmental pollution related to fossil fuel use, the search for alternative fuels for diesel engines has been intensified in the last few decades [35]. Modified maintenance schedule may be adopted to control carbon deposits formed during long-term usage of vegetable oil blends. Technical problems associated with the biodiesel is its susceptibility to oxidation, which can cause the fuel to become acidic and to form insoluble gums and sediments that can plug fuel filters [64]. Esterification is a process, which changes molecular structure of the vegetable oil molecules thus reduces viscosity and unsaturation. A diesel engine can perform satisfactorily on biodiesel blends without any engine hardware modifications [85, 89].

1.2  Definition of Biodiesel

The search for substitutes for petroleum derivatives resulted in an alternative fuel called "biodiesel". The concept of biodiesel is still under discussion. Technically speaking, biodiesel is the alkyl ester of fatty acids, made by the transesterification of oils or fats, from plants or animals, with short chain alcohols such as methanol and ethanol. Glycerine is, consequently, a by-product from biodiesel production [25]. It is defined as mono-alkyl esters of long chain fatty acids derived from vegetable oils or animal fats [48], which conform to ASTM specifications for use in diesel engines [64].

1.3  Rise of Biodiesel

Fuel crisis because of dramatic increase in vehicular population and environmental concerns have renewed interest of scientific community to look for alternative fuels of bio-origin such as vegetable oils. As an alternative fuel for compression ignition engines, plant oils are in principle renewable and carbon neutral [56]. Vegetable oils can be produced from forests, vegetable oil crops, and oil bearing biomass materials. Non-edible vegetable oils such as linseed oil, mahua oil, rice bran oil, etc. are potentially effective diesel substitute. Vegetable oils have high-energy content. Besides, vegetable oils naturally fix the solar energy and do not contain sulphur [25].The prospects for large-scale vegetable oil-based fuel production are very attractive for developing countries like India Vegetable oil blends showed performance characteristics close to diesel. Therefore, vegetable oil blends can be used in compression ignition engines in rural areas for agriculture, irrigation and electricity generation. Twenty percent LOME blend was found to be the optimum concentration, which improved the thermal efficiency of the engine, reduced the smoke density and BSEC. Using primary ester of vegetable oil also eliminates the durability problems associated with the vegetable oil thus making it a safe and suitable fuel for long-term usage in IC engine [85].

Numerous laboratory studies report carbon monoxide, hydrocarbon and particulate matter emission reductions with a slight nitrogen oxides emission increase from engines operating with biodiesel and biodiesel blends as compared to using petroleum diesel. Today it is important to use these techniques to evaluate the effectiveness of new fuels in reducing pollutants in the real-world. The remote sensing system results provided us with an evidence of emission increase, and also guided us in understanding the most probable cause for the failure in reducing PM emissions with this fuel switch. Real world data analysis represents not only an important scientific research tool but also a method to assure the quality of new commercial fuels and the adherence to fuel standards [81].

1.4  Indian Energy Scenario of Biofuels

Recent environmental (e.g. Kyoto Protocol) and economic concerns have prompted resurgence in the use of biodiesel throughout the world. In 1991, the European Community proposed a 90% tax reduction for the use of bio fuels, including biodiesel. Today 21 countries worldwide produce biodiesel. India is one of the largest petroleum consuming and importing countries. India imports about 70 % of its petroleum demands. The current yearly consumption of diesel oil in India is approximately 40 million tones constituting about 40% of the total petro-product consumption [35]. Diesel estimated requirement of biodiesel pattern in India has not varied much and is around 36x106 tonnes as reported by the Ministry of Petroleum and Natural Gas is shown in table 1.1 [38].

Table 1.1: Estimated biodiesel requirement in India

| Year | Diesel requirement MMT | Biodiesel requirement blending, MMT |
| --- | --- | --- |
|  |  | 5% | 10% | 20% |
| 2004-05 | 46.97 | 2.35 | 4.70 | 9.40 |
| 2006-07 | 52.33 | 2.62 | 5.23 | 9.92 |
| 2011-12 | 66.90 | 3.35 | 6.69 | 13.38 |

In 2005, India consumed 30 million tons of oil in the transport sector, of which 29% is gasoline and 71% is diesel. The Indian energy demand is expected to grow at an annual rate of 4.8% over the next couple of decades. Many scenarios projected that India will at least double its oil consumption by 2030, which will make India the third largest oil consumer in the world. Biofuel production could potentially play a major role in the country [53].

Biodiesel can be converted into wide variety of energy carriers (ethanol, methanol, biogas, biodiesel, dimethyl esters, diesel, gasoline, hydrogen) as of recent fossil fuel through conversion technologies and thus have the potential to be significant new sources of energy into the 21st century [2]. Biodiesel, a renewable source of energy seems to be an ideal solution for global energy demands including India as well. In XIth plan, a growth rate of more than 8.0% is envisaged. It could only be achieved by availability of enough energy. As fossil fuels are dwindling, development and application of biodiesel, that too from non-edible oils seems to be a solution [49].

1.5  Resources of  Biodiesel

Many developed countries have active biodiesel programs. Currently biodiesel is produced mainly from field crop oil like rapeseed, sunflower etc. in Europe and soybean in US. Malaysia utilizes palm oil for biodiesel production while in Nicaragua it is jatropha oil. There are several choices for vegetable oil sources. In Brazil, soybean oil is a source that is already scaled up for biodiesel production. Nevertheless, other sources, such as sunflower, peanut, cotton, palm oil, coconut, babassu and, especially, castor oil, may be used in the near future, once their cultivation could achieve an economic up-scaling. The alcohol source in general is methanol. In Brazil, ethanol from sugar cane has a great potential as an alcohol source, since it may ally its non toxicity with a ready availability. But, it is less reactive than methanol and there are some technological problems in its industrial use [25].

The productions of vegetable oil globally and in India are given in Table 1.2 [53]. There are many countries which have large amount of bio-diesel potential because the plants oil are renewable, as the carbon released by the burning of vegetable oils is used when the oil crops undergo photosynthesis [110]. In Table 1.3 [49] top 10 countries biodiesel potential (Liter) and there production cost ($/Liter) is given.

Table 1.2: Global productions of the major vegetable oils [53]

| Oil | Production (million tons) | Oil | Production (million tons) | Oil | Production (million tons) |
| --- | --- | --- | --- | --- | --- |
| Soybean | 27.8 | Palm kernel | 2.9 | Sesame | 0.26 |
| Rapeseed | 13.7 | Olive | 2.7 | Castor | 0.25 |
| Cottonseed | 4.0 | Corn | 2.0 | Niger | 0.03 |
| Sunflower | 8.2 | Castor | 0.5 | Coconut | 0.55 |
| Peanut | 5.1 | Groundnut | 1.40 | Rice Bran | 0.55 |
| Coconut | 3.5 | Soya | 0.82 | Linseeds | 0.1 |
| Linseeds | 0.6 | Mustard | 1.55 | Cottonseed | 0.44 |
| Palm | 23.4 | Sunflower | 0.3 |  |  |
| Total | 86.3 | Total | 12.17 | Total | 2.18 |

Table 1.3: Top 10 countries in terms of biodiesel potential [49]

| Rank | country | Volume potential (Liter) | Production cost ($/L) |
| --- | --- | --- | --- |
| 1 2 3 4 5 6 7 8 9 10 | Malaysia Indonesia Argentina USA Brazil Netherlands Germany Philippines Belgium Spain | 14540,000,000 7595,000,000 5255,000,000 3212,000,000 2567,000,000 2496,000,000 2024,000,000 1234,000,000 1213,000,000 1073,000,000 | $ 0.53 $ 0.49 $ 0.62 $ 0.70 $ 0.62 $ 0.75 $ 0.79 $ 0.53 $ 0.78 $ 1.71 |

As in this thesis the source used for biodiesel production is Tumba (Citrullus Colocynthis) oil whose sources are discussed in detail is as follows:

Colocynthis (tumba) is a multipurpose crop belonging to family Cucurbitaceae. This is known by different name in different states of India,Viz. Ghumba in Punjab, Indark in Gujarat, Makal in Bengal and Kartama in south India. The extensive growth of it’s branches to greater lengths, in sandy undulated plains and sand dunes play an important role in controlling soil erosion in desert areas.

Tumba is a native of warmer parts of Asia and Africa. It occurs throughout in India and is seen growing wild in the warm arid and sandy tracts of North West, Central and South India and on the sea shores of Coromondal coast, Gujarat and other parts of Western India. It is found in wild form in desert area of Rajasthan, namely Bikaner, Barmer and Jaisalmer and is found growing wild in the district of Jodhpur, Nagaur, Churu and Sikkar. It is annual or  perennial herb with a prostrate and climbing stem, bearing smooth spherical fruits which are mottled green when young and some what yellow when ripe. The fruits are of the size of small orange, 3-4 inches in diameter and contain a soft spongy pulp and numerous ovate compressed, white or brownish seeds. It spreads upto 4-5m, on all sides all over as shown in Figure 1. Its average speed production is 450-600 kg/ha and oil content is 25-27%. The seeds contain 30-34% of pale oil. Citrullus clocynthis plant with fruits and seeds are shown in Figure 1.1(a) and 1.1(b), respectively [117].

Figure 1.1(a): Citrullus Colocynthis plant                 Figure 1.1(b): Tumba fruit and seeds

1.6  Chemistry of Biodiesel

In the transesterification of different types of oils, triglycerides react with an alcohol, generally methanol or ethanol, to produce esters and glycerin. To make it possible, a catalyst is added to the reaction [23, 38, 39, 50, 54].

CH2-OOC-R1				                        R1-COO-R’	                  CH2-OH

|				              Catalyst				       |

CH-OOC-R2      +    3R’OH	       	                        R2-COO-R’         +           CH-OH

|									                   |

CH2-OOC-R3				                        R3-COO-R’	                  CH2-OH

Glycerides	           Alcohol			                Esters		       Glycerin

The overall process is normally a sequence of three consecutive steps, which are reversible reactions. In the first step, from triglycerides diglyceride is obtained, from diglyceride monoglyceride is produced and in the last step, from monoglycerides glycerin is obtained. In all these reactions esters are produced. The stochoimetric relation between alcohol and the oil is 3:1. However, an excess of alcohol is usually more appropriate to improve the reaction towards the desired product [39, 54]:

Triglycerides (TG) + R’OH                                       Diglycerides (DG)    +     R’COOR1

Diglycerides (DG) + R’OH                                       Monoglycerides (MG) + R’COOR2

Monoglycerides (MG) + R’OH                                 Glycerin (GL)     +    R’COOR3

1.7  Properties of Biodiesel

The properties of biodiesel are as follows :

The flash point is defined as the “lowest temperature corrected to a barometric pressure of 101.3 kPa (760 mm Hg), at which application of an ignition source causes the vapors of a specimen to ignite under the specified conditions of test.” This test, in part, is a measure of residual alcohol in the B100. The flash point is also a determinant for flammability classification of materials. B100’s typical flash point is >200°C, classifying it as “non-flammable”. Water and sediment is a test that “determines the volume of free water and sediment in middle distillate fuels having viscosities at 40°C in the range 1.0 to 4.1 mm2/s and densities in the range of 700 to 900 kg/m3.” This test is a measure of cleanliness of the fuel. For B100 it is particularly important because water can react with the esters, making free fatty acids, and can support microbial growth in storage tanks [54]. The flash point values of vegetable oil methyl esters are much lower than those of vegetable oils. An increase in density from 860 to 885 kg/m3 for vegetable oil methyl esters or biodiesels increases the viscosity from 3.59 to 4.63 mm2/s. There is high regression between the density and viscosity values of vegetable oil methyl esters. The relationships between viscosity and flash point for vegetable oil methyl esters are irregular [52].

Kinematic viscosity- The resistance to flow of a fluid under gravity. The kinematic viscosity is a basic design specification for the fuel injectors used in diesel engines. Too high a viscosity, and the injectors do not perform properly [54].

Dynamic viscosity – Ratio between applied shear stress and rate of shear of a liquid [54].

Density – The mass per unit volume of a substance at a given temperature [54].

Acid Value-Acid value is defined as milligrams of potassium hydroxide necessary to neutralize fatty acids in 1 g of sample [45].

Sulfated ash – The residue remaining after a sample has been carbonized, and the residue subsequently treated with sulfuric acid and heated to a constant weight. This test monitors the mineral ash residual when a fuel is burned. For biodiesel, this test is an important indicator of the quantity of residual metals in the fuel that came from the catalyst used in the esterification process [54].

Copper strip corrosion – Detection of the corrosiveness to copper of fuels and solvents. This test monitors the presence of acids in the fuel. For B100, the most likely source of a test failure would be excessive free fatty acids, which are determined in accordance with an additional specification [54].

Cetane number – A measure of the ignition performance of a diesel fuel obtained by comparing it to reference fuels in a standardized engine test. Cetane for diesel engines is analogous to the octane rating in a spark ignition engine. It is a measure of how the fuel will ignite in the engine. For B100, the cetane number can be very accurately predicted using the ester’s composition. It is unlikely that an individual producer will ever run cetane tests on-site [54]. The cetane number (CN) is based on two compounds, hexadecane, with a CN of 100, and heptamethylnonane, with a CN of 15. The CN is a measure of the ignition quality of diesel fuels, and a high CN implies short ignition delay. The CN of biodiesel is generally higher than conventional diesel. The longer the fatty acid carbon chains and the more saturated the molecules, the higher the CN. The CN of biodiesel from animal fats is higher than those of vegetable oils [52].

Cloud point – The temperature at which a cloud of wax crystals first appears in a liquid when it is cooled down under conditions prescribed in this test method. The cloud point is a critical factor in cold weather performance for all diesel fuels. The chemical composition of some biodiesel feedstocks leads to a B100 that may have higher cloud points than desired. The cloud point, however, is another parameter that can be predicted accurately with knowledge of the esters composition, but producers are advised to be able to perform this test [54]. The CP is the temperature at which wax first becomes visible when the fuel is cooled. Biodiesel has a higher cloud point compared to conventional diesel [52].

Pour Point - The pour point is the temperature at which the amount of wax from a solution is sufficient to gel the fuel; thus it is the lowest temperature at which the fuel can flow. Biodiesel has a higher pour point compared to conventional diesel [52].

Carbon residue – In petroleum products, the part remaining after a sample has been subjected to thermal decomposition. The carbon residue is a measure of how much residual carbon remains after combustion. This is particularly important in diesel engines because of the possibility of carbon residues clogging the fuel injectors. The most common cause of excess carbon residues in B100 is an excessive level of total glycerin. Total glycerin is also measured directly using an additional procedure specified in this Standard [54].

Acid number – The quantity of base, expressed as milligrams of potassium hydroxide per gram of sample, required to titrate a sample to a specified end point. The acid number is a direct measure of free fatty acids in B100. The free fatty acids can lead to corrosion and may be a symptom of water in the fuel [54].

Free glycerin – Glycerin present as molecular form in the fuel. Free glycerin results from incomplete separation of the ester and glycerin products after the esterification reaction. This can be a result of incomplete washing and may be accompanied by incomplete alcohol removal and a lowered flash point. The free glycerin is a source of carbon deposits in the engine because of incomplete combustion[54].

Total glycerin – Sum of free and bonded glycerin. Bonded glycerin – “is the glycerin portion of the mono-, di-, and triglyceride molecules.” Elevated total glycerin values are indicators of incomplete esterification reactions and predictors of excessive carbon deposits in the engine. The terms “glycerin” and “glycerol” are used interchangeably [54].

Phosphorus – This test covers the quantitative determination of barium, calcium, copper, magnesium, phosphorus, sulfur, and zinc in unused lubricating oils and additive packages. In the case of B 100, phosphorus can come from incomplete refining of the vegetable oil and from bone and proteins encountered in the rendering process [54].

Vacuum distillation end-point – This test covers the determination, at reduced pressures, of the range of boiling points for petroleum products that can be partially or completely vaporized at a maximum liquid temperature of 400°C. Petroleum fractions have tens to hundreds of individual compounds mixed together. The distillation curves are used to characterize the broad chemistry of a given crude oil source. In B100 there are at most ten different esters present, and they can be identified using gas or liquid chromatography. The same chromatograph that determines free and total glycerin can determine the esters composition in the B100. This composition allows calculation of the T-90 point for the fuel, without having to perform the testing for every batch of product. The “T-90” point is the temperature at which 90 percent of the liquid volume has been distilled [54].

Storage stability – All fuels are subject to degradation over time when they are stored. This degradation may be due to microbial action, water intrusion, air oxidation, etc. The standard and the test methods for determining storage stability for B100 are still in the development stage within the ASTM process [54]. This is due to the unsaturated fatty acid chains and the presence of the double bond in the molecule, which produce a high level of reactivity with the oxygen, especially when it placed in contact with air. The oxidation of fatty acid chains is a complex process that proceeds by a variety of mechanisms. The various other factors influence the oxidation process of biodiesel includes light, temperature, extraneous materials, peroxides, size of the surface area between biodiesel and air. One of the methods of improving biodiesel oxidative stability includes the deliberate addition of antioxidants or modification of the fatty ester profile [64].

1.8  Motivation

The decrease of world petroleum reserves and high energy demand in the power industries and transport sector has necessitated the need for an alternative source of energy. Due to harmful emission and green house gas from fossil fuel, environment is continuously degrading. Therefore there is an also need of alternative fuel which improve the environmental condition. Biodiesel obtained from vegetable oil can be alternative source of energy because its property is similar to petroleum derived diesel oil and produces favourable effects on the environment, such as a decrease in acid rain and greenhouse effect. Due to these factors, the use of biodiesel is considered an advantage to that of fossil fuels.

This work hoped a positive way towards security of energy in future. The aim of this project to search for suitable and effective method of biodiesel production, and performance in I.C.Engine.

1.9 Objective

The aim of this thesis is to produce biodiesel by using Tumba (Citrullus Colocynthis) oil through conventional mechanical stirring and cavitation methods, and their comparison. Performance and emission testing of Tumba blends fuel by comparing it from diesel of various parameters.

1.10 Organization of the Report

First chapter is introduction which deals with the energy demand over world and need of renewable energy to secure the future demand of energy. This chapter comprises of background and concept of biofuels, definition of biodiesel, need of biodiesel, Indian energy scenario, the resources of biodiesel, biodiesel properties according to the literatures, role of biodiesel produ ction, performance and emission testing.

Second chapter is literature review in which literatures available on biodiesel production, it’s properties and its performance testing are summarized.

Third chapter deals with biodiesel production techniques and its feasibility. In this chapter conventional mechanical stirring, ultrasonic and hydrodynamic cavitation methods as well as supercritical methanol technology has been discussed.

Fourth chapter is biodiesel production through conventional mechanical stirring and ultrasonic cavitation method.

Fifth chapter includes biodiesel production through hydrodynamic cavitation method. This chapter includes the comparison of hydrodynamic cavitation method with other two methods describe in the fourth chapter.

Sixth chapter is performance studies of biodiesel derived from tumba oil using various performance parameters.

CHAPTER-3

BIODIESEL PRODUCTION TECHNIQUES

3.1  Process overview

There are severally generally accepted ways to make biodiesel some more common than others e.g. blending and transesterification, and several others that are more recent developments e.g. reaction with supercritical methanol. An overview of these processes is as follows:

1). Direct use and blending, which is the use of pure vegetable oil or the blending with diesel

fuel in various ratios,

2). Microemulsions with simple alcohol,

3). Thermal cracking (pyrolysis) with alkanes, alkenes, alkadienes etc.

4). Transesterification (alcoholysis) which consists of several sub categories

i). Alkali-catalyzed Transesterification

ii). Acid Catalyzed Pretreatment

iii). Lipase as catalyst

5). Other forms of catalysis

i). Biocatalyst

ii). Reaction with supercritical methanol

iii).Catalyst free

3.1.1 Direct use and blending

The direct use of vegetable oils in diesel engine is problematic and has many inherent failings. Although some diesel engines can run pure vegetable oils engines, turbocharged direct injection engines such as trucks are prone to many problems. Energy consumption with the use of pure vegetable oils, was found to be similar to that of diesel fuel for short term use ratios of 1:10 to 2:10 oil to diesel have been found to be successful [23].

3.1.2 Microemulsions

Microemulsions are defined as a colloidal equilibrium dispersions of optical isotropic fluid structures, with dimensions generally in the 1-150 nm range. These are formed spontaneously from two normally immiscible  liquids and one or more ionic or non ionic amphophiles. A microemulsion is designed to tackle the problem of high viscosity of pure vegetable oils by reducing the viscosity of oils with solvents such as simple alcohols. The performances of ionic or non ionic microemulsion were found to be similar to diesel fuel, over short term testing They also achieved short term characteristics. In longer term testing no significant deterioration in performance was observed, however significant injector needle sticking, carbon deposites incomplete combustion and increasing viscosity of lubricating oil [23, 48].

3.1.3 Thermal Cracking  (Pyrolysis)

Pyrolysis is the conversion of one substance into another by means of applying heat i.e. heating in the absence of air or oxygen with temperatures ranging from 450oC-850oC. In some situating this is with the aid of a catalyst leading to the cleavage of chemical bonds to yield smaller molecules. Unlike direct blending, fats can be pyrolysed successfully to produce many smaller chain compounds. The pyrolysis of fats has been successfully to produce many smaller chain compounds. Typical catalyst that can be employed in pyrolysis are SiO2 and Al2O3.The ratios of light to heavy compounds are temperature and time dependent. The equipment for pyrolysis or thermal cracking is expensive for modest throughout. Although the products are chemically similar to pyrochemically based diesel, oxygen removal from the process decreases the products benefits of being an oxygenated fuel. This decreases its environmental benefits and generally produces more fuel similar in properties of gasoline than diesel, with the addition of some low value materials [23, 48].

3.1.4  Transesterification

Refer section 1.6 of chapter-1. Some of the types of transesterification phenomena are discussed below:

(A). Alkali-catalyzed Transesterification

Figure 3.1 shows a schematic diagram of the processes involved in biodiesel production from feedstocks containing low levels of free fatty acids (FFA). This includes soybean oil, canola (rapeseed) oil, and the higher grades of waste restaurant oils. Alcohol, catalyst, and oil are combined in a reactor and agitated for approximately one hour at 60ºC. Smaller plants often use batch reactors [22] but most larger plants (> 4 million liters/yr) use continuous flow processes involving continuous stirred-tank reactors (CSTR) or plug flow reactors [8]. The reaction is sometimes done in two steps where approximately 80% of the alcohol and catalyst is added to the oil in a first stage CSTR. Then, the product stream from this reactor goes through a glycerol removal step before entering a second CSTR. The remaining 20% of the alcohol and catalyst are added in this second reactor. This system provides a very complete reaction with the potential of using less alcohol than single step systems. Following the reaction, the glycerol is removed from the methyl esters. Due to the low solubility of glycerol in the esters, this separation generally occurs quickly and may be accomplished with either a settling tank or a centrifuge. The excess methanol tends to act as a solubilizer and can slow the separation. However, this excess methanol is usually not removed from the reaction stream until after the glycerol and methyl esters are separated due to concern about reversing the transesterification reaction. Water may be added to the reaction mixture after the transesterification is complete to improve the separation of glycerol [54, 25, 39].

Figure 3.1: Process Flow Schematic for Biodiesel Production [54]

(B). Acid Catalyzed Pretreatment

Special processes are required if the oil or fat contains significant amounts of FFAs. Used cooking oils typically contain 2-7% FFAs and animal fats contain from 5-30% FFAs. Some very low quality feedstocks, such as trap grease, can approach 100% FFAs. When an alkali catalyst is added to these feedstocks, the free fatty acids react with the catalyst to form soap and water as shown in the reaction below:

Up to about 5% FFAs, the reaction can still be catalyzed with an alkali catalyst but additional catalyst must be added to compensate for that lost to soap. The soap created during the reaction is either removed with the glycerol or is washed out during the water wash. When the FFA level is above 5%, the soap inhibits separation of the glycerol from the methyl esters and contributes to emulsion formation during the water wash. For these cases, an acid catalyst such as sulfuric acid can be used to esterify the FFAs to methyl esters in the following reactions [54, 25, 39].

(C). Lipase as catalyst

Lipases are enzymes used to catalyze some reaction such as hydrolysis of glycerol, alcoholysis and acidolysis, but it has been discovered that they can be used as catalyst for tranesterification and esterification reactions too. Biocompatibility, biodegradability and environmental acceptability of the biotechnical procedure are the desired properties in agricultural and medical applications. The extra cellular and the intracellular lipases are also able to catalyze the transesterification of triglycerides effectively [39].

3.2   Conventional Mechanical Stirring Method

3.2.1  Principle

Conventional mechanical stirring machine consist of temperature controller to control temperature within the range of 0-100oC and speed controller is for controlling speed of stirrer in terms of revolution per minute (rpm). In this machine hot plate functions as a heating source to maintain the temperature of the solution. The beaker is placed on the hot plate then vegetable oil as per the requirement was poured into it at the beginning. The reaction started when a quantitative amount of methanol liquor dissolved in catalyst was poured into the beaker and than immediately drop the magnetic stirrer so that through it’s stirring action at a particular rpm, dilution of mixture can take place by switching the button on.

3.2.2  General reviews

Figure 3.2: Scheme of the reactor used in the transesterification experiments. [1. Stirrer engine. 2. Stirrer steel bar. 3. Coupling device. 4. Stirrer lubricant reservoir. 5. Glass stirrer. 6. Funnel. 7. Thermocouple. 8. Water condenser. 9. Glass tank reactor. 10. Heating mantle. 11. PID temperature controller.]

In a 2 litre glass reactor (see Fig. 3.2) equipped with a glass anchor-shaped stirrer, a type K thermocouple, a water condenser and funnel, and surrounded by a heating mantle controlled by a proportional integral derivative (PID) temperature controller device, 873 ml (702 g, 0.80 mol) of used frying oil and 244 ml (6 mol) of methanol were placed. The temperature was raised to 60oC and the mixture was stirred at 600 rpm. When this temperature was reached, sodium methoxide (7 g, 0.13 mol, 1% w/w of oil, prepared recently from sodium metal and anhydrous methanol) was added; the temperature increased by two to three degrees, decreasing later to 60oC by the action of the PID controller. Samples of 10 ml (8 g) were taken from the reaction mixture at regular intervals, typically 10 min, neutralized, and analysed by gas chromatography. When the conversion of the oil was quantitative, as determined by the GC, the heating mantle was switched on. The mixture was then allowed to cool in the reactor and was neutralized with the stoichiometric amount of concentrated hydrochloric acid (11.5 ml, 35% w/w), appearing as two distinct phases after switching of the stirrer. These two phases were decanted using the bottom outlet of the reactor. The excess methanol in both phases was evaporated at vacuum, and 580 g of biodiesel, 17 g of glycerine and water interface and 200 ml of methanol were recovered. The interface was composed of glycerine, water and sodium chloride. Biodiesel, used without further purification, was a clear, light yellow liquid [1].

Cotton oil soapstock that was used in this study contains 85.3% free fatty acid. Before the transesterification, cotton oil soapstock was filtered and dried for removing water and impurities at 100oC. Transestrification process was carried out in a 1000 ml reaction vessel equipped with reflux condenser, magnetic stirrer and thermometer. At this reaction, sulfuric acid was used as catalyst. 500 grams of cotton oil soapstock, 100 g of methyl alcohol and 25 g of sulfuric acid were mixed. The mixture was heated to

75oC and held at this temperature with stirring for 2 hours. Eight hours after the reaction, water, catalyst and glycerine (brown and sticky) settled at the bottom of the reaction vessel and were separated by separation funnel. And then, this mixture was washed with the solution of sodium bicarbonate in order to remove

suspended glycerol, unreacted methanol and catalyst. Sodium bicarbonate is alkali, and therefore it reduced acid value of crude biodiesel (methyl ester). Crude biodiesel was distillated for obtaining pure methyl ester by means of batch distillation apparatus. Flow diagram of cotton oil soapstock biodiesel production process is shown in Figure 3.3.

Figure 3.3: Flow diagram of cotton oil soapstock biodiesel production process [3]

3.3  Cavitation Methods

Cavitation can be in general defined as the generation, subsequent growth and collapse of cavities resulting in very high energy densities of the order of 1 to 1018 kW/m3. Cavitation can occur at millions of locations in a reactor simultaneously and generate conditions of very high temperatures and pressures (few thousand atmospheres pressure and few thousand Kelvin temperature) locally, with the overall environment being that of ambient conditions. Thus, chemical reactions requiring stringent conditions

can be effectively carried out using cavitation at ambient conditions. Moreover, free radicals are generated in the process due to the dissociation of vapours trapped in the cavitating bubbles, which results in either intensification of the chemical reactions or in the propagation of certain unexpected reactions. Cavitation also results in the generation of local turbulence and liquid micro-circulation (acoustic streaming) in the reactor, enhancing the rates of transport processes. The four principle types of cavitation and their causes can be summarized as follows [17]:

1). Acoustic cavitation- In this case, pressure variations in the liquid are effected using sound waves,  usually ultrasound (16 kHz–100 MHz). The chemical changes associated with the cavitation induced by the passage of sound waves are commonly termed as sonochemistry.

2). Hydrodynamic cavitation- Cavitation is produced by pressure variations, which is obtained using the geometry of the system creating velocity variation. For example, based on the geometry of the system, the interchange of pressure and kinetic energy can be achieved resulting in the generation of cavities as in the case of flow through orifice, venturi, etc.

3). Optic cavitation- This is produced by photons of high intensity light (laser) rupturing the liquid continuum.

4). Particle cavitation- This is produced by a beam of elementary particles, e.g. a neutron beam rupturing a liquid, as in the case of a bubble chamber.

3.3.1   Ultrasonic Cavitation Method

3.3.1.1  Principle

Principal of ultrasonic cavitation method is the process of creating cavities  by the irradiation of power ultrasonic with sufficient energy in immiscible liquid (oil and alcohol are not miscible with each other) as a result micro fine bubbles are formed and these bubbles are collapsing at various place of the reactor and disturb the phase boundary between two immiscible liquid and resulted emulsification of mixture. In the cavitation process small bubbles are formed in liquids at mechanically weak points, usually at phase boundaries, as a result of intense sonication. These bubbles increase in size due to resonance in areas of under pressure. Small gas bubbles present in the liquid initiate the process. This process is directly related to oscillatory velocity which is directly related to vibration amplitude at given frequency [15]. More the oscillatory velocity the reaction time will be short. On the other hand oscillating velocity of ultrasonic transducer is insufficient for the sonochemical reaction in the mixture so acoustic rod horn connected to the transducer are used to amplify the vibration amplitude this rod permit achieving higher velocity and less reaction time. Low frequency ultrasonic irradiation is a useful tool for emulsification of immiscible liquids. The collapse of the cavitation bubbles disrupts the phase boundary and causes emulsification, by ultrasonic jets that impinge one liquid to another.

3.3.1.2 General reviews

Figure 3.4: Schematic representation                    Figure 3.5: Schematic representation of and

of ultrasonic horn[17]                                               ultrasonic bath [17]

A schematic diagram of these standard configurations has been depicted in Figure 3.4 and 3.5. The horn operates at a frequency of 22.7 kHz and a rated power dissipation of 240 W. Two different tips (irradiating surface area of 3.46 and 4.91 cm2) can be used so as to change the operating intensity of irradiation (defined as power dissipated per unit area of the horn). The capacity of the reactor generally ranges from 10 to 200 ml. Ultrasonic horn-type of configurations are generally suitable for laboratory scale characterization/ feasibility experiments, as they provide intense but local cavitation. The ultrasonic bath has a fixed operating frequency of 22 kHz (one can get these at different operating frequencies) with a rated output power of 120 W (again variable power dissipation is possible). Three transducers are placed at the bottom of the reactor in a triangular pitch. The maximum operating capacity of the ultrasonic bath is about 3 litre, but in general baths with higher capacity (up to 1000 litre) can be used with some modification in terms of larger number of transducers in different configurations. Again, ultrasonic bath-type of reactors are suitable for laboratory to pilot-scale operations, as there is a limitation on the number of transducers that can be incorporated in the system for a large-scale operation [17].

By using ultrasounds the reaction time is much shorter (10–40 min) than for mechanical stirring. The quantity of required catalyst is 2 or 3 times lower. The molar ratio of alcohol/oil used is only 6:1. Normal chain alcohols react fast, while secondary and tertiary alcohols show some or no conversion after 60 min of reaction. Surprisingly, 40 kHz ultrasounds are much more effective in the reduction of the reaction time (10–20 min). Twenty eight kilohertz give slightly better yields (98–99%), but longer reaction time, while higher frequencies are not useful at all for the transesterification of fatty acids [9].

The biodiesel production through transesterification of triolein with various alcohols such as methanol, ethanol, propanol, butanol, hexanol, octanol and decanol was investigated at molar ratio 6:1 (alcohol: triolein) and 25oC in the presence of base catalysts (NaOH and KOH) under ultrasonic irradiation (40 kHz) and mechanical stirring (1800 rot/min) conditions.

3.3.2   Hydrodynamic Cavitation Method

3.3.2.1   Principle

The principle of hydrodynamic cavitation machine resembles the ultrasonic cavitational method as the fundamental of working is cavitation phenomena. In the cavitation process small bubbles are formed in liquids at mechanically weak points, usually at phase boundaries, as a result of intense sonication. These bubbles increase in size due to resonance in areas of under pressure. Small gas bubbles present in the liquid initiate the process. This process is directly related to oscillatory velocity which is directly related to vibration amplitude at given frequency. The series of working is bubble formation, growth and when it collapses, due to the rapid kinetic motions of molecules due to high generation of pressure inside. Using cavitation as an alternative technique for the synthesis of biodiesel results in conditions of very high local temperatures and pressures at the same time releasing free radicals which intensifies many chemical reactions [17, 12].

3.3.2.2  General reviews

Esterification of Fatty acid (FA) with methanol in the presence of concentrated H2SO4 as a catalyst has been studied in hydrodynamic cavitation reactor as well as in the sonochemical reactor. The hydrodynamic cavitation reactor consists of a reservoir or a collecting tank with (10 lit) capacity that is connected to the multistage centrifugal pump with power rating of 1.5 kW. A schematic representation of the setup has been shown in the Figure 3.6(a) and 3.6(b). The pipe connected to the discharge side of the pump branches into main and bypass lines. The main line has the facility to incorporate different orifice plate to generate cavitation of different intensities and characteristics. The main line and bypass line having the throttling valves and pressure gauges for the adjusting the pressure.

Figure 3.6(a): Schematic representation of the               Figure 3.6(b): Schematic diagram of

experimental setup for hydrodynamic cavitation           hydrodynamic cavitation system setup.

reactor [12]                                                                     1–tank; water; 2 – cold, 3 –pump;

4 – orifice plate [16]

The operating temperature of the reactor was maintained by circulating water within the jacket surrounding the tank as the energy dissipated by the pump can increase the temperature of the mixture [16]. The sonochemical reactor is a conventional cleaning tank type reactor equipped with 3 transducers at the bottom of the tank in triangular pitch and operates at an irradiating frequency of 20 kHz and power dissipation of 120 kW. Few experiments have also been carried out with other acid/alcohol combination viz. coconut fatty acids with methanol and ethanol and FA odour cut with fatty alcohols with an aim of investigating the efficacy of cavitation for giving the desired yields and also to quantify the degree of process intensification that can be achieved using the same [12].

Figure 3.9: Test rig for biodiesel production by hydrodynamic cavitation

The schematic diagram of the test rig developed at Delhi Technological University is shown in Figure 3.7. The setup consists of a closed loop circuit comprising a feed tank, centrifugal pump (2.2 kW), control valve and a coupling to accommodate the orifice plate. The suction side of the pump is connected to the bottom of the feed tank. Discharge from the pump branches into two lines, which help in the control of inlet pressure and inlet flow rate into the main line housing and the orifice with the help of valves V1 and V2. The main line consists of a coupling to accommodate the orifice plate (single or multiple holes with different configurations). Four orifice plates with the numbers of holes 1, 3, 5 and 7 are used during experimentation. The diameter of each hole was 3 mm.

The vegetable Thumba oil of (3.5–5.5 kg) is filtered to remove impurities. It is heated up to 110oC in order to remove water content of oil to avoid soap formation and allowed to cool upto room temperature. As given in 0.63 kg methyl alcohol (CH3OH) with a molar ratio of 1:4.5 and 0.038kg sodium hydroxide (1% by weight of oil), are mixed and stirred till sodium hydroxide is dissolve in alcohol. This liquid mixture is mixed with vegetable oil and supplied to the feed tank of hydrodynamic cavitation reactor test rig. The pump of hydrodynamic cavitation reactor is started and whole mixture is allowed to pass through orifice hole to generate the favourable cavitation conditions. During the reaction the temperature of mixture is kept between 45 and 55oC. The temperature of mixture is controlled by circulation of cooling water in the jacket of the reactor. After 10 min the first sample of 100 ml was collected from the bottom of the feed tank. Samples were further collected after an interval of five minutes. After 45 min the process is stopped and the mixture is collected in a bucket. The glycerin is allowed to settle down in the mixture as it has higher density than methyl esters. A layer of glycerin and methyl esters will be visible in 10 min of settling while complete settling takes place in 2–3 h. After the separation of the glycerin and methyl esters, the methyl esters have been washed for all samples to remove residual catalyst or soaps. For washing, first methyl esters are kept in a separating funnel and water up to 30% of methyl esters (at a temperature of 40oC) is mixed and the mixture is stirred for one minute and then left for settling of water with impurities. After complete settling of water with impurities at the bottom of separating funnel, the same is removed by opening the tab provided at the bottom of separating funnel.

Figure 3.8: Amount of biodiesel yield v/s time for 1:4.5 molar ratio of oil to alcohol [21]

The biodiesel yield obtained for 1:4.5 molar ratio is shown in Figure 3.8, for different orifice plates are shown in Figure 3.8. It can be observed that for all the orifice plates, around 80% yield is obtained within 30 min. The yield increases with increase in the number of holes and afterwards it remains more or less constant for all type of orifice plates [21].

3.4   Suprcritical & Co-solvent Method

3.4.1  Principle

There are two methods of transesterification reaction. One is the method using a catalyst and the other is without the help of a catalyst. However, there are at least two problems associated with the former process; the process is relatively time consuming and purification of the product for catalyst and saponified products are necessary. The first problem due to the two phase nature of vegetable oil/methanol mixture requires vigorous stirring to proceed in the transesterification reaction. To resolve it the use of a simple ether such as tetrahydrofuran can make this two phase nature into one phase of its mixture and that methyl esters can be produced in less than 15 min depending on the catalyst concentration. Yet, the catalyst problem cannot be solved for purification. Therefore, this conventional process still requires a high production cost and energy. The overall process, thus, includes transesterification reaction, recovery of unreacted methanol, purification of methyl esters from catalyst and separation of glycerin as a co-product from saponified products.

The latter method involves uncatalyzed transesterification of vegetable oil in supercritical methanol. The supercritical state of methanol is believed to solve the two phase nature of oil/ methanol mixture to form a single phase due to a decrease in dielectric constant of methanol in supercritical state. As a result, the reaction was found to be complete in a very short time within 2±4 min, as described in their previous work. In addition, because of non-catalytic process, the purification of products after transesterification reaction is much simpler and environmentally friendly, compared with the conventional commercial method in which all the catalyst and saponified products have to be removed for biodiesel fuel [22].

3.4.2 General reviews

Figure 3.9: Effect of the molar ratios of             Figure 3.10: Effect the reaction temperature

methanol to rapeseed oil in transesterification       on  methyl esters formation [22]

reaction on  producing methyl esters, as

treated at 350oC [22]

Figure 3.11: Unmethyl esters content in rapeseed oil during transesterification reaction [27]

To determine the effect of temperature on methyl esters formation, transesterification reactions of rapeseed oil were carried out with a fixed molar ratio of 42 in methanol, the best condition found in Figure 3.9, at various temperatures ranging from 200 to 500oC. the content of methyl esters obtained is shown in Figure 3.10, in which the obtained experimental data are shown by the symbols, whereas the simulated curves are shown by the lines Figure 3.11 shows the correlation between the content of unmethyl esterified compounds and reaction times. As mentioned previously, unmethyl esterified compounds are defined as other compounds obtained from the upper portion excluding five types of methyl esters, such as methyl palmitate, methyl oleate, methyl stearate, methyl linoleate and methyl linolenate. The straight line was determined to it the data in order to adopt the first order rate equation.

A highly efficient transesterification process has been described and the proposed kinetics in transesterification of rapeseed oil has been proven to it very well with those of experimental data. A reaction temperature of 350oC with the molar ratio of methanol being 42 were considered as the best condition for a free-catalyst process of biodiesel fuel production. The supercritical methanol method, therefore, offers a potentially low cost method with simpler technology for producing an alternative fuel for compression ignition engines. The considerable yield of methyl esters by the environmentally friendly method renders this technique ideally suited for industrialization [22].

A set of experiments was carried out to study the effect of reaction temperature, reaction pressure and molar ratio of methanol to triglycerides in the methyl esters formation. The results revealed that the supercritical treatment of 350oC, 30 MPa and 240 sec with molar ratio of 42 in methanol is the best condition for transesterification of rapeseed oil to biodiesel fuel [24].

Figure 3.12: Supercritical continuous reaction device [27]. [1, 2. high-pressure pump; 3, 4, 10, 12, 15, 16. valve; 5. preheater; 6. blender; 7. tube reactor; 8. thermometer; 9. manometer; 11. condenser; 13. pressure regulator; 14. separatory funnel]

As depicted in Figure 3.12, the reaction of transesterification was carried out in a 75 ml tube reactor, equipped with a preheater, blender, condenser and separatory funnel. An electric thermostat was used to control the temperature of the reactor. First, the preheater (50–400oC) and reactor (200–400oC) were preheated at a designated temperature respectively. Then calculated amounts of soybean oil and methanol (the molar ratio of methanol to oil was taken at 6:1– 80:1) were synchronously pumped into the tube preheater by high pressure pump and heated to the predetermined temperature. At the blender, the soybean oil and methanol were mixed at a constant stirring rate. And then the reaction mixture was pumped into the tube reactor. The residence time (12.5–50 min) of reactants in the reactor could be regulated by adjusting the flux of the high-pressure pump (0.10–9.99 ml/min). The reaction temperature (240– 340oC) and pressure (10–40 MPa) inside the tube reactor could be adjusted by an electric thermostat and pressure regulator, respectively. Through the condenser, the product was cooled to the normal temperature, and then the crude methyl esters could be obtained in the separatory funnel. The methyl ester concentration was quantified using a Hewlett–Packard 6890 gas chromatograph equipped with a HP-INNOWAX capillary column (30 m, 0.15 mm) and a flame ionization detector. 4l litre of crude ester layer was dissolved in 300 ll n-hexane and 100 litre internal standards (heptadecanoic acid methyl ester) for GC analysis. Samples (1 litre) were injected by a sampler at an oven temperature of 220oC. After an isothermal period of 4 min, the GC oven was heated at 10oC/min to 230oC, and held for 7.5 min. Nitrogen was used as carrier gas at a flow rate of 2 ml/min measured at 20oC. The detector make up gas was used at a flow rate of 30 ml/min. The inlet pressure was 96.4 kPa. The split ratio was 10:1 and the injector and detector temperatures were 300oC and 320oC, respectively. The methyl ester yield of oil in each experiment was calculated [27].

CHAPTER-4

BIODIESEL PRODUCTION THROUGH ULTRASONIC HORN TYPE & COVENTIONAL STIRRING METHOD

In this report biodiesel is produced from hydrodynamic cavitation, ultrasonic cavitation and conventional magnetic stirring method. This chapter contains the details of biodiesel production by using Tumba (citrullus colocynthis) oil, emphasizing on ultrasonic cavitation and conventional magnetic stirring method  and results of these methods are relatively compared.

4.1 Ultrasonic Cavitation

The principle of ultrasonic cavitation is discussed in chapter 3. The development of experimental set up, reagents and material used, procedure and collection of experimental datas is discussed below.

4.1.1 Experimental Set-up

The transesterification reactions were carried out in an ultrasonic reactor. Schematic diagram of it’s front view, side view and photograph of ultrasonic horn type processor is shown in figure 4.1(a), 4.1(b) and 4.2, respectively. In horn type reactor, horn is attached with the transducer which produce ultrasonic irradiation in the mixture. Horn type reactor has been used for this experiment. The ultrasonic cavitation generates ultrasonic processor frequency ranging from 25 kHz to 30 kHz for a time limit ranging from 3 min to 30 min. There is an integrated arrangement for supporting the beaker (100 ml) so that the transducer horn should be dipped at the separating boundary. The horn of the transducer was submerged 2 cm in the reactive mixture of methanol and vegetable oil. The temperature of the reaction mixture was controlled by a water bath.  Heated fatty acid oil (50 g) was poured into the reactor at the beginning. The reaction started when a quantitative amount of methanol liquor dissolved in KOH was poured into the heated reactor. The reaction is carried out by ultrasonic irradiation produced by ultrasonic generator through the transducer incorporated with acoustic rod horn. There is a temperature measurement device which indicates the temperature of mixture and provides a measure to control it.

Figure 4.1(a): Schematic diagram of ultrasonic horn type reactor

Figure 4.1(b): Side view of the Horn type Processor

Figure 4.2: Photograph of ultrasonic horn type processor (TU-50)

## 4.1.2 Reagents and Materials used

1. Tumba originated from the Tumba seeds, 50g/sample for preparing experimental biodiesel sample.

2. Methyl alcohol (CH3OH) (99% pure) for removing the free fatty acid from the oil.

3. Base catalyst (KOH or NaOH) (85% pure) for accelerating the reaction mixture.

## 4.1.3 Procedure

## This experiment has been performed to evaluate performance of ultrasonic cavitation method for biodiesel production in terms of yield (%) and time. Same amount of sample (50g) has been taken of raw vegetable oil for both ultrasonic cavitation method and conventional method to facilitate comparison. Experiment has been performed with the following steps:

1. Tumba oil (50g) is taken in a 100 ml beaker and filtered it to remove impurities. Than it is heated through a heating device up to 110oC measured by an alcoholic column thermometer in order to remove water content of oil to avoid soap formation as shown figure 4.3(a). This oil is allowed to cool up to 50oC temperature so as to reaction can take place.

Figure 4.3(a): Heating of raw vegetable oil

Figure 4.3(b): Methanol and KOH                    Figure 4.3(c): Weighing machine

2. Now methyl alcohol (CH3OH) is taken with a molar ratio of (1:4.5 & 1:6) and catalyst (KOH) is     taken as 0.5%, 0.75% and 1% by weight of oil as shown in Figures 4.3(b) and 4.3(c). Then mixer of methyl alcohol and KOH is stirred until KOH dissolve in methyl alcohol.

3. This liquid mixture is mixed with vegetable oil. Initially the methanol is immiscible with the oil.

4. The mixture of oil, methanol and catalyst come in contact with ultrasonic processor transducer (model TU-50) which is shown in Figure 4.3(d).

Figure 4.3(d): Transesterification, Separation of Layers, Washing processes

6. Test is performed for the ultrasonic frequency (28.5 kHz). During the reaction the temperature of mixture is kept between 40-55oC.

7. When reaction is completed the beaker is kept for the separation of glycerol and biodiesel. Glycerol has higher specific weight therefore it will settle at bottom as shown in Figure 4.3(d). Separation of methyl ester and glycerol will takes 2 to 3 hr duration.

8. After complete separation bio-diesel (Methyl Ester) is visible in the upper layer and glycerol.

9. Bio-diesel is separated and collected for purification process.

10. To remove the catalyst, water should be 33% wt. of biodiesel at around 40-45oC is mixed with the methyl ester and left for settling down will take 12-24 hrs. Water due to its higher specific gravity collected at bottom. This is shown in Figure 4.3(d).

11. Excess methanol present in biodiesel has been removed by distillation process. This methanol can be again used for transesterification process.

12. Finally separated biodiesel is heated to remove moisture present in it due to washing.

4.1.4 Experiment Data

Weighing uncertainity occurs in weighing machine in terms of fixed error of weighing machine, confidence limit that is probable measurement error (Pe), relative uncertainty (Ur)   are 0.01g, + 0.005g, + 8.0645 X 10-5 ( ie. + 0.0081%), respectively. Thermometer  uncertainity occurs in thermometer in terms of fixed error of the scale,  confidence limit that is probable measurement error (Pe),  relative uncertainty (Ur) are 1oC ,  + 0.5oC, + 4.5 X 10-3( ie.+ 0.45%),

respectively. The detail calculations of these terms and yield percentage is shown in Appendix-I. The remaining required calculations are shown below.

(A). Materials

The experiments are performed with alcohol to oil molar ratio as 6:1 and 4.5:1. The amount of oil, alcohol and catalyst taken is shown in Table 4.1.

Table 4.1: Oil, alcohol and catalyst during the experimentation

| Molar ratio (alcohol/oil) | Quantity of non-edible oil (g) | Quantity of methanol (g) | Catalyst (KOH) |
| --- | --- | --- | --- |
|  |  |  | 0.5% | 0.75% | 1.0% |
| 6:1 | 50 g | 11 g | 0.25 g | 0.375 g | 0.5 g |
| 4.5:1 | 50 g | 8.28 g | 0.25 g | 0.375 g | 0.5 g |

(B). Calculations

(i). For calculation of molar ratio following data are used

Molecular weight of triglycerides from vegetable oil = 870

Molecular weight of methanol = 32

Hence, 1 gm mole of vegetable oil = 870 gm

1 gm mole of methanol = 32 gm

Catalyst (KOH) = 0.5%, 0.75% and 1% by weight of oil

(ii). Amount of methanol for 50 g of vegetable oil

For 1:6 molar ratio = (32 / 870) ×50 × 6 = 11 g

1:4.5 molar ratio = (32 / 870) ×50 × 4.5  = 8.28 g

(iii). Total energy consumed by ultrasonic processor power consumption/sample

Power of motor used = 50 W

Time of experiment = 20 minutes = 1200 s

Total energy consumed = 50 W × 1200 s

= 60 kW-hr

(C). Time and yield (%) produced from Tumba oil

Experiments have been performed to prepare biodiesel from Tumba oil by ultrasonic cavitation method and conventional magnetic stirring method. Main aim of this experiment to calculate time, catalyst percentage and molar ratio (alcohol/oil) for biodiesel production with maximum yield and comparison  with the conventional method. Our main emphasis on this project is to reduce the use of catalyst (KOH) and alcohol because catalyst (KOH) is pollutant for the water and land. If biodiesel produced on industrial scale, large amount of catalyst will be discharged in river or land and this will be harmful for environment and local area. The results obtained from experiment are shown below in tabular form.

(D). Experimental Data for Ultrasonic Cavitation Method

Here data is generated by performing ultrasonic cavitation on the sample which is a mixture of vegetable oil (Tumba oil), methanol (CH3OH) and catalyst (KOH). For every sample reaction time required for biodiesel production and yield of methyl ester is calculated. Time and yield for every sample is shown in tabular form given below.

Table 4.2: Ultrasonic horn type method at 28 kHz (molar ratio 4.5:1)

| Quantity of Tumba oil | Quantity of methanol | Catalyst used KOH | Yield obtained |
| --- | --- | --- | --- |
|  |  |  | 20min | 30 min | 40 min |
| (in gm) | (in gm) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) |
| 50 | 8.28 | 0.25 | 0.50 | 40.50 | 81 | 42.50 | 85 | 42.80 | 85.60 |
| 50 | 8.28 | 0.375 | 0.75 | 43.21 | 86.42 | 44.74 | 89.48 | 46 | 92 |
| 50 | 8.28 | 0.50 | 1.00 | 44.44 | 88.88 | 45.05 | 90.12 | 46.11 | 92.11 |

Table 4.3:  Ultrasonic horn type method at 28 kHz (molar  ratio 6:1)

| Quantity of Tumba oil | Quantity of methanol | Catalyst used KOH | Yield obtained |
| --- | --- | --- | --- |
|  |  |  | 10min | 20min | 30 min | 40 min |
| (in gm) | (in gm) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) |
| 50 | 11 | 0.25 | 0.50 | 44.5 | 89 | 44.86 | 89.72 | 45 | 90 | 47 | 94 |
| 50 | 11 | 0.375 | 0.75 | 44 | 88 | 43.68 | 87.36 | 44 | 88 | 44.91 | 89.82 |
| 50 | 11 | 0.50 | 1.00 | 43.5 | 87 | 43.29 | 86.58 | 42.37 | 84.74 | 43 | 83.60 |

Figure 4.4(a): Yield(%) Vs reaction time in       Figure 4.4(b): Yield(%) Vs reaction time in                                         
                         minute for molar ratio of 4.5:1                              minute  for molar ratio of 6:1

Using data from Tables 4.2 and 4.3 are plotted in the graphical form in Figures 4.4(a) and 4.4(b), which  shows that  for molar ratio 4.5:1, percentage conversion of methyl ester increases with respect to time and  catalyst (0.50%, 0.75%, 1%) too whereas for molar ratio 6:1, percentage conversion of methyl esters increases proportionally with time for catalyst using 0.50% and 0.75%, but for catalyst 1% ,there is sudden drop in yield percentage is observed as the time increases.

4.2 Conventional Mechanical Stirring Method

4.2.1 Experimantal Set-up

The transesterification reactions were carried out in an conventional mechanical stirring method, photograph is shown in Figure 4.5. Conventional mechanical stirring machine consist of temperature controller to control temperature within the range of 0-100oC and speed controller is for controlling speed of stirrer. In this machine hot plate functions as a heating source to maintain the temperature of the solution. The beaker (100 ml) is placed on the hot plate and Tumba oil (50 g) was poured into it at the beginning. The reaction started when a quantitative amount of methanol dissolved with KOH was poured into the beaker. The magnetic stirrer due to it’s stirring action enhances the transesterification reaction.

Figure 4.5: Conventional mechanical stirring method

4.2.2  Ragents and Material used

Same as given in section 4.1.2.

4.2.3  Procedure

1. Do the same steps from 1 to 3 as given in section 4.1.2.

2. The mixture of oil, methanol and catalyst come in contact due to stirring action as shown in Figure 4.5.

3. During the reaction the temperature of mixture is kept between 40-55oC and controlling the motion of capsule shaped magnetic stirrer by speed controller.

4. Repeat the same steps from 7 to 11 as given in section 4.1.2.

4.2.4  Experimental Data

The calculations will remain same as given in the section 4.2.4. For the comparison purpose similar experiment has also been performed in magnetic stirrer using the same amount of sample. Time and yield of methyl ester for Tumba oil and catalyst (%) of oil is shown in tables 4.4 and 4.5 for molar ratio 4.5:1 and 6:1 is given below.

Table 4.4: Conventional mechanical stirring method (molar  ratio 4.5:1)

| Quantity of Tumba oil | Quantity of methanol | Catalyst used KOH | Yield obtained |
| --- | --- | --- | --- |
|  |  |  | 45 min | 60 min | 75 min | 90 min |
| (in gm) | (in gm) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) |
| 50 | 8.28 | 0.35 | 0.70 | 42.31 | 84.62 | 37.07 | 74.14 | 35.63 | 71.26 | 34 | 68 |
| 50 | 8.28 | 0.375 | 0.75 | 43.6 | 87.2 | 40.96 | 81.92 | 38.72 | 77.44 | 38.7 | 77.41 |
| 50 | 8.28 | 0.50 | 1.00 | 45.66 | 91.32 | 41.7 | 83.4 | 39.37 | 78.74 | 38.83 | 77.66 |

Table 4.5: Conventional mechanical stirring method (molar  ratio 6:1)

| Quantity of Tumba oil | Quantity of methanol | Catalyst used KOH | Yield obtained |
| --- | --- | --- | --- |
|  |  |  | 45 min | 60 min | 75 min | 90 min |
| (in gm) | (in gm) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) | (in gm) | (in %) |
| 50 | 11 | 0.325 | 0.65 | 41.11 | 82.22 | 38.2 | 76.4 | 38.05 | 90 | 45.05 | 90.1 |
| 50 | 11 | 0.35 | 0.70 | 44.63 | 89.26 | 45.35 | 90.6 | 46.1 | 92.2 | 46.17 | 92.34 |
| 50 | 11 | 0.375 | 0.75 | 45.05 | 90.1 | 46.5 | 93 | 46.55 | 93.1 | 46.71 | 93.42 |
| 50 | 11 | 0.50 | 1.00 | 44.62 | 89.24 | 44 | 88 | 44.75 | 84.74 | 45.02 | 90.04 |

From above Tables 4.4 and 4.5, Figures 4.6(a) and 4.6(b) are shown below  for mechanical stirring process of two different molar ratios 4.5:1 and 6:1 in terms of percentage conversion of methyl esters Vs time in minute:

Figure 4.6(a): Yield(%) Vs reaction time in minute for the molar ratio 4.5:1 from the data

Table 4.4

Figure 4.6(b): Yield(%) Vs reaction time in minute for the molar ratio 6:1 from the data

Table 4.5

Figures 4.4(a) and 4.4(b) shows that  for molar ratio 4.5:1, percentage conversion of methyl ester declined with respect to time and  catalyst (0.50%, 0.75%, 1%) and the optimum yield of 91.32% in 45 minutes is achieved. The lower value of catalyst percent at which conversion of methyl esters takes place is 0.70%. In litratures[1,3,6,7] by using 4.5:1(alcohol:oil ratio) the yield increases proportionally with respect to  reaction time and catalyst both but through this experimentation the yield decreases. It happens because of volatility of methanol. Using molar ratio 6:1, percentage conversion of methyl esters increases proportionally with respect to time for catalyst using 0.65%, 0.70% and 0.75%, but for catalyst 1%, there is sudden drop in yield percentage is observed as the time increases. So we can conclude that as 6:1 molar ratio can produce yield at least value of catalyst is 0.65% whereas 4.5:1 can produce yield at least value of catalyst is 0.70%, which shows 6:1 molar ratio is more efficient value for biodiesel production.

4.3 Results & Discussion

On the basis of data collected for methods ultrasonic cavitation and conventional magnetic stirring method. The main emphasis of this work is to evaluate the performance of ultrasonic cavitation over conventional method for different oils.

From the above mentioned table graphs have been plotted to compare between biodiesel production  methods and various parameters (reaction time, % conversion of methyl ester, catalyst %, molar ratio). Comparisons of ultrasonic and magnetic stirrer methods for Tumba oil is plotted here.

(A) Comparison of ultrasonic and mechanical stirring methods at optimum catalyst &

molar ratio

Figure 4.7(a): Comparison of methods                    Figure 4.7(b): Comparison of methods through yield (%) Vs reaction   time in                     through yield (%) Vs reaction time in

minute for catalyst 0.75% at molar ratio 4.5:1          minute 1% at molar ratio 4.5:1

Figure 4.7(c): Comparison of methods                     Figure 4.7(d): Comparison of methods through  yield (%) Vs reaction time  in                       through yield (%) Vs reaction time in

minute for catalyst 0.75% at molar ratio 6:1               minute for catalyst 1% at molar ratio 6:1

Figure 4.7(a) shows in ultrasonic method for catalyst 0.75% and molar ratio of 4.5:1, least reaction timing is 20 minute but by using molar ratio of 6:1 the least reaction timing is 10 minute as shown in figure 4.7(c) which proves that using molar ratio 6:1 instead of 4.5:1 is more beneficial for ultrasonic cavitation method to obtain yield. However, in figure 4.7(b) and 4.7(d) shows that in conventional mechanical stirring method the percentage of yield declined as the reaction time increase for 4.5:1 molar ratio because of volatile property of the methanol

as the reaction time increases and catalyst of 1% but in ultrasonic method using catalyst 1% and molar ratio the yield percent increases as shown in figure 4.7(b).

Figure 4.7(e): Comparison of methods through          Figure 4.7(f): Comparison of methods yield (%) Vs reaction time in minute for                     through yield (%) Vs reaction time in

catalyst   0.65%  for MS & 0.50% for U                       minute for catalyst 0.70%  for MS &

at molar ratio 6:1                                                            0.50% for U at molar ratio 4.5:1

Figure 4.7(e) shows in ultrasonic method for catalyst 0.65% the least reaction timing is 10 minute by using molar ratio of 6:1 whereas the least reaction timing for mechanical stirring method is 45 minute as at catalyst percent of 0.50. Figure 4.7(f) shows that in conventional mechanical stirring method the percentage of yield declined as the reaction time increases for 4.5:1 molar ratio and catalyst of 0.70% but in ultrasonic method using catalyst 0.50% the yield percent increases. Hence, we can conclude that ultrasonic method is more efficient, less time consuming using reduced percentage of catalyst as compare to conventional mechanical stirring method.

CHAPTER-5

# DEVELOPMENT OF A BIODIESEL PRODUCTION TEST RIG BASED ON HYDRODYNAMIC CAVITATION

This chapter contains the detail work of biodiesel produced from hydrodynamic cavitation methodology. The existing model of hydrodynamic cavitation machine present in the Biodiesel Lab of Delhi Technological University can achieve the pressure of 10 bar, which lead to achieve high yield of biodiesel production at large scale and comparison of all the biodiesel production techniques are  discussed here.

5.1   Working and Constructions

The developed set up of  hydrodynamic cavitation machine consist of an A.C. induction motor, pressure pumps, flow meter, nozzle spray gun, pressure gauge, temperature indicator, control valves, throttle valve, couplings, provided with water cooling jacket.

In this experiment we have used orifice plate made of stainless steel 304, containing one hole of 1.90 mm diameter fixed in a nozzle spray gun. An A.C. induction motor  is a single phase motor of 1 horse power(hp) having voltage of 220 V and ampere of 8A with a specified value of speed 1440 rpm (revolution per minute). Reciprocating pressure pump of model AV3 PS 18 is being used in modeling of hydrodynamic cavitation machine with plunger diameter 3*18 mm, working pressure 15.25 kgcm2   required  motor  of range 5 to 1.5 hp having speed range 800 to 1000 rpm. It’s weight is 7 kg. A rotameter is fitted in between two couplings to measure fluid in terms of LPM (litre per minute) which ranges from 0 to 20. The Pressure gauge is attached at the top of the model to control the pressure inside the cylindrical tank of range 0 to 350 Psi or 0 to 20 bar. The model consist of one temperature indicator too, to maintain the temperature of the mixture (catalyzed alcohol and Tumba oil) which ranges from 0 to 150oC. The cylindrical tank is prepared by rolling process using 304 SS having the capacity of 10 litres. And its joints are welded using gas welding. It consists of two coaxial cylinders. Inner cylinder is for holding mixture of vegetable oil and methanol and outer cylinder for cooling water circulation. The coupling is made by turning process on lath machine. After that the entire component (pressure gauge, valve, pump, tank and coupling) are assembled using 304 SS pipe of 1.5” and 1” diameter.

The cavitating conditions are generated just after the orifice plates and hence the intensity of the cavitating conditions strongly depends on the geometry of the orifice plate. The pressures in the main line before the orifice plate and after the orifice plate at vena contracta are measured with the help of pressure gauge p1 and p2. The holding tank is provided with a cooling jacket to control the temperature of the circulating liquid.

Figure 5.1(a): Hydrodynamic cavitation setup

Figure 5.1(b): Front view of the experimental set up

Figure 5.2: Schematic diagram of hydrodynamic cavitation machine

Figure 5.3: Nozzle spray gun

Figure 5.4: Schematic diagram of Cylindrical Pipe

Figure 5.5(a): Top view of Base supporting frame

Figure 5.5(b): Schematic diagram of Base supporting frame

5.2  Reagents and Materials used

1. Tumba originated from the Tumba seeds.

2. Methyl alcohol (CH3OH) (99% pure) for removing the free fatty acid from the oil.

3. Base catalyst (KOH or NaOH) (85% pure) for accelerating the reaction mixture.

5.3 Procedure

1. Tumba oil (2000g) is taken in a 2000 ml beaker and filtered it to remove impurities. Than it is heated through a heating device up to 110oC measured by an alcoholic column thermometer in order to remove water content of oil to avoid soap formation as shown figure 5.6(a). This oil is allowed to cool up to 50oC temperature so as to reaction can take place.

Figure 5.6(a): Heating of raw vegetable oil

Figure 5.6 (b): Methanol and KOH                 Figure 5.6 (c): Weighing machine

2. Now methyl alcohol (CH3OH) is taken with a molar ratio of (1:4.5 & 1:6) and catalyst (KOH) is     taken as 0.75% by weight of oil as shown in Figures 5.6(b) and 5.6(c). Then mixer of methyl alcohol and KOH is stirred until KOH dissolve in methyl alcohol.

3. This liquid mixture is mixed with vegetable oil. Initially the methanol is immiscible with the oil.

## 4. Open fully bypass valve (as shown in Figure 5.7) before starting.

## Figure 5.7: Throttle valve and plungers

## 5. Check out that all the line valves should be open and drain valve should be closed.

## 6. Pour the solution prepared in section 5.1.2 through inlet manifold as shown in Figure 5.8.

## Figure 5.8: Mixture inlet manifold

## 7. Switch on the plug for voltage supply.

## 8. Maintain the pressure upto 10 bar in the pressure gauge and flow rate 12 lpm (litre per

## minute) in the rotameter as shown in the Figure 5.9 and 5.10, respectively. Reciprocating pressure pump(Figure 5.11) is responsible to generate high pressure inside the chamber.

## Figure 5.9: Pressure gauge and spray gun                        Figure 5.10: Rotameter

## Figure 5.11: Reciprocating pressure pump

5.4 Experimental Data

Table 5.1: Yield observed at various reaction time for molar ratio of 6:1

| Tumba oil (kg) | Methanol Consumed (gm) | Catalyst consumed | Reaction time (in min) | Yield (%) |
| --- | --- | --- | --- | --- |
| 2 | 440 | 0.75 w/w% (i.e.15 gm) | 5 | 83 |
|  |  |  | 10 | 88.3 |
|  |  |  | 15 | 91.8 |
|  |  |  | 30 | 95.76 |
|  |  |  | 45 | 95.74 |
|  |  |  | 60 | 95.69 |
|  |  |  | 75 | 95.67 |
|  |  |  | 90 | 95.65 |
|  |  |  | 105 | 95.65 |
|  |  |  | 120 | 95.60 |

Table 5.2: Yield observed at various reaction time for molar ratio of 4.5:1

| Tumba oil (kg) | Methanol Consumed (gm) | Catalyst consumed | Reaction time (in min) | Yield (%) |
| --- | --- | --- | --- | --- |
| 2 | 331.2 | 0.75 w/w% (i.e.15 gm) | 5 | 76 |
|  |  |  | 10 | 80.4 |
|  |  |  | 15 | 86 |
|  |  |  | 30 | 92.36 |
|  |  |  | 45 | 92.33 |
|  |  |  | 60 | 92.18 |
|  |  |  | 75 | 92 |
|  |  |  | 90 | 91.98 |
|  |  |  | 105 | 91.97 |
|  |  |  | 120 | 91.97 |

Experimental datas obtained in Table 5.1 and 5.2 is presented in graphical form shown below:

Figure 5.12(a): Yield% Vs Reaction time (min) for 6:1 molar ratio

Figure 5.12(a) shows that the optimum yield obtained at 6:1 alcohol:oil ratio is 95.76% by using catalyst of 0.75% within the reaction time of 30 minutes where as 83% of yield is obtained in very little time of range within the reaction time of 5 minutes.

Figure 5.12(b): Yield% Vs Reaction time (min) for 4.5:1 molar ratio

Figure 5.12(b) shows that the optimum yield obtained at 4.5:1 alcohol:oil ratio is 92.36% by using catalyst of 0.75% within the reaction time of 30 minutes where as 76% of yield is obtained in very little time of range within the reaction time of 5 minutes.

5.5 Results and Discussion

(A) Comparison of molar ratio

Figure 5.13: Comparison of molar ratios of hydrodynamic cavitation method

In Figure 5.13, we can observe the variations in obtaining yield using same catalyst 0.75% for both 6:1 and 4.5:1 molar ratio. In both the conditions the optimum yield obtained at the reaction time of 30 minutes with the difference of 3.40%. At the reaction time of 5 minutes lowest yield is obtained for both the conditions with the yield difference of 7%. The highest yield productivity is obtained by using the molar ratio of 6:1.

(B) Comparison of hydrodynamic and ultrasonic cavitation method with respect to conventional mechanical stirring method

Figure 5.14(a): Comparison of methods for 0.75% catalyst by hydrodynamic, ultrasonic &

stirring method 6:1

At molar ratio 6:1 using catalyst of 0.75%, the optimum yields obtained through hydrodynamic(HC) and ultrasonic(US) cavitation method is compared with the conventional mechanical stirring(MS) method. The highest yield obtained in hydrodynamic and ultrasonic cavitation, and conventional mechanical stirring method for the same condition is 95.76% within 30 minutes, 94% within 40 minutes and 93.42% within 90 minutes, respectively. In HC the yield is higher than MS by 2.34% whereas in US, it is 0.58%. This data proves that hydrodynamic and ultrasonic cavitation methods are efficient than the conventional mechanical stirring method. Among all the methods hydrodynamic cavitation method is the most efficient, less time consuming and catalyst reducing method.

Figure 5.14(b): Comparison of methods for 0.75% catalyst by hydrodynamic, ultrasonic &

stirring method 4.5:1

At molar ratio 4.5:1 using catalyst of 0.75%, the optimum yields obtained through hydrodynamic(HC) and ultrasonic(US) cavitation method is compared with the conventional mechanical stirring(MS) method. The highest yield obtained in hydrodynamic and ultrasonic cavitation, and conventional mechanical stirring method for the same condition is 92.36% within 30 minutes, 92% within 40 minutes and 87.22% within 45 minutes, respectively. In HC the yield is higher than MS by 5.14% whereas in US, it is 4.78%. This data proves that hydrodynamic and ultrasonic cavitation methods are efficient than the conventional mechanical stirring method. Among all the methods hydrodynamic cavitation method is the most efficient, less time consuming and catalyst reducing method.

CHAPTER-6

PERFORMANCE AND EMISSION TESTING

This chapter contains the performance and emission testing of biodiesel extracted from Tumba (Citrullus Colcynthis) oil by applying various biodiesel production techniques, as discussed in the previous chapters 4 and 5. The chapter consist of engine details, procedure

followed by various performance and emission parameters.

6.1 Engine Test Setup

The engine test setup consists of one cylinder, four stroke, diesel engine connected to eddy current type dynamometer for loading, facilitated with water cooling jacket. It is provided with necessary instruments (Table 6.1) for combustion pressure and crank-angle measurements. These signals are interfaced to computer through engine indicator for P-θ and P-V diagrams. Provision is also made for interfacing airflow, fuel flow, temperatures and load measurement. The set up has stand-alone panel box consisting of air box, fuel tank, manometer, fuel measuring unit, transmitters for air and fuel flow measurements, load  and speed display. Rotameters are provided for cooling water and calorimeter for water flow measurement. Smoke meter is also attached with the engine set up to measure the smoke opacity of the engine on a particular fuel being used to run it.

The setup enables study of engine performance for brake power, indicated power, frictional power, brake mean effective pressure, indicated mean effective pressure, brake thermal efficiency, indicated thermal efficiency, mechanical efficiency and brake specific fuel consumption. Windows based Engine Performance Analysis software package “Engine soft” is provided for on line performance evaluation. The detailed specifications of various components are given in Table 6.1. The main aim of this experiment is to investigate the effects on performance of blending of biodiesel with gasoline diesel fuel in a Kirloskar diesel engine for wide range of operating parameters.

The photographs of specified engine set-up for performance and emission testing is shown in Figure 6.1and schematic diagram in Figure 6.1(c).

Figure 6.1(a): Actual experimental set-up of Kirloskar diesel engine

Figure 6.1(b): Rear view of the Kirloskar diesel engine

Figure 6.1(c): Schematic Diagram of the Experimental set-up

Table 6.1: Specifications of component used

| Component | Specifications |
| --- | --- |
| Product | Kirloskar engine test setup 1 cylinder, 4 stroke, Diesel (Computerized) |
| Product code | 234 |
| Engine | Make Kirloskar, Type 1 cylinder, 4 stroke Diesel, water cooled, power 3.5 kW at 1500 rpm, stroke 110 mm, bore 87.5 mm. 661 cc, CR 17.5 |
| Dynamometer | Type eddy current, water cooled, with loading unit |
| Propeller shaft | With universal joints |
| Air box | M S fabricated with orifice meter and manometer |
| Fuel tank | Capacity 15 L with glass fuel metering column |
| Calorimeter | Type Pipe in pipe |
| Piezo sensor | Range 5000 PSI, with low noise cable |
| Crank angle sensor | Resolution 1 Deg, Speed 5500 RPM with TDC pulse |
| Data acquisition device | NI USB-6210, 16-bit, 250kS/s |
| Piezo powering unit | Make-Cuadra, Model AX-409 |
| Digital milivolTOMEter | Range 0-200mV, panel mounted |
| Temperature sensor | Type RTD, PT100 and Thermocouple, Type K |
| Temperature transmitter | Type two wire, Input RTD PT100, Range 0–1000C, Output 4–20 mA and Type two wire, Input Thermocouple, Range 0–1200 0C, Output 4–20 mA |
| Load indicator | Digital, Range 0-50 Kg, Supply 230 VAC |
| Load sensor | Load cell, type strain gauge, range 0-50 Kg |
| Fuel flow transmitter | DP transmitter, Range 0-500 mm WC |
| Air flow transmitter | Pressure transmitter, Range (-) 250 mm WC |
| Software | “Enginesoft” Engine performance analysis software |
| Rotameter | Engine cooling 40-400 LPH; Calorimeter 25-250 LPH |
| Pump | Type Monoblock |
| Overall dimensions | W 2000 x D 2500 x H 1500 mm |
| Optional | Computerized Diesel injection pressure measurement |
| Shipping details | Gross volume 1.33m3, Gross weight 619kg, Net weight 543kg |
| Electric supply | Provide 230 +/- 10 VAC, 50 Hz, single phase electric supply with proper earthing. (Neutral – Earth voltage less than 5 VAC) 5A, three pin socket with switch (2 Nos.) |
| Water supply | Continuous, clean and soft water Supply @ 1000 LPH, at 10 m. head. Provide tap with 1” BSP size connection |
| Computer | IBM compatible with standard configuration (with free PCI slot on motherboard) |
| Space | 3300Lx3200Wx1700H in mm |
| Drain | Provide suitable drain arrangement (Drain pipe 65 NB/2.5” size) |
| Exhaust | Provide suitable exhaust arrangement (Exhaust pipe 32 NB/1.25” size) |
| Fuel, oil | Diesel@10 lit. Oil @ 3.5 lit. (20W40) |

Smokemeters

There are two basic types of smoke meters which are used to measure smoke density:

(i) Filter darkening type

(ii) Light extinction type

The light extinction type of meters can measure both white and black smoke whereas the filter paper darkening type meters can give only black smoke. The light extinction meter can be used for continuous measurements while the filter type can be used only under steady state conditions.

AVL smoker meter

AVL smoker meter works on the light extinction principle, shown in Figure 6.1(d). A continuously taken exhaust sample is passed through a tube of about 46 cm length which has a light source at one end and photocell or solar cell at the other end. The amount of light passed through this smoke column is used as an indication of smoke level. This smoke density is defined as the ratio of electric output from the photocell or solar cell when sample is passed through this smoke column to the electric output when clean air is passed through it. The fraction of the light transmitted through the smoke (T) and the length of the light path (L) are related by the Beer-Lambert law.

T = e –KL

K = n A θ

Where K is the optional absorption coefficient of the obscuring matter per unit length, n the number of soot particles per unit volume; ‘A’ is the average projected area for each particles; and ‘θ’ is the specific absorbance per particle.

Figure 6.1(d): AVL smoke meter

6.2  Preparation of biodiesel blends

Five different Tumba blends B20 (20 % biodiesel + 80 % diesel v/v), B40 (40 % biodiesel + 60 % diesel v/v), B60 (60 % biodiesel + 40 % diesel v/v), B80 (80 % biodiesel + 20 % diesel v/v) and B100 (100 % biodiesel + 0 % diesel v/v) were prepared. The total quantity of each Tumba blend is equal to one litre. These blends were prepared for Tumba biodiesel.

Calorific value of petroleum diesel [10] = 43000 kJ/kg.

Calorific value of biodiesel = 38550 kJ/kg.

Density of petroleum diesel = 821 kg/m3.

Density of biodiesel = 870 kg/m3 [tested in laboratory]

Calculation for the values of blends of Tumba biodiesel with diesel is given in Appendix III. The calorific value and densities of biodiesel blends have been calculated by volume fraction and are shown in Table 6.2.

Table 6.2: Description of different blends of biodiesel

| Type of blend | Amount of biodiesel (ml) | Amount of diesel (ml) | Resultant calorific value (kJ/kg) | Resultant density (kg/m3) |
| --- | --- | --- | --- | --- |
| Diesel | 0 | 1000 | 43000 | 821 |
| B-20 | 200 | 800 | 42067.78 | 830.8 |
| B-40 | 400 | 600 | 41157.74 | 840.6 |
| B-60 | 600 | 400 | 40268.46 | 850.4 |
| B-80 | 800 | 200 | 39399.42 | 860.2 |
| B-100 | 1000 | 0 | 38550 | 870 |

6.3 Performance Evaluation

A single cylinder diesel engine was used for the experimental analysis. Fuel was supplied to the engine from an outside tank. All runs started with a 5-min warm-up period prior to data collection. The gap of 3 to 4 minutes was provided between the two consecutive runs. The data measured during the tests included engine speed, brake power, torque, and fuel consumption. During the test engine load was varied from 0 to 12 kg by adjusting the load knob provided on the control panel of the test rig while maintaining a constant engine speed of about 1550 rpm. The tests were performed with pure diesel fuel and biodiesel blends (B20, B40, B60, B80, B100).

Formulation used for calculation of various parameters incorporated in software are described below:

Torque (Nm) = Load × Arm length

Brake power (kW) = (2 × π × Speed × Torque × 9.81) / (60 × 1000)

Brake Thermal Efficiency (%) =  Brake power (kW)    X    3600     X    100

Fuel flow(kg/h) X Calorific value(kJ/kg)

Specific fuel consumption (Kg/kWh) =    Fuel flow (kg/hr)

Brake power (kW)

Brake specific energy consumption (MJ/kWh)= BSFC (kg/kW-h) X Calorific value(kJ/kg)

1000

Percentage change (%) = Biodiesel – Diesel  X 100

Diesel

Mechanical Efficiency (%) = Brake power (kW) X 100

Indicated power (kW)

6.4 Performance data of load test

Experimental data from performance study is categorized on the basis of diesel and Tumba blends fuels are discussed below:

6.4.1 Pure diesel

Engine performance parameters obtained from performance testing in 4 cylinder CI engine against different speeds for pure diesel are given below in Table 6.3.

Table 6.3: Performance parameters for pure diesel V speed

| SPEED (rpm) | TORQUE (Nm) | BP (kw) | FP (kw) | IP (kw) | BThE (%) | IThE (%) | MechE (%) | SFC (kg/kwhr) | BSEC (MJ/kW-h) | Opacity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1596 | 0 | 0 | 1.92 | 1.92 | 0.10 | 42.35 | 0.23 | 5.10 | 219.3 | 8.2 |
| 1567 | 3.21 | 0.5 | 2.06 | 2.58 | 10.31 | 50.59 | 20.38 | 0.81 | 34.83 | 13.5 |
| 1558 | 6.25 | 1 | 1.84 | 2.86 | 15.84 | 44.38 | 35.69 | 0.53 | 22.79 | 19.2 |
| 1537 | 9.54 | 1.5 | 1.81 | 3.35 | 20.03 | 43.70 | 45.83 | 0.42 | 18.06 | 26.2 |
| 1530 | 12.38 | 2 | 1.68 | 3.66 | 23.44 | 43.25 | 54.21 | 0.36 | 16.48 | 31.1 |
| 1520 | 15.78 | 2.5 | 1.54 | 4.05 | 26.42 | 45.79 | 62.07 | 0.29 | 12.47 | 39.5 |
| 1509 | 18.71 | 3 | 1.44 | 4.40 | 27.84 | 41.46 | 67.14 | 0.30 | 12.90 | 54.6 |
| 1499 | 22.21 | 3.5 | 1.33 | 4.80 | 29.56 | 40.89 | 72.29 | 0.28 | 12.04 | 74.5 |

6.4.2 Biodiesel blends from Tumba Oil

Table 6.4 to 6.9 shows the observations for load test for B20, B40, B60, B80 and B100 blends of Tumba biodiesel. The speed is maintained almost constant during all the readings; it is varying in very narrow range of 1596 to 1499 rpm. The exhaust gas temperature is increasing from 150oC at minimum load to 220oC  at maximum load. As expected mass flow rate is also increasing with increase in load in case of all fuel blends. Water flow rate to engine and to calorimeter were maintained at almost constant value of 200 lph and 75 lph respectively. The performance parameters observed for various blends are as follows:

Table 6.4: Performance parameters for B20 V speed

| SPEED (rpm) | TORQUE (Nm) | BP (kW) | FP (kW) | IP (kW) | BThE (%) | IThE (%) | MechE (%) | SFC (kg/kWhr) | BSEC (MJ/kW-h) | Opacity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1575 | -0.02 | 0 | 2.67 | 2.66 | 0.15 | 52.60 | -0.13 | 4.95 | 208.24 | 9 |
| 1563 | 3.03 | 0.50 | 2.56 | 3.05 | 8.16 | 50.32 | 16.23 | 1.05 | 44.17 | 12.9 |
| 1548 | 6.26 | 1.00 | 2.50 | 3.52 | 14.25 | 49.38 | 28.85 | 0.60 | 25.24 | 16.7 |
| 1539 | 9.32 | 1.50 | 2.39 | 3.89 | 19.25 | 49.86 | 38.60 | 0.44 | 18.51 | 21.9 |
| 1523 | 12.55 | 2.00 | 2.33 | 4.33 | 22.24 | 48.16 | 46.19 | 0.38 | 15.99 | 27.6 |
| 1512 | 15.79 | 2.50 | 2.24 | 4.74 | 24.82 | 47.07 | 52.73 | 0.34 | 14.30 | 37.7 |
| 1504 | 19.04 | 3.00 | 2.08 | 5.08 | 26.44 | 44.80 | 59.01 | 0.32 | 13.46 | 42.3 |
| 1495 | 22.13 | 3.50 | 1.74 | 5.21 | 28.14 | 42.31 | 66.51 | 0.30 | 12.62 | 56.6 |

Table 6.5: Performance parameters for B40 V speed

| SPEED (rpm) | TORQUE (Nm) | BP (kW) | FP (kW) | IP (kW) | BThE (%) | IThE (%) | MechE (%) | SFC (kg/kWhr) | BSEC (MJ/kW-h) | Opacity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1587 | -0.02 | -0.00 | 2.39 | 2.39 | 0.02 | 51.63 | -0.11 | 4.87 | 200.44 | 9.5 |
| 1563 | 3.04 | 0.50 | 2.24 | 2.74 | 8.84 | 48.62 | 18.18 | 0.99 | 40.75 | 13.9 |
| 1552 | 6.08 | 0.99 | 2.09 | 3.08 | 15.19 | 47.37 | 32.06 | 0.58 | 23.87 | 15.7 |
| 1537 | 9.31 | 1.50 | 2.03 | 3.53 | 20.44 | 48.11 | 42.49 | 0.43 | 17.70 | 23.9 |
| 1523 | 12.39 | 1.98 | 2.00 | 3.97 | 22.83 | 45.93 | 49.71 | 0.38 | 15.64 | 28.6 |
| 1515 | 15.81 | 2.51 | 1.83 | 4.34 | 25.66 | 44.39 | 57.80 | 0.34 | 13.99 | 36.7 |
| 1503 | 18.90 | 2.97 | 1.65 | 4.62 | 27.22 | 42.27 | 64.39 | 0.32 | 13.17 | 44.3 |
| 1489 | 22.17 | 3.46 | 1.48 | 4.94 | 28.59 | 40.87 | 69.96 | 0.31 | 12.75 | 56.6 |

Table 6.6: Performance parameters for B60 V speed

| SPEED (rpm) | TORQUE (Nm) | BP (kW) | FP (kW) | IP (kW) | BThE (%) | IThE (%) | MechE (%) | SFC (kg/kWhr) | BSEC (MJ/kW-h) | Opacity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1576 | 0.01 | 0.00 | 2.00 | 2.01 | 0.03 | 44.23 | 0.07 | 4.32 | 173.96 | 8.9 |
| 1575 | 3.04 | 0.50 | 1.86 | 2.36 | 9.12 | 43.45 | 21.00 | 0.98 | 39.46 | 12.5 |
| 1557 | 6.25 | 1.01 | 1.78 | 2.79 | 15.72 | 43.42 | 36.21 | 0.57 | 22.95 | 15.7 |
| 1547 | 9.33 | 1.50 | 1.71 | 3.20 | 19.95 | 42.66 | 46.76 | 0.45 | 18.12 | 20.9 |
| 1534 | 12.38 | 1.97 | 1.61 | 3.58 | 23.12 | 42.00 | 55.04 | 0.39 | 15.70 | 27.2 |
| 1522 | 15.69 | 2.49 | 1.57 | 4.06 | 25.74 | 41.98 | 61.31 | 0.35 | 14.09 | 34.9 |
| 1505 | 19.17 | 3.02 | 1.48 | 4.50 | 27.69 | 41.24 | 67.15 | 0.32 | 12.89 | 40.9 |
| 1488 | 22.69 | 3.54 | 1.41 | 4.94 | 29.12 | 40.72 | 71.52 | 0.31 | 12.48 | 45.6 |

Table 6.7: Performance parameters for B80 V speed

| SPEED (rpm) | TORQUE (Nm) | BP (kW) | FP (kW) | IP (kW) | BThE (%) | IThE (%) | MechE (%) | SFC (kg/kWhr) | BSEC (MJ/kW-h) | Opacity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1563 | 0.01 | 0.00 | 1.95 | 1.95 | 0.04 | 44.06 | 0.10 | 4.28 | 168.63 | 9.8 |
| 1555 | 2.88 | 0.47 | 1.86 | 2.33 | 8.73 | 43.39 | 20.11 | 1.05 | 41.37 | 13.6 |
| 1544 | 6.23 | 1.01 | 1.82 | 2.83 | 15.64 | 43.90 | 35.62 | 0.58 | 22.85 | 16.5 |
| 1531 | 9.15 | 1.47 | 1.72 | 3.18 | 19.76 | 42.86 | 46.11 | 0.46 | 18.12 | 20.3 |
| 1521 | 12.93 | 2.06 | 1.64 | 3.70 | 23.66 | 42.50 | 55.68 | 0.39 | 15.36 | 29.4 |
| 1561 | 15.81 | 2.51 | 1.58 | 4.09 | 25.97 | 42.26 | 61.44 | 0.35 | 13.79 | 38.7 |
| 1507 | 19.07 | 3.01 | 1.48 | 4.49 | 27.74 | 41.36 | 67.08 | 0.33 | 13.00 | 43.3 |
| 1491 | 22.32 | 3.48 | 1.49 | 4.98 | 29.01 | 41.43 | 70.02 | 0.31 | 12.21 | 55.2 |

Table 6.8: Performance parameters for B100 V speed

| SPEED (rpm) | TORQUE (Nm) | BP (kW) | FP (kW) | IP (kW) | BThE (%) | IThE (%) | MechE (%) | SFC (kg/kWhr) | BSEC (MJ/kW-h) | Opacity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1567 | 0.01 | 0.00 | 2.01 | 2.01 | 0.05 | 45.17 | 0.11 | 4.20 | 161.91 | 10.5 |
| 1555 | 3.24 | 0.53 | 1.84 | 2.37 | 9.57 | 42.94 | 22.29 | 0.98 | 37.78 | 13.2 |
| 1547 | 5.97 | 0.97 | 1.72 | 2.69 | 15.32 | 42.63 | 35.95 | 0.61 | 23.52 | 14.7 |
| 1528 | 9.52 | 1.52 | 1.69 | 3.22 | 20.11 | 42.47 | 47.35 | 0.46 | 17.73 | 22.7 |
| 1524 | 12.58 | 2.01 | 1.66 | 3.67 | 23.34 | 42.69 | 54.67 | 0.40 | 15.42 | 29.6 |
| 1514 | 15.63 | 2.48 | 1.62 | 4.09 | 25.56 | 42.23 | 60.52 | 0.37 | 14.26 | 35.8 |
| 1506 | 19.24 | 3.03 | 1.56 | 4.59 | 27.84 | 42.13 | 66.07 | 0.34 | 13.12 | 49.5 |
| 1488 | 22.34 | 3.48 | 1.50 | 4.98 | 28.92 | 41.34 | 69.95 | 0.32 | 12.34 | 66.6 |

Table 6.9: Observation data of exhaust temperature (Ex. Temp.) and air/fuel (A/F) ratio

| LOAD | DIESEL | B20 | B40 | B60 | B80 | B100 |
| --- | --- | --- | --- | --- | --- | --- |
|  | Ex.Te-mp. (oC) | A/F ratio | Ex.Te-mp. (oC) | A/F ratio | Ex.Te-mp. (oC) | A/F ratio | Ex.Te-mp. (oC) | A/F ratio | Ex.Te-mp. (oC) | A/F ratio | Ex.Te-mp. (oC) | A/F ratio |
| 0 | 158.12 | 81.16 | 162.23 | 68.02 | 157.98 | 74.28 | 164.02 | 76.53 | 164.03 | 72.81 | 155.06 | 70.71 |
| 0.5 | 184.49 | 68.32 | 183.21 | 54.28 | 180.02 | 61.72 | 178.76 | 62.51 | 175.76 | 58.05 | 172.68 | 54.36 |
| 1 | 203.24 | 55.33 | 209.94 | 47.36 | 203.13 | 49.13 | 200.16 | 50.17 | 198.85 | 49.64 | 192.08 | 48.05 |
| 1.5 | 231.85 | 46.78 | 231.96 | 44.84 | 228.94 | 45.95 | 224.32 | 41.98 | 222.55 | 41.58 | 222.56 | 40.16 |
| 2 | 252.70 | 40.68 | 259.06 | 36.75 | 254.89 | 36.21 | 246.49 | 36.79 | 254.12 | 35.79 | 249.33 | 36.13 |
| 2.5 | 281.10 | 39.51 | 288.48 | 31.52 | 283.43 | 33.40 | 279.26 | 31.26 | 278.02 | 32.07 | 277.02 | 30.87 |
| 3 | 306.63 | 30.43 | 321.51 | 27.42 | 314.08 | 30.19 | 309.30 | 27.35 | 306.01 | 28.43 | 309.49 | 27.06 |
| 3.5 | 339.43 | 28.44 | 351.53 | 25.16 | 344.94 | 25.51 | 339.07 | 24.47 | 336.18 | 25.29 | 338.48 | 23.19 |

6.5 Results and Discussion

The data from Table 6.3 to 6.9 are used to plot graphs for various performance parameters to understand the performance characteristics of Tumba biodiesel blends are discussed below:

6.5.1 Brake thermal efficiency (BThE) V Brake Power

Brake thermal efficiency of the blends fuel such as B20, B40, B60, B80 and B100 observed at various brake power with respect to diesel are shown from the Figures 6.2(a) to 6.2(e).

Figure 6.2(a): BThE (%) V brake power for B20                 Figure 6.2(b): BThE (%) V brake power for B40

Figure 6.2(c): BThE (%) V brake power for B60               Figure 6.2(d): BThE (%) V brake power for B80

Figure 6.2(e): BThE (%) V brake power for B100

Figure 6.3: Comparison of BThE(%) V brake power for B20, B40, B60, B80, B100 from

diesel

Figure 6.4: Percentage Change of various Tumba biodiesel blends BThE V brake power

B20, B40, B80 and B100 blends of Tumba biodiesel shows that the maximum brake thermal efficiency achieved is 28.14%, 28.59%, 29.12%, 29.01% and 28.92%, respectively which are slightly lower than the pure diesel’s maximum value 29.56%. The BThE increases proportionally with increase in brake power. Above Figure 6.3 also shows that the curves obtained by B20, B40, B60, B80 and B100 are very similar to the pure diesel performed on the same engine.

The percentage change of biodiesel blends with respect to diesel using BThE parameter is calculated shown in the Table 6.10. Figure 6.4 shows the percentage change of biodiesel  for  BThE at various loads.

Table 6.10: Percentage change of biodiesel with respect to diesel using BThE parameter

| BRAKE POWER (kW) | B20 | B40 | B60 | B80 | B100 |
| --- | --- | --- | --- | --- | --- |
| IDLING | 50 | -80 | -70 | -60 | -50 |
| 0.5 | -20.8535 | -14.258 | -11.5422 | -15.3249 | -7.1775 |
| 1 | -10.0379 | -4.10354 | -0.75758 | -1.26263 | -3.28283 |
| 1.5 | -3.89416 | 2.04693 | -0.3994 | -1.34798 | 0.399401 |
| 2 | -5.11945 | -2.60239 | -1.36519 | 0.938567 | -0.42662 |
| 2.5 | -6.05602 | -2.87661 | -2.57381 | -1.70326 | -3.25511 |
| 3 | -5.02874 | -2.22701 | -0.53879 | -0.3592 | 0 |
| 3.5 | -4.80379 | -3.28146 | -1.4885 | -1.86062 | -2.16509 |

For the loads ranging 1kW to 3.5 kW, percentage change of biodiesel blends for brake thermal efficiency is +5% where as for 0.5 kW its +5 to 21% the variation may be explained by the higher density, higher viscosity and better combustion. In the test operations the performance of the blends can attributed to the promoted combustion due to the oxygen content present in  blends. Since the engine is operated under constant injection advance and TOME has a smaller ignition delay, combustion is initiated much before TDC is reached. This increases compression work and more heat loss and thus reduces the brake thermal efficiency of the engine. This can also be explained by the fact that maximum efficiency is obtained when most of the heat is released close to TDC. The start of heat release much before TDC for TOME and its blends results in larger deviation from the ideal cycle and hence lower thermal efficiency is recorded. Also it is noticed from the Figure 6.8, that the decrease in BThE is not proportional to the increase in % TOME in the fuel. This variation is due to better lubricating properties of TOME as compared to diesel.

6.5.2 Brake specific fuel consumption (BSFC) V Brake Power

Specific fuel consumption of the blends fuel such as B20, B40, B60, B80 and B100 observed at various brake power in compared to diesel are shown from the Figures 6.2(a) to 6.2(e).

Figure 6.5(a):  BSFC V Brake power for B20                            Figure 6.5(b): BSFC V Brake power for B40

Figure 6.5(c): BSFC V Brake power for B60                        Figure 6.5(d): BSFC V Brake power for B80

Figure 6.5(e): BSFC V Brake power for B100

Figure 6.6: Comparison of BSFC V Brake power for B 20, B 40, B 60, B 80, B100 from

diesel

Figure 6.7: Percentage change of biodiesel V brake power for BSFC

The brake specific fuel consumption for B20, B40, B80 and B100 blends of Tumba biodiesel at maximum brake power 3.5 kW is 0.30, 0.31, 0.31, 0.31 and 0.32 in kg/kW-h, respectively which are slightly higher than the pure diesel’s value 0.28 kg/kW-h. As Figure 6.6 shows that as BSFC decreases sharply upto 0.5kW and with further decrease in brake power, slightly reduces the BSFC value. Above Figure 6.6 also shows that the curves obtained by B20, B40, B60, B80 and B100 are very similar to the pure diesel performed on the same engine.

The percentage change of biodiesel with respect to diesel using BSFC parameter is calculated shown in the Table 6.11. Figure 6.7 shows the percentage difference of biodiesel  for BSFC at various loads.

Table 6.11: Percentage change of biodiesel with respect to diesel using SFC parameter

| Brake power (kW) | B 20 | B 40 | B 60 | B 80 | B 100 |
| --- | --- | --- | --- | --- | --- |
| IDLING | -2.94118 | -4.5098 | -15.2941 | -16.0784 | -17.6471 |
| 0.5 | 29.62963 | 22.22222 | 20.98765 | 29.62963 | 20.98765 |
| 1 | 13.20755 | 9.433962 | 7.54717 | 9.433962 | 15.09434 |
| 1.5 | 4.761905 | 2.380952 | 7.142857 | 9.52381 | 9.52381 |
| 2 | 5.555556 | 5.555556 | 8.333333 | 8.333333 | 11.11111 |
| 2.5 | 17.24138 | 17.24138 | 20.68966 | 20.68966 | 27.58621 |
| 3 | 6.666667 | 6.666667 | 6.666667 | 10 | 13.33333 |
| 3.5 | 7.142857 | 10.71429 | 10.71429 | 10.71429 | 14.28571 |

Among the fuels tested the lowest BSFC values are obtain with diesel fuel due to low fuel consumption rate and high brake power.  There are significant increases in BSFC when the engine is fuelled with blends because of higher fuel consumption rates and reductions in brake power. TOME has lower calorific value than that of diesel. Hence the BSFC is slightly higher than that of diesel for TOME  blends.

6.5.3 Brake Specific Energy Consumption (BSEC) V Brake Power

Brake specific energy consumption of the blends fuel such as B20, B40, B60, B80 and B100 observed at various brake power in compared to diesel are shown from the Figures 6.8(a) to 6.8(e).

Figure 6.8(a): BSEC V Brake power for B20                      Figure 6.8(b): BSEC V Brake power for B40

Figure 6.8(c): BSEC V Brake power for B60                          Figure 6.8(d): BSEC V Brake power for B80

Figure 6.8(e): BSEC V Brake power for B100

Figure 6.9: Comparison of BSEC V Brake power for B 20, B 40, B 60, B 80, B100 from

diesel

Figure 6.10: Percentage change of biodiesel V brake power for BSEC

The  brake specific energy consumption for B20, B40, B80 and B100 blends of Tumba biodiesel at maximum brake power 3.5kW is 12.62, 12.75, 12.48, 12.21 and 12.34 in MJ/kW-h, respectively which are slightly higher than the pure diesel value of 12.04 kg/kW-h. Figure 6.6 also shows that the curves obtained by B20, B40, B60, B80 and B100 are very similar to the pure diesel performed on the same engine.

The percentage change of biodiesel with respect to diesel using BSEC parameter is calculated shown in the Table 6.12. Figure 6.10 shows the percentage change of biodiesel for BSEC at various loads.

Table 6.12: Percentage change of biodiesel with respect to diesel using BSEC parameter

| Brake Power (kW) | B20 | B40 | B60 | B80 | B100 |
| --- | --- | --- | --- | --- | --- |
| IDLING | -5.04332 | -8.60009 | -20.6749 | -23.1053 | -26.1696 |
| 0.5 | 26.81596 | 16.99684 | 13.29314 | 18.77692 | 8.46971 |
| 1 | 10.75033 | 4.738921 | 0.702062 | 0.263273 | 3.203159 |
| 1.5 | 2.491694 | -1.99336 | 0.332226 | 0.332226 | -1.82724 |
| 2 | -2.9733 | -5.09709 | -4.73301 | -6.79612 | -6.43204 |
| 2.5 | 14.67522 | 12.18925 | 12.99118 | 10.5854 | 14.35445 |
| 3 | 4.341085 | 2.093023 | -0.07752 | 0.775194 | 1.705426 |
| 3.5 | 4.817276 | 5.89701 | 3.654485 | 1.41196 | 2.491694 |

6.5.4 Air/Fuel Ratio (A/F Ratio)

Air/Fuel ratio of the blends fuel such as B20, B40, B60, B80 and B100 observed at various brake power compared to diesel are shown from the Figures 6.11(a) to 6.11(e). The A/F Ratio for B20, B40, B80 and B100 blends of Tumba biodiesel at maximum brake power 3.5 kW achieved is 25.16, 25.51, 24.47, 25.29 and 23.19, respectively which are slightly lower than the pure diesel’s maximum value 28.44. From Figure 6.12 shows that as the brake power increases the A/F Ratio decreases. Above Figure 6.12 also shows that the trends obtained for B20, B40, B60, B80 and B100 are similar to the pure diesel performed on the same engine, but with a lower magnitude of a given power output.

Figure 6.11(a): A/F Ratio V brake power for B 20           Figure 6.11(b): A/F Ratio V brake power for B 40

Figure 6.11(c): A/F Ratio V Brake power for B 60            Figure 6.11(d): A/F Ratio V Brake power for B 80

Figure 6.11(d): A/F Ratio V Brake power for B 100

Figure 6.12: Comparison of Air/Fuel Ratio V Brake power for B20, B40, B60, B80, B100

from diesel

Figure 6.13: Percentage change of biodiesel V brake power for A/F Ratio

The percentage change of biodiesel with respect to diesel using BSEC parameter is calculated shown in the Table 6.13. Figure 6.13 shows the percentage change of Tumba biodiesel for BSEC at various loads. The maximum reduction in A/F ratio is assumed -20%.

Table 6.13: Percentage change of biodiesel with respect to diesel using A/F Ratio parameter

| Brake Power (kW) | B20 | B40 | B60 | B80 | B100 |
| --- | --- | --- | --- | --- | --- |
| IDLING | -16.1902 | -8.47708 | -5.70478 | -10.2883 | -12.8758 |
| 0.5 | -20.5504 | -9.66042 | -8.5041 | -15.0322 | -20.4333 |
| 1 | -14.4045 | -11.2055 | -9.32586 | -10.2838 | -13.1574 |
| 1.5 | -4.14707 | -1.77426 | -10.2608 | -11.1159 | -14.1513 |
| 2 | -9.66077 | -10.9882 | -9.56244 | -12.0206 | -11.1849 |
| 2.5 | -20.2227 | -15.4644 | -20.8808 | -18.8307 | -21.8679 |
| 3 | -9.89155 | -0.7887 | -10.1216 | -6.57246 | -11.0746 |
| 3.5 | -11.5331 | -10.3024 | -13.9592 | -11.0759 | -18.4599 |

6.5.5 Exhaust Temperature (Ex. Temp.) V Brake Power

Exhaust Temperature of the blends fuel such as B20, B40, B60, B80 and B100 observed at various brake power compared to diesel are shown from the Figures 6.14(a) to 6.14(e). The Ex. Temp.  for B20, B40, B80 and B100 blends of Tumba biodiesel at maximum brake power 3.5 kW achieved is 351.53, 344.94, 339.07, 336.18 and 338.48oC, respectively which are slightly higher than the pure diesel’s value 339.43oC. Figure 6.12 shows that as the brake power increases the Ex. Temp. decreases. Figure 6.12 also shows that the curves obtained by B20, B40, B60, B80 and B100 are very similar to the pure diesel performed on the same engine.

The percentage change of biodiesel with respect to diesel using Ex. Temp. parameter is calculated shown in the Table 6.14. Figure 6.16 shows the percentage difference of biodiesel  for Ex. Temp. at various loads. The maximum variation in Ext. Temp. is +6% for entire range of brake power.

Figure 6.14(a): Ex. Temp. V Brake Power for B20         Figure 6.14(b): Ex. Temp. V Brake Power for B40

Figure 6.14(c): Ex. Temp.V Brake Power for B60             Figure 6.14(d): Ex. Temp.  V Brake Power for B80

Figure 6.14(e): Ex. Temp.  V Brake Power for B100

Figure 6.15: Comparison of Ex. Temp.  V Brake Power for B20, B 40, B 60, B 80, B100

from  diesel

Figure 6.16: Percentage change of biodiesel for Ex. Temp. V brake power

Table 6.14: Percentage change of biodiesel with respect to diesel using Ex. Temp. parameter

| Brake Power (kW) | B20 | B40 | B60 | B80 | B100 |
| --- | --- | --- | --- | --- | --- |
| IDLING | 2.599292 | -0.08854 | 3.731343 | 3.733668 | -1.93524 |
| 0.5 | -0.6938 | -2.4229 | -3.10586 | -4.73196 | -6.40143 |
| 1 | 3.296595 | -0.05412 | -1.51545 | -2.16001 | -5.49105 |
| 1.5 | 0.047444 | -1.25512 | -3.24779 | -4.01121 | -4.0069 |
| 2 | 2.516818 | 0.86664 | -2.45749 | 0.561931 | -1.3336 |
| 2.5 | 2.6254 | 0.828887 | -0.65457 | -1.0957 | -1.45144 |
| 3 | 4.852754 | 2.429638 | 0.870756 | -0.2022 | 0.93272 |
| 3.5 | 3.5648 | 1.62331 | -0.10606 | -0.95749 | -0.27988 |

At various load there is sudden drop occurs more than 5% of Tumba biodiesel blends because as the performance must be attributed to the higher exhaust temperature which increases losses  and also low cylinder liner temperature which increases the emissions due to incomplete combustion. The exhaust gas temperatures with the blends are usually lower than that of diesel fuel. This may be attributed to the lower energy content of the blends as a result of the oxygen content and their lower cetane number. Having oxygen and a lower energy content, oxygenated fuels usually cause lower combustion temperature. The highest decrease in the Ex. Temp.  was observed with the blends of B20 which has lowest energy content among the fuels tested. It is observed that the exhaust gas temperature increases with load because more fuel is burnt at higher loads to meet the power requirement. It is also observed that the exhaust gas temperature increases with percentage of TOME in the test fuel for all the loads. This may be due to the oxygen content of the TOME, which improves combustion and thus may increase the exhaust gas temperature.

6.5.6 Smoke Opacity V Brake Power

Smoke opacity of the blends fuel such as B20, B40, B60, B80 and B100 observed at various brake power with respect to diesel are shown from the Figures 6.21(a) to 6.21(e).       The smoke opacity for B20, B40, B80 and B100 blends of Tumba biodiesel at maximum brake power 3.5 kW achieved is 26, 27.5, 25.57, 29 and 30, respectively which are slightly lower than the pure diesel’s value 27.5. From Figure 6.22 shows that as the brake power increases the smoke opacity have fluctuating curve for B20 and B40 but optimum smoke opacity is obtained for B60, and then sudden rise in the curve is observed for B80 and B100. Above Figure 6.22 also shows that the curves obtained by B20, B40, B60, B80 and B100 are similar to the pure diesel performed on the same engine.

Figure 6.21(a): Smoke Opacity V BP for B20                     Figure 6.21(b): Smoke Opacity V BP for B40

Figure 6.21(c): Smoke Opacity V BP for B60                       Figure 6.21(d): Smoke Opacity V BP for B80

Figure 6.21(e): Smoke Opacity V Brake power for B100

Figure 6.22: Comparison of Smoke Opacity V Brake power for B20, B40, B60, B100 from

diesel

Figure 6.23: Percentage change V brake power for smoke opacity

The percentage change of biodiesel with respect to diesel using smoke opacity parameter is calculated shown in the Table 6.16. Figure 6.23 shows the percentage change of biodiesel for smoke opacity at various loads.

Table 6.16: Percentage change of biodiesel from diesel in terms of smoke opacity

| Brake Power(kW) | B20 | B40 | B60 | B80 | B100 |
| --- | --- | --- | --- | --- | --- |
| IDLING | -16.6667 | -16.6667 | -25 | 0 | 16.66667 |
| 0.5 | -17.1429 | -28.5714 | -28.5714 | -2.85714 | 8.571429 |
| 1 | -6.09756 | -2.43902 | -3.65854 | -2.43902 | -2.43902 |
| 1.5 | -2.11268 | -0.70423 | -2.8169 | -0.70423 | 1.408451 |
| 2 | -3.31126 | 0.662252 | -2.64901 | -0.66225 | 2.649007 |
| 2.5 | -4.57143 | -6.28571 | -6.28571 | 1.714286 | 2.857143 |
| 3 | -5.75221 | -0.44248 | -13.7168 | 8.40708 | 9.734513 |
| 3.5 | -5.45455 | -0.36364 | -7.27273 | 5.454545 | 9.090909 |

Smoke emissions usually increase very slowly at low engine speeds, while they favourably decrease at medium and high speeds as compared to diesel fuel. B60 yield the highest engine power and BThE values among the blends tested. The decreasing cetane number of the blends deteriorates the combustion process. Aditionally, the oxygen content of the blends enhanced the fuel air mixing process especially in the fuel rich region of the cylinder by providing more oxygen, and mixing Tumba biodiesel with diesel fuel causes a leaning effect of the blends due to lower stochiometric air/fuel ratio of the Tumba biodiesel, thus lowering the smoke opacity. Increase in oxygen content in the Tumba methyl esters (TOME)-diesel blends as compared to diesel results in better combustion and increase in the combustion chamber temperature.

    - Pressure V Crank Angle (Ѳ)

(A)The P-Ѳ curves of blends of Tumba biodiesel a with reference to the diesel at idle load are discussed below on the basis of the data Table 1 of Appendix II.

P-Ѳ diagram of B20, B40, B60, B80 and B100 blends of Tumba biodiesel is shown from Figure 6.17(a) to 6.18. Figure 6.18 shows that P-Ѳ curve of Tumba biodiesel blends are almost resembles to the P-Ѳ curve of pure diesel. At various crank angle pressure observed for B20, B40, B60, B80, B100 and diesel are 51.5136 at 367o, 51.9112 at 366o, 52.9227 at 365o, 52.1492 at 365o, 53.104 at 364o ,  54.3653 at 367o. As the pressure increases maximum Ѳ value 367o is observed and after this point pressure starts declining and at 450o but at the end of 720o it decreases in fraction that is almost constant for idle load. TOME  blends follow the similar pattern of pressure rise to that of diesel at all load conditions. Table 1 in Appendix-II  indicates that, when compared to diesel oil, the values of pressure data of 20% TOME and 40%TOME are lower while for 60%TOME, 80%TOME and 100%TOME are higher. These distinct differences may be due to variations of viscosity and heating value with percentage of TOME in the fuel.

Figure 6.17(a): Pressure V Ѳ for B20 at idle load         Figure 6.17(b): Pressure V Ѳ for B40 at idle load

Figure 6.17(c): Pressure V Ѳ for B60 at idle load              Figure 6.17(d): Pressure V Ѳ for B80 at idle load

Figure 6.17(e): Pressure V Ѳ for B100 at idle load

Figure 6.18: Comparison of pressure V Ѳ for B20, B40, B60, B100 from diesel at idle load

(B) The P-Ѳ curves of blends of Tumba biodiesel a with reference to the diesel at 3.5kW (maximum) load are discussed below on the basis of the data Table 2 of Appendix II.

Figure 19(a): Pressure V Ѳ for B20 at 3.5kW                   Figure 19(b): Pressure V Ѳ for B40 at 3.5kW

Figure 19(c): Pressure V Ѳ for B60 at 3.5kW                      Figure 19(d): Pressure V Ѳ for B80 at 3.5kW

Figure 19(e): Pressure V Ѳ for B100 at 3.5kW

Figure 6.20: Comparison of pressure V Ѳ for B20, B40, B60, B100 from diesel at 3.5kW

P-Ѳ diagram of B20, B40, B60, B80 and B100 blends of Tumba biodiesel is shown from Figure 6.19(e) to 6.20. Figure 6.18 shows that P-Ѳ curve of Tumba biodiesel blends are almost resembles to the P-Ѳ curve of pure diesel. At various crank angle pressure observed for B20, B40, B60, B80, B100 and diesel. As the pressure increases maximum Ѳ value 369o at 66.259273 bar is observed and after this point though the Ѳ increases but the pressure starts declining but at the end of 720o it decreases in fraction that is almost constant for 3.5kW load.

It can be seen that the peak pressure is slightly higher for TOME and its blends when compared to that of diesel. This is due to the lower ignition delay of TOME and its blends. The oxygen content of TOME, which results in better combustion, may also result in higher peak pressure compared to diesel. The maximum Rate of Pressure Rise occurs within this period for all fuel blends. It can be observed that the rate of pressure rise for diesel is higher compared to those of TOME and its blends. This is due to the longer ignition delay and shorter combustion duration of diesel compared to TOME and its blends.

\

CHAPTER-7

CONCLUSION & FUTURE SCOPE

7.1 Conclusion

(A)  Biodiesel Production Techniques:

Following  conclusion has been made from the experiments:

1. The least reaction time required for methyl ester formation through hydrodynamic cavitation method is 5 minutes which is much shorter as compare to conventional mechanical stirring method.

2. Slightly more yield is obtained by US technique as compare to MS method of biodiesel production.

3. Yield obtained in HC technique is 1.76% and 2.34%, which are higher as compare to US and MS methods, repectively.

4. The experimental results shows that by taking catalyst 0.5%, 0.75% and 1% of oil through the US and HC is 0.75% catalyst is optimum catalyst to be used because catalyst is an impurity and its use should be low as much as possible.

5. Higher biodiesel productivity is obtained using molar ratio 6:1 in biodiesel production techniques (HC, US & MS)  as compare to molar ratio 4.5:1.

6.  Both HC and US methods are industrially viable at large scale.

(B) Performance and Engine Testing:

From the engine performance testing it can be concluded that the performance parameter and emission characteristics for Tumba (Citrullus Colocynthis) biodiesel have better results than the diesel oil are:

1. The BThE increases proportionally with increase in brake power. The decrease in BThE

is not proportional to the increase in % TOME in the fuel. This variation is due to better

lubricating properties of TOME as compared to diesel.

2. BSFC decreases sharply upto 0.5kW and with further decrease in brake power, slightly   reduces the BSFC value. The BSFC is slightly higher than that of diesel for TOME  blends.   3. The BSEC curves obtained by B20, B40, B60, B80 and B100 are very similar to the pure diesel performed on the same engine.

4. As the brake power increases the A/F Ratio of Tumba blends decreases.

5. The exhaust emissions from  Tumba biodiesel are lower than with regular diesel fuel.

6. The smoke opacity for B20, B40, B80 and B100 blends of Tumba biodiesel at maximum brake power 3.5 kW achieved is 26, 27.5, 25.57, 29 and 30, respectively which are slightly lower than the pure diesel’s value 27.5. So Tumba biodiesel is an industrially viable substitute for petrol-diesel engine.

7. The peak pressure is slightly higher for TOME and its blends when compared to that of diesel.

7.2 Recommendation for future work

There are certain reasons for encouraging the development of biodiesel are:

1. For long term use of biodiesel in an engine, high maintenance required is need to be investigate.

2. Viscosity for biodiesel is an issue, while using in a diesel based engine and can be reduced by increasing the injector pressure.

3. Further research in dynamic response of fuel is required. As the biodiesel fuel has excellent lubricating property, so either some modification is required in the fuel injector of the engine or some additive should be search to make it easily viable for a diesel based engine.

APPENDIX-I

1. Weighing Uncertainity

(a) Fixed error

Maximum capacity of weighing machine = 600g

Minimum measurement = 0.2g

Divisioning = 0.01g

Least count of weighing machine = 0.01g

Observed weight (Wo) = (wt. of non edible oil + wt. of methanol + wt. of catalyst [KOH])

= (50 + 11 + 1) g

= 62g

(b) Confidence limit

Probable measurement error (Pe) =   + (0.01/2) g = + 0.005g

Probable value of a single measurement = (62 + 0.005)g

(c) Propagation of uncertainty

Relative uncertainty in weighing (Ur) = +   (Pe / Wo)

= + (0.005/ 62)

= + 8.0645 X 10-5

Ur   in terms of percentage = + Ur X 100

= + (8.0645/100000) X 100

= + 0.0081%

2. Thermometer  Uncertainity

(a) Fixed error

Maximum observed temperature of alcohol column (Wo) = 110oC

Least count of the scale  = 1oC

(b) Confidence limit

Probable measurement error (Pe) =   + (1/2)oC = + 0.5oC

Probable value of a single measurement = (110 + 0.5)oC

(c) Propagation of uncertainty

Relative uncertainty in temperature (Ur) = + (Pe / Wo )

= + (0.5/ 110)

= + 4.5 X 10-3

Ur   in terms of percentage = + Ur X 100

= + (4.5 X 10-3) X 100

= + 0.45%

3. Yield percentage

Molar ratio = 6:1

Reaction time = 40 min.

Quantity of non-edible oil (Q) = 50g

Quantity of methanol (CH3OH) = 11g

Catalyst (KOH) used = 0.75 wt%/wt.

= (75/100) X 50g

= 0.375g

Biodiesel obtained (B) = 46.5g

Yield percentage of one sample = (B/Q) X 100

= (46.5/50) X 100

= 93.00%

APPENDIX II

Table 1: Data of pressure and crank angle for 0 load

| Ѳ | Diesel | B 20 | B 40 | B 60 | B 80 | B 100 |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 1.59655 | -1.59658 | 0.59655 | 0.60791 | 0.676072 | 0.437505 |
| 1 | 1.539748 | -1.69882 | 0.528388 | 0.630631 | 0.460225 | 0.335262 |
| 2 | 1.482946 | -1.74426 | 0.562469 | 0.539748 | 0.551108 | 0.403424 |
| 3 | 1.448865 | -1.7329 | 0.528388 | 0.59655 | 0.482946 | 0.437505 |
| 4 | 1.517027 | -1.7329 | 0.471586 | 0.551108 | 0.437505 | 0.392063 |
| 5 | 1.426144 | -1.71018 | 0.494306 | 0.562469 | 0.471586 | 0.380703 |
| 6 | 1.448865 | -1.76698 | 0.471586 | 0.60791 | 0.460225 | 0.357982 |
| 7 | 1.448865 | -1.68746 | 0.414784 | 0.517027 | 0.403424 | 0.346622 |
| 8 | 1.403424 | -1.76698 | 0.437505 | 0.528388 | 0.437505 | 0.301181 |
| 9 | 1.403424 | -1.80106 | 0.392063 | 0.505667 | 0.482946 | 0.28982 |
| 10 | 1.414784 | -1.76698 | 0.380703 | 0.448865 | 0.426144 | 0.312541 |
| 11 | 1.335262 | -1.81242 | 0.392063 | 0.482946 | 0.448865 | 0.301181 |
| 12 | 1.312541 | -1.72154 | 0.369343 | 0.471586 | 0.414784 | 0.2671 |
| 13 | 1.301181 | -1.8465 | 0.346622 | 0.460225 | 0.357982 | 0.221658 |
| 14 | 1.323901 | -1.80106 | 0.357982 | 0.403424 | 0.392063 | 0.255739 |
| 15 | 1.244379 | -1.86922 | 0.346622 | 0.403424 | 0.323901 | 0.28982 |
| 16 | 1.244379 | -1.81242 | 0.255739 | 0.471586 | 0.392063 | 0.255739 |
| 17 | 1.28982 | -1.86922 | 0.301181 | 0.403424 | 0.346622 | 0.357982 |
| 18 | 1.153496 | -1.80106 | 0.312541 | 0.392063 | 0.301181 | 0.2671 |
| 19 | 1.221658 | -1.88059 | 0.27846 | 0.448865 | 0.312541 | 0.2671 |
| 20 | 1.164857 | -1.86922 | 0.2671 | 0.346622 | 0.301181 | 0.323901 |
| 21 | 1.130776 | -1.82378 | 0.255739 | 0.335262 | 0.335262 | 0.346622 |
| 22 | 1.210298 | -1.88059 | 0.28982 | 0.369343 | 0.301181 | 0.335262 |
| 23 | 1.119415 | -1.85786 | 0.27846 | 0.414784 | 0.323901 | 0.301181 |
| 24 | 1.187577 | -1.86922 | 0.244379 | 0.392063 | 0.198938 | 0.346622 |
| 25 | 1.073974 | -1.81242 | 0.27846 | 0.335262 | 0.210298 | 0.312541 |
| 26 | 1.164857 | -1.8465 | 0.255739 | 0.301181 | 0.301181 | 0.323901 |
| 27 | 1.108055 | -1.81242 | 0.244379 | 0.357982 | 0.27846 | 0.323901 |
| 28 | 1.164857 | -1.81242 | 0.28982 | 0.426144 | 0.2671 | 0.323901 |
| 29 | 1.142136 | -1.7897 | 0.335262 | 0.357982 | 0.255739 | 0.323901 |
| 30 | 1.198938 | -1.88059 | 0.27846 | 0.346622 | 0.096695 | 0.301181 |
| 31 | 1.153496 | -1.7897 | 0.255739 | 0.369343 | 0.176217 | 0.369343 |
| 32 | 1.198938 | -1.85786 | 0.28982 | 0.403424 | 0.198938 | 0.312541 |
| 33 | 1.153496 | -1.77834 | 0.335262 | 0.323901 | 0.176217 | 0.2671 |
| 34 | 1.176217 | -1.82378 | 0.255739 | 0.346622 | 0.142136 | 0.346622 |
| 35 | 1.142136 | -1.83514 | 0.244379 | 0.437505 | 0.198938 | 0.312541 |
| 36 | 1.233019 | -1.76698 | 0.233019 | 0.346622 | 0.198938 | 0.301181 |
| 37 | 1.187577 | -1.80106 | 0.27846 | 0.403424 | 0.142136 | 0.312541 |
| 38 | 1.198938 | -1.66474 | 0.301181 | 0.380703 | 0.187577 | 0.323901 |
| 39 | 1.221658 | -1.77834 | 0.323901 | 0.369343 | 0.153496 | 0.323901 |
| 40 | 1.2671 | -1.75562 | 0.255739 | 0.437505 | 0.176217 | 0.27846 |
| 41 | 1.244379 | -1.83514 | 0.244379 | 0.414784 | 0.198938 | 0.233019 |
| 42 | 1.233019 | -1.77834 | 0.28982 | 0.335262 | 0.221658 | 0.2671 |
| 43 | 1.244379 | -1.77834 | 0.255739 | 0.369343 | 0.244379 | 0.335262 |
| 44 | 1.210298 | -1.8465 | 0.27846 | 0.414784 | 0.119415 | 0.244379 |
| 45 | 1.210298 | -1.81242 | 0.312541 | 0.448865 | 0.210298 | 0.255739 |
| 46 | 1.221658 | -1.80106 | 0.312541 | 0.380703 | 0.187577 | 0.255739 |
| 47 | 1.233019 | -1.7897 | 0.2671 | 0.460225 | 0.198938 | 0.28982 |
| 48 | 1.233019 | -1.7897 | 0.312541 | 0.437505 | 0.233019 | 0.357982 |
| 49 | 1.2671 | -1.82378 | 0.369343 | 0.380703 | 0.198938 | 0.210298 |
| 50 | 1.255739 | -1.83514 | 0.255739 | 0.482946 | 0.2671 | 0.255739 |
| 51 | 1.28982 | -1.83514 | 0.244379 | 0.414784 | 0.2671 | 0.301181 |
| 52 | 1.335262 | -1.80106 | 0.312541 | 0.460225 | 0.2671 | 0.210298 |
| 53 | 1.198938 | -1.77834 | 0.255739 | 0.460225 | 0.210298 | 0.233019 |
| 54 | 1.27846 | -1.83514 | 0.2671 | 0.357982 | 0.187577 | 0.323901 |
| 55 | 1.27846 | -1.77834 | 0.221658 | 0.357982 | 0.255739 | 0.323901 |
| 56 | 1.312541 | -1.8465 | 0.255739 | 0.448865 | 0.221658 | 0.244379 |
| 57 | 1.28982 | -1.77834 | 0.323901 | 0.414784 | 0.233019 | 0.233019 |
| 58 | 1.210298 | -1.76698 | 0.301181 | 0.414784 | 0.27846 | 0.244379 |
| 59 | 1.255739 | -1.7897 | 0.28982 | 0.369343 | 0.164857 | 0.198938 |
| 60 | 1.28982 | -1.7329 | 0.27846 | 0.403424 | 0.221658 | 0.255739 |
| 61 | 1.2671 | -1.76698 | 0.28982 | 0.437505 | 0.233019 | 0.233019 |
| 62 | 1.233019 | -1.83514 | 0.301181 | 0.357982 | 0.255739 | 0.312541 |
| 63 | 1.323901 | -1.85786 | 0.233019 | 0.346622 | 0.221658 | 0.346622 |
| 64 | 1.323901 | -1.80106 | 0.346622 | 0.301181 | 0.312541 | 0.233019 |
| 65 | 1.357982 | -1.7897 | 0.2671 | 0.346622 | 0.233019 | 0.27846 |
| 66 | 1.312541 | -1.88059 | 0.312541 | 0.346622 | 0.221658 | 0.28982 |
| 67 | 1.312541 | -1.74426 | 0.28982 | 0.301181 | 0.27846 | 0.27846 |
| 68 | 1.27846 | -1.8465 | 0.2671 | 0.335262 | 0.221658 | 0.301181 |
| 69 | 1.346622 | -1.8465 | 0.255739 | 0.221658 | 0.323901 | 0.2671 |
| 70 | 1.27846 | -1.8465 | 0.27846 | 0.27846 | 0.233019 | 0.392063 |
| 71 | 1.380703 | -1.82378 | 0.2671 | 0.301181 | 0.244379 | 0.28982 |
| 72 | 1.312541 | -1.80106 | 0.2671 | 0.301181 | 0.244379 | 0.210298 |
| 73 | 1.403424 | -1.77834 | 0.346622 | 0.301181 | 0.301181 | 0.244379 |
| 74 | 1.2671 | -1.7897 | 0.2671 | 0.255739 | 0.312541 | 0.233019 |
| 75 | 1.357982 | -1.83514 | 0.210298 | 0.187577 | 0.28982 | 0.357982 |
| 76 | 1.346622 | -1.75562 | 0.255739 | 0.27846 | 0.312541 | 0.27846 |
| 77 | 1.312541 | -1.76698 | 0.301181 | 0.2671 | 0.323901 | 0.323901 |
| 78 | 1.323901 | -1.7897 | 0.244379 | 0.301181 | 0.28982 | 0.312541 |
| 79 | 1.2671 | -1.7329 | 0.2671 | 0.221658 | 0.28982 | 0.312541 |
| 80 | 1.28982 | -1.81242 | 0.210298 | 0.27846 | 0.323901 | 0.357982 |
| 81 | 1.380703 | -1.75562 | 0.142136 | 0.357982 | 0.301181 | 0.2671 |
| 82 | 1.448865 | -1.72154 | 0.244379 | 0.312541 | 0.346622 | 0.346622 |
| 83 | 1.357982 | -1.82378 | 0.255739 | 0.2671 | 0.301181 | 0.312541 |
| 84 | 1.369343 | -1.82378 | 0.153496 | 0.357982 | 0.346622 | 0.335262 |
| 85 | 1.380703 | -1.74426 | 0.187577 | 0.28982 | 0.301181 | 0.335262 |
| 86 | 1.323901 | -1.75562 | 0.2671 | 0.403424 | 0.346622 | 0.357982 |
| 87 | 1.323901 | -1.72154 | 0.142136 | 0.335262 | 0.380703 | 0.335262 |
| 88 | 1.335262 | -1.68746 | 0.130776 | 0.28982 | 0.323901 | 0.403424 |
| 89 | 1.28982 | -1.72154 | 0.244379 | 0.357982 | 0.323901 | 0.312541 |
| 90 | 1.255739 | -1.6761 | 0.142136 | 0.335262 | 0.380703 | 0.301181 |
| 91 | 1.426144 | -1.59658 | 0.210298 | 0.414784 | 0.369343 | 0.346622 |
| 92 | 1.392063 | -1.6761 | 0.210298 | 0.357982 | 0.346622 | 0.312541 |
| 93 | 1.346622 | -1.64202 | 0.210298 | 0.460225 | 0.369343 | 0.369343 |
| 94 | 1.494306 | -1.57386 | 0.187577 | 0.346622 | 0.312541 | 0.392063 |
| 95 | 1.357982 | -1.7329 | 0.210298 | 0.392063 | 0.380703 | 0.403424 |
| 96 | 1.369343 | -1.64202 | 0.210298 | 0.357982 | 0.403424 | 0.28982 |
| 97 | 1.414784 | -1.5625 | 0.210298 | 0.369343 | 0.414784 | 0.426144 |
| 98 | 1.482946 | -1.57386 | 0.244379 | 0.448865 | 0.369343 | 0.380703 |
| 99 | 1.403424 | -1.65338 | 0.255739 | 0.335262 | 0.471586 | 0.357982 |
| 100 | 1.414784 | -1.63066 | 0.255739 | 0.323901 | 0.369343 | 0.403424 |
| 101 | 1.437505 | -1.57386 | 0.233019 | 0.346622 | 0.357982 | 0.380703 |
| 102 | 1.494306 | -1.59658 | 0.2671 | 0.380703 | 0.460225 | 0.426144 |
| 103 | 1.505667 | -1.58522 | 0.28982 | 0.414784 | 0.346622 | 0.403424 |
| 104 | 1.494306 | -1.58522 | 0.312541 | 0.426144 | 0.426144 | 0.346622 |
| 105 | 1.471586 | -1.64202 | 0.187577 | 0.403424 | 0.482946 | 0.312541 |
| 106 | 1.448865 | -1.58522 | 0.28982 | 0.460225 | 0.380703 | 0.437505 |
| 107 | 1.505667 | -1.6193 | 0.346622 | 0.380703 | 0.414784 | 0.301181 |
| 108 | 1.528388 | -1.63066 | 0.312541 | 0.437505 | 0.471586 | 0.312541 |
| 109 | 1.573829 | -1.60794 | 0.369343 | 0.448865 | 0.414784 | 0.437505 |
| 110 | 1.585189 | -1.59658 | 0.380703 | 0.448865 | 0.426144 | 0.357982 |
| 111 | 1.460225 | -1.6761 | 0.244379 | 0.414784 | 0.403424 | 0.2671 |
| 112 | 1.630631 | -1.6761 | 0.403424 | 0.426144 | 0.482946 | 0.369343 |
| 113 | 1.641991 | -1.60794 | 0.312541 | 0.414784 | 0.380703 | 0.323901 |
| 114 | 1.551108 | -1.5625 | 0.27846 | 0.494306 | 0.448865 | 0.323901 |
| 115 | 1.562469 | -1.66474 | 0.426144 | 0.471586 | 0.505667 | 0.27846 |
| 116 | 1.630631 | -1.57386 | 0.164857 | 0.482946 | 0.369343 | 0.312541 |
| 117 | 1.573829 | -1.63066 | 0.437505 | 0.505667 | 0.426144 | 0.312541 |
| 118 | 1.664712 | -1.59658 | 0.312541 | 0.471586 | 0.460225 | 0.210298 |
| 119 | 1.630631 | -1.57386 | 0.403424 | 0.460225 | 0.426144 | 0.369343 |
| 120 | 1.528388 | -1.58522 | 0.335262 | 0.505667 | 0.426144 | 0.28982 |
| 121 | 1.60791 | -1.64202 | 0.335262 | 0.528388 | 0.528388 | 0.2671 |
| 122 | 1.60791 | -1.6761 | 0.448865 | 0.414784 | 0.494306 | 0.301181 |
| 123 | 1.505667 | -1.59658 | 0.335262 | 0.505667 | 0.482946 | 0.27846 |
| 124 | 1.59655 | -1.64202 | 0.369343 | 0.448865 | 0.517027 | 0.312541 |
| 125 | 1.630631 | -1.58522 | 0.437505 | 0.471586 | 0.426144 | 0.346622 |
| 126 | 1.585189 | -1.63066 | 0.312541 | 0.573829 | 0.61927 | 0.301181 |
| 127 | 1.59655 | -1.63066 | 0.414784 | 0.482946 | 0.653351 | 0.28982 |
| 128 | 1.676072 | -1.59658 | 0.392063 | 0.471586 | 0.573829 | 0.27846 |
| 129 | 1.517027 | -1.58522 | 0.357982 | 0.448865 | 0.60791 | 0.403424 |
| 130 | 1.59655 | -1.59658 | 0.357982 | 0.505667 | 0.59655 | 0.335262 |
| 131 | 1.641991 | -1.69882 | 0.335262 | 0.505667 | 0.517027 | 0.312541 |
| 132 | 1.60791 | -1.51705 | 0.471586 | 0.482946 | 0.585189 | 0.312541 |
| 133 | 1.630631 | -1.64202 | 0.426144 | 0.539748 | 0.61927 | 0.346622 |
| 134 | 1.687432 | -1.63066 | 0.448865 | 0.414784 | 0.630631 | 0.357982 |
| 135 | 1.61927 | -1.52841 | 0.460225 | 0.482946 | 0.641991 | 0.437505 |
| 136 | 1.585189 | -1.58522 | 0.403424 | 0.539748 | 0.562469 | 0.357982 |
| 137 | 1.721513 | -1.66474 | 0.471586 | 0.437505 | 0.59655 | 0.448865 |
| 138 | 1.59655 | -1.55114 | 0.482946 | 0.505667 | 0.664712 | 0.482946 |
| 139 | 1.641991 | -1.55114 | 0.448865 | 0.551108 | 0.585189 | 0.403424 |
| 140 | 1.59655 | -1.60794 | 0.346622 | 0.482946 | 0.61927 | 0.380703 |
| 141 | 1.585189 | -1.53978 | 0.437505 | 0.573829 | 0.59655 | 0.369343 |
| 142 | 1.61927 | -1.5625 | 0.426144 | 0.517027 | 0.60791 | 0.369343 |
| 143 | 1.539748 | -1.60794 | 0.426144 | 0.528388 | 0.573829 | 0.357982 |
| 144 | 1.551108 | -1.55114 | 0.437505 | 0.539748 | 0.641991 | 0.426144 |
| 145 | 1.573829 | -1.6761 | 0.426144 | 0.562469 | 0.630631 | 0.471586 |
| 146 | 1.653351 | -1.60794 | 0.437505 | 0.528388 | 0.664712 | 0.471586 |
| 147 | 1.585189 | -1.63066 | 0.482946 | 0.562469 | 0.585189 | 0.357982 |
| 148 | 1.59655 | -1.57386 | 0.460225 | 0.517027 | 0.687432 | 0.414784 |
| 149 | 1.653351 | -1.51705 | 0.528388 | 0.539748 | 0.573829 | 0.392063 |
| 150 | 1.630631 | -1.6193 | 0.471586 | 0.517027 | 0.60791 | 0.369343 |
| 151 | 1.59655 | -1.64202 | 0.517027 | 0.59655 | 0.60791 | 0.414784 |
| 152 | 1.573829 | -1.50569 | 0.517027 | 0.539748 | 0.641991 | 0.460225 |
| 153 | 1.676072 | -1.57386 | 0.505667 | 0.585189 | 0.573829 | 0.414784 |
| 154 | 1.562469 | -1.59658 | 0.460225 | 0.539748 | 0.59655 | 0.460225 |
| 155 | 1.653351 | -1.48297 | 0.494306 | 0.59655 | 0.698793 | 0.392063 |
| 156 | 1.573829 | -1.53978 | 0.437505 | 0.59655 | 0.517027 | 0.437505 |
| 157 | 1.59655 | -1.57386 | 0.482946 | 0.641991 | 0.641991 | 0.505667 |
| 158 | 1.664712 | -1.51705 | 0.482946 | 0.641991 | 0.551108 | 0.517027 |
| 159 | 1.61927 | -1.49433 | 0.494306 | 0.641991 | 0.664712 | 0.517027 |
| 160 | 1.61927 | -1.52841 | 0.482946 | 0.61927 | 0.641991 | 0.471586 |
| 161 | 1.630631 | -1.52841 | 0.517027 | 0.698793 | 0.653351 | 0.437505 |
| 162 | 1.61927 | -1.53978 | 0.482946 | 0.698793 | 0.687432 | 0.437505 |
| 163 | 1.60791 | -1.52841 | 0.517027 | 0.698793 | 0.641991 | 0.573829 |
| 164 | 1.641991 | -1.51705 | 0.505667 | 0.766955 | 0.630631 | 0.471586 |
| 165 | 1.573829 | -1.43753 | 0.528388 | 0.812396 | 0.664712 | 0.539748 |
| 166 | 1.653351 | -1.53978 | 0.528388 | 0.755594 | 0.710153 | 0.471586 |
| 167 | 1.61927 | -1.51705 | 0.562469 | 0.766955 | 0.653351 | 0.414784 |
| 168 | 1.664712 | -1.48297 | 0.528388 | 0.755594 | 0.641991 | 0.505667 |
| 169 | 1.60791 | -1.53978 | 0.551108 | 0.789675 | 0.585189 | 0.505667 |
| 170 | 1.653351 | -1.51705 | 0.562469 | 0.801036 | 0.664712 | 0.517027 |
| 171 | 1.630631 | -1.48297 | 0.585189 | 0.755594 | 0.59655 | 0.60791 |
| 172 | 1.641991 | -1.48297 | 0.630631 | 0.789675 | 0.710153 | 0.460225 |
| 173 | 1.721513 | -1.46025 | 0.60791 | 0.823756 | 0.60791 | 0.528388 |
| 174 | 1.653351 | -1.53978 | 0.641991 | 0.778315 | 0.698793 | 0.505667 |
| 175 | 1.630631 | -1.50569 | 0.61927 | 0.801036 | 0.630631 | 0.551108 |
| 176 | 1.653351 | -1.5625 | 0.676072 | 0.801036 | 0.653351 | 0.517027 |
| 177 | 1.630631 | -1.46025 | 0.653351 | 0.766955 | 0.710153 | 0.551108 |
| 178 | 1.676072 | -1.50569 | 0.664712 | 0.857837 | 0.710153 | 0.562469 |
| 179 | 1.698793 | -1.47161 | 0.664712 | 0.744234 | 0.641991 | 0.528388 |
| 180 | 1.687432 | -1.53978 | 0.698793 | 0.766955 | 0.641991 | 0.494306 |
| 181 | 1.744234 | -1.53978 | 0.732874 | 0.698793 | 0.698793 | 0.539748 |
| 182 | 1.687432 | -1.52841 | 0.676072 | 0.766955 | 0.710153 | 0.573829 |
| 183 | 1.641991 | -1.51705 | 0.744234 | 0.835117 | 0.61927 | 0.585189 |
| 184 | 1.721513 | -1.57386 | 0.676072 | 0.721513 | 0.710153 | 0.528388 |
| 185 | 1.710153 | -1.55114 | 0.744234 | 0.869198 | 0.687432 | 0.517027 |
| 186 | 1.721513 | -1.63066 | 0.698793 | 0.823756 | 0.744234 | 0.528388 |
| 187 | 1.721513 | -1.58522 | 0.698793 | 0.778315 | 0.755594 | 0.585189 |
| 188 | 1.732874 | -1.60794 | 0.778315 | 0.755594 | 0.687432 | 0.573829 |
| 189 | 1.732874 | -1.51705 | 0.687432 | 0.778315 | 0.766955 | 0.585189 |
| 190 | 1.744234 | -1.72154 | 0.721513 | 0.869198 | 0.721513 | 0.528388 |
| 191 | 1.710153 | -1.65338 | 0.676072 | 0.766955 | 0.755594 | 0.585189 |
| 192 | 1.744234 | -1.52841 | 0.687432 | 0.778315 | 0.710153 | 0.562469 |
| 193 | 1.778315 | -1.57386 | 0.766955 | 0.801036 | 0.744234 | 0.551108 |
| 194 | 1.698793 | -1.60794 | 0.766955 | 0.823756 | 0.710153 | 0.528388 |
| 195 | 1.744234 | -1.59658 | 0.766955 | 0.755594 | 0.755594 | 0.61927 |
| 196 | 1.732874 | -1.55114 | 0.744234 | 0.835117 | 0.732874 | 0.539748 |
| 197 | 1.687432 | -1.65338 | 0.732874 | 0.778315 | 0.732874 | 0.585189 |
| 198 | 1.744234 | -1.63066 | 0.687432 | 0.857837 | 0.778315 | 0.573829 |
| 199 | 1.698793 | -1.50569 | 0.721513 | 0.732874 | 0.801036 | 0.61927 |
| 200 | 1.732874 | -1.53978 | 0.732874 | 0.823756 | 0.755594 | 0.630631 |
| 201 | 1.676072 | -1.58522 | 0.698793 | 0.823756 | 0.766955 | 0.653351 |
| 202 | 1.676072 | -1.50569 | 0.744234 | 0.812396 | 0.744234 | 0.60791 |
| 203 | 1.732874 | -1.60794 | 0.710153 | 0.835117 | 0.778315 | 0.653351 |
| 204 | 1.687432 | -1.57386 | 0.698793 | 0.755594 | 0.801036 | 0.59655 |
| 205 | 1.641991 | -1.51705 | 0.710153 | 0.869198 | 0.823756 | 0.630631 |
| 206 | 1.687432 | -1.49433 | 0.710153 | 0.835117 | 0.732874 | 0.664712 |
| 207 | 1.664712 | -1.46025 | 0.710153 | 0.789675 | 0.755594 | 0.721513 |
| 208 | 1.630631 | -1.46025 | 0.789675 | 0.812396 | 0.812396 | 0.710153 |
| 209 | 1.641991 | -1.57386 | 0.653351 | 0.846477 | 0.801036 | 0.721513 |
| 210 | 1.698793 | -1.53978 | 0.698793 | 0.891918 | 0.744234 | 0.789675 |
| 211 | 1.528388 | -1.41481 | 0.698793 | 0.869198 | 0.846477 | 0.823756 |
| 212 | 1.641991 | -1.48297 | 0.721513 | 0.869198 | 0.846477 | 0.721513 |
| 213 | 1.653351 | -1.44889 | 0.766955 | 0.801036 | 0.687432 | 0.812396 |
| 214 | 1.676072 | -1.44889 | 0.766955 | 0.880558 | 0.789675 | 0.766955 |
| 215 | 1.630631 | -1.50569 | 0.766955 | 0.812396 | 0.778315 | 0.812396 |
| 216 | 1.687432 | -1.43753 | 0.687432 | 0.857837 | 0.801036 | 0.812396 |
| 217 | 1.732874 | -1.44889 | 0.778315 | 0.914639 | 0.766955 | 0.801036 |
| 218 | 1.641991 | -1.42617 | 0.778315 | 0.857837 | 0.755594 | 0.778315 |
| 219 | 1.710153 | -1.42617 | 0.721513 | 0.891918 | 0.721513 | 0.869198 |
| 220 | 1.664712 | -1.41481 | 0.789675 | 0.94872 | 0.812396 | 0.846477 |
| 221 | 1.641991 | -1.31257 | 0.880558 | 0.982801 | 0.710153 | 0.778315 |
| 222 | 1.687432 | -1.40345 | 0.778315 | 0.93736 | 0.732874 | 0.846477 |
| 223 | 1.755594 | -1.39209 | 0.766955 | 0.94872 | 0.732874 | 0.835117 |
| 224 | 1.676072 | -1.40345 | 0.778315 | 0.93736 | 0.710153 | 0.778315 |
| 225 | 1.755594 | -1.32393 | 0.823756 | 0.93736 | 0.755594 | 0.857837 |
| 226 | 1.766955 | -1.36937 | 0.846477 | 0.982801 | 0.755594 | 0.812396 |
| 227 | 1.710153 | -1.41481 | 0.846477 | 1.005522 | 0.732874 | 0.835117 |
| 228 | 1.755594 | -1.32393 | 0.732874 | 0.971441 | 0.835117 | 0.891918 |
| 229 | 1.744234 | -1.31257 | 0.846477 | 0.96008 | 0.789675 | 0.914639 |
| 230 | 1.823756 | -1.33529 | 0.789675 | 1.062323 | 0.789675 | 0.891918 |
| 231 | 1.823756 | -1.31257 | 0.903279 | 1.085044 | 0.846477 | 0.925999 |
| 232 | 1.789675 | -1.24441 | 0.891918 | 1.039603 | 0.812396 | 0.880558 |
| 233 | 1.857837 | -1.28985 | 0.914639 | 1.085044 | 0.766955 | 0.96008 |
| 234 | 1.812396 | -1.22169 | 0.891918 | 1.085044 | 0.835117 | 0.925999 |
| 235 | 1.812396 | -1.19896 | 0.96008 | 1.073684 | 0.823756 | 0.891918 |
| 236 | 1.925999 | -1.1876 | 0.891918 | 1.096404 | 0.835117 | 0.869198 |
| 237 | 1.914639 | -1.26713 | 0.925999 | 1.050963 | 0.891918 | 0.880558 |
| 238 | 1.94872 | -1.22169 | 0.971441 | 1.141846 | 0.925999 | 0.925999 |
| 239 | 1.94872 | -1.19896 | 0.982801 | 1.175927 | 0.93736 | 0.925999 |
| 240 | 1.891918 | -1.25577 | 1.028242 | 1.119125 | 0.914639 | 0.96008 |
| 241 | 1.94872 | -1.26713 | 1.016882 | 1.141846 | 0.96008 | 0.971441 |
| 242 | 1.994161 | -1.21033 | 1.005522 | 1.164566 | 0.93736 | 0.994161 |
| 243 | 1.982801 | -1.15352 | 1.016882 | 1.175927 | 0.914639 | 1.005522 |
| 244 | 2.028242 | -1.11944 | 1.028242 | 1.119125 | 0.982801 | 1.028242 |
| 245 | 2.016882 | -1.15352 | 1.085044 | 1.221368 | 1.062323 | 1.028242 |
| 246 | 2.050963 | -1.08536 | 1.096404 | 1.210008 | 1.050963 | 1.050963 |
| 247 | 2.096404 | -1.02856 | 1.119125 | 1.210008 | 1.028242 | 1.073684 |
| 248 | 2.085044 | -1.02856 | 1.107765 | 1.266809 | 1.141846 | 1.096404 |
| 249 | 2.107765 | -1.06264 | 1.085044 | 1.244089 | 1.107765 | 1.119125 |
| 250 | 2.130485 | -1.074 | 1.119125 | 1.266809 | 1.073684 | 1.141846 |
| 251 | 2.187287 | -1.03992 | 1.153206 | 1.346332 | 1.119125 | 1.164566 |
| 252 | 2.107765 | -0.99448 | 1.175927 | 1.255449 | 1.187287 | 1.198647 |
| 253 | 2.198647 | -0.92632 | 1.164566 | 1.380413 | 1.164566 | 1.130485 |
| 254 | 2.244089 | -0.92632 | 1.153206 | 1.255449 | 1.221368 | 1.119125 |
| 255 | 2.27817 | -0.89224 | 1.164566 | 1.334971 | 1.164566 | 1.210008 |
| 256 | 2.266809 | -0.89224 | 1.198647 | 1.28953 | 1.28953 | 1.232728 |
| 257 | 2.255449 | -0.85815 | 1.175927 | 1.334971 | 1.255449 | 1.210008 |
| 258 | 2.380413 | -0.84679 | 1.28953 | 1.323611 | 1.266809 | 1.210008 |
| 259 | 2.369052 | -0.83543 | 1.255449 | 1.232728 | 1.369052 | 1.27817 |
| 260 | 2.357692 | -0.82407 | 1.30089 | 1.323611 | 1.346332 | 1.334971 |
| 261 | 2.471296 | -0.77863 | 1.334971 | 1.391773 | 1.334971 | 1.255449 |
| 262 | 2.369052 | -0.73319 | 1.312251 | 1.346332 | 1.482656 | 1.334971 |
| 263 | 2.482656 | -0.74455 | 1.346332 | 1.357692 | 1.425854 | 1.369052 |
| 264 | 2.494016 | -0.61959 | 1.448575 | 1.471296 | 1.550818 | 1.391773 |
| 265 | 2.528097 | -0.63095 | 1.471296 | 1.459935 | 1.471296 | 1.448575 |
| 266 | 2.539458 | -0.67639 | 1.459935 | 1.505377 | 1.505377 | 1.471296 |
| 267 | 2.584899 | -0.66503 | 1.448575 | 1.505377 | 1.505377 | 1.505377 |
| 268 | 2.584899 | -0.60823 | 1.482656 | 1.596259 | 1.516737 | 1.61898 |
| 269 | 2.641701 | -0.54007 | 1.516737 | 1.596259 | 1.63034 | 1.653061 |
| 270 | 2.687142 | -0.49462 | 1.596259 | 1.641701 | 1.61898 | 1.60762 |
| 271 | 2.732583 | -0.40374 | 1.528097 | 1.584899 | 1.664421 | 1.653061 |
| 272 | 2.800745 | -0.3583 | 1.573539 | 1.766664 | 1.755304 | 1.721223 |
| 273 | 2.766664 | -0.3583 | 1.653061 | 1.755304 | 1.823466 | 1.755304 |
| 274 | 2.834826 | -0.27878 | 1.687142 | 1.800745 | 1.857547 | 1.857547 |
| 275 | 2.868907 | -0.26742 | 1.687142 | 1.834826 | 1.868907 | 1.857547 |
| 276 | 2.937069 | -0.17653 | 1.766664 | 1.902988 | 1.846187 | 1.902988 |
| 277 | 2.937069 | -0.19926 | 1.778025 | 1.97115 | 1.95979 | 1.95979 |
| 278 | 3.005231 | -0.07429 | 1.914349 | 1.97115 | 2.016592 | 1.95979 |
| 279 | 3.073393 | -0.00613 | 1.846187 | 2.050673 | 2.027952 | 2.062033 |
| 280 | 3.118835 | 0.062033 | 1.891628 | 2.073393 | 2.073393 | 2.107474 |
| 281 | 3.221078 | 0.175636 | 1.94843 | 2.141555 | 2.152916 | 2.164276 |
| 282 | 3.232438 | 0.209717 | 2.050673 | 2.255159 | 2.232438 | 2.232438 |
| 283 | 3.3006 | 0.243798 | 2.141555 | 2.209717 | 2.232438 | 2.3006 |
| 284 | 3.380123 | 0.380123 | 2.221078 | 2.334681 | 2.357402 | 2.334681 |
| 285 | 3.459645 | 0.277879 | 2.3006 | 2.414204 | 2.425564 | 2.391483 |
| 286 | 3.482366 | 0.425564 | 2.3006 | 2.471005 | 2.414204 | 2.482366 |
| 287 | 3.493726 | 0.516447 | 2.402843 | 2.584609 | 2.436924 | 2.539167 |
| 288 | 3.652771 | 0.61869 | 2.448285 | 2.595969 | 2.539167 | 2.61869 |
| 289 | 3.686852 | 0.652771 | 2.595969 | 2.675491 | 2.595969 | 2.675491 |
| 290 | 3.755014 | 0.698212 | 2.584609 | 2.789095 | 2.720933 | 2.686852 |
| 291 | 3.857257 | 0.755014 | 2.686852 | 2.811815 | 2.789095 | 2.766374 |
| 292 | 3.9595 | 0.857257 | 2.811815 | 2.902698 | 2.891338 | 2.868617 |
| 293 | 4.084463 | 1.004941 | 2.948139 | 3.027662 | 3.016301 | 2.98222 |
| 294 | 4.129905 | 0.993581 | 2.98222 | 3.129905 | 3.118544 | 3.050382 |
| 295 | 4.243508 | 1.152625 | 3.050382 | 3.186706 | 3.141265 | 3.163986 |
| 296 | 4.334391 | 1.266229 | 3.186706 | 3.334391 | 3.220787 | 3.220787 |
| 297 | 4.516156 | 1.345751 | 3.31167 | 3.413913 | 3.425274 | 3.402553 |
| 298 | 4.527517 | 1.425274 | 3.459355 | 3.550237 | 3.561598 | 3.425274 |
| 299 | 4.663841 | 1.584318 | 3.470715 | 3.572958 | 3.607039 | 3.572958 |
| 300 | 4.856966 | 1.675201 | 3.595679 | 3.686561 | 3.777444 | 3.766084 |
| 301 | 4.936489 | 1.856966 | 3.743363 | 3.99329 | 3.811525 | 3.720642 |
| 302 | 5.084173 | 1.947849 | 3.879687 | 3.959209 | 3.98193 | 3.879687 |
| 303 | 5.243218 | 2.004651 | 4.027371 | 4.129614 | 4.072813 | 3.925128 |
| 304 | 5.459064 | 2.220497 | 4.209137 | 4.3341 | 4.345461 | 4.072813 |
| 305 | 5.595388 | 2.368181 | 4.390902 | 4.390902 | 4.390902 | 4.300019 |
| 306 | 5.788514 | 2.436344 | 4.424983 | 4.595388 | 4.618109 | 4.368181 |
| 307 | 5.924838 | 2.66355 | 4.708992 | 4.788514 | 4.799874 | 4.493145 |
| 308 | 6.106603 | 2.879397 | 4.811235 | 5.027081 | 4.879397 | 4.743073 |
| 309 | 6.288369 | 3.049802 | 4.993 | 5.129324 | 5.174765 | 4.970279 |
| 310 | 6.504215 | 3.265648 | 5.220207 | 5.265648 | 5.277008 | 5.117964 |
| 311 | 6.765503 | 3.390612 | 5.413332 | 5.572377 | 5.538296 | 5.390612 |
| 312 | 6.879106 | 3.6519 | 5.708701 | 5.822305 | 5.788224 | 5.492855 |
| 313 | 7.185835 | 3.867746 | 5.867746 | 5.981349 | 6.00407 | 5.776863 |
| 314 | 7.435763 | 4.083592 | 6.140394 | 6.231277 | 6.33352 | 6.083592 |
| 315 | 7.628888 | 4.35624 | 6.35624 | 6.492564 | 6.469844 | 6.299439 |
| 316 | 7.878816 | 4.628888 | 6.594807 | 6.799294 | 6.799294 | 6.560726 |
| 317 | 8.196905 | 4.935618 | 6.946978 | 6.981059 | 7.071942 | 6.787933 |
| 318 | 8.412752 | 5.230986 | 7.162824 | 7.287788 | 7.378671 | 7.106023 |
| 319 | 8.776282 | 5.514995 | 7.583157 | 7.628598 | 7.651319 | 7.458193 |
| 320 | 9.151174 | 5.810363 | 7.833084 | 7.901246 | 8.071651 | 7.855805 |
| 321 | 9.435182 | 6.219336 | 8.230696 | 8.230696 | 8.446542 | 8.117093 |
| 322 | 9.821433 | 6.651028 | 8.605587 | 8.685109 | 8.798713 | 8.480623 |
| 323 | 10.13952 | 6.912316 | 8.935037 | 9.094081 | 9.071361 | 8.923676 |
| 324 | 10.62802 | 7.355369 | 9.366729 | 9.423531 | 9.525774 | 9.355369 |
| 325 | 11.01427 | 7.764341 | 9.832503 | 9.877945 | 10.00291 | 9.70754 |
| 326 | 11.4346 | 8.252836 | 10.21876 | 10.30964 | 10.52548 | 10.17331 |
| 327 | 11.94582 | 8.684528 | 10.72997 | 10.76405 | 10.88901 | 10.71861 |
| 328 | 12.47975 | 9.138942 | 11.22983 | 11.30935 | 11.38887 | 11.19574 |
| 329 | 12.94553 | 9.729679 | 11.70696 | 11.87736 | 12.00233 | 11.72968 |
| 330 | 13.54762 | 10.30906 | 12.32042 | 12.39994 | 12.55898 | 12.28634 |
| 331 | 14.19516 | 10.85435 | 12.91115 | 12.99068 | 13.127 | 12.85435 |
| 332 | 14.75182 | 11.50189 | 13.57005 | 13.60414 | 13.68366 | 13.6155 |
| 333 | 15.42208 | 12.17215 | 14.16079 | 14.24031 | 14.34256 | 14.17215 |
| 334 | 16.13778 | 12.91057 | 14.88785 | 14.95601 | 15.1037 | 14.89921 |
| 335 | 16.8762 | 13.56947 | 15.59219 | 15.62627 | 15.79668 | 15.62627 |
| 336 | 17.54646 | 14.37606 | 16.34198 | 16.38742 | 16.56918 | 16.39878 |
| 337 | 18.44393 | 15.18264 | 17.20536 | 17.21672 | 17.35305 | 17.2508 |
| 338 | 19.27323 | 16.05739 | 18.03467 | 18.09147 | 18.14827 | 18.06875 |
| 339 | 20.18206 | 16.93213 | 18.93213 | 18.88669 | 19.14798 | 19.03438 |
| 340 | 21.04544 | 17.8296 | 19.80688 | 19.86368 | 19.93184 | 19.78416 |
| 341 | 22.03379 | 18.79523 | 20.82931 | 20.85203 | 20.99971 | 20.89747 |
| 342 | 23.06758 | 19.77222 | 21.66997 | 21.78358 | 21.85174 | 21.84038 |
| 343 | 24.05593 | 20.80601 | 22.82873 | 22.85145 | 23.03321 | 22.88553 |
| 344 | 25.16925 | 21.90796 | 23.81708 | 23.8398 | 24.0102 | 23.93068 |
| 345 | 26.19168 | 22.90767 | 24.89631 | 24.90767 | 25.08943 | 25.06671 |
| 346 | 27.40723 | 24.1005 | 26.05506 | 26.02098 | 26.24819 | 26.08914 |
| 347 | 28.49782 | 25.16837 | 27.20245 | 27.12293 | 27.31606 | 27.35014 |
| 348 | 29.69066 | 26.30441 | 28.38393 | 28.29305 | 28.47481 | 28.45209 |
| 349 | 30.79261 | 27.40636 | 29.47452 | 29.395 | 29.57676 | 29.65629 |
| 350 | 32.05361 | 28.59919 | 30.59919 | 30.656 | 30.7128 | 30.81504 |
| 351 | 33.11012 | 29.67843 | 31.71251 | 31.66707 | 31.88291 | 31.88291 |
| 352 | 34.26887 | 30.83718 | 32.81446 | 32.83718 | 32.98486 | 33.01895 |
| 353 | 35.2913 | 31.81417 | 33.87097 | 33.80281 | 33.97321 | 34.10954 |
| 354 | 36.33645 | 32.71163 | 34.84796 | 34.73436 | 34.8934 | 35.06381 |
| 355 | 37.06351 | 33.59774 | 35.68862 | 35.65454 | 35.7227 | 35.91583 |
| 356 | 37.93826 | 34.41568 | 36.41568 | 36.46113 | 36.55201 | 36.72241 |
| 357 | 38.61988 | 35.06322 | 37.16547 | 37.18819 | 37.23363 | 37.38131 |
| 358 | 39.25606 | 35.80165 | 37.80165 | 37.71076 | 37.96069 | 37.96069 |
| 359 | 39.80135 | 36.55143 | 38.46054 | 38.51735 | 38.44918 | 38.60823 |
| 360 | 40.6193 | 37.63066 | 39.17625 | 39.60794 | 39.58522 | 39.81242 |
| 361 | 41.48268 | 40.74339 | 40.59629 | 42.03905 | 41.78912 | 42.15265 |
| 362 | 45.50424 | 46.10547 | 45.68572 | 48.62804 | 47.54881 | 47.96914 |
| 363 | 50.62775 | 50.07022 | 48.0373 | 48.27587 | 49.23014 | 49.40054 |
| 364 | 50.26422 | 50.44511 | 51.00235 | 53.10401 | 50.75242 | 51.2182 |
| 365 | 54.3653 | 52.14916 | 50.88875 | 51.42268 | 51.92254 | 51.84301 |
| 366 | 52.46812 | 50.93361 | 51.91118 | 52.21791 | 50.74106 | 51.16139 |
| 367 | 52.76349 | 51.79699 | 50.74106 | 51.39996 | 50.5593 | 51.51356 |
| 368 | 52.30908 | 50.05886 | 51.36588 | 51.4454 | 50.33209 | 50.97963 |
| 369 | 52.64989 | 50.86544 | 50.76378 | 50.10488 | 50.62746 | 50.65018 |
| 370 | 51.25257 | 49.25228 | 50.47977 | 49.42326 | 48.71892 | 49.32102 |
| 371 | 50.62775 | 49.07051 | 49.52551 | 49.46871 | 49.21878 | 48.99157 |
| 372 | 49.96885 | 47.60503 | 48.6962 | 47.44657 | 47.68513 | 47.66241 |
| 373 | 48.25344 | 46.86661 | 47.35568 | 47.11712 | 46.58318 | 46.69678 |
| 374 | 47.07197 | 45.01487 | 46.32189 | 45.7198 | 44.93593 | 45.0609 |
| 375 | 45.97001 | 44.10605 | 44.77689 | 44.28839 | 44.07255 | 44.08391 |
| 376 | 44.53861 | 42.53832 | 43.64086 | 42.10721 | 41.97089 | 42.27762 |
| 377 | 42.75504 | 41.20916 | 41.92545 | 41.47103 | 40.98254 | 40.88029 |
| 378 | 41.69853 | 39.24383 | 40.89166 | 39.52842 | 39.41481 | 39.26713 |
| 379 | 39.63095 | 37.55114 | 38.81271 | 38.23334 | 37.41539 | 37.51764 |
| 380 | 38.23363 | 36.33558 | 37.25635 | 36.48385 | 35.84767 | 35.93855 |
| 381 | 36.4955 | 34.34752 | 35.57502 | 34.79116 | 34.38219 | 34.59803 |
| 382 | 35.08682 | 33.08653 | 34.31402 | 33.15527 | 32.87126 | 32.75766 |
| 383 | 33.21236 | 31.30295 | 32.45093 | 31.92835 | 31.33762 | 31.20129 |
| 384 | 32.24673 | 29.83747 | 31.23537 | 30.39471 | 29.86077 | 29.86077 |
| 385 | 30.5086 | 28.33791 | 29.63357 | 28.95195 | 28.15672 | 28.38393 |
| 386 | 29.24761 | 26.97467 | 28.134 | 27.63415 | 27.15701 | 27.08885 |
| 387 | 27.69124 | 25.48646 | 26.92981 | 26.13458 | 25.62337 | 25.70289 |
| 388 | 26.4416 | 24.38451 | 25.88466 | 25.11215 | 24.54414 | 24.46461 |
| 389 | 25.36237 | 22.96447 | 24.37373 | 23.81708 | 23.24906 | 23.30586 |
| 390 | 24.09001 | 21.94204 | 23.21498 | 22.71512 | 22.01078 | 22.06758 |
| 391 | 22.93126 | 20.6924 | 22.05622 | 21.52229 | 20.89747 | 21.04515 |
| 392 | 21.79523 | 19.62453 | 21.19284 | 20.32945 | 19.76144 | 19.9432 |
| 393 | 20.81824 | 18.5453 | 19.95456 | 19.52287 | 19.04574 | 18.89805 |
| 394 | 19.80717 | 17.54559 | 19.02301 | 18.48908 | 18.09147 | 18.01195 |
| 395 | 18.80746 | 16.70493 | 18.08011 | 17.62569 | 17.0236 | 17.18264 |
| 396 | 17.90999 | 15.71658 | 17.194 | 16.5919 | 16.16021 | 16.3647 |
| 397 | 17.11477 | 14.85319 | 16.44422 | 15.77396 | 15.28546 | 15.58083 |
| 398 | 16.38771 | 14.08069 | 15.62627 | 15.11506 | 14.66065 | 14.81969 |
| 399 | 15.59248 | 13.36499 | 14.92193 | 14.388 | 14.01311 | 14.03583 |
| 400 | 14.77454 | 12.66065 | 14.11535 | 13.74046 | 13.37693 | 13.39965 |
| 401 | 14.02476 | 11.99039 | 13.53597 | 13.13836 | 12.5817 | 12.76347 |
| 402 | 13.57034 | 11.44509 | 12.85435 | 12.50218 | 11.95689 | 12.22953 |
| 403 | 13.11593 | 10.77483 | 12.2977 | 11.88872 | 11.36615 | 11.60472 |
| 404 | 12.43431 | 10.26362 | 11.76376 | 11.29799 | 10.83221 | 11.07078 |
| 405 | 11.95718 | 9.706959 | 11.24119 | 10.70725 | 10.3778 | 10.55957 |
| 406 | 11.17331 | 9.150302 | 10.66181 | 10.23012 | 9.923386 | 10.04835 |
| 407 | 10.76434 | 8.684528 | 10.21876 | 9.832503 | 9.468973 | 9.628017 |
| 408 | 10.33265 | 8.241475 | 9.70754 | 9.412171 | 8.969118 | 9.150883 |
| 409 | 10.01456 | 7.73026 | 9.309928 | 8.957757 | 8.514704 | 8.71919 |
| 410 | 9.582866 | 7.332648 | 8.844154 | 8.526065 | 8.094372 | 8.344299 |
| 411 | 9.35566 | 7.003199 | 8.605587 | 8.207975 | 7.753562 | 7.935327 |
| 412 | 8.799003 | 6.639668 | 8.151174 | 7.855805 | 7.378671 | 7.617238 |
| 413 | 8.503634 | 6.219336 | 7.844444 | 7.480914 | 7.071942 | 7.321869 |
| 414 | 8.128743 | 5.946687 | 7.605877 | 7.174185 | 6.765213 | 6.981059 |
| 415 | 7.799294 | 5.628598 | 7.276428 | 6.890176 | 6.526645 | 6.651609 |
| 416 | 7.560726 | 5.333229 | 6.969699 | 6.606168 | 6.219916 | 6.367601 |
| 417 | 7.34488 | 4.969699 | 6.651609 | 6.322159 | 5.856386 | 6.106313 |
| 418 | 6.958629 | 4.787933 | 6.378961 | 6.049511 | 5.595098 | 5.822305 |
| 419 | 6.742782 | 4.549366 | 6.163115 | 5.833665 | 5.481494 | 5.561017 |
| 420 | 6.549657 | 4.33352 | 5.867746 | 5.617819 | 5.174765 | 5.379251 |
| 421 | 6.242927 | 4.072232 | 5.640539 | 5.481494 | 4.958919 | 5.208846 |
| 422 | 6.095243 | 3.890467 | 5.526936 | 5.220207 | 4.788514 | 4.947559 |
| 423 | 5.902117 | 3.67462 | 5.277008 | 4.936198 | 4.629469 | 4.799874 |
| 424 | 5.697631 | 3.401972 | 5.083883 | 4.799874 | 4.424983 | 4.618109 |
| 425 | 5.493145 | 3.299729 | 4.879397 | 4.66355 | 4.31138 | 4.424983 |
| 426 | 5.424983 | 3.072522 | 4.686271 | 4.504506 | 4.095533 | 4.265938 |
| 427 | 5.163695 | 2.924838 | 4.572668 | 4.31138 | 3.936489 | 4.004651 |
| 428 | 5.061452 | 2.754433 | 4.402262 | 4.084173 | 3.777444 | 3.834246 |
| 429 | 4.947849 | 2.629469 | 4.300019 | 4.004651 | 3.618399 | 3.766084 |
| 430 | 4.720642 | 2.402262 | 4.084173 | 3.788804 | 3.538877 | 3.62976 |
| 431 | 4.675201 | 2.243218 | 3.902408 | 3.732003 | 3.368472 | 3.482075 |
| 432 | 4.413913 | 2.152335 | 3.868327 | 3.618399 | 3.209427 | 3.402553 |
| 433 | 4.368472 | 1.99329 | 3.697922 | 3.504796 | 3.152625 | 3.32303 |
| 434 | 4.220787 | 1.868327 | 3.561598 | 3.334391 | 3.016301 | 3.186706 |
| 435 | 4.084463 | 1.822885 | 3.436634 | 3.209427 | 2.902698 | 3.027662 |
| 436 | 3.993581 | 1.64112 | 3.30031 | 3.107184 | 2.800455 | 2.936779 |
| 437 | 3.902698 | 1.607039 | 3.266229 | 3.016301 | 2.766374 | 2.857257 |
| 438 | 3.789095 | 1.459355 | 3.163986 | 2.9595 | 2.573248 | 2.777734 |
| 439 | 3.675491 | 1.402553 | 2.97086 | 2.868617 | 2.561888 | 2.561888 |
| 440 | 3.686852 | 1.186706 | 2.9595 | 2.709572 | 2.436924 | 2.584609 |
| 441 | 3.505086 | 1.163986 | 2.925419 | 2.652771 | 2.357402 | 2.493726 |
| 442 | 3.391483 | 1.084463 | 2.755014 | 2.482366 | 2.221078 | 2.357402 |
| 443 | 3.414204 | 0.97086 | 2.664131 | 2.436924 | 2.175636 | 2.357402 |
| 444 | 3.266519 | 0.902698 | 2.595969 | 2.357402 | 2.152916 | 2.221078 |
| 445 | 3.255159 | 0.879977 | 2.595969 | 2.3006 | 2.050673 | 2.164276 |
| 446 | 3.107474 | 0.766374 | 2.357402 | 2.130195 | 1.937069 | 2.107474 |
| 447 | 3.141555 | 0.64141 | 2.425564 | 2.073393 | 1.902988 | 1.982511 |
| 448 | 3.027952 | 0.607329 | 2.323321 | 2.062033 | 1.846187 | 2.016592 |
| 449 | 2.925709 | 0.573248 | 2.209717 | 1.914349 | 1.812106 | 1.891628 |
| 450 | 2.94843 | 0.448285 | 2.175636 | 1.880268 | 1.778025 | 1.902988 |
| 451 | 2.823466 | 0.414204 | 2.130195 | 1.812106 | 1.675782 | 1.823466 |
| 452 | 2.743944 | 0.357402 | 2.039312 | 1.721223 | 1.664421 | 1.778025 |
| 453 | 2.755304 | 0.28924 | 1.937069 | 1.698502 | 1.61898 | 1.675782 |
| 454 | 2.675782 | 0.28924 | 1.925709 | 1.61898 | 1.573539 | 1.584899 |
| 455 | 2.61898 | 0.141555 | 1.891628 | 1.539458 | 1.482656 | 1.596259 |
| 456 | 2.550818 | 0.096114 | 1.834826 | 1.562178 | 1.505377 | 1.505377 |
| 457 | 2.61898 | 0.084754 | 1.778025 | 1.505377 | 1.448575 | 1.584899 |
| 458 | 2.471296 | 0.027952 | 1.709863 | 1.437215 | 1.414494 | 1.482656 |
| 459 | 2.448575 | 0.005231 | 1.641701 | 1.437215 | 1.414494 | 1.369052 |
| 460 | 2.414494 | -0.02885 | 1.528097 | 1.346332 | 1.27817 | 1.380413 |
| 461 | 2.323611 | -0.01749 | 1.516737 | 1.323611 | 1.244089 | 1.244089 |
| 462 | 2.312251 | -0.09701 | 1.448575 | 1.312251 | 1.244089 | 1.255449 |
| 463 | 2.30089 | -0.11973 | 1.403133 | 1.28953 | 1.27817 | 1.210008 |
| 464 | 2.221368 | -0.10837 | 1.369052 | 1.27817 | 1.130485 | 1.244089 |
| 465 | 2.27817 | -0.16517 | 1.357692 | 1.141846 | 1.187287 | 1.255449 |
| 466 | 2.175927 | -0.21062 | 1.312251 | 1.232728 | 1.119125 | 1.164566 |
| 467 | 2.210008 | -0.21062 | 1.27817 | 1.164566 | 1.050963 | 1.175927 |
| 468 | 2.164566 | -0.2447 | 1.346332 | 1.198647 | 1.050963 | 1.175927 |
| 469 | 2.107765 | -0.25606 | 1.187287 | 1.164566 | 0.982801 | 1.096404 |
| 470 | 2.085044 | -0.29014 | 1.221368 | 1.119125 | 0.982801 | 1.085044 |
| 471 | 2.016882 | -0.32422 | 1.141846 | 1.039603 | 0.982801 | 1.039603 |
| 472 | 2.050963 | -0.3583 | 1.198647 | 1.062323 | 0.994161 | 1.039603 |
| 473 | 1.971441 | -0.31286 | 1.073684 | 0.96008 | 0.93736 | 1.005522 |
| 474 | 2.005522 | -0.32422 | 1.119125 | 1.039603 | 0.891918 | 1.028242 |
| 475 | 1.94872 | -0.42646 | 1.096404 | 0.925999 | 0.891918 | 0.94872 |
| 476 | 1.93736 | -0.42646 | 1.062323 | 0.982801 | 0.812396 | 0.982801 |
| 477 | 1.914639 | -0.46054 | 1.062323 | 0.891918 | 0.891918 | 0.93736 |
| 478 | 1.914639 | -0.5287 | 1.005522 | 0.93736 | 0.846477 | 0.835117 |
| 479 | 1.903279 | -0.56279 | 1.028242 | 0.880558 | 0.801036 | 0.846477 |
| 480 | 1.869198 | -0.56279 | 0.994161 | 0.903279 | 0.789675 | 0.846477 |
| 481 | 1.846477 | -0.61959 | 0.94872 | 0.857837 | 0.789675 | 0.857837 |
| 482 | 1.846477 | -0.58551 | 1.039603 | 0.857837 | 0.732874 | 0.801036 |
| 483 | 1.835117 | -0.63095 | 0.982801 | 0.801036 | 0.766955 | 0.744234 |
| 484 | 1.789675 | -0.60823 | 1.039603 | 0.766955 | 0.766955 | 0.812396 |
| 485 | 1.812396 | -0.74455 | 0.846477 | 0.732874 | 0.676072 | 0.766955 |
| 486 | 1.755594 | -0.72183 | 0.94872 | 0.778315 | 0.653351 | 0.755594 |
| 487 | 1.846477 | -0.73319 | 0.903279 | 0.721513 | 0.630631 | 0.664712 |
| 488 | 1.766955 | -0.76727 | 0.891918 | 0.778315 | 0.676072 | 0.653351 |
| 489 | 1.744234 | -0.76727 | 0.880558 | 0.698793 | 0.653351 | 0.59655 |
| 490 | 1.698793 | -0.82407 | 0.812396 | 0.766955 | 0.687432 | 0.573829 |
| 491 | 1.721513 | -0.85815 | 0.789675 | 0.687432 | 0.60791 | 0.437505 |
| 492 | 1.676072 | -0.85815 | 0.846477 | 0.721513 | 0.687432 | 0.494306 |
| 493 | 1.744234 | -0.85815 | 0.835117 | 0.687432 | 0.59655 | 0.528388 |
| 494 | 1.687432 | -0.88088 | 0.857837 | 0.687432 | 0.59655 | 0.573829 |
| 495 | 1.766955 | -0.86952 | 0.857837 | 0.698793 | 0.630631 | 0.426144 |
| 496 | 1.755594 | -0.85815 | 0.812396 | 0.630631 | 0.59655 | 0.471586 |
| 497 | 1.721513 | -0.89224 | 0.778315 | 0.653351 | 0.641991 | 0.482946 |
| 498 | 1.721513 | -0.94904 | 0.823756 | 0.664712 | 0.562469 | 0.392063 |
| 499 | 1.710153 | -0.93768 | 0.789675 | 0.676072 | 0.528388 | 0.471586 |
| 500 | 1.721513 | -0.99448 | 0.766955 | 0.664712 | 0.551108 | 0.517027 |
| 501 | 1.653351 | -0.91496 | 0.755594 | 0.61927 | 0.539748 | 0.357982 |
| 502 | 1.755594 | -1.03992 | 0.698793 | 0.641991 | 0.551108 | 0.448865 |
| 503 | 1.698793 | -0.98312 | 0.676072 | 0.585189 | 0.562469 | 0.369343 |
| 504 | 1.676072 | -0.99448 | 0.721513 | 0.59655 | 0.585189 | 0.392063 |
| 505 | 1.732874 | -1.05128 | 0.641991 | 0.61927 | 0.60791 | 0.403424 |
| 506 | 1.710153 | -1.02856 | 0.710153 | 0.573829 | 0.59655 | 0.414784 |
| 507 | 1.59655 | -1.00584 | 0.653351 | 0.585189 | 0.585189 | 0.403424 |
| 508 | 1.744234 | -1.05128 | 0.641991 | 0.517027 | 0.664712 | 0.437505 |
| 509 | 1.61927 | -0.98312 | 0.573829 | 0.562469 | 0.630631 | 0.403424 |
| 510 | 1.698793 | -1.08536 | 0.732874 | 0.517027 | 0.585189 | 0.414784 |
| 511 | 1.59655 | -1.11944 | 0.687432 | 0.59655 | 0.573829 | 0.482946 |
| 512 | 1.630631 | -1.08536 | 0.698793 | 0.551108 | 0.59655 | 0.392063 |
| 513 | 1.562469 | -1.09672 | 0.664712 | 0.562469 | 0.585189 | 0.357982 |
| 514 | 1.641991 | -1.02856 | 0.641991 | 0.517027 | 0.630631 | 0.448865 |
| 515 | 1.551108 | -1.08536 | 0.676072 | 0.551108 | 0.630631 | 0.403424 |
| 516 | 1.664712 | -1.08536 | 0.630631 | 0.573829 | 0.59655 | 0.414784 |
| 517 | 1.585189 | -1.11944 | 0.664712 | 0.460225 | 0.573829 | 0.414784 |
| 518 | 1.641991 | -1.14216 | 0.630631 | 0.505667 | 0.585189 | 0.335262 |
| 519 | 1.539748 | -1.05128 | 0.59655 | 0.551108 | 0.539748 | 0.380703 |
| 520 | 1.539748 | -1.074 | 0.60791 | 0.528388 | 0.551108 | 0.414784 |
| 521 | 1.494306 | -1.16488 | 0.573829 | 0.494306 | 0.585189 | 0.346622 |
| 522 | 1.494306 | -1.15352 | 0.573829 | 0.517027 | 0.494306 | 0.403424 |
| 523 | 1.471586 | -1.09672 | 0.59655 | 0.562469 | 0.59655 | 0.426144 |
| 524 | 1.517027 | -1.1876 | 0.59655 | 0.460225 | 0.551108 | 0.392063 |
| 525 | 1.494306 | -1.19896 | 0.61927 | 0.460225 | 0.482946 | 0.437505 |
| 526 | 1.528388 | -1.16488 | 0.573829 | 0.539748 | 0.448865 | 0.357982 |
| 527 | 1.448865 | -1.25577 | 0.539748 | 0.471586 | 0.505667 | 0.437505 |
| 528 | 1.426144 | -1.23305 | 0.517027 | 0.471586 | 0.494306 | 0.335262 |
| 529 | 1.414784 | -1.1876 | 0.573829 | 0.482946 | 0.437505 | 0.403424 |
| 530 | 1.494306 | -1.24441 | 0.539748 | 0.426144 | 0.426144 | 0.357982 |
| 531 | 1.414784 | -1.24441 | 0.505667 | 0.505667 | 0.437505 | 0.357982 |
| 532 | 1.437505 | -1.22169 | 0.505667 | 0.414784 | 0.528388 | 0.323901 |
| 533 | 1.471586 | -1.1876 | 0.460225 | 0.392063 | 0.448865 | 0.27846 |
| 534 | 1.426144 | -1.26713 | 0.494306 | 0.494306 | 0.403424 | 0.357982 |
| 535 | 1.437505 | -1.25577 | 0.505667 | 0.482946 | 0.357982 | 0.312541 |
| 536 | 1.426144 | -1.27849 | 0.460225 | 0.437505 | 0.403424 | 0.2671 |
| 537 | 1.380703 | -1.31257 | 0.426144 | 0.426144 | 0.392063 | 0.312541 |
| 538 | 1.380703 | -1.32393 | 0.414784 | 0.482946 | 0.482946 | 0.27846 |
| 539 | 1.357982 | -1.32393 | 0.460225 | 0.448865 | 0.392063 | 0.335262 |
| 540 | 1.346622 | -1.33529 | 0.471586 | 0.380703 | 0.357982 | 0.2671 |
| 541 | 1.357982 | -1.35801 | 0.426144 | 0.460225 | 0.357982 | 0.27846 |
| 542 | 1.323901 | -1.36937 | 0.437505 | 0.448865 | 0.392063 | 0.335262 |
| 543 | 1.312541 | -1.31257 | 0.392063 | 0.460225 | 0.426144 | 0.221658 |
| 544 | 1.323901 | -1.36937 | 0.403424 | 0.426144 | 0.323901 | 0.255739 |
| 545 | 1.312541 | -1.36937 | 0.426144 | 0.494306 | 0.312541 | 0.255739 |
| 546 | 1.323901 | -1.38073 | 0.426144 | 0.482946 | 0.335262 | 0.210298 |
| 547 | 1.233019 | -1.39209 | 0.403424 | 0.494306 | 0.323901 | 0.255739 |
| 548 | 1.27846 | -1.43753 | 0.403424 | 0.551108 | 0.380703 | 0.176217 |
| 549 | 1.255739 | -1.47161 | 0.414784 | 0.448865 | 0.2671 | 0.221658 |
| 550 | 1.323901 | -1.46025 | 0.414784 | 0.482946 | 0.346622 | 0.198938 |
| 551 | 1.27846 | -1.42617 | 0.369343 | 0.460225 | 0.28982 | 0.221658 |
| 552 | 1.187577 | -1.48297 | 0.414784 | 0.448865 | 0.27846 | 0.244379 |
| 553 | 1.233019 | -1.53978 | 0.414784 | 0.437505 | 0.301181 | 0.187577 |
| 554 | 1.221658 | -1.50569 | 0.403424 | 0.426144 | 0.27846 | 0.233019 |
| 555 | 1.198938 | -1.52841 | 0.392063 | 0.369343 | 0.323901 | 0.198938 |
| 556 | 1.244379 | -1.65338 | 0.369343 | 0.448865 | 0.335262 | 0.198938 |
| 557 | 1.221658 | -1.65338 | 0.482946 | 0.403424 | 0.301181 | 0.153496 |
| 558 | 1.187577 | -1.6193 | 0.369343 | 0.403424 | 0.255739 | 0.187577 |
| 559 | 1.198938 | -1.63066 | 0.403424 | 0.414784 | 0.335262 | 0.153496 |
| 560 | 1.233019 | -1.68746 | 0.369343 | 0.392063 | 0.357982 | 0.233019 |
| 561 | 1.221658 | -1.66474 | 0.357982 | 0.357982 | 0.2671 | 0.221658 |
| 562 | 1.244379 | -1.65338 | 0.414784 | 0.357982 | 0.27846 | 0.073974 |
| 563 | 1.176217 | -1.7329 | 0.482946 | 0.380703 | 0.28982 | 0.119415 |
| 564 | 1.164857 | -1.69882 | 0.482946 | 0.346622 | 0.28982 | 0.108055 |
| 565 | 1.255739 | -1.75562 | 0.335262 | 0.448865 | 0.301181 | 0.164857 |
| 566 | 1.198938 | -1.7329 | 0.380703 | 0.369343 | 0.27846 | 0.153496 |
| 567 | 1.187577 | -1.7329 | 0.437505 | 0.346622 | 0.198938 | 0.130776 |
| 568 | 1.176217 | -1.6761 | 0.414784 | 0.369343 | 0.255739 | 0.176217 |
| 569 | 1.108055 | -1.80106 | 0.369343 | 0.335262 | 0.27846 | 0.176217 |
| 570 | 1.176217 | -1.74426 | 0.323901 | 0.369343 | 0.28982 | 0.130776 |
| 571 | 1.198938 | -1.75562 | 0.369343 | 0.312541 | 0.221658 | 0.233019 |
| 572 | 1.198938 | -1.75562 | 0.380703 | 0.255739 | 0.2671 | 0.187577 |
| 573 | 1.108055 | -1.81242 | 0.312541 | 0.210298 | 0.2671 | 0.119415 |
| 574 | 1.187577 | -1.7897 | 0.323901 | 0.323901 | 0.255739 | 0.142136 |
| 575 | 1.119415 | -1.83514 | 0.301181 | 0.210298 | 0.233019 | 0.130776 |
| 576 | 1.164857 | -1.83514 | 0.301181 | 0.210298 | 0.255739 | 0.187577 |
| 577 | 1.130776 | -1.8465 | 0.426144 | 0.233019 | 0.28982 | 0.130776 |
| 578 | 1.164857 | -1.82378 | 0.335262 | 0.28982 | 0.2671 | 0.233019 |
| 579 | 1.108055 | -1.82378 | 0.255739 | 0.380703 | 0.323901 | 0.187577 |
| 580 | 1.062614 | -1.7329 | 0.380703 | 0.244379 | 0.233019 | 0.176217 |
| 581 | 1.130776 | -1.77834 | 0.28982 | 0.221658 | 0.233019 | 0.210298 |
| 582 | 1.130776 | -1.8465 | 0.2671 | 0.255739 | 0.244379 | 0.210298 |
| 583 | 1.119415 | -1.81242 | 0.233019 | 0.233019 | 0.233019 | 0.244379 |
| 584 | 1.085334 | -1.77834 | 0.28982 | 0.312541 | 0.2671 | 0.198938 |
| 585 | 1.062614 | -1.80106 | 0.301181 | 0.233019 | 0.255739 | 0.176217 |
| 586 | 1.108055 | -1.77834 | 0.28982 | 0.210298 | 0.27846 | 0.187577 |
| 587 | 1.085334 | -1.7897 | 0.233019 | 0.312541 | 0.198938 | 0.255739 |
| 588 | 1.005812 | -1.81242 | 0.28982 | 0.210298 | 0.233019 | 0.28982 |
| 589 | 1.039893 | -1.83514 | 0.244379 | 0.176217 | 0.221658 | 0.312541 |
| 590 | 1.039893 | -1.75562 | 0.233019 | 0.255739 | 0.221658 | 0.323901 |
| 591 | 1.017172 | -1.82378 | 0.210298 | 0.198938 | 0.255739 | 0.221658 |
| 592 | 0.994452 | -1.8465 | 0.233019 | 0.221658 | 0.221658 | 0.255739 |
| 593 | 0.93765 | -1.82378 | 0.255739 | 0.233019 | 0.176217 | 0.210298 |
| 594 | 0.994452 | -1.77834 | 0.301181 | 0.27846 | 0.176217 | 0.255739 |
| 595 | 0.994452 | -1.88059 | 0.2671 | 0.221658 | 0.153496 | 0.255739 |
| 596 | 0.93765 | -1.86922 | 0.130776 | 0.233019 | 0.210298 | 0.233019 |
| 597 | 1.005812 | -1.76698 | 0.244379 | 0.255739 | 0.187577 | 0.323901 |
| 598 | 0.994452 | -1.75562 | 0.221658 | 0.221658 | 0.085334 | 0.312541 |
| 599 | 0.983091 | -1.83514 | 0.301181 | 0.198938 | 0.108055 | 0.27846 |
| 600 | 1.005812 | -1.83514 | 0.221658 | 0.233019 | 0.096695 | 0.27846 |
| 601 | 0.94901 | -1.86922 | 0.221658 | 0.255739 | 0.073974 | 0.312541 |
| 602 | 0.94901 | -1.81242 | 0.210298 | 0.27846 | 0.039893 | 0.301181 |
| 603 | 1.062614 | -1.81242 | 0.255739 | 0.27846 | 0.108055 | 0.221658 |
| 604 | 0.93765 | -1.83514 | 0.301181 | 0.221658 | 0.085334 | 0.301181 |
| 605 | 0.971731 | -1.81242 | 0.2671 | 0.312541 | 0.096695 | 0.2671 |
| 606 | 1.028533 | -1.77834 | 0.27846 | 0.346622 | 0.119415 | 0.27846 |
| 607 | 1.005812 | -1.76698 | 0.28982 | 0.27846 | 0.119415 | 0.2671 |
| 608 | 1.051253 | -1.80106 | 0.221658 | 0.380703 | 0.153496 | 0.244379 |
| 609 | 1.017172 | -1.7329 | 0.255739 | 0.357982 | 0.096695 | 0.312541 |
| 610 | 1.073974 | -1.64202 | 0.323901 | 0.28982 | 0.142136 | 0.335262 |
| 611 | 1.096695 | -1.71018 | 0.301181 | 0.346622 | 0.142136 | 0.28982 |
| 612 | 1.198938 | -1.71018 | 0.28982 | 0.323901 | 0.130776 | 0.2671 |
| 613 | 1.108055 | -1.66474 | 0.335262 | 0.346622 | 0.164857 | 0.2671 |
| 614 | 1.085334 | -1.68746 | 0.244379 | 0.346622 | 0.153496 | 0.244379 |
| 615 | 1.130776 | -1.71018 | 0.301181 | 0.403424 | 0.153496 | 0.323901 |
| 616 | 1.153496 | -1.71018 | 0.357982 | 0.369343 | 0.176217 | 0.335262 |
| 617 | 1.164857 | -1.72154 | 0.357982 | 0.346622 | 0.198938 | 0.198938 |
| 618 | 1.130776 | -1.66474 | 0.335262 | 0.403424 | 0.198938 | 0.2671 |
| 619 | 1.176217 | -1.66474 | 0.323901 | 0.335262 | 0.119415 | 0.346622 |
| 620 | 1.153496 | -1.69882 | 0.369343 | 0.403424 | 0.221658 | 0.312541 |
| 621 | 1.210298 | -1.69882 | 0.403424 | 0.482946 | 0.244379 | 0.28982 |
| 622 | 1.233019 | -1.6193 | 0.414784 | 0.426144 | 0.244379 | 0.301181 |
| 623 | 1.221658 | -1.6193 | 0.357982 | 0.448865 | 0.2671 | 0.357982 |
| 624 | 1.153496 | -1.69882 | 0.380703 | 0.403424 | 0.27846 | 0.369343 |
| 625 | 1.255739 | -1.68746 | 0.392063 | 0.460225 | 0.357982 | 0.323901 |
| 626 | 1.244379 | -1.63066 | 0.346622 | 0.426144 | 0.312541 | 0.460225 |
| 627 | 1.255739 | -1.65338 | 0.437505 | 0.482946 | 0.255739 | 0.414784 |
| 628 | 1.27846 | -1.6193 | 0.414784 | 0.448865 | 0.244379 | 0.414784 |
| 629 | 1.301181 | -1.60794 | 0.448865 | 0.392063 | 0.27846 | 0.380703 |
| 630 | 1.2671 | -1.60794 | 0.482946 | 0.471586 | 0.312541 | 0.437505 |
| 631 | 1.312541 | -1.5625 | 0.482946 | 0.471586 | 0.392063 | 0.403424 |
| 632 | 1.346622 | -1.57386 | 0.426144 | 0.414784 | 0.414784 | 0.460225 |
| 633 | 1.335262 | -1.53978 | 0.494306 | 0.437505 | 0.312541 | 0.403424 |
| 634 | 1.2671 | -1.59658 | 0.460225 | 0.448865 | 0.380703 | 0.369343 |
| 635 | 1.323901 | -1.58522 | 0.505667 | 0.517027 | 0.357982 | 0.482946 |
| 636 | 1.312541 | -1.5625 | 0.494306 | 0.471586 | 0.346622 | 0.414784 |
| 637 | 1.392063 | -1.5625 | 0.528388 | 0.346622 | 0.357982 | 0.414784 |
| 638 | 1.346622 | -1.51705 | 0.505667 | 0.414784 | 0.437505 | 0.437505 |
| 639 | 1.357982 | -1.50569 | 0.471586 | 0.426144 | 0.437505 | 0.403424 |
| 640 | 1.403424 | -1.47161 | 0.448865 | 0.426144 | 0.392063 | 0.392063 |
| 641 | 1.369343 | -1.57386 | 0.528388 | 0.403424 | 0.460225 | 0.448865 |
| 642 | 1.437505 | -1.51705 | 0.505667 | 0.426144 | 0.460225 | 0.448865 |
| 643 | 1.392063 | -1.51705 | 0.482946 | 0.448865 | 0.460225 | 0.437505 |
| 644 | 1.392063 | -1.47161 | 0.460225 | 0.437505 | 0.460225 | 0.482946 |
| 645 | 1.414784 | -1.41481 | 0.517027 | 0.460225 | 0.414784 | 0.505667 |
| 646 | 1.494306 | -1.47161 | 0.539748 | 0.482946 | 0.437505 | 0.505667 |
| 647 | 1.471586 | -1.35801 | 0.562469 | 0.482946 | 0.505667 | 0.494306 |
| 648 | 1.528388 | -1.42617 | 0.573829 | 0.448865 | 0.482946 | 0.494306 |
| 649 | 1.517027 | -1.47161 | 0.517027 | 0.517027 | 0.528388 | 0.505667 |
| 650 | 1.517027 | -1.39209 | 0.517027 | 0.517027 | 0.505667 | 0.562469 |
| 651 | 1.517027 | -1.35801 | 0.528388 | 0.517027 | 0.562469 | 0.585189 |
| 652 | 1.460225 | -1.31257 | 0.505667 | 0.528388 | 0.551108 | 0.573829 |
| 653 | 1.551108 | -1.40345 | 0.494306 | 0.517027 | 0.539748 | 0.60791 |
| 654 | 1.573829 | -1.30121 | 0.460225 | 0.551108 | 0.528388 | 0.539748 |
| 655 | 1.539748 | -1.30121 | 0.482946 | 0.562469 | 0.505667 | 0.562469 |
| 656 | 1.551108 | -1.27849 | 0.494306 | 0.562469 | 0.573829 | 0.505667 |
| 657 | 1.494306 | -1.30121 | 0.471586 | 0.562469 | 0.562469 | 0.664712 |
| 658 | 1.585189 | -1.30121 | 0.517027 | 0.551108 | 0.59655 | 0.59655 |
| 659 | 1.539748 | -1.25577 | 0.494306 | 0.562469 | 0.539748 | 0.573829 |
| 660 | 1.528388 | -1.32393 | 0.505667 | 0.573829 | 0.61927 | 0.664712 |
| 661 | 1.585189 | -1.24441 | 0.448865 | 0.551108 | 0.562469 | 0.562469 |
| 662 | 1.59655 | -1.26713 | 0.471586 | 0.585189 | 0.585189 | 0.653351 |
| 663 | 1.562469 | -1.27849 | 0.551108 | 0.59655 | 0.551108 | 0.573829 |
| 664 | 1.664712 | -1.23305 | 0.482946 | 0.573829 | 0.539748 | 0.60791 |
| 665 | 1.61927 | -1.27849 | 0.539748 | 0.562469 | 0.573829 | 0.59655 |
| 666 | 1.539748 | -1.27849 | 0.482946 | 0.59655 | 0.630631 | 0.60791 |
| 667 | 1.641991 | -1.30121 | 0.517027 | 0.698793 | 0.585189 | 0.551108 |
| 668 | 1.573829 | -1.26713 | 0.517027 | 0.562469 | 0.528388 | 0.59655 |
| 669 | 1.60791 | -1.21033 | 0.539748 | 0.710153 | 0.59655 | 0.585189 |
| 670 | 1.61927 | -1.34665 | 0.517027 | 0.653351 | 0.494306 | 0.630631 |
| 671 | 1.528388 | -1.28985 | 0.505667 | 0.585189 | 0.573829 | 0.562469 |
| 672 | 1.676072 | -1.31257 | 0.505667 | 0.630631 | 0.551108 | 0.528388 |
| 673 | 1.551108 | -1.30121 | 0.528388 | 0.562469 | 0.585189 | 0.539748 |
| 674 | 1.585189 | -1.34665 | 0.494306 | 0.641991 | 0.528388 | 0.551108 |
| 675 | 1.585189 | -1.34665 | 0.539748 | 0.551108 | 0.641991 | 0.448865 |
| 676 | 1.59655 | -1.32393 | 0.528388 | 0.59655 | 0.551108 | 0.448865 |
| 677 | 1.60791 | -1.33529 | 0.528388 | 0.60791 | 0.528388 | 0.482946 |
| 678 | 1.528388 | -1.36937 | 0.551108 | 0.573829 | 0.562469 | 0.505667 |
| 679 | 1.562469 | -1.40345 | 0.539748 | 0.59655 | 0.551108 | 0.448865 |
| 680 | 1.528388 | -1.36937 | 0.551108 | 0.641991 | 0.494306 | 0.403424 |
| 681 | 1.539748 | -1.32393 | 0.539748 | 0.539748 | 0.551108 | 0.414784 |
| 682 | 1.551108 | -1.40345 | 0.517027 | 0.61927 | 0.539748 | 0.392063 |
| 683 | 1.573829 | -1.36937 | 0.573829 | 0.60791 | 0.539748 | 0.403424 |
| 684 | 1.573829 | -1.40345 | 0.505667 | 0.494306 | 0.528388 | 0.346622 |
| 685 | 1.562469 | -1.41481 | 0.551108 | 0.630631 | 0.482946 | 0.357982 |
| 686 | 1.59655 | -1.33529 | 0.505667 | 0.585189 | 0.539748 | 0.380703 |
| 687 | 1.562469 | -1.44889 | 0.562469 | 0.482946 | 0.505667 | 0.369343 |
| 688 | 1.653351 | -1.42617 | 0.505667 | 0.664712 | 0.551108 | 0.323901 |
| 689 | 1.641991 | -1.39209 | 0.539748 | 0.59655 | 0.517027 | 0.346622 |
| 690 | 1.687432 | -1.49433 | 0.460225 | 0.551108 | 0.539748 | 0.346622 |
| 691 | 1.61927 | -1.41481 | 0.505667 | 0.573829 | 0.539748 | 0.403424 |
| 692 | 1.676072 | -1.36937 | 0.471586 | 0.551108 | 0.494306 | 0.28982 |
| 693 | 1.562469 | -1.49433 | 0.494306 | 0.539748 | 0.60791 | 0.312541 |
| 694 | 1.60791 | -1.48297 | 0.460225 | 0.551108 | 0.517027 | 0.403424 |
| 695 | 1.630631 | -1.43753 | 0.562469 | 0.539748 | 0.59655 | 0.346622 |
| 696 | 1.641991 | -1.53978 | 0.414784 | 0.494306 | 0.528388 | 0.335262 |
| 697 | 1.59655 | -1.47161 | 0.448865 | 0.517027 | 0.562469 | 0.346622 |
| 698 | 1.630631 | -1.49433 | 0.482946 | 0.562469 | 0.630631 | 0.392063 |
| 699 | 1.630631 | -1.50569 | 0.471586 | 0.528388 | 0.61927 | 0.312541 |
| 700 | 1.562469 | -1.55114 | 0.448865 | 0.471586 | 0.585189 | 0.369343 |
| 701 | 1.585189 | -1.48297 | 0.505667 | 0.562469 | 0.562469 | 0.403424 |
| 702 | 1.528388 | -1.48297 | 0.448865 | 0.505667 | 0.562469 | 0.323901 |
| 703 | 1.551108 | -1.58522 | 0.517027 | 0.448865 | 0.573829 | 0.357982 |
| 704 | 1.494306 | -1.57386 | 0.471586 | 0.482946 | 0.562469 | 0.392063 |
| 705 | 1.551108 | -1.55114 | 0.437505 | 0.448865 | 0.551108 | 0.312541 |
| 706 | 1.517027 | -1.59658 | 0.517027 | 0.460225 | 0.585189 | 0.27846 |
| 707 | 1.539748 | -1.55114 | 0.426144 | 0.414784 | 0.528388 | 0.392063 |
| 708 | 1.505667 | -1.55114 | 0.482946 | 0.471586 | 0.562469 | 0.403424 |
| 709 | 1.494306 | -1.59658 | 0.460225 | 0.471586 | 0.585189 | 0.335262 |
| 710 | 1.494306 | -1.5625 | 0.437505 | 0.426144 | 0.585189 | 0.335262 |
| 711 | 1.528388 | -1.52841 | 0.448865 | 0.448865 | 0.562469 | 0.392063 |
| 712 | 1.460225 | -1.64202 | 0.460225 | 0.414784 | 0.517027 | 0.369343 |
| 713 | 1.517027 | -1.66474 | 0.392063 | 0.448865 | 0.573829 | 0.346622 |
| 714 | 1.505667 | -1.60794 | 0.505667 | 0.482946 | 0.551108 | 0.346622 |
| 715 | 1.494306 | -1.5625 | 0.448865 | 0.505667 | 0.517027 | 0.426144 |
| 716 | 1.539748 | -1.59658 | 0.471586 | 0.517027 | 0.528388 | 0.414784 |
| 717 | 1.528388 | -1.59658 | 0.494306 | 0.505667 | 0.505667 | 0.335262 |
| 718 | 1.471586 | -1.5625 | 0.392063 | 0.460225 | 0.60791 | 0.414784 |
| 719 | 1.505667 | -1.57386 | 0.448865 | 0.551108 | 0.471586 | 0.403424 |

Table 2: P-Ѳ data for the load 3.5kW

| Ѳ | Diesel | B20 | B40 | B60 | B80 | B100 |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0.449155 | 0.392354 | -0.56221 | -0.55085 | -1.58493 | -0.70989 |
| 1 | 0.449155 | 0.27875 | -0.66445 | -0.60765 | -1.64173 | -0.75533 |
| 2 | 0.426435 | 0.312831 | -0.58493 | -0.60765 | -1.70989 | -0.78941 |
| 3 | 0.392354 | 0.324192 | -0.65309 | -0.66445 | -1.66445 | -0.78941 |
| 4 | 0.415074 | 0.312831 | -0.61901 | -0.68717 | -1.64173 | -0.82349 |
| 5 | 0.358273 | 0.26739 | -0.67581 | -0.67581 | -1.64173 | -0.74397 |
| 6 | 0.335552 | 0.290111 | -0.69853 | -0.64173 | -1.67581 | -0.78941 |
| 7 | 0.290111 | 0.290111 | -0.70989 | -0.65309 | -1.73261 | -0.75533 |
| 8 | 0.25603 | 0.27875 | -0.70989 | -0.66445 | -1.70989 | -0.75533 |
| 9 | 0.26739 | 0.26739 | -0.68717 | -0.73261 | -1.81213 | -0.78941 |
| 10 | 0.210588 | 0.25603 | -0.70989 | -0.68717 | -1.80077 | -0.81213 |
| 11 | 0.176507 | 0.25603 | -0.74397 | -0.77805 | -1.77805 | -0.92574 |
| 12 | 0.108345 | 0.301471 | -0.74397 | -0.78941 | -1.77805 | -0.90302 |
| 13 | 0.108345 | 0.233309 | -0.75533 | -0.80077 | -1.91438 | -0.92574 |
| 14 | 0.074264 | 0.25603 | -0.88029 | -0.84621 | -1.88029 | -0.9371 |
| 15 | 0.051544 | 0.199228 | -0.82349 | -0.76669 | -1.88029 | -0.85757 |
| 16 | 0.119706 | 0.233309 | -0.92574 | -0.83485 | -1.84621 | -0.94846 |
| 17 | 0.006102 | 0.210588 | -0.78941 | -0.78941 | -1.84621 | -0.95982 |
| 18 | 0.040183 | 0.210588 | -0.84621 | -0.76669 | -1.81213 | -0.97118 |
| 19 | 0.085625 | 0.187868 | -0.83485 | -0.80077 | -1.81213 | -0.9939 |
| 20 | -0.00526 | 0.176507 | -0.89166 | -0.84621 | -1.88029 | -0.97118 |
| 21 | 0.040183 | 0.27875 | -0.86893 | -0.81213 | -1.83485 | -0.98254 |
| 22 | 0.028823 | 0.312831 | -0.88029 | -0.78941 | -1.78941 | -0.90302 |
| 23 | 0.051544 | 0.233309 | -0.81213 | -0.80077 | -1.82349 | -0.95982 |
| 24 | 0.017463 | 0.25603 | -0.77805 | -0.78941 | -1.77805 | -0.91438 |
| 25 | 0.062904 | 0.25603 | -0.78941 | -0.83485 | -1.82349 | -0.95982 |
| 26 | 0.074264 | 0.25603 | -0.78941 | -0.70989 | -1.73261 | -0.92574 |
| 27 | 0.051544 | 0.290111 | -0.82349 | -0.74397 | -1.73261 | -0.9371 |
| 28 | 0.108345 | 0.25603 | -0.80077 | -0.73261 | -1.76669 | -0.91438 |
| 29 | 0.085625 | 0.290111 | -0.73261 | -0.80077 | -1.69853 | -0.98254 |
| 30 | 0.074264 | 0.221949 | -0.77805 | -0.73261 | -1.78941 | -0.98254 |
| 31 | 0.028823 | 0.244669 | -0.75533 | -0.74397 | -1.73261 | -0.91438 |
| 32 | 0.176507 | 0.27875 | -0.83485 | -0.70989 | -1.73261 | -0.90302 |
| 33 | 0.085625 | 0.301471 | -0.80077 | -0.72125 | -1.70989 | -0.86893 |
| 34 | 0.108345 | 0.244669 | -0.73261 | -0.78941 | -1.69853 | -1.01662 |
| 35 | 0.142426 | 0.25603 | -0.80077 | -0.68717 | -1.63037 | -0.88029 |
| 36 | 0.142426 | 0.210588 | -0.76669 | -0.75533 | -1.68717 | -0.91438 |
| 37 | 0.119706 | 0.233309 | -0.83485 | -0.72125 | -1.69853 | -0.83485 |
| 38 | 0.085625 | 0.233309 | -0.84621 | -0.81213 | -1.68717 | -0.81213 |
| 39 | 0.108345 | 0.210588 | -0.82349 | -0.74397 | -1.68717 | -0.81213 |
| 40 | 0.131066 | 0.25603 | -0.80077 | -0.69853 | -1.72125 | -0.78941 |
| 41 | 0.221949 | 0.26739 | -0.81213 | -0.68717 | -1.67581 | -0.80077 |
| 42 | 0.187868 | 0.210588 | -0.86893 | -0.67581 | -1.69853 | -0.82349 |
| 43 | 0.176507 | 0.301471 | -0.84621 | -0.81213 | -1.69853 | -0.69853 |
| 44 | 0.187868 | 0.221949 | -0.86893 | -0.69853 | -1.73261 | -0.77805 |
| 45 | 0.221949 | 0.233309 | -0.85757 | -0.70989 | -1.76669 | -0.75533 |
| 46 | 0.165147 | 0.25603 | -0.85757 | -0.72125 | -1.73261 | -0.73261 |
| 47 | 0.176507 | 0.210588 | -0.85757 | -0.73261 | -1.69853 | -0.74397 |
| 48 | 0.153787 | 0.210588 | -0.88029 | -0.76669 | -1.66445 | -0.73261 |
| 49 | 0.108345 | 0.301471 | -0.88029 | -0.73261 | -1.64173 | -0.73261 |
| 50 | 0.108345 | 0.199228 | -0.94846 | -0.74397 | -1.74397 | -0.78941 |
| 51 | 0.131066 | 0.290111 | -0.92574 | -0.80077 | -1.72125 | -0.75533 |
| 52 | 0.131066 | 0.176507 | -0.92574 | -0.83485 | -1.77805 | -0.78941 |
| 53 | 0.165147 | 0.26739 | -0.89166 | -0.78941 | -1.80077 | -0.78941 |
| 54 | 0.142426 | 0.290111 | -0.85757 | -0.80077 | -1.72125 | -0.75533 |
| 55 | 0.153787 | 0.176507 | -0.91438 | -0.85757 | -1.70989 | -0.85757 |
| 56 | 0.165147 | 0.26739 | -0.89166 | -0.83485 | -1.74397 | -0.67581 |
| 57 | 0.142426 | 0.176507 | -0.92574 | -0.83485 | -1.78941 | -0.75533 |
| 58 | 0.131066 | 0.187868 | -0.91438 | -0.78941 | -1.76669 | -0.74397 |
| 59 | 0.131066 | 0.221949 | -0.88029 | -0.86893 | -1.70989 | -0.81213 |
| 60 | 0.085625 | 0.25603 | -0.84621 | -0.85757 | -1.74397 | -0.84621 |
| 61 | 0.096985 | 0.25603 | -0.82349 | -0.88029 | -1.73261 | -0.68717 |
| 62 | 0.119706 | 0.244669 | -0.92574 | -0.83485 | -1.77805 | -0.80077 |
| 63 | 0.187868 | 0.244669 | -0.88029 | -0.85757 | -1.69853 | -0.80077 |
| 64 | 0.176507 | 0.221949 | -0.85757 | -0.89166 | -1.74397 | -0.83485 |
| 65 | 0.153787 | 0.244669 | -0.89166 | -0.91438 | -1.70989 | -0.77805 |
| 66 | 0.153787 | 0.199228 | -0.84621 | -0.82349 | -1.83485 | -0.81213 |
| 67 | 0.165147 | 0.210588 | -0.88029 | -0.91438 | -1.75533 | -0.73261 |
| 68 | 0.233309 | 0.26739 | -0.78941 | -0.81213 | -1.73261 | -0.83485 |
| 69 | 0.187868 | 0.26739 | -0.88029 | -0.81213 | -1.73261 | -0.83485 |
| 70 | 0.187868 | 0.221949 | -0.77805 | -0.83485 | -1.75533 | -0.78941 |
| 71 | 0.290111 | 0.233309 | -0.90302 | -0.78941 | -1.76669 | -0.78941 |
| 72 | 0.176507 | 0.244669 | -0.86893 | -0.69853 | -1.77805 | -0.85757 |
| 73 | 0.290111 | 0.176507 | -0.86893 | -0.85757 | -1.77805 | -0.82349 |
| 74 | 0.26739 | 0.301471 | -0.83485 | -0.86893 | -1.72125 | -0.80077 |
| 75 | 0.25603 | 0.26739 | -0.81213 | -0.82349 | -1.76669 | -0.78941 |
| 76 | 0.312831 | 0.244669 | -0.86893 | -0.88029 | -1.74397 | -0.78941 |
| 77 | 0.301471 | 0.301471 | -0.84621 | -0.78941 | -1.77805 | -0.77805 |
| 78 | 0.335552 | 0.324192 | -0.85757 | -0.89166 | -1.77805 | -0.86893 |
| 79 | 0.290111 | 0.358273 | -0.78941 | -0.82349 | -1.78941 | -0.85757 |
| 80 | 0.335552 | 0.301471 | -0.73261 | -0.77805 | -1.78941 | -0.76669 |
| 81 | 0.312831 | 0.324192 | -0.78941 | -0.75533 | -1.74397 | -0.72125 |
| 82 | 0.346912 | 0.27875 | -0.78941 | -0.74397 | -1.72125 | -0.82349 |
| 83 | 0.335552 | 0.27875 | -0.77805 | -0.77805 | -1.70989 | -0.83485 |
| 84 | 0.27875 | 0.335552 | -0.83485 | -0.74397 | -1.75533 | -0.82349 |
| 85 | 0.415074 | 0.346912 | -0.77805 | -0.76669 | -1.67581 | -0.77805 |
| 86 | 0.324192 | 0.290111 | -0.78941 | -0.74397 | -1.77805 | -0.77805 |
| 87 | 0.392354 | 0.301471 | -0.76669 | -0.69853 | -1.76669 | -0.76669 |
| 88 | 0.403714 | 0.415074 | -0.68717 | -0.77805 | -1.66445 | -0.74397 |
| 89 | 0.324192 | 0.221949 | -0.73261 | -0.74397 | -1.76669 | -0.73261 |
| 90 | 0.380993 | 0.301471 | -0.69853 | -0.69853 | -1.72125 | -0.74397 |
| 91 | 0.403714 | 0.403714 | -0.74397 | -0.73261 | -1.65309 | -0.70989 |
| 92 | 0.392354 | 0.26739 | -0.73261 | -0.58493 | -1.67581 | -0.83485 |
| 93 | 0.392354 | 0.426435 | -0.68717 | -0.67581 | -1.63037 | -0.81213 |
| 94 | 0.403714 | 0.290111 | -0.74397 | -0.76669 | -1.66445 | -0.69853 |
| 95 | 0.244669 | 0.312831 | -0.69853 | -0.68717 | -1.64173 | -0.74397 |
| 96 | 0.380993 | 0.369633 | -0.73261 | -0.65309 | -1.72125 | -0.83485 |
| 97 | 0.335552 | 0.244669 | -0.69853 | -0.72125 | -1.70989 | -0.69853 |
| 98 | 0.324192 | 0.27875 | -0.66445 | -0.70989 | -1.63037 | -0.78941 |
| 99 | 0.380993 | 0.25603 | -0.72125 | -0.66445 | -1.55085 | -0.77805 |
| 100 | 0.27875 | 0.233309 | -0.56221 | -0.68717 | -1.64173 | -0.73261 |
| 101 | 0.392354 | 0.301471 | -0.63037 | -0.67581 | -1.66445 | -0.83485 |
| 102 | 0.301471 | 0.233309 | -0.61901 | -0.63037 | -1.64173 | -0.74397 |
| 103 | 0.335552 | 0.119706 | -0.53948 | -0.67581 | -1.63037 | -0.77805 |
| 104 | 0.392354 | 0.335552 | -0.73261 | -0.69853 | -1.64173 | -0.69853 |
| 105 | 0.312831 | 0.233309 | -0.70989 | -0.72125 | -1.60765 | -0.73261 |
| 106 | 0.369633 | 0.221949 | -0.67581 | -0.60765 | -1.58493 | -0.75533 |
| 107 | 0.415074 | 0.221949 | -0.74397 | -0.61901 | -1.65309 | -0.72125 |
| 108 | 0.380993 | 0.233309 | -0.66445 | -0.66445 | -1.72125 | -0.69853 |
| 109 | 0.415074 | 0.233309 | -0.65309 | -0.66445 | -1.66445 | -0.69853 |
| 110 | 0.471876 | 0.290111 | -0.64173 | -0.64173 | -1.64173 | -0.70989 |
| 111 | 0.380993 | 0.221949 | -0.55085 | -0.64173 | -1.64173 | -0.67581 |
| 112 | 0.392354 | 0.25603 | -0.65309 | -0.65309 | -1.67581 | -0.67581 |
| 113 | 0.369633 | 0.244669 | -0.60765 | -0.64173 | -1.69853 | -0.68717 |
| 114 | 0.426435 | 0.244669 | -0.56221 | -0.63037 | -1.70989 | -0.72125 |
| 115 | 0.403714 | 0.210588 | -0.73261 | -0.63037 | -1.68717 | -0.65309 |
| 116 | 0.426435 | 0.26739 | -0.73261 | -0.60765 | -1.76669 | -0.70989 |
| 117 | 0.358273 | 0.26739 | -0.65309 | -0.70989 | -1.69853 | -0.72125 |
| 118 | 0.415074 | 0.25603 | -0.66445 | -0.68717 | -1.70989 | -0.70989 |
| 119 | 0.403714 | 0.244669 | -0.56221 | -0.67581 | -1.75533 | -0.74397 |
| 120 | 0.312831 | 0.210588 | -0.63037 | -0.64173 | -1.80077 | -0.66445 |
| 121 | 0.369633 | 0.210588 | -0.61901 | -0.59629 | -1.76669 | -0.73261 |
| 122 | 0.403714 | 0.25603 | -0.61901 | -0.61901 | -1.82349 | -0.68717 |
| 123 | 0.324192 | 0.27875 | -0.65309 | -0.58493 | -1.70989 | -0.69853 |
| 124 | 0.369633 | 0.25603 | -0.65309 | -0.66445 | -1.64173 | -0.68717 |
| 125 | 0.415074 | 0.27875 | -0.58493 | -0.63037 | -1.72125 | -0.67581 |
| 126 | 0.369633 | 0.27875 | -0.59629 | -0.64173 | -1.69853 | -0.66445 |
| 127 | 0.380993 | 0.290111 | -0.60765 | -0.58493 | -1.77805 | -0.68717 |
| 128 | 0.449155 | 0.25603 | -0.53948 | -0.55085 | -1.68717 | -0.69853 |
| 129 | 0.426435 | 0.346912 | -0.55085 | -0.61901 | -1.77805 | -0.72125 |
| 130 | 0.483236 | 0.312831 | -0.5054 | -0.56221 | -1.70989 | -0.74397 |
| 131 | 0.403714 | 0.290111 | -0.4486 | -0.56221 | -1.69853 | -0.77805 |
| 132 | 0.380993 | 0.415074 | -0.42588 | -0.52812 | -1.66445 | -0.81213 |
| 133 | 0.392354 | 0.301471 | -0.43724 | -0.53948 | -1.60765 | -0.83485 |
| 134 | 0.403714 | 0.324192 | -0.48268 | -0.58493 | -1.64173 | -0.78941 |
| 135 | 0.449155 | 0.369633 | -0.5054 | -0.53948 | -1.66445 | -0.85757 |
| 136 | 0.403714 | 0.26739 | -0.51676 | -0.57357 | -1.63037 | -0.80077 |
| 137 | 0.449155 | 0.324192 | -0.43724 | -0.55085 | -1.70989 | -0.73261 |
| 138 | 0.551398 | 0.301471 | -0.45996 | -0.53948 | -1.65309 | -0.77805 |
| 139 | 0.449155 | 0.27875 | -0.43724 | -0.53948 | -1.57357 | -0.74397 |
| 140 | 0.517317 | 0.392354 | -0.41452 | -0.48268 | -1.70989 | -0.77805 |
| 141 | 0.494597 | 0.380993 | -0.4486 | -0.5054 | -1.59629 | -0.80077 |
| 142 | 0.426435 | 0.312831 | -0.4486 | -0.45996 | -1.58493 | -0.78941 |
| 143 | 0.460516 | 0.346912 | -0.42588 | -0.40316 | -1.67581 | -0.74397 |
| 144 | 0.471876 | 0.324192 | -0.36908 | -0.41452 | -1.65309 | -0.75533 |
| 145 | 0.483236 | 0.392354 | -0.3918 | -0.47132 | -1.68717 | -0.73261 |
| 146 | 0.505957 | 0.380993 | -0.43724 | -0.3918 | -1.57357 | -0.67581 |
| 147 | 0.483236 | 0.415074 | -0.3918 | -0.42588 | -1.53948 | -0.73261 |
| 148 | 0.528678 | 0.415074 | -0.41452 | -0.42588 | -1.57357 | -0.77805 |
| 149 | 0.460516 | 0.415074 | -0.3918 | -0.3918 | -1.53948 | -0.73261 |
| 150 | 0.551398 | 0.449155 | -0.42588 | -0.40316 | -1.57357 | -0.68717 |
| 151 | 0.437795 | 0.483236 | -0.43724 | -0.32364 | -1.58493 | -0.69853 |
| 152 | 0.415074 | 0.483236 | -0.36908 | -0.34636 | -1.60765 | -0.64173 |
| 153 | 0.517317 | 0.437795 | -0.3918 | -0.40316 | -1.55085 | -0.68717 |
| 154 | 0.449155 | 0.392354 | -0.3918 | -0.3918 | -1.56221 | -0.70989 |
| 155 | 0.437795 | 0.415074 | -0.41452 | -0.42588 | -1.52812 | -0.68717 |
| 156 | 0.437795 | 0.415074 | -0.41452 | -0.41452 | -1.56221 | -0.68717 |
| 157 | 0.471876 | 0.437795 | -0.47132 | -0.36908 | -1.56221 | -0.68717 |
| 158 | 0.494597 | 0.415074 | -0.42588 | -0.41452 | -1.56221 | -0.60765 |
| 159 | 0.540038 | 0.426435 | -0.3918 | -0.3918 | -1.60765 | -0.61901 |
| 160 | 0.471876 | 0.403714 | -0.38044 | -0.36908 | -1.66445 | -0.65309 |
| 161 | 0.415074 | 0.437795 | -0.42588 | -0.42588 | -1.57357 | -0.60765 |
| 162 | 0.449155 | 0.426435 | -0.3918 | -0.43724 | -1.60765 | -0.72125 |
| 163 | 0.426435 | 0.426435 | -0.41452 | -0.35772 | -1.48268 | -0.60765 |
| 164 | 0.403714 | 0.437795 | -0.49404 | -0.38044 | -1.4486 | -0.67581 |
| 165 | 0.392354 | 0.449155 | -0.47132 | -0.35772 | -1.47132 | -0.64173 |
| 166 | 0.403714 | 0.483236 | -0.45996 | -0.3918 | -1.4486 | -0.58493 |
| 167 | 0.369633 | 0.471876 | -0.42588 | -0.35772 | -1.5054 | -0.53948 |
| 168 | 0.335552 | 0.449155 | -0.48268 | -0.38044 | -1.47132 | -0.60765 |
| 169 | 0.449155 | 0.460516 | -0.3918 | -0.36908 | -1.43724 | -0.58493 |
| 170 | 0.369633 | 0.483236 | -0.38044 | -0.36908 | -1.40316 | -0.59629 |
| 171 | 0.369633 | 0.449155 | -0.45996 | -0.43724 | -1.5054 | -0.63037 |
| 172 | 0.346912 | 0.449155 | -0.4486 | -0.35772 | -1.49404 | -0.59629 |
| 173 | 0.358273 | 0.426435 | -0.40316 | -0.40316 | -1.51676 | -0.57357 |
| 174 | 0.358273 | 0.437795 | -0.42588 | -0.42588 | -1.41452 | -0.59629 |
| 175 | 0.392354 | 0.460516 | -0.47132 | -0.35772 | -1.41452 | -0.53948 |
| 176 | 0.358273 | 0.426435 | -0.38044 | -0.38044 | -1.45996 | -0.55085 |
| 177 | 0.380993 | 0.449155 | -0.34636 | -0.42588 | -1.36908 | -0.48268 |
| 178 | 0.437795 | 0.494597 | -0.3918 | -0.45996 | -1.45996 | -0.52812 |
| 179 | 0.403714 | 0.449155 | -0.43724 | -0.31228 | -1.4486 | -0.53948 |
| 180 | 0.426435 | 0.471876 | -0.42588 | -0.35772 | -1.38044 | -0.52812 |
| 181 | 0.415074 | 0.551398 | -0.4486 | -0.32364 | -1.51676 | -0.59629 |
| 182 | 0.403714 | 0.562759 | -0.40316 | -0.35772 | -1.43724 | -0.47132 |
| 183 | 0.426435 | 0.460516 | -0.47132 | -0.35772 | -1.4486 | -0.49404 |
| 184 | 0.449155 | 0.505957 | -0.4486 | -0.38044 | -1.49404 | -0.48268 |
| 185 | 0.380993 | 0.59684 | -0.43724 | -0.3918 | -1.45996 | -0.5054 |
| 186 | 0.415074 | 0.528678 | -0.43724 | -0.31228 | -1.43724 | -0.43724 |
| 187 | 0.426435 | 0.585479 | -0.42588 | -0.34636 | -1.48268 | -0.5054 |
| 188 | 0.392354 | 0.6082 | -0.40316 | -0.28956 | -1.45996 | -0.52812 |
| 189 | 0.426435 | 0.59684 | -0.36908 | -0.38044 | -1.42588 | -0.4486 |
| 190 | 0.460516 | 0.61956 | -0.40316 | -0.32364 | -1.38044 | -0.4486 |
| 191 | 0.471876 | 0.642281 | -0.40316 | -0.41452 | -1.4486 | -0.5054 |
| 192 | 0.562759 | 0.59684 | -0.41452 | -0.24412 | -1.42588 | -0.47132 |
| 193 | 0.494597 | 0.61956 | -0.38044 | -0.34636 | -1.40316 | -0.49404 |
| 194 | 0.346912 | 0.744524 | -0.35772 | -0.30092 | -1.36908 | -0.52812 |
| 195 | 0.528678 | 0.699083 | -0.28956 | -0.31228 | -1.38044 | -0.42588 |
| 196 | 0.517317 | 0.642281 | -0.32364 | -0.36908 | -1.35772 | -0.43724 |
| 197 | 0.562759 | 0.710443 | -0.32364 | -0.25548 | -1.35772 | -0.48268 |
| 198 | 0.517317 | 0.642281 | -0.28956 | -0.30092 | -1.35772 | -0.45996 |
| 199 | 0.471876 | 0.653642 | -0.32364 | -0.2782 | -1.35772 | -0.51676 |
| 200 | 0.551398 | 0.710443 | -0.34636 | -0.28956 | -1.335 | -0.52812 |
| 201 | 0.505957 | 0.721804 | -0.34636 | -0.35772 | -1.3918 | -0.5054 |
| 202 | 0.562759 | 0.687723 | -0.30092 | -0.31228 | -1.41452 | -0.4486 |
| 203 | 0.551398 | 0.676362 | -0.25548 | -0.26684 | -1.36908 | -0.47132 |
| 204 | 0.562759 | 0.665002 | -0.28956 | -0.26684 | -1.36908 | -0.45996 |
| 205 | 0.505957 | 0.676362 | -0.31228 | -0.23276 | -1.30092 | -0.4486 |
| 206 | 0.540038 | 0.676362 | -0.32364 | -0.26684 | -1.26684 | -0.4486 |
| 207 | 0.517317 | 0.665002 | -0.26684 | -0.28956 | -1.23276 | -0.4486 |
| 208 | 0.574119 | 0.721804 | -0.26684 | -0.26684 | -1.21003 | -0.38044 |
| 209 | 0.59684 | 0.676362 | -0.32364 | -0.30092 | -1.24412 | -0.40316 |
| 210 | 0.562759 | 0.744524 | -0.2782 | -0.25548 | -1.23276 | -0.43724 |
| 211 | 0.630921 | 0.733164 | -0.335 | -0.2214 | -1.2782 | -0.35772 |
| 212 | 0.61956 | 0.721804 | -0.35772 | -0.14187 | -1.24412 | -0.40316 |
| 213 | 0.59684 | 0.733164 | -0.31228 | -0.28956 | -1.17595 | -0.3918 |
| 214 | 0.59684 | 0.721804 | -0.31228 | -0.19867 | -1.09643 | -0.41452 |
| 215 | 0.630921 | 0.710443 | -0.32364 | -0.25548 | -1.23276 | -0.4486 |
| 216 | 0.665002 | 0.676362 | -0.32364 | -0.18731 | -1.23276 | -0.25548 |
| 217 | 0.642281 | 0.767245 | -0.28956 | -0.2214 | -1.13051 | -0.2782 |
| 218 | 0.630921 | 0.721804 | -0.32364 | -0.18731 | -1.17595 | -0.36908 |
| 219 | 0.574119 | 0.733164 | -0.28956 | -0.26684 | -1.11915 | -0.34636 |
| 220 | 0.721804 | 0.755885 | -0.335 | -0.23276 | -1.16459 | -0.21003 |
| 221 | 0.721804 | 0.778605 | -0.26684 | -0.25548 | -1.17595 | -0.23276 |
| 222 | 0.687723 | 0.721804 | -0.32364 | -0.2214 | -1.11915 | -0.24412 |
| 223 | 0.687723 | 0.710443 | -0.34636 | -0.17595 | -1.16459 | -0.24412 |
| 224 | 0.733164 | 0.710443 | -0.32364 | -0.23276 | -1.14187 | -0.18731 |
| 225 | 0.676362 | 0.812686 | -0.36908 | -0.2214 | -1.13051 | -0.16459 |
| 226 | 0.778605 | 0.812686 | -0.31228 | -0.18731 | -1.16459 | -0.28956 |
| 227 | 0.699083 | 0.824047 | -0.335 | -0.24412 | -1.19867 | -0.13051 |
| 228 | 0.755885 | 0.733164 | -0.26684 | -0.21003 | -1.11915 | -0.13051 |
| 229 | 0.744524 | 0.812686 | -0.25548 | -0.18731 | -1.13051 | -0.21003 |
| 230 | 0.699083 | 0.755885 | -0.21003 | -0.19867 | -1.09643 | -0.17595 |
| 231 | 0.744524 | 0.824047 | -0.31228 | -0.2214 | -1.13051 | -0.03963 |
| 232 | 0.789966 | 0.835407 | -0.21003 | -0.19867 | -1.07371 | -0.17595 |
| 233 | 0.778605 | 0.824047 | -0.24412 | -0.21003 | -1.09643 | -0.14187 |
| 234 | 0.812686 | 0.846767 | -0.24412 | -0.2214 | -1.05099 | -0.09643 |
| 235 | 0.767245 | 0.858128 | -0.24412 | -0.23276 | -0.99419 | -0.03963 |
| 236 | 0.824047 | 0.880848 | -0.24412 | -0.17595 | -1.08507 | -0.14187 |
| 237 | 0.789966 | 0.801326 | -0.2214 | -0.15323 | -1.08507 | -0.07371 |
| 238 | 0.846767 | 0.880848 | -0.24412 | -0.16459 | -1.08507 | -0.07371 |
| 239 | 0.858128 | 0.869488 | -0.14187 | -0.14187 | -1.00555 | -0.01691 |
| 240 | 0.846767 | 0.94901 | -0.17595 | -0.15323 | -0.97147 | -0.01691 |
| 241 | 0.869488 | 0.93765 | -0.11915 | -0.13051 | -1.02827 | -0.05099 |
| 242 | 0.892209 | 0.92629 | -0.11915 | -0.11915 | -0.99419 | -0.08507 |
| 243 | 0.94901 | 0.892209 | -0.11915 | -0.14187 | -0.93739 | 0.028533 |
| 244 | 0.914929 | 0.92629 | -0.08507 | -0.14187 | -1.01691 | 0.028533 |
| 245 | 0.960371 | 0.93765 | -0.07371 | -0.05099 | -0.97147 | 0.017172 |
| 246 | 0.903569 | 1.017172 | -0.01691 | -0.07371 | -0.96011 | -0.01691 |
| 247 | 0.994452 | 1.005812 | -0.03963 | -0.05099 | -0.92603 | 0.028533 |
| 248 | 0.994452 | 0.892209 | -0.03963 | -0.06235 | -0.93739 | 0.051253 |
| 249 | 1.028533 | 0.94901 | -0.03963 | 0.005812 | -0.92603 | -0.00555 |
| 250 | 1.073974 | 0.960371 | -0.00555 | 0.017172 | -0.88059 | 0.039893 |
| 251 | 1.051253 | 1.028533 | 0.051253 | -0.01691 | -0.85786 | 0.051253 |
| 252 | 1.119415 | 1.028533 | -0.01691 | 0.096695 | -0.83514 | 0.073974 |
| 253 | 1.108055 | 1.130776 | 0.108055 | 0.073974 | -0.82378 | 0.039893 |
| 254 | 1.176217 | 1.119415 | 0.130776 | 0.028533 | -0.82378 | 0.130776 |
| 255 | 1.28982 | 1.164857 | 0.176217 | 0.130776 | -0.7897 | 0.153496 |
| 256 | 1.255739 | 1.153496 | 0.176217 | 0.142136 | -0.80106 | 0.096695 |
| 257 | 1.2671 | 1.221658 | 0.2671 | 0.142136 | -0.77834 | 0.233019 |
| 258 | 1.28982 | 1.233019 | 0.255739 | 0.187577 | -0.7897 | 0.210298 |
| 259 | 1.380703 | 1.244379 | 0.221658 | 0.233019 | -0.7329 | 0.233019 |
| 260 | 1.369343 | 1.27846 | 0.255739 | 0.221658 | -0.71018 | 0.255739 |
| 261 | 1.437505 | 1.255739 | 0.27846 | 0.28982 | -0.65338 | 0.255739 |
| 262 | 1.482946 | 1.369343 | 0.346622 | 0.301181 | -0.59658 | 0.2671 |
| 263 | 1.471586 | 1.437505 | 0.312541 | 0.357982 | -0.59658 | 0.312541 |
| 264 | 1.482946 | 1.369343 | 0.392063 | 0.426144 | -0.6193 | 0.346622 |
| 265 | 1.494306 | 1.392063 | 0.380703 | 0.426144 | -0.51705 | 0.392063 |
| 266 | 1.61927 | 1.460225 | 0.562469 | 0.448865 | -0.48297 | 0.426144 |
| 267 | 1.641991 | 1.494306 | 0.562469 | 0.482946 | -0.41481 | 0.471586 |
| 268 | 1.61927 | 1.482946 | 0.59655 | 0.505667 | -0.38073 | 0.460225 |
| 269 | 1.687432 | 1.573829 | 0.551108 | 0.585189 | -0.41481 | 0.517027 |
| 270 | 1.732874 | 1.60791 | 0.641991 | 0.528388 | -0.35801 | 0.573829 |
| 271 | 1.698793 | 1.60791 | 0.60791 | 0.641991 | -0.32393 | 0.573829 |
| 272 | 1.789675 | 1.60791 | 0.653351 | 0.641991 | -0.27849 | 0.61927 |
| 273 | 1.789675 | 1.698793 | 0.744234 | 0.755594 | -0.24441 | 0.641991 |
| 274 | 1.925999 | 1.732874 | 0.801036 | 0.778315 | -0.21033 | 0.687432 |
| 275 | 1.891918 | 1.732874 | 0.891918 | 0.789675 | -0.16488 | 0.732874 |
| 276 | 1.93736 | 1.789675 | 0.914639 | 0.835117 | -0.074 | 0.755594 |
| 277 | 1.96008 | 1.846477 | 0.903279 | 0.857837 | 0.028242 | 0.744234 |
| 278 | 2.039603 | 1.903279 | 1.005522 | 0.96008 | -0.02856 | 0.93736 |
| 279 | 2.050963 | 1.880558 | 1.073684 | 0.982801 | 0.028242 | 0.982801 |
| 280 | 2.107765 | 1.982801 | 1.062323 | 1.028242 | 0.187287 | 1.016882 |
| 281 | 2.153206 | 2.005522 | 1.141846 | 1.130485 | 0.187287 | 1.016882 |
| 282 | 2.210008 | 2.016882 | 1.27817 | 1.164566 | 0.232728 | 1.198647 |
| 283 | 2.266809 | 2.050963 | 1.27817 | 1.266809 | 0.27817 | 1.221368 |
| 284 | 2.357692 | 2.107765 | 1.30089 | 1.334971 | 0.334971 | 1.221368 |
| 285 | 2.391773 | 2.210008 | 1.346332 | 1.403133 | 0.414494 | 1.232728 |
| 286 | 2.437215 | 2.210008 | 1.482656 | 1.437215 | 0.369052 | 1.437215 |
| 287 | 2.550818 | 2.30089 | 1.539458 | 1.494016 | 0.528097 | 1.448575 |
| 288 | 2.573539 | 2.369052 | 1.63034 | 1.562178 | 0.539458 | 1.550818 |
| 289 | 2.664421 | 2.459935 | 1.709863 | 1.63034 | 0.63034 | 1.573539 |
| 290 | 2.789385 | 2.494016 | 1.743944 | 1.755304 | 0.698502 | 1.675782 |
| 291 | 2.800745 | 2.61898 | 1.891628 | 1.857547 | 0.857547 | 1.778025 |
| 292 | 2.902988 | 2.641701 | 1.891628 | 1.880268 | 0.834826 | 1.834826 |
| 293 | 3.027952 | 2.800745 | 1.993871 | 2.027952 | 0.95979 | 2.005231 |
| 294 | 3.073393 | 2.925709 | 2.118835 | 2.096114 | 1.050673 | 2.039312 |
| 295 | 3.164276 | 3.016592 | 2.175636 | 2.152916 | 1.209717 | 2.175636 |
| 296 | 3.380123 | 3.107474 | 2.31196 | 2.232438 | 1.255159 | 2.186997 |
| 297 | 3.425564 | 3.198357 | 2.346041 | 2.346041 | 1.3006 | 2.368762 |
| 298 | 3.527807 | 3.357402 | 2.595969 | 2.493726 | 1.425564 | 2.425564 |
| 299 | 3.595969 | 3.471005 | 2.64141 | 2.652771 | 1.573248 | 2.573248 |
| 300 | 3.743653 | 3.595969 | 2.755014 | 2.789095 | 1.664131 | 2.63005 |
| 301 | 3.857257 | 3.664131 | 2.868617 | 2.902698 | 1.766374 | 2.834536 |
| 302 | 3.993581 | 3.868617 | 3.061743 | 2.993581 | 1.914058 | 2.914058 |
| 303 | 4.163986 | 3.98222 | 3.198067 | 3.163986 | 2.039022 | 3.061743 |
| 304 | 4.32303 | 4.107184 | 3.32303 | 3.31167 | 2.243508 | 3.186706 |
| 305 | 4.447994 | 4.31167 | 3.550237 | 3.425274 | 2.32303 | 3.32303 |
| 306 | 4.607039 | 4.504796 | 3.675201 | 3.64112 | 2.504796 | 3.527517 |
| 307 | 4.766084 | 4.64112 | 3.879687 | 3.754723 | 2.62976 | 3.697922 |
| 308 | 4.98193 | 4.868327 | 4.016011 | 3.947849 | 2.845606 | 3.800165 |
| 309 | 5.129614 | 4.99329 | 4.231857 | 4.220497 | 3.106894 | 4.004651 |
| 310 | 5.345461 | 5.31138 | 4.481785 | 4.345461 | 3.31138 | 4.118254 |
| 311 | 5.572668 | 5.481785 | 4.64083 | 4.618109 | 3.515866 | 4.493145 |
| 312 | 5.765793 | 5.708992 | 4.913478 | 4.833955 | 3.708992 | 4.674911 |
| 313 | 6.061162 | 5.913478 | 5.140684 | 5.038441 | 3.947559 | 4.879397 |
| 314 | 6.33381 | 6.197486 | 5.34517 | 5.33381 | 4.242927 | 5.106603 |
| 315 | 6.561017 | 6.458774 | 5.708701 | 5.561017 | 4.561017 | 5.356531 |
| 316 | 6.810944 | 6.67462 | 5.981349 | 5.856386 | 4.685981 | 5.595098 |
| 317 | 7.163115 | 7.060872 | 6.242637 | 6.129034 | 5.00407 | 5.935908 |
| 318 | 7.413042 | 7.265358 | 6.515285 | 6.515285 | 5.35624 | 6.310799 |
| 319 | 7.799294 | 7.572087 | 6.867456 | 6.799294 | 5.68569 | 6.538006 |
| 320 | 8.049221 | 7.981059 | 7.230986 | 7.208266 | 5.981059 | 6.901537 |
| 321 | 8.401391 | 8.36731 | 7.594517 | 7.503634 | 6.469553 | 7.333229 |
| 322 | 8.776282 | 8.764922 | 7.980768 | 7.946687 | 6.6854 | 7.605877 |
| 323 | 9.242056 | 9.151174 | 8.35566 | 8.321579 | 7.219336 | 8.02621 |
| 324 | 9.685109 | 9.605587 | 8.787352 | 8.741911 | 7.560146 | 8.491984 |
| 325 | 10.1168 | 9.957757 | 9.196324 | 9.230405 | 8.03728 | 8.923676 |
| 326 | 10.57122 | 10.35537 | 9.673459 | 9.741621 | 8.423531 | 9.423531 |
| 327 | 11.07107 | 10.96883 | 10.18467 | 10.20739 | 9.036989 | 9.912026 |
| 328 | 11.58229 | 11.5482 | 10.66181 | 10.76405 | 9.548204 | 10.41188 |
| 329 | 12.07078 | 12.07078 | 11.2071 | 11.26391 | 10.0935 | 10.9231 |
| 330 | 12.7524 | 12.65016 | 11.77512 | 11.82056 | 10.66152 | 11.6388 |
| 331 | 13.32042 | 13.24089 | 12.34314 | 12.45674 | 11.26362 | 12.16137 |
| 332 | 14.00204 | 13.96796 | 13.00204 | 13.13836 | 11.89979 | 12.85435 |
| 333 | 14.60414 | 14.53597 | 13.71774 | 13.7291 | 12.53597 | 13.49053 |
| 334 | 15.27439 | 15.29712 | 14.4448 | 14.49024 | 13.36528 | 14.28576 |
| 335 | 16.0469 | 16.02418 | 15.13778 | 15.22866 | 14.02418 | 15.00146 |
| 336 | 16.83076 | 16.8762 | 15.98981 | 16.06933 | 14.92164 | 15.8762 |
| 337 | 17.72823 | 17.6487 | 16.81911 | 16.81911 | 15.70551 | 16.73959 |
| 338 | 18.54617 | 18.52345 | 17.70522 | 17.72794 | 16.59161 | 17.56889 |
| 339 | 19.46636 | 19.48908 | 18.59132 | 18.61404 | 17.455 | 18.50044 |
| 340 | 20.50015 | 20.43199 | 19.56831 | 19.56831 | 18.51151 | 19.42063 |
| 341 | 21.39762 | 21.40898 | 20.49986 | 20.6021 | 19.4885 | 20.44306 |
| 342 | 22.42005 | 22.38596 | 21.51093 | 21.56773 | 20.59045 | 21.55637 |
| 343 | 23.47656 | 23.49928 | 22.53336 | 22.71512 | 21.522 | 22.59016 |
| 344 | 24.48763 | 24.57851 | 23.66939 | 23.74891 | 22.64667 | 23.70347 |
| 345 | 25.62366 | 25.65774 | 24.77134 | 24.85087 | 23.80542 | 24.74862 |
| 346 | 26.73697 | 26.77105 | 25.9301 | 25.97554 | 25.00962 | 25.88466 |
| 347 | 27.92981 | 27.80484 | 26.99797 | 27.12293 | 26.05477 | 27.14565 |
| 348 | 29.0204 | 28.98632 | 28.21352 | 28.28169 | 27.23625 | 28.39529 |
| 349 | 30.12235 | 30.16779 | 29.3382 | 29.4518 | 28.36092 | 29.4518 |
| 350 | 31.36063 | 31.29247 | 30.45151 | 30.53103 | 29.48559 | 30.656 |
| 351 | 32.40578 | 32.3717 | 31.57618 | 31.57618 | 30.57618 | 31.70115 |
| 352 | 33.36005 | 33.38277 | 32.50773 | 32.55317 | 31.53045 | 32.71222 |
| 353 | 34.31431 | 34.24615 | 33.43928 | 33.43928 | 32.58696 | 33.70057 |
| 354 | 35.16634 | 35.05274 | 34.26858 | 34.41627 | 33.46171 | 34.60939 |
| 355 | 35.99564 | 36.01836 | 35.08653 | 35.30237 | 34.18877 | 35.4955 |
| 356 | 36.67726 | 36.75679 | 36.13168 | 36.3816 | 35.22256 | 36.79058 |
| 357 | 38.10866 | 37.91554 | 37.22227 | 39.074 | 37.09701 | 38.67639 |
| 358 | 41.35772 | 41.90302 | 42.98196 | 44.27703 | 42.72038 | 44.99273 |
| 359 | 47.61726 | 46.56075 | 46.06061 | 49.2415 | 45.67406 | 49.46871 |
| 360 | 49.96885 | 52.78621 | 51.47948 | 53.01313 | 52.3085 | 52.94497 |
| 361 | 57.72796 | 56.48968 | 55.84185 | 58.47745 | 56.01196 | 57.78447 |
| 362 | 58.44366 | 57.2849 | 57.76175 | 60.78359 | 56.02332 | 61.02216 |
| 363 | 63.94206 | 60.56804 | 59.10227 | 61.22665 | 59.81768 | 61.38569 |
| 364 | 63.16955 | 63.13547 | 62.12411 | 63.94177 | 61.3286 | 62.46492 |
| 365 | 63.54445 | 65.83923 | 63.78272 | 63.72592 | 62.86224 | 64.71427 |
| 366 | 62.82874 | 63.05595 | 64.88467 | 65.61173 | 62.40783 | 65.42997 |
| 367 | 66.35045 | 66.60037 | 64.4189 | 65.80486 | 64.50949 | 64.64611 |
| 368 | 65.45298 | 67.22519 | 66.87273 | 67.2249 | 63.75971 | 66.4524 |
| 369 | 66.1346 | 67.04343 | 65.7367 | 66.13431 | 63.35074 | 66.25927 |
| 370 | 66.32773 | 67.10023 | 66.61144 | 66.71369 | 64.49813 | 65.77078 |
| 371 | 65.49842 | 67.79321 | 65.91846 | 65.45269 | 63.15761 | 66.17975 |
| 372 | 64.49871 | 65.63475 | 65.27092 | 65.15732 | 63.19169 | 64.65747 |
| 373 | 63.70349 | 66.52085 | 64.28258 | 63.97585 | 61.94206 | 64.25986 |
| 374 | 62.14712 | 63.88526 | 62.3286 | 62.82845 | 60.5561 | 62.19228 |
| 375 | 61.19286 | 63.55581 | 61.46521 | 61.56746 | 59.11333 | 61.46521 |
| 376 | 59.36384 | 61.06789 | 59.07954 | 59.43171 | 57.18208 | 58.96594 |
| 377 | 57.93244 | 59.87506 | 58.07984 | 57.93215 | 55.40987 | 57.98895 |
| 378 | 55.94438 | 57.0009 | 55.46696 | 55.60328 | 53.69446 | 55.25111 |
| 379 | 53.92225 | 55.97847 | 54.24004 | 53.74019 | 51.83136 | 54.09236 |
| 380 | 51.99099 | 52.83165 | 51.42268 | 51.68397 | 49.71834 | 51.3318 |
| 381 | 49.91205 | 52.19548 | 49.94584 | 49.9004 | 47.87797 | 50.0708 |
| 382 | 48.24208 | 48.84418 | 47.3784 | 47.82146 | 45.77631 | 47.51473 |
| 383 | 46.1177 | 48.25344 | 45.99244 | 46.03789 | 43.89049 | 46.07197 |
| 384 | 44.61813 | 45.04983 | 43.66358 | 43.7431 | 42.0842 | 43.57269 |
| 385 | 42.39151 | 44.07284 | 42.16401 | 41.91409 | 40.36879 | 42.16401 |
| 386 | 40.6761 | 41.42588 | 39.92603 | 39.97147 | 38.40345 | 39.69882 |
| 387 | 38.63124 | 40.06264 | 38.16518 | 38.4151 | 36.5858 | 38.4151 |
| 388 | 37.25664 | 38.00642 | 36.34752 | 36.44977 | 34.85903 | 36.0976 |
| 389 | 35.3481 | 36.42734 | 34.71163 | 34.80252 | 33.32538 | 34.99564 |
| 390 | 33.87126 | 34.6324 | 33.10983 | 33.06439 | 31.6895 | 32.79174 |
| 391 | 31.98545 | 33.24644 | 31.4285 | 31.66707 | 30.06497 | 31.71251 |
| 392 | 30.75853 | 31.47423 | 29.98574 | 30.03118 | 28.61085 | 29.9403 |
| 393 | 29.21352 | 30.3382 | 28.6225 | 28.65658 | 27.31577 | 28.70202 |
| 394 | 27.90709 | 28.75911 | 27.21382 | 27.3047 | 25.96389 | 27.2479 |
| 395 | 26.61201 | 27.49811 | 25.89602 | 26.07778 | 24.68017 | 26.06642 |
| 396 | 25.39645 | 26.36208 | 24.64638 | 24.7259 | 23.60094 | 24.81678 |
| 397 | 24.22634 | 24.96476 | 23.4081 | 23.61259 | 22.39674 | 23.66939 |
| 398 | 23.10167 | 23.98777 | 22.36295 | 22.522 | 21.24935 | 22.49928 |
| 399 | 22.02243 | 22.8631 | 21.22692 | 21.48821 | 20.15876 | 21.46549 |
| 400 | 21.12497 | 21.85203 | 20.29537 | 20.4317 | 19.30673 | 20.53394 |
| 401 | 20.1139 | 20.8864 | 19.30702 | 19.45471 | 18.31838 | 19.60239 |
| 402 | 19.20507 | 19.97757 | 18.40956 | 18.47772 | 17.42092 | 18.57996 |
| 403 | 18.45529 | 19.15963 | 17.50073 | 17.64841 | 16.63705 | 17.80746 |
| 404 | 17.4783 | 18.27352 | 16.68279 | 16.88727 | 15.75095 | 17.01224 |
| 405 | 16.7058 | 17.55782 | 15.94436 | 16.09205 | 15.01253 | 16.22837 |
| 406 | 16.06962 | 16.7626 | 15.20594 | 15.2741 | 14.26274 | 15.39907 |
| 407 | 15.35392 | 16.03554 | 14.4448 | 14.68337 | 13.60384 | 14.94465 |
| 408 | 14.69502 | 15.39936 | 13.80862 | 13.8995 | 13.01311 | 14.13807 |
| 409 | 14.0134 | 14.79726 | 13.20652 | 13.29741 | 12.37693 | 13.50189 |
| 410 | 13.36586 | 14.17244 | 12.55898 | 12.66123 | 11.76347 | 12.79755 |
| 411 | 12.88872 | 13.55898 | 11.96825 | 12.07049 | 11.19545 | 12.25226 |
| 412 | 12.26391 | 13.07049 | 11.42295 | 11.50247 | 10.66152 | 11.68424 |
| 413 | 11.84357 | 12.50247 | 10.99126 | 11.04806 | 10.18438 | 11.21846 |
| 414 | 11.30964 | 12.0367 | 10.50276 | 10.50276 | 9.661808 | 10.75269 |
| 415 | 10.8325 | 11.50276 | 10.02563 | 9.957467 | 9.161953 | 10.23012 |
| 416 | 10.43489 | 11.11651 | 9.593936 | 9.616657 | 8.775702 | 9.821143 |
| 417 | 10.02592 | 10.68482 | 9.162243 | 9.128162 | 8.309928 | 9.40081 |
| 418 | 9.548785 | 10.1736 | 8.753271 | 8.741911 | 7.912316 | 9.071361 |
| 419 | 9.219336 | 9.844154 | 8.35566 | 8.35566 | 7.526065 | 8.639668 |
| 420 | 8.821724 | 9.469263 | 8.071651 | 8.003489 | 7.185255 | 8.242056 |
| 421 | 8.492274 | 9.105732 | 7.69676 | 7.730841 | 6.901246 | 7.935327 |
| 422 | 8.140104 | 8.833084 | 7.321869 | 7.401391 | 6.526355 | 7.639958 |
| 423 | 7.912897 | 8.503634 | 7.01514 | 7.037861 | 6.208266 | 7.287788 |
| 424 | 7.594807 | 8.253707 | 6.731131 | 6.742492 | 5.924257 | 6.992419 |
| 425 | 7.35624 | 7.833375 | 6.424402 | 6.560726 | 5.606168 | 6.594807 |
| 426 | 7.072232 | 7.560726 | 6.163115 | 6.163115 | 5.401682 | 6.458483 |
| 427 | 6.776863 | 7.33352 | 5.856386 | 5.958629 | 5.038151 | 6.163115 |
| 428 | 6.549657 | 7.117673 | 5.640539 | 5.697341 | 4.788224 | 5.822305 |
| 429 | 6.311089 | 6.890467 | 5.413332 | 5.504215 | 4.572377 | 5.66326 |
| 430 | 6.117964 | 6.572377 | 5.208846 | 5.231567 | 4.413332 | 5.413332 |
| 431 | 5.890757 | 6.401972 | 5.015721 | 4.993 | 4.220207 | 5.208846 |
| 432 | 5.65219 | 6.163405 | 4.811235 | 4.754433 | 3.98164 | 4.958919 |
| 433 | 5.549947 | 5.958919 | 4.686271 | 4.549947 | 3.788514 | 4.765793 |
| 434 | 5.368181 | 5.788514 | 4.447704 | 4.436344 | 3.515866 | 4.527226 |
| 435 | 5.254578 | 5.549947 | 4.300019 | 4.277299 | 3.345461 | 4.379542 |
| 436 | 5.027371 | 5.413623 | 4.095533 | 4.084173 | 3.209137 | 4.186416 |
| 437 | 4.845606 | 5.243218 | 3.959209 | 3.879687 | 3.084173 | 4.072813 |
| 438 | 4.720642 | 5.095533 | 3.788804 | 3.709282 | 2.902408 | 3.879687 |
| 439 | 4.572958 | 4.97057 | 3.607039 | 3.595679 | 2.720642 | 3.675201 |
| 440 | 4.391193 | 4.822885 | 3.470715 | 3.470715 | 2.584318 | 3.572958 |
| 441 | 4.266229 | 4.618399 | 3.334391 | 3.30031 | 2.425274 | 3.459355 |
| 442 | 4.129905 | 4.482075 | 3.254868 | 3.163986 | 2.368472 | 3.334391 |
| 443 | 4.027662 | 4.402553 | 3.084463 | 3.084463 | 2.232148 | 3.186706 |
| 444 | 3.925419 | 4.220787 | 2.993581 | 3.050382 | 2.084463 | 3.095824 |
| 445 | 3.834536 | 4.084463 | 2.891338 | 2.811815 | 1.9595 | 2.902698 |
| 446 | 3.686852 | 4.016301 | 2.709572 | 2.709572 | 1.823176 | 2.755014 |
| 447 | 3.561888 | 3.936779 | 2.675491 | 2.527807 | 1.755014 | 2.686852 |
| 448 | 3.459645 | 3.823176 | 2.539167 | 2.471005 | 1.61869 | 2.64141 |
| 449 | 3.402843 | 3.675491 | 2.493726 | 2.368762 | 1.561888 | 2.550528 |
| 450 | 3.277879 | 3.573248 | 2.357402 | 2.31196 | 1.459645 | 2.425564 |
| 451 | 3.209717 | 3.493726 | 2.31196 | 2.232438 | 1.425564 | 2.323321 |
| 452 | 3.073393 | 3.357402 | 2.198357 | 2.164276 | 1.243798 | 2.221078 |
| 453 | 3.039312 | 3.323321 | 2.141555 | 2.039312 | 1.186997 | 2.130195 |
| 454 | 2.902988 | 3.175636 | 2.039312 | 1.937069 | 1.050673 | 2.039312 |
| 455 | 2.857547 | 3.118835 | 1.94843 | 1.891628 | 1.050673 | 1.982511 |
| 456 | 2.789385 | 3.016592 | 1.880268 | 1.812106 | 0.94843 | 1.891628 |
| 457 | 2.675782 | 2.891628 | 1.823466 | 1.766664 | 0.857547 | 1.766664 |
| 458 | 2.584899 | 2.846187 | 1.721223 | 1.709863 | 0.732583 | 1.743944 |
| 459 | 2.494016 | 2.766664 | 1.675782 | 1.675782 | 0.721223 | 1.687142 |
| 460 | 2.482656 | 2.653061 | 1.528097 | 1.584899 | 0.709863 | 1.641701 |
| 461 | 2.403133 | 2.60762 | 1.414494 | 1.528097 | 0.63034 | 1.573539 |
| 462 | 2.346332 | 2.562178 | 1.448575 | 1.494016 | 0.550818 | 1.482656 |
| 463 | 2.266809 | 2.471296 | 1.323611 | 1.425854 | 0.482656 | 1.494016 |
| 464 | 2.221368 | 2.391773 | 1.232728 | 1.323611 | 0.437215 | 1.391773 |
| 465 | 2.164566 | 2.30089 | 1.255449 | 1.232728 | 0.346332 | 1.346332 |
| 466 | 2.096404 | 2.28953 | 1.210008 | 1.210008 | 0.312251 | 1.244089 |
| 467 | 2.096404 | 2.198647 | 1.153206 | 1.153206 | 0.232728 | 1.198647 |
| 468 | 2.062323 | 2.210008 | 1.107765 | 1.130485 | 0.221368 | 1.187287 |
| 469 | 1.94872 | 2.141846 | 1.062323 | 1.119125 | 0.107765 | 1.085044 |
| 470 | 1.891918 | 2.005522 | 1.028242 | 1.028242 | 0.039603 | 1.096404 |
| 471 | 1.869198 | 2.016882 | 0.94872 | 1.039603 | -0.05128 | 1.039603 |
| 472 | 1.823756 | 2.005522 | 0.891918 | 0.982801 | -0.03992 | 1.005522 |
| 473 | 1.744234 | 1.994161 | 0.869198 | 0.96008 | -0.09672 | 0.94872 |
| 474 | 1.755594 | 1.925999 | 0.891918 | 0.835117 | -0.1308 | 0.925999 |
| 475 | 1.744234 | 1.914639 | 0.846477 | 0.823756 | -0.19896 | 0.846477 |
| 476 | 1.653351 | 1.94872 | 0.755594 | 0.766955 | -0.24441 | 0.857837 |
| 477 | 1.698793 | 1.823756 | 0.698793 | 0.721513 | -0.25577 | 0.835117 |
| 478 | 1.585189 | 1.766955 | 0.687432 | 0.710153 | -0.26713 | 0.766955 |
| 479 | 1.59655 | 1.766955 | 0.664712 | 0.710153 | -0.32393 | 0.778315 |
| 480 | 1.551108 | 1.676072 | 0.630631 | 0.676072 | -0.46025 | 0.653351 |
| 481 | 1.539748 | 1.630631 | 0.653351 | 0.687432 | -0.52841 | 0.59655 |
| 482 | 1.505667 | 1.630631 | 0.676072 | 0.562469 | -0.49433 | 0.59655 |
| 483 | 1.392063 | 1.653351 | 0.573829 | 0.59655 | -0.47161 | 0.551108 |
| 484 | 1.369343 | 1.585189 | 0.539748 | 0.528388 | -0.44889 | 0.539748 |
| 485 | 1.346622 | 1.562469 | 0.551108 | 0.505667 | -0.49433 | 0.482946 |
| 486 | 1.28982 | 1.551108 | 0.517027 | 0.471586 | -0.55114 | 0.403424 |
| 487 | 1.357982 | 1.59655 | 0.517027 | 0.482946 | -0.64202 | 0.403424 |
| 488 | 1.323901 | 1.505667 | 0.460225 | 0.505667 | -0.71018 | 0.414784 |
| 489 | 1.312541 | 1.562469 | 0.471586 | 0.471586 | -0.68746 | 0.369343 |
| 490 | 1.335262 | 1.517027 | 0.528388 | 0.460225 | -0.65338 | 0.301181 |
| 491 | 1.301181 | 1.460225 | 0.448865 | 0.482946 | -0.66474 | 0.312541 |
| 492 | 1.28982 | 1.448865 | 0.403424 | 0.414784 | -0.69882 | 0.312541 |
| 493 | 1.198938 | 1.471586 | 0.426144 | 0.27846 | -0.6761 | 0.244379 |
| 494 | 1.233019 | 1.357982 | 0.494306 | 0.27846 | -0.64202 | 0.2671 |
| 495 | 1.187577 | 1.357982 | 0.426144 | 0.369343 | -0.72154 | 0.27846 |
| 496 | 1.198938 | 1.335262 | 0.392063 | 0.323901 | -0.69882 | 0.28982 |
| 497 | 1.153496 | 1.335262 | 0.301181 | 0.335262 | -0.69882 | 0.233019 |
| 498 | 1.142136 | 1.335262 | 0.357982 | 0.312541 | -0.72154 | 0.221658 |
| 499 | 1.210298 | 1.2671 | 0.357982 | 0.369343 | -0.71018 | 0.255739 |
| 500 | 1.108055 | 1.312541 | 0.335262 | 0.312541 | -0.81242 | 0.187577 |
| 501 | 1.119415 | 1.312541 | 0.335262 | 0.312541 | -0.80106 | 0.142136 |
| 502 | 1.062614 | 1.244379 | 0.28982 | 0.323901 | -0.8465 | 0.176217 |
| 503 | 1.073974 | 1.255739 | 0.198938 | 0.323901 | -0.85786 | 0.142136 |
| 504 | 1.039893 | 1.255739 | 0.28982 | 0.357982 | -0.85786 | 0.028533 |
| 505 | 1.073974 | 1.244379 | 0.244379 | 0.2671 | -0.77834 | 0.062614 |
| 506 | 1.108055 | 1.233019 | 0.27846 | 0.312541 | -0.90331 | 0.062614 |
| 507 | 1.130776 | 1.221658 | 0.221658 | 0.312541 | -0.89195 | 0.073974 |
| 508 | 1.073974 | 1.2671 | 0.2671 | 0.2671 | -0.89195 | 0.062614 |
| 509 | 1.085334 | 1.2671 | 0.233019 | 0.301181 | -0.82378 | -0.00555 |
| 510 | 1.017172 | 1.221658 | 0.221658 | 0.28982 | -0.94875 | 0.051253 |
| 511 | 0.994452 | 1.187577 | 0.210298 | 0.2671 | -0.92603 | -0.00555 |
| 512 | 0.994452 | 1.187577 | 0.164857 | 0.244379 | -0.91467 | 0.017172 |
| 513 | 1.017172 | 1.221658 | 0.164857 | 0.221658 | -0.90331 | 0.062614 |
| 514 | 1.028533 | 1.187577 | 0.164857 | 0.244379 | -1.00555 | 0.017172 |
| 515 | 1.028533 | 1.210298 | 0.198938 | 0.244379 | -1.00555 | 0.005812 |
| 516 | 0.983091 | 1.198938 | 0.198938 | 0.198938 | -0.98283 | 0.062614 |
| 517 | 0.94901 | 1.210298 | 0.176217 | 0.164857 | -0.92603 | 0.005812 |
| 518 | 0.914929 | 1.198938 | 0.119415 | 0.176217 | -0.94875 | -0.00555 |
| 519 | 0.880848 | 1.164857 | 0.142136 | 0.130776 | -0.93739 | -0.05099 |
| 520 | 0.914929 | 1.164857 | 0.164857 | 0.142136 | -0.92603 | -0.03963 |
| 521 | 0.858128 | 1.164857 | 0.153496 | 0.176217 | -0.86922 | 0.017172 |
| 522 | 0.869488 | 1.176217 | 0.062614 | 0.142136 | -0.94875 | -0.06235 |
| 523 | 0.835407 | 1.085334 | 0.085334 | 0.096695 | -0.98283 | -0.03963 |
| 524 | 0.778605 | 1.073974 | 0.085334 | 0.028533 | -0.98283 | -0.00555 |
| 525 | 0.789966 | 1.073974 | -0.00555 | 0.028533 | -0.97147 | -0.00555 |
| 526 | 0.789966 | 1.028533 | 0.028533 | 0.062614 | -0.98283 | -0.03963 |
| 527 | 0.687723 | 1.017172 | 0.005812 | 0.073974 | -1.00555 | -0.10779 |
| 528 | 0.687723 | 0.960371 | 0.028533 | 0.062614 | -1.02827 | -0.06235 |
| 529 | 0.642281 | 1.017172 | -0.00555 | -0.00555 | -1.01691 | -0.03963 |
| 530 | 0.642281 | 0.92629 | -0.05099 | 0.017172 | -0.99419 | -0.09643 |
| 531 | 0.653642 | 0.93765 | -0.06235 | -0.05099 | -1.01691 | -0.06235 |
| 532 | 0.61956 | 0.94901 | -0.02827 | -0.07371 | -1.02827 | -0.16459 |
| 533 | 0.630921 | 0.971731 | -0.11915 | -0.07371 | -1.03963 | -0.05099 |
| 534 | 0.642281 | 0.960371 | -0.14187 | -0.06235 | -1.05099 | -0.16459 |
| 535 | 0.551398 | 0.94901 | -0.18731 | -0.05099 | -1.09643 | -0.17595 |
| 536 | 0.528678 | 0.869488 | -0.17595 | -0.18731 | -1.14187 | -0.18731 |
| 537 | 0.630921 | 0.92629 | -0.23276 | -0.2214 | -1.23276 | -0.19867 |
| 538 | 0.460516 | 0.824047 | -0.2782 | -0.24412 | -1.17595 | -0.15323 |
| 539 | 0.528678 | 0.846767 | -0.26684 | -0.23276 | -1.24412 | -0.25548 |
| 540 | 0.460516 | 0.733164 | -0.25548 | -0.18731 | -1.23276 | -0.31228 |
| 541 | 0.505957 | 0.721804 | -0.38044 | -0.26684 | -1.2782 | -0.30092 |
| 542 | 0.437795 | 0.755885 | -0.36908 | -0.25548 | -1.34636 | -0.35772 |
| 543 | 0.426435 | 0.733164 | -0.335 | -0.31228 | -1.335 | -0.3918 |
| 544 | 0.358273 | 0.665002 | -0.335 | -0.30092 | -1.35772 | -0.38044 |
| 545 | 0.380993 | 0.653642 | -0.38044 | -0.38044 | -1.38044 | -0.42588 |
| 546 | 0.346912 | 0.6082 | -0.4486 | -0.41452 | -1.43724 | -0.40316 |
| 547 | 0.27875 | 0.540038 | -0.43724 | -0.3918 | -1.49404 | -0.5054 |
| 548 | 0.25603 | 0.449155 | -0.5054 | -0.41452 | -1.42588 | -0.53948 |
| 549 | 0.221949 | 0.540038 | -0.47132 | -0.47132 | -1.42588 | -0.51676 |
| 550 | 0.210588 | 0.483236 | -0.55085 | -0.47132 | -1.49404 | -0.63037 |
| 551 | 0.165147 | 0.471876 | -0.55085 | -0.48268 | -1.60765 | -0.65309 |
| 552 | 0.221949 | 0.460516 | -0.64173 | -0.55085 | -1.57357 | -0.73261 |
| 553 | 0.244669 | 0.483236 | -0.64173 | -0.55085 | -1.59629 | -0.70989 |
| 554 | 0.210588 | 0.494597 | -0.67581 | -0.58493 | -1.61901 | -0.72125 |
| 555 | 0.187868 | 0.460516 | -0.64173 | -0.57357 | -1.53948 | -0.76669 |
| 556 | 0.153787 | 0.494597 | -0.68717 | -0.66445 | -1.66445 | -0.75533 |
| 557 | 0.142426 | 0.437795 | -0.68717 | -0.68717 | -1.67581 | -0.74397 |
| 558 | 0.096985 | 0.460516 | -0.72125 | -0.67581 | -1.75533 | -0.78941 |
| 559 | 0.051544 | 0.403714 | -0.70989 | -0.70989 | -1.70989 | -0.78941 |
| 560 | 0.074264 | 0.335552 | -0.67581 | -0.74397 | -1.75533 | -0.80077 |
| 561 | 0.085625 | 0.324192 | -0.73261 | -0.76669 | -1.72125 | -0.78941 |
| 562 | 0.017463 | 0.403714 | -0.76669 | -0.76669 | -1.70989 | -0.90302 |
| 563 | 0.040183 | 0.380993 | -0.80077 | -0.80077 | -1.74397 | -0.86893 |
| 564 | 0.040183 | 0.25603 | -0.81213 | -0.82349 | -1.69853 | -0.91438 |
| 565 | -0.00526 | 0.25603 | -0.82349 | -0.76669 | -1.77805 | -0.91438 |
| 566 | -0.00526 | 0.233309 | -0.83485 | -0.78941 | -1.74397 | -0.92574 |
| 567 | -0.00526 | 0.25603 | -0.81213 | -0.76669 | -1.78941 | -0.95982 |
| 568 | -0.02798 | 0.233309 | -0.85757 | -0.83485 | -1.77805 | -0.91438 |
| 569 | -0.03934 | 0.210588 | -0.88029 | -0.84621 | -1.73261 | -0.98254 |
| 570 | -0.07342 | 0.199228 | -0.92574 | -0.92574 | -1.75533 | -1.02798 |
| 571 | -0.08478 | 0.142426 | -0.97118 | -0.86893 | -1.82349 | -1.0507 |
| 572 | -0.03934 | 0.131066 | -0.97118 | -0.94846 | -1.82349 | -1.01662 |
| 573 | -0.09614 | 0.187868 | -0.97118 | -0.97118 | -1.75533 | -1.01662 |
| 574 | -0.11886 | 0.040183 | -0.9939 | -0.95982 | -1.84621 | -0.9939 |
| 575 | -0.09614 | 0.062904 | -1.00526 | -0.95982 | -1.90302 | -1.00526 |
| 576 | -0.18702 | 0.062904 | -1.00526 | -1.07342 | -1.89166 | -0.9371 |
| 577 | -0.13022 | 0.040183 | -1.03934 | -0.9939 | -1.90302 | -0.98254 |
| 578 | -0.15294 | 0.062904 | -1.09614 | -0.98254 | -1.84621 | -1.01662 |
| 579 | -0.13022 | 0.051544 | -1.07342 | -0.95982 | -1.95982 | -1.03934 |
| 580 | -0.15294 | 0.017463 | -1.03934 | -1.03934 | -1.91438 | -0.9371 |
| 581 | -0.14158 | 0.017463 | -1.09614 | -1.03934 | -2.00526 | -1.02798 |
| 582 | -0.19838 | -0.06206 | -1.1075 | -1.01662 | -1.94846 | -1.07342 |
| 583 | -0.18702 | -0.03934 | -1.14158 | -1.06206 | -1.98254 | -1.09614 |
| 584 | -0.26655 | -0.1075 | -1.20974 | -1.08478 | -1.9939 | -0.97118 |
| 585 | -0.1643 | -0.1075 | -1.18702 | -1.13022 | -1.92574 | -1.06206 |
| 586 | -0.13022 | -0.03934 | -1.19838 | -1.08478 | -2.00526 | -1.07342 |
| 587 | -0.20974 | -0.0507 | -1.17566 | -1.11886 | -1.97118 | -1.1075 |
| 588 | -0.1643 | -0.0507 | -1.19838 | -1.08478 | -2.00526 | -1.1075 |
| 589 | -0.20974 | -0.08478 | -1.23247 | -1.1643 | -2.02798 | -1.1075 |
| 590 | -0.24383 | -0.09614 | -1.22111 | -1.09614 | -1.98254 | -1.08478 |
| 591 | -0.20974 | -0.01662 | -1.17566 | -1.13022 | -2.06206 | -1.06206 |
| 592 | -0.25519 | -0.07342 | -1.19838 | -1.13022 | -2.03934 | -1.1075 |
| 593 | -0.30063 | -0.13022 | -1.23247 | -1.17566 | -2.0507 | -1.18702 |
| 594 | -0.22111 | -0.14158 | -1.25519 | -1.18702 | -1.98254 | -1.00526 |
| 595 | -0.14158 | -0.1075 | -1.1643 | -1.11886 | -2.03934 | -1.08478 |
| 596 | -0.17566 | -0.08478 | -1.23247 | -1.17566 | -1.98254 | -1.07342 |
| 597 | -0.18702 | -0.11886 | -1.14158 | -1.19838 | -2.06206 | -1.11886 |
| 598 | -0.1643 | -0.06206 | -1.19838 | -1.25519 | -2.01662 | -1.07342 |
| 599 | -0.22111 | -0.06206 | -1.13022 | -1.15294 | -2.06206 | -1.07342 |
| 600 | -0.15294 | -0.01662 | -1.14158 | -1.1643 | -1.98254 | -1.07342 |
| 601 | -0.15294 | -0.07342 | -1.13022 | -1.17566 | -2.01662 | -1.0507 |
| 602 | -0.08478 | -0.01662 | -1.1643 | -1.20974 | -1.97118 | -1.03934 |
| 603 | -0.0507 | 0.040183 | -1.18702 | -1.11886 | -1.9371 | -1.06206 |
| 604 | -0.07342 | -0.03934 | -1.07342 | -1.13022 | -2.03934 | -1.02798 |
| 605 | -0.02798 | -0.02798 | -1.07342 | -1.11886 | -1.95982 | -1.0507 |
| 606 | -0.0507 | 0.028823 | -1.0507 | -1.14158 | -1.98254 | -1.02798 |
| 607 | -0.02798 | 0.028823 | -1.07342 | -1.1075 | -1.95982 | -1.00526 |
| 608 | -0.00526 | 0.062904 | -1.02798 | -1.11886 | -2.01662 | -1.00526 |
| 609 | -0.02798 | 0.074264 | -1.02798 | -1.07342 | -1.9371 | -1.07342 |
| 610 | 0.040183 | 0.096985 | -1.07342 | -1.0507 | -1.86893 | -1.00526 |
| 611 | 0.062904 | 0.085625 | -1.00526 | -1.01662 | -1.92574 | -0.85757 |
| 612 | -0.00526 | 0.119706 | -1.00526 | -1.11886 | -1.84621 | -0.91438 |
| 613 | 0.142426 | 0.074264 | -0.98254 | -0.98254 | -1.90302 | -0.89166 |
| 614 | 0.153787 | 0.210588 | -0.89166 | -1.00526 | -1.92574 | -0.95982 |
| 615 | 0.153787 | 0.221949 | -0.91438 | -0.9939 | -1.88029 | -0.86893 |
| 616 | 0.199228 | 0.233309 | -0.88029 | -0.94846 | -1.86893 | -0.82349 |
| 617 | 0.290111 | 0.244669 | -0.91438 | -0.9939 | -1.70989 | -0.9371 |
| 618 | 0.301471 | 0.26739 | -0.88029 | -0.92574 | -1.84621 | -0.94846 |
| 619 | 0.335552 | 0.244669 | -0.84621 | -0.90302 | -1.82349 | -0.80077 |
| 620 | 0.324192 | 0.290111 | -0.77805 | -0.82349 | -1.78941 | -0.83485 |
| 621 | 0.301471 | 0.26739 | -0.83485 | -0.88029 | -1.75533 | -0.83485 |
| 622 | 0.415074 | 0.358273 | -0.81213 | -0.81213 | -1.70989 | -0.89166 |
| 623 | 0.335552 | 0.335552 | -0.78941 | -0.83485 | -1.77805 | -0.78941 |
| 624 | 0.380993 | 0.392354 | -0.76669 | -0.74397 | -1.70989 | -0.80077 |
| 625 | 0.415074 | 0.426435 | -0.74397 | -0.73261 | -1.73261 | -0.78941 |
| 626 | 0.483236 | 0.335552 | -0.74397 | -0.66445 | -1.64173 | -0.83485 |
| 627 | 0.449155 | 0.380993 | -0.72125 | -0.76669 | -1.66445 | -0.74397 |
| 628 | 0.471876 | 0.369633 | -0.67581 | -0.77805 | -1.59629 | -0.75533 |
| 629 | 0.449155 | 0.358273 | -0.66445 | -0.70989 | -1.63037 | -0.76669 |
| 630 | 0.483236 | 0.483236 | -0.61901 | -0.70989 | -1.60765 | -0.74397 |
| 631 | 0.494597 | 0.426435 | -0.66445 | -0.68717 | -1.55085 | -0.76669 |
| 632 | 0.494597 | 0.403714 | -0.68717 | -0.67581 | -1.59629 | -0.67581 |
| 633 | 0.449155 | 0.437795 | -0.63037 | -0.64173 | -1.56221 | -0.73261 |
| 634 | 0.517317 | 0.460516 | -0.56221 | -0.69853 | -1.64173 | -0.73261 |
| 635 | 0.483236 | 0.415074 | -0.61901 | -0.65309 | -1.65309 | -0.63037 |
| 636 | 0.505957 | 0.437795 | -0.64173 | -0.61901 | -1.51676 | -0.65309 |
| 637 | 0.483236 | 0.403714 | -0.65309 | -0.60765 | -1.60765 | -0.63037 |
| 638 | 0.528678 | 0.437795 | -0.49404 | -0.58493 | -1.56221 | -0.66445 |
| 639 | 0.540038 | 0.346912 | -0.58493 | -0.53948 | -1.56221 | -0.59629 |
| 640 | 0.540038 | 0.358273 | -0.53948 | -0.59629 | -1.57357 | -0.57357 |
| 641 | 0.528678 | 0.358273 | -0.59629 | -0.55085 | -1.55085 | -0.64173 |
| 642 | 0.562759 | 0.415074 | -0.56221 | -0.58493 | -1.53948 | -0.59629 |
| 643 | 0.528678 | 0.346912 | -0.53948 | -0.55085 | -1.5054 | -0.64173 |
| 644 | 0.505957 | 0.380993 | -0.56221 | -0.55085 | -1.5054 | -0.66445 |
| 645 | 0.494597 | 0.358273 | -0.52812 | -0.51676 | -1.51676 | -0.65309 |
| 646 | 0.517317 | 0.324192 | -0.57357 | -0.57357 | -1.57357 | -0.52812 |
| 647 | 0.585479 | 0.335552 | -0.53948 | -0.60765 | -1.53948 | -0.58493 |
| 648 | 0.540038 | 0.324192 | -0.57357 | -0.53948 | -1.52812 | -0.57357 |
| 649 | 0.494597 | 0.335552 | -0.57357 | -0.56221 | -1.60765 | -0.59629 |
| 650 | 0.528678 | 0.346912 | -0.58493 | -0.59629 | -1.61901 | -0.64173 |
| 651 | 0.517317 | 0.369633 | -0.58493 | -0.58493 | -1.61901 | -0.53948 |
| 652 | 0.551398 | 0.346912 | -0.58493 | -0.58493 | -1.61901 | -0.56221 |
| 653 | 0.585479 | 0.335552 | -0.59629 | -0.53948 | -1.63037 | -0.60765 |
| 654 | 0.517317 | 0.301471 | -0.61901 | -0.64173 | -1.61901 | -0.69853 |
| 655 | 0.505957 | 0.27875 | -0.64173 | -0.63037 | -1.67581 | -0.68717 |
| 656 | 0.415074 | 0.233309 | -0.65309 | -0.61901 | -1.68717 | -0.59629 |
| 657 | 0.437795 | 0.335552 | -0.67581 | -0.60765 | -1.73261 | -0.70989 |
| 658 | 0.460516 | 0.27875 | -0.63037 | -0.60765 | -1.69853 | -0.66445 |
| 659 | 0.403714 | 0.27875 | -0.69853 | -0.65309 | -1.81213 | -0.69853 |
| 660 | 0.483236 | 0.244669 | -0.69853 | -0.65309 | -1.84621 | -0.72125 |
| 661 | 0.415074 | 0.25603 | -0.69853 | -0.67581 | -1.81213 | -0.78941 |
| 662 | 0.415074 | 0.244669 | -0.68717 | -0.67581 | -1.78941 | -0.80077 |
| 663 | 0.392354 | 0.233309 | -0.69853 | -0.70989 | -1.78941 | -0.81213 |
| 664 | 0.358273 | 0.233309 | -0.67581 | -0.68717 | -1.77805 | -0.77805 |
| 665 | 0.301471 | 0.210588 | -0.70989 | -0.64173 | -1.81213 | -0.88029 |
| 666 | 0.290111 | 0.233309 | -0.58493 | -0.65309 | -1.88029 | -0.90302 |
| 667 | 0.403714 | 0.27875 | -0.68717 | -0.73261 | -1.75533 | -0.86893 |
| 668 | 0.26739 | 0.210588 | -0.64173 | -0.69853 | -1.82349 | -0.89166 |
| 669 | 0.312831 | 0.233309 | -0.72125 | -0.81213 | -1.80077 | -0.86893 |
| 670 | 0.335552 | 0.176507 | -0.64173 | -0.81213 | -1.77805 | -0.9371 |
| 671 | 0.358273 | 0.233309 | -0.68717 | -0.75533 | -1.76669 | -0.98254 |
| 672 | 0.290111 | 0.244669 | -0.72125 | -0.78941 | -1.78941 | -0.95982 |
| 673 | 0.210588 | 0.187868 | -0.67581 | -0.74397 | -1.84621 | -0.90302 |
| 674 | 0.221949 | 0.199228 | -0.72125 | -0.76669 | -1.86893 | -0.89166 |
| 675 | 0.27875 | 0.233309 | -0.60765 | -0.77805 | -1.78941 | -0.94846 |
| 676 | 0.221949 | 0.210588 | -0.63037 | -0.75533 | -1.88029 | -0.94846 |
| 677 | 0.221949 | 0.176507 | -0.66445 | -0.73261 | -1.86893 | -0.92574 |
| 678 | 0.210588 | 0.119706 | -0.66445 | -0.77805 | -1.95982 | -0.9371 |
| 679 | 0.221949 | 0.142426 | -0.68717 | -0.78941 | -1.88029 | -0.95982 |
| 680 | 0.233309 | 0.176507 | -0.66445 | -0.69853 | -1.88029 | -0.97118 |
| 681 | 0.199228 | 0.210588 | -0.68717 | -0.67581 | -1.84621 | -0.91438 |
| 682 | 0.221949 | 0.176507 | -0.67581 | -0.70989 | -1.90302 | -0.97118 |
| 683 | 0.233309 | 0.244669 | -0.65309 | -0.77805 | -1.83485 | -1.00526 |
| 684 | 0.187868 | 0.210588 | -0.67581 | -0.75533 | -1.83485 | -0.91438 |
| 685 | 0.244669 | 0.210588 | -0.69853 | -0.69853 | -1.82349 | -0.97118 |
| 686 | 0.176507 | 0.165147 | -0.68717 | -0.68717 | -1.77805 | -0.9371 |
| 687 | 0.25603 | 0.233309 | -0.64173 | -0.67581 | -1.77805 | -0.9371 |
| 688 | 0.165147 | 0.233309 | -0.68717 | -0.70989 | -1.77805 | -0.90302 |
| 689 | 0.244669 | 0.290111 | -0.58493 | -0.65309 | -1.89166 | -0.94846 |
| 690 | 0.210588 | 0.25603 | -0.69853 | -0.69853 | -1.76669 | -0.94846 |
| 691 | 0.25603 | 0.27875 | -0.66445 | -0.73261 | -1.77805 | -0.9371 |
| 692 | 0.27875 | 0.187868 | -0.61901 | -0.67581 | -1.82349 | -0.90302 |
| 693 | 0.301471 | 0.25603 | -0.64173 | -0.72125 | -1.86893 | -0.92574 |
| 694 | 0.335552 | 0.26739 | -0.60765 | -0.64173 | -1.82349 | -0.84621 |
| 695 | 0.290111 | 0.210588 | -0.72125 | -0.66445 | -1.81213 | -0.95982 |
| 696 | 0.26739 | 0.210588 | -0.68717 | -0.63037 | -1.80077 | -0.91438 |
| 697 | 0.26739 | 0.165147 | -0.66445 | -0.66445 | -1.76669 | -0.92574 |
| 698 | 0.26739 | 0.26739 | -0.64173 | -0.65309 | -1.74397 | -0.92574 |
| 699 | 0.324192 | 0.187868 | -0.66445 | -0.61901 | -1.76669 | -0.88029 |
| 700 | 0.312831 | 0.221949 | -0.68717 | -0.59629 | -1.72125 | -0.94846 |
| 701 | 0.346912 | 0.26739 | -0.60765 | -0.64173 | -1.75533 | -0.91438 |
| 702 | 0.312831 | 0.233309 | -0.59629 | -0.72125 | -1.69853 | -0.84621 |
| 703 | 0.312831 | 0.26739 | -0.56221 | -0.61901 | -1.72125 | -0.85757 |
| 704 | 0.335552 | 0.25603 | -0.63037 | -0.63037 | -1.70989 | -0.86893 |
| 705 | 0.324192 | 0.244669 | -0.60765 | -0.56221 | -1.74397 | -0.80077 |
| 706 | 0.312831 | 0.244669 | -0.66445 | -0.60765 | -1.73261 | -0.81213 |
| 707 | 0.358273 | 0.27875 | -0.59629 | -0.63037 | -1.67581 | -0.77805 |
| 708 | 0.358273 | 0.26739 | -0.61901 | -0.59629 | -1.73261 | -0.81213 |
| 709 | 0.335552 | 0.301471 | -0.64173 | -0.65309 | -1.73261 | -0.83485 |
| 710 | 0.290111 | 0.25603 | -0.66445 | -0.65309 | -1.64173 | -0.85757 |
| 711 | 0.346912 | 0.312831 | -0.65309 | -0.66445 | -1.64173 | -0.82349 |
| 712 | 0.312831 | 0.233309 | -0.70989 | -0.59629 | -1.66445 | -0.73261 |
| 713 | 0.426435 | 0.301471 | -0.65309 | -0.57357 | -1.63037 | -0.81213 |
| 714 | 0.369633 | 0.290111 | -0.66445 | -0.59629 | -1.66445 | -0.77805 |
| 715 | 0.437795 | 0.27875 | -0.65309 | -0.52812 | -1.66445 | -0.75533 |
| 716 | 0.369633 | 0.233309 | -0.66445 | -0.65309 | -1.65309 | -0.77805 |
| 717 | 0.415074 | 0.27875 | -0.63037 | -0.60765 | -1.64173 | -0.77805 |
| 718 | 0.403714 | 0.346912 | -0.59629 | -0.59629 | -1.59629 | -0.70989 |
| 719 | 0.426435 | 0.27875 | -0.58493 | -0.64173 | -1.60765 | -0.75533 |

# Text boxes

Thermometer

Electric heating device

Weighing  machine

Alcohol

Beaker

Potassium

Hydroxide

(KOH)

90

Methanol

Separating Funnel

Thumba biodiesel

Formation of biodiesel after washing

Transesterification

Settled Water

Glycerineee

Magnetic stirrer (capsule)

Switch (on/off)

Speed controller

Hot plate

Beaker

Mixture of methanol and alcohol

Temperature cotroller

Base Supporting Frame

Reciprocating

Pump

Ladder

Nozzle Spray Gun

Pressure

Gauge

Cylindrical

Pipe

Base Supporting

Frame

Water Outlet

Draining Valve

Mixture Inlet Manifold

Water Inlet

Thermometer

Electric heating device

Beaker

Alcohol

Weighing machine

Potassium

Hydroxide

(KOH)

90

Methanol

Throttle Valve

Plungers

Mixture

Inlet

Rotameter

Connecting wire

Reciprocating pump

Data

Acquisition

System

Eddy Current Dynamometer

Calorimeter

Engine Exhaust