Chapter    1

INTRODUCTION

1.1	General

Wastewater or sewage is produced by every day human activities and various industrial processes. It may contain organic compounds, inorganic nutrients such as carbon, nitrogen and phosphorous, trace elements, heavy metals, toxic organic and inorganic substances, disease-producing (pathogenic) microorganisms, and other substances that without appropriate treatment, can impair the quality of receiving streams and lakes, making them toxic  to aquatic flora and fauna and vehicles for transmission  of disease. Broadly classified, wastewater contains about 70% organic and 30% inorganic material. The organic portion of the sewage is used as food for bacteria, while the inorganic portion passes on through the entire treatment process unaffected.

Inorganic material i.e. grit, rags, plastic, metal, etc. are normally removed in pretreatment units such as bar screens, grit chambers etc. After pretreatment, the remaining solids are settleable, suspended or dissolved. Settleable solids are those which are heavy enough to settle out when the wastewater flow is slowed down and enough time is allowed for them to settle. These solids are removed in primary clarifiers.

The remaining solids are either suspended in the water or dissolved. Most of this material passes on to some form of biological treatment process where it is converted to biological solids heavy enough to settle. These solids are removed from the wastewater flow in secondary clarifiers.

Thus the constituents removed in wastewater treatment plants include screenings, grit, scum, solids and bio solids.

## 1.2  Objective of Wastewater Treatment

The principal objective of wastewater treatment is generally to allow domestic and industrial effluents to be disposed of without danger to human health or unacceptable damage to the natural environment.

## 1.3	Wastewater Treatment Processes

### Wastewater treatment consists of a combination of physical, chemical, and biological processes. The constituents removed in wastewater treatment plants include screenings, grit, scum, solids and biosolids. The organic portion of the sewage is used as food for bacteria, while the inorganic portion passes on through the entire treatment process unaffected. General terms used to describe different degrees of treatment, in order of increasing treatment level, are preliminary, primary, secondary, and tertiary and/or advanced wastewater treatment. In some countries, disinfection to remove pathogens sometimes follows the last treatment step.

### Preliminary treatment

### The objective of preliminary treatment is the removal of coarse solids and other large materials often found in raw wastewater. Removal of these materials is necessary to enhance the operation and maintenance of subsequent treatment units. Preliminary treatment operations typically include coarse screening and grit removal.

Screening removes coarse solids such as rags that would interfere with mechanical equipment. Grit removal separates heavy, inorganic, sand like solids that would settle in channels and interfere with treatment processes.

Preliminary treatment serves to prepare wastewater for subsequent treatment, but it effects little change in wastewater quality.

### 1.3.2	Primary treatment

The objective of primary treatment is the elimination of suspended solids (S.S.). Removal of settleable organic and inorganic solids is done by sedimentation, and the removal of materials that will float (scum) by skimming. Approximately 25 to 50% of the incoming biochemical oxygen demand (BOD5), 50 to 70% of the total suspended solids (SS), and 65% of the oil and grease are removed during primary treatment. Some organic nitrogen, organic phosphorus, and heavy metals associated with solids are also removed during primary sedimentation but colloidal and dissolved constituents are not affected. The constituents that are removed are contained in primary sludge.

### 1.3.3	Secondary treatment

The objective of secondary treatment is the further treatment of the effluent from primary treatment to remove the residual organics and suspended solids. Secondary treatment follows primary treatment and involves the removal of biodegradable dissolved and colloidal organic matter using aerobic biological treatment processes. Aerobic biological treatment is performed in the presence of oxygen by aerobic microorganisms (principally bacteria) that metabolize the organic matter in the wastewater, thereby producing more microorganisms and inorganic end-products (principally CO2, NH3, and H2O). Several aerobic biological processes are used for secondary treatment differing primarily in the manner in which oxygen is supplied to the microorganisms and in the rate at which organisms metabolize the organic matter.

Commonly used high-rate biological processes are activated sludge process, trickling filter or biofilter, oxidation ditch, and rotating biological contactor (RBC).

During these processes the micro-organisms biologically flocculate to form settleable particles, and, following biological treatment, this excess biomass is separated in sedimentation tanks as a concentrated suspension called "secondary sludge" (also known as "biological sludge" or "waste activated sludge"), to produce clarified secondary effluent.

### 1.3.4	Tertiary (Advanced) treatment

Tertiary treatment is used at municipal wastewater treatment plants when receiving water conditions or other uses require higher quality effluent than that produced by secondary wastewater treatment. Secondary treatment can remove between 85 and 95% of the BOD and TSS in raw sanitary sewage. Generally, this leaves 30 mg/L or less of BOD and TSS in the secondary effluent.  But some times this level of sewage treatment is not sufficient to protect the aquatic environment.  Another limitation of secondary treatment is that it does not significantly reduce the effluent concentrations of nitrogen and phosphorous in the sewage.  Nitrogen & Phosphorous are important plant nutrients.  If they are discharged into a lake, algal blooms and accelerated lake aging or cultural eutrophication may be the result. Individual treatment processes are necessary to remove nitrogen, phosphorus, additional suspended solids, refractory organics, heavy metals and dissolved solids.

Tertiary treatment can remove more than 99% of the pollutants from raw sewage and can produce an effluent of almost drinking water quality.  But the cost of tertiary treatment, for operation and maintenance as well as for construction, is very high, some times doubling the cost of secondary treatment.

There can also be a final disinfecting treatment, when the receiver water body is intended for a use requiring a particular hygienic-sanitary safeguard (e.g. bathing).

  - Scope and Objectives of The Study

    - Scope

The broad scope of the study is:

- To collect the performance parameters such as BOD, COD, SS and volatile organic 	matter of raw sewage and before and after the treatment by individual units.

- To analyze the performance parameters and evaluate the performance of various 	treatment units viz. primary clarifier, aeration tank, secondary clarifier and 	digestion tank.

    - Objectives

The objectives of the study are:

- To study the performance of 16 MGD Sewage Treatment Plant at Okhla, Delhi.

- To evaluate the overall performance of 16 MGD Sewage Treatment Plant at Okhla, 	Delhi.

- To suggest improvement in the existing plant.

Chapter    2

LITRERATURE REVIEW

The activated sludge process was invented in England at the beginning of 20th century. At that time England was the country with probably most urgent problems in water pollution because of dense population and advanced industry. Repeated hygienic problems in English towns and cities and the demand of industry for clean water led to the formation of  the Royal Commission on Sewage Disposal in 1898 which can be considered as the milestone in the development of wastewater treatment technology. This commission co-ordinated the activities leading to better understanding of factors affecting the water quality in receiving waters and to evaluation of new treatment procedures. One of the best known outputs of the commission is the BOD5 test recommended in 1908. The famous "30:20 + full nitrification" effluent standard was adopted in 1912 which was a great challenge for the development of wastewater treatment processes capable of meeting this standard.
	Dr. Fowler, the initiator of the first activated sludge studies in England, made a trip to Lawrence Experimental Station in Massachusetts, USA in 1912 and studied the aeration of municipal wastewater in different arrangements. After his return to England, Dr. Fowler informed about his experience at the Lawrence Station experiments to Mr. Edward Ardern, chemist at the Manchester - Davyhulme wastewater treatment plant, and his co-worker, Mr. William Lockett. Ardern and Lockett understood for the first time the active role of suspension formed during the aeration, known now as activated sludge.

Lockett and Ardern found soon that the amount of the sediment increased with increasing number of batches. At the same time the aeration time necessary for "full oxidation" of sewage (full oxidation was a term used for description of removal of degradable organics and for complete nitrification). By this technique of repeated batch aeration with the sediment remaining in the bottle Lockett and Ardern were able to shorten the required aeration time for "full oxidation" from weeks to less than 24 hours which made the process technically feasible. The sediment formed during the aeration of sewage was called activated sludge for its appearance and activity.

The effort of English engineers, chemists and microbiologists led finally to the invention of activated sludge process in 1914.

One of the most widely used methods of wastewater treatment is the activated sludge process (ASP) (Snidaro et al 1997). The activated sludge process has been used for more than 60 years and continues to be used for the treatment of both industrial and municipal wastewaters (Wong et al 1997). One of the most widely used methods of wastewater treatment is the activated sludge process (ASP) (Snidaro et al 1997). The activated sludge process has been used for more than 60 years and continues to be used for the treatment of both industrial and municipal wastewaters (Wong et al 1997). In the activated sludge process, the quality of the effluent is to a large extent dependent on how the biological sludge mass can be separated from the treated  wastewater. The solids/liquid separation traditionally takes place through a separation of spontaneously aggregated flocs of activated sludge by gravity sedimentation in secondary clarifiers.

The activated sludge process is governed by the microorganism characteristics and the physical configuration of aeration tank. As such, the biological kinetics and the process kinetics are closely interconnected. Process kinetics is based on the Monod equation and it has been described by many authors (Metcalf and Eddy, 1979; Eckenfelder and Grau, 1992).

In the optimal design of an activated sludge system there is a relationship between the design of the aeration tank and the secondary clarifier. The performance of the aeration tank varies with the return sludge concentration and flow rate while the clarification and thickening functions of the clarifier depend on the effluent from the activated sludge tank. Clarification efficiency of a secondary clarifier is a critical factor in determining the efficiency of the entire wastewater treatment system. According to Laquidara and Keinath (1983), the clarification criterion is important only at severe changes in hydraulic load and then only for a short period of time, because if the hydraulic loading persists the thickening or solids handling criterion will in time becomes the governing one.

Fitch (1957) maintained that hydraulic detention time rather than overflow rate was the major variable governing solids removal from secondary clarifiers. Pflanz  (1969) carried out a 2-year study of secondary sedimentation on one circular and two rectangular tanks. Overflow rate, the concentration of solids in the feed to the settler, sludge settleability as measured by sludge volume index (SVI) and temperature were all found to affect the effluent clarity. Because of the concentration of suspended solids in the mixed liquor was the most important factor, Pflanz recommended that the secondary settlers be designed on the basis of mixed liquor suspended solids (MLSS) concentration as well as hydraulic loading.

Excessive solids in secondary clarifier effluents occur primarily because of one or more of the following (Ekama et al., 1997):

- hydraulic short-circuiting or resuspension of solids from the surface of the sludge blankets by high velocity currents;

- thickening overloads resulting in high sludge blankets and potential loss of solids when the blanket reaches the effluent weir;

- denitrification, causing solids to float to the surface;

- flocculation problems due to either flocks breakup or poor floc formation;

- insufficient capacity of the sludge collection system

The problem of excessive hydraulic loading to a treatment facility, especially as a result of storm runoff often occurs at many wastewater treatment plants. Exceeding treatment capacity can jeopardize further treatment efficiency as well as result in serious effluent deterioration.

Typical designs for activated sludge systems do not ease the effects of hydraulic overloading. However, the pilot studies conducted by Olsson et al. (1986) showed that the provision of freeboard in the aeration basin coupled with the use of an appropriate effluent weir design lessen the hydraulic effect and reduced the effluent SS.

The ability of microorganisms to form flocs is vital for the activated sludge treatment of wastewater. The flocs are aggregates of suspended solids containing different groups of microorganisms resulting from physicochemical and biochemical flocculation. They are irregularly shaped, fragile and have high water content. Particles in activated sludge vary from a single microorganism cell, the size of a few microns or less to a large number of cells up to several thousand microns in size. Finstein and Heukelekian (1967) considered flocs as particles with diameters larger then 20µm. Javakeri and Dick (1969) defined a floc as a group of primarily particles and the liquid within it and an aggregate as a cluster of flocs and the liquid between them.

Physical state and properties of activated sludge flocs influence the mass transport and effectiveness of wastewater treatment process. The floc structure enables not only the adsorption of soluble substrates but also the adsorption of the colloidal matter and macro- molecules additionally found in most wastewater. The adsorptive capacity of flocs therefore facilitates the oxidation of this complex wastewater. However, important also is their ability to settle in a relatively short time under quiescent conditions; otherwise the biomass produced as a result of oxidation of the waste would pass to the receiving watercourse exerting a large pollution load.

There are four main phenomena that lead to a decrease of the quality of the effluent due to the escape of flocs:

• 	Bulking sludge due to an excessive growth of filamentous organisms and/or surface polymer presence (Sezgin et al. 1978, Jenkins et al. 1984, Chudoba et al. 1985; Forster, 1971; Pavoni et al. 1972)

• 	Pinpoint floc consisting of small floc particles present in the supernatant after the sludge has settled (Sezgin et al. 1978, Pipes, 1978, Palm and Jenkins, 1980)

• 	Floating sludge attributed to the presence of filamentous organisms that originate a foam in the aeration basin ( Strom and Jenkins 1984, Pujol, 1991)

• 	Rising of the sludge after settlement in the clarifier due to the nitrogen produced in the denitrification process (Wagner, 1984)

When sludge settles poorly it is generally described as being a bulking type. Bulking is attributed to an infection of the sludge by filamentous organisms. A highly filamentous sludge can have a relatively low SVI. SVI of the filamentous sludge can change rapidly, whereas the SVI of a nonfilamentous sludge is stable (Pipes, 1979).

There are many factors that influence the growth of filamentous bacteria. They include: low oxygen concentration, high oxygen concentration, high sulfide concentration, lack of certain nutrients like N and P, too high or too low sludge loading, high carbohydrate concentration, high concentration of fatty acids and the feed pattern.

The activated sludge bulking can also occur when filamentous microorganisms are completely missing. Such phenomena is called zoogleal or more exactly nonfilamentous bulking and is related to viscous exocellular polymers produced in excess by some kinds of bacteria. This phenomena was for the first time described by Heukelekian and Weisberg (1956).

Novak et al. (1993) summarized several different reasons of non-filamentous bulking. They include:

• 	the composition of wastewater supports the formation of zoogleal growth, mainly the high content of low and long chain fatty acids and oleic compounds;

• 	the high sludge loading and/or an influent containing an insufficient amount of certain nutrients;

• 	in some cases selector systems significantly stimulate the growth of zoogleal colonies;

It was observed long ago that under environmental shock conditions activated sludge microorganisms do not agglomerate and form a settleable flocs, but occur mostly in the form of non- settleable suspended solids (pin-point floc). These dispersed biosolids (primary solids) either have not been incorporated into a floc particle or have been sheared from a floc particle as a result of excessive turbulence in the aeration basin or some other operational disturbances. Secondary effluents from such systems are very turbid and have high values of BOD and COD. The causes of the dispersed growth can be divided into two groups (Chudoba, 1989). One group involves parameters of the technological process e.g. MLSS concentration, sludge retention time (SRT). Usually, lower SRT results in higher proportion of sludge becoming a non-settleable dispersion. At such a high loading bacteria live in the environment containing higher concentrations of substrate, and so they cease producing glycocalyx which is responsible for flocculation. The other group involves factors connected with the wastewater composition. Temporary deflocculation also occurs as a result of the sudden changes in temperature, salinity and pH value (Pipes, 1969). Permanent deflocculation may occur due of the absence of macro or micronutrients or the presence of toxic materials in the process; the toxicity of heavy metals results from the binding reactions between them and the active cellular components to form inactive complexes (Pearson and Dugan 1971).

The overall efficiency of a biological treatment process depends on the settling characteristics of the activated sludge flocs. In wastewater treatment plants sludge thickening occurs in the lower portions of clarifiers. A number of parameters have been developed to obtain a quantitative measure of the settleability of activated sludges. The traditional sludge volume index (SVI) (Mohlman sludge index) is the mainly performed test. The shortcomings of SVI have been discussed by Dick and Vesilind (1969). Their data show that SVI does not relate to such parameters as sludge yield strength, plastic viscosity, and an initial settling velocity. The variation of SVI values with the suspended solids concentration and the sludge volume makes it difficult to compare the SVI values for instance between different plants. Two sludges with the same SVI may have different sedimentation and dewatering properties.

Pipes (1979) reported that high SVI is usually the result of filamentous microorganisms presence in the sludge and that higher SVI usually produces a lower effluent TSS. The relationship between SVI and organic loading has been investigated for instance by Ford and Eckenfelder (1967), Ganczarczyk (1970), Rensink (1974), Pipes (1979). They found low SVI within the intermediate range of the loading 0.2 - 0.4 g /g d.

In spite of these weaknesses the wastewater treatment plant operators keep using the SVI successfully on a day-today basis.

Although ASP is advantageous compared to many methods of wastewater treatment, but the rate of sludge production is relatively high for most of its versions. Excess biomass produced during the biological treatment of wastewaters requires costly disposal. Its disposal may account for 60% of total plant operating cost (Horan 1990). Further, as environmental and legislative constraints increase, the cost of sludge disposal is significantly going to increase (Lapinski and Tunnacliffe 2003). Thus, there is a considerable impetus for reducing the amount of sludge produced from wastewater treatment.

At steady state, the rate of sludge production (QwXu + QeXe) for ASP can be estimated according to the following definitions (Lawrence and McCarty 1970):

QwXu + QeXe = YQo (So-S)-VXKd

In practice, the following equation can also be used to estimate the rate of sludge production (Metcalf & Eddy 1991);

QwXu + QeXe = YabsQo (So-S)

where Yabs is obtained as Y/(1+c Kd) in which, Y=yield coefficient; V=reactor volume; Qo=flow rate into the reactor; c =sludge residence time; and Kd=the specific decay rate.

On the basis of the above equations, the sludge production is significantly reduced for higher values of c and Kd as well as lower value of Y (Henze et al. 1987; Saunamaki 1988; Horan 1990). Consequently, numerous techniques were developed for reducing the sludge production in ASP by optimizing the parameters Y, Kd, and c. The most accepted techniques for optimizing these parameters biologically are to:

- Increase the solid retention time (Sakai et al 1992).

- Incorporate anaerobic, or attached operation in sequence with ASP (Chudoba et al.1992).

- Operate the process under a low loading rate with a high biomass concentration and high sludge age (Henze et al. 1987; Saunamaki 1988),

- Charge the reactor with special cultures (e.g. Bdelliod rotifers), which consume high amounts of biomass (Lapinski and Tunnacliffe 2003), and

- Manage the food chain, which stimulates the balanced growth of cells, and thus the growth of higher organisms such as protozoa and metazoa (Ratsak et al. 1994; Lee and Welander 1996 a,b).

In the conventional ASP, the approximate values of Yobs can easily be predicted from the above equation under any conditions. It increases with lower levels of c until reaching maximum value at a biomass washout conditions at minimum sludge age (Mc). Its maximum value [(Yobs)max] can be estimated from the following equation:

(Yobs)max = Y/(1+ Mc Kd)

Generally, (Yobs)max, in ASP, has a fixed value for each specific wastewater and can be obtained by substituting 1/ Mc  as YK-Kd

(Yobs)max = Y-Kd/K

where K= maximum specific rate of substrate utilization.

Solids handling costs constitute a considerable portion (upto 50-60%) of the operating budget of a typical waste water treatment plant (Evans 1989) and have been  steadily increasing as more stringent regulations governing biosolids disposal practices are promulgated (Balm’er 1994). A cost effective approach would include ways to reduce sludge production and facilitate sludge processing while simultaneously improving operation and increasing unit process loading rates. Clearly, any process, which can reliably improve the efficiency of existing wastewater treatment processes, will have an economically significant cost savings potential (David et al. 2004).

The performance of activated sludge wastewater treatment and sludge management systems is limited by the maximum operational efficiency of the unit processes, most of which have not changed substantially in the last several decades. Operational problems that inhibit treatment performance will hinder the ability to deal with expected increased loading in the future. In the United States, more than $2 billion is spent annually treating and managing approximately 5-7 million tones of biosolids from over 13,000 publicly owned treatment works (POTWs) (Ponugoti et al 1997).

The U.S. EPA secondary treatment regulatory standards, set in 1972 and still in effect, were focused mainly on the removal of BOD and TSS and require 85 percent removal of each. Most treatment applications involve the removal of organic constituents and compounds. Because a wide range of constituents and compounds exist in waste water, the organic content is quantified in terms of biodegradable soluble COD (bs COD) or BOD.

Biochemical oxygen demand (BOD) is currently considered to be the most important parameter of wastewater quality, but the standard laboratory procedure to measure it takes five days from sample collection to result (Standard 1992). This is far too slow to use for wastewater treatment plant process control (Iranpour et al. 1997)

In all treatment systems overall performance is gauged by sampling the influent to the plant and the effluent from it. Accomplishments of component units are determined in similar fashion (Fair et al. 1968).

Expected efficiencies of various treatment units are given in Table-2.1

Table-2.1  Expected efficiencies of various treatment units

| Unit | Percentage SS | Reduction BOD | Total Coliform |
| --- | --- | --- | --- |
| 1. Primary Treatment (Sedimentation) | 45-60 | 30-45 | 40-60 |
| 2. Secondary Treatment Activated sludge plants | 85-90 | 85-95 | 90-96 |

Source: Adopted from CPHEEO Manual.

I.S.: 4764 – 1973, lays down the standards for treated effluent from a sewage treatment plant, as under:

Maximum Biochemical Oxygen Demand (BOD5)	- 20 mg/L

Maximum Suspended Solids (SS)			- 30 mg/L

Chapter    3

ACTIVATED SLUDGE PROCESS

  - Activated Sludge Process

The activated sludge process is an aerobic treatment process which converts non-settleable substances in finely divided, colloidal and dissolved form into a biological floc, or activated sludge. The process uses microorganisms to feed on organic contaminants in wastewater, producing a high-quality effluent. The basic principle behind all activated sludge processes is that as microorganisms grow, they form flocs that clump together. The biochemical oxygen demand (BOD) in the form of suspended solids is removed by physical enmeshment with biological flocs. Colloidal organics are flocculated and absorbed with the biological flocs. These flocs are allowed to settle to the bottom of the tank, leaving a relatively clear liquid free of organic material and suspended solids.

It is rather a unique biotechnological process which consists of an aerated suspension of mixed bacterial cultures which carry out the biological conversion of the contaminants in the wastewater. The aeration tank, while having many possible configurations, basically retains the influent wastewater for a number of hours (or days) in a well mixed/aerated environment, before forwarding the effluent for further settling to the secondary clarifier. The end products of the clarification process are clarified effluent that is discharged to the open water bodies and sludge. A fraction of the sludge is returned to the aeration tank and is called returned activated sludge. The sludge contains a high density of biomass and an active population of microorganisms is always maintained in the tank. The influent wastewater provides the basic food source for the microorganisms in the aeration tank. This biodegradable organic material is converted into new bacterial cells and other end products include CO2, NO3 and SO4.

  - Process Kinetics

The activated sludge process is a suspended-culture process with sludge return.  The process is aerobic, with oxygen being supplied by dissolution from entrained air. The removal of dissolved and particulate carbonaceous BOD and the stabilization of organic matter found in waste water is accomplished biologically using a variety of microorganisms, principally bacteria. Aerobic bacteria thrive as they travel through the aeration tank. They multiply rapidly with sufficient food and oxygen.  Microorganisms are used to oxidize (i.e. convert) the dissolved and particular carbonaceous organic matter into simple end products and additional biomass. By the time the waste reaches the end of the tank (between four to eight hours), the bacteria has used most of the organic matter to produce new cells.  Because the biomass floc particles size (50-200 micrometer) has a specific gravity slightly greater than that of water. The biomass can be removed from the treated liquid by gravity settling.

The biochemical equation for bacterial cell respiration and synthesis, in using organic matter as substrate, in the activated sludge process is:

bacteria

organic matter + O2 + nutrients                     CO2 + NH3 + new biomass + end products

For a completely mixed system, mass balance equations, at steady-state conditions, i.e. no change in biomass or food concentrations with time, are as follows (Peavy et al. 1985):

Biomass		Biomass		Biomass out

in		+          growth        =   (effluent + wasted sludge)

Qo Xo+ V  ( ko XS  - kdX ) = (Qo - Qw) Xe + Qw Xu			(3.1)

Ks + S

Food in –  Food consumed = Food out

Qo So -  V    ko SX    = (Qo-Qw) S + QwS			(3.2)

Y (Ks + S)

where Qo, Qw = influent and waste-sludge flow rate, respectively, m3/d

Xo, X, Xe, Xu = biomass concentration in influent, reactor, effluent, and clarifier

underflow (waste sludge), respectively, kg/m3

So, S	= soluble food concentration in the influent and reactor, respectively,      			   kg/m3

V =   volume

Ks, ko, kd, Y =   Kinetic constants having units, kg/m3, d-1, d-1, kg/kg

Equations (3.1) and (3.2) can be simplified by making the following assumptions:

- The influent and effluent biomass concentrations are negligible compared to biomass at other points in the system.

- The influent food concentration So is immediately diluted to the reactor concentration S because of the complete-mix regime.

- All reactions occur in the reactor; i.e., neither biomass production nor food utilization occurs in the clarifier.

- Because of assumption 3, the volume V represents the volume of the reactor only.

With these assumptions,  Eqs. (3.1) and (3.2) are rearranged as follows:

koS      =        Qw Xu   + kd					(3.3)

Ks + S             VX

koS        =      Qo  Y   + (So – S)				(3.4)

Ks + S             V  X

Combining these equations give

Qw Xu         =      Qo  Y   + (So – S) - kd				(3.5)

V  X   	    	   V  X

The inverse of the expressions Qw Xu / VX and Qo/V have unique physical significance in the activated-sludge system. The quantity

V/Qo = 							(3.6)

is the hydraulic detention time in the reactor based on influent flow. The ratio of the total biomass in the reactor to the biomass wasted per given time

VX         = c

Qw Xu  								(3.7)

represents the average time that microorganisms spend in the reactor. This parameter, called the mean cell-residence time will be greater than the hydraulic detention time since most of the sludge from the clarifier is returned to the reactor. Substituting Eqs. (3.6) and (3.7) into Eq. (3.5)

1   = Y (So – S)    - kd					(3.8)

c        X

The concentration of biomass or mixed-liquor suspended solids (MLSS) as it is more often called, in the reactor is related to the mean cell-residence time and the hydraulic detention time, and is found by solving Eq. (3.8) for X.

X = c Y(So – S)						(3.9)

 (1 + kd c)

Although this equation indicates that shortening the hydraulic detention time increases the MLSS when the other variables are held constant, there is a limit beyond which this is not true. When the hydraulic detention time approaches the regeneration time for the microorganisms, cells are washed out of the reactor before growth can occur. Consequently, X decreases and S approaches So, meaning that no treatment is occurring.

  - Design Considerations

Many factors affect the design of activated-sludge systems. One factor in activated-sludge design that should be stressed is the inter dependence of the biological reactor and the secondary clarifier. High biomass concentrations and short aeration periods may produce good treatment efficiencies with respect to soluble BOD. The savings in aeration tank volume is offset, however, by the large secondary clarifier required to clarify the effluent and thicken the sludge. Because of thickening limitations, it is the secondary clarifier that usually sets the upper limits on the biomass concentrations in the reactor.

Design variables for activated sludge reactors include (1) volumetric loading rates, (2) food-to-mass ratios, and (3) mean cell-residence times. The volumetric loading rate VL is the mass of BOD in the influent divided by the volume of the reactor, or

V L = QSo					(3.10)

V

the units of which are kilograms of BOD per cubic meter-day. The food-to-mass ratio F/M is the mass of BOD removed divided by the biomass in the reactor, or

F/M = Q(So – S)				(3.11)

VX

The units being kilograms of BOD per kilogram of biomass.day.

The mean cell residence time, c in Eqs. (3.7) and (3.8) is currently the most commonly used design parameter. Both the F/M-ratio and c, approach to design allow for trade-off between reactor volume and concentration of MLSS in the reactor.

3.4	Factors Affecting Performance

The activated sludge wastewater treatment process is capable of producing an excellent effluent quality when properly designed, constructed and operated. BOD and TSS removal rates in excess of 99% are not unusual. There are three areas of major concern in an activated sludge plant:

1. The characteristics of the influent that is going to the aeration basin.

2. The environment in the aeration basin that must be maintained to ensure good treatment.

3. The operating conditions within the secondary clarifier, which affects how well solids separation will occur.

All three of these areas are closely related and influence each other.

3.4.1	 Influent characteristics

3.4.1.1	Organic and Hydraulic Loading

In most municipal activated sludge wastewater treatment facilities, the influent flow and BOD/TSS concentration does not vary by more than 10% from day to day. This results in a relatively stable (and predictable) loading being applied to the aeration basin.

3.4.1.2	Effect of Toxic Substances

Toxic substances affect the performance of an activated sludge plant. If the influent that is being fed to the organisms in the aeration basin cannot be metabolized or if it is toxic, the organisms will die off and the process will fail. According to Adams et al. (1975) the degree of toxicity of heavy metals is related to overall metal equilibrium in the aeration tank and is independent of heavy metals concentration, microorganism concentration and organic loading. The concentration of these variables affects the proportion of the active components tied up in the metal ligand complexes, and subsequently affects the extent of metal toxicity.

3.4.2	 Aeration basin environment

3.4.2.1	Food and Dissolved Oxygen

The aeration basin environment can best be described as a zoo of microorganisms each competing for oxygen, food and the ability to reproduce. This zoo of organisms needs correct amount of oxygen, mixing and food. The food is of course supplied in the form of dissolved and suspended solids in the wastewater itself. The level of oxygen in the aeration basin can be controlled (to an extent). A dissolved oxygen level of >1.0 mg/L is desirable, but it is important to understand that the required level of dissolved oxygen is actually related to the F:M ratio that the system is operating under. This is because the microorganisms in the basin primarily consume the oxygen as they capture and metabolize the dissolved and particulate waste solids. If the BOD loading increases, the amount of dissolved oxygen that is needed in order for the microbes to capture and stabilize the waste will increase. If the BOD loading decreases, the oxygen demand for the system will go down.

3.4.2.2	Adequate Mixing

Thorough mixing of the contents of the aeration basin is very important. No settling should occur in the basin itself. Solids that settle to the bottom of the basin will rapidly become septic and cause a variety of problems, such as increased oxygen demand, lower aeration basin detention times and excess growth of the types of filamentous bacteria that are associated with septic conditions. However, excessive mixing also has a down side. If the turbulence in the aeration basin is too high, a phenomenon known as floc shear will occur. Floc shear is characterized by floc particles that are broken up. In the secondary clarifier, this leads to increased effluent TSS concentrations.

3.4.2.3	Correct F:M

In order to achieve good treatment and a stable system, the mass of microorganisms must be maintained at the correct level needed to consume virtually all of the food that enters the system each day. Conventional systems run at an F:M between 0.25 and 0.5 to 1.00. By increasing or decreasing the overall mass of MLSS, the number of microorganisms available to consume the daily load of waste solids can be changed. Although the amount of loading (food) varies a little each day, overall, it stays close to the same. The key to stabilizing the activated sludge process lies in doing a good job of maintaining the right mass of microorganisms to fully consume the daily loading, all of the time. To accomplish this, the amount wasted from the system each day needs to be close to the amount that enters the system each day, with some allowance for solids that are destroyed through digestion while in the aeration basin or lost to the effluent. Typically, this means that the number of kilograms of solids wasted from a system each day must be around 50 – 70% of the total number of kilograms of solids that enter the system each day. The difference between the influent loading and the required WAS kgs./day is made up through digestion in the aeration basin and solids lost to the effluent.

3.4.3 	Secondary clarifier conditions

3.4.3.1 Clarifier Design Features

The design of the secondary clarifier of an activated sludge wastewater treatment plant can have a strong effect on how the system will perform as a whole. Desirable features that should be included in activated sludge secondary clarifiers include:

• Good inlet flow control structures that allow to carefully regulating the hydraulic loading to the clarifier.

• Energy dissipating baffles at the mixed liquor inlet area that quickly slow the mixed liquor and direct it downward. Some provision for gentle mixing during entry into the clarifier is helpful at starting bio-flocculation.

• Short-circuiting should be eliminated. Short-circuiting occurs when a portion of the mixed liquor that enters the clarifier is allowed to move rapidly toward the weirs and out of the clarifier. There are many causes of short-circuiting, such as thermal density-currents and poor baffle design; however, the most common cause is uneven weirs that draw the clarifier supernatant over one area at a much higher rate than other areas of the weir.

• Secondary clarifiers should be deep enough to allow some process upsets without the loss of the sludge blanket. Normally the clarifier depth should be greater than 3.5 m.

• A detention time of between 2 and 4 hours should be provided for the highest flow (peak flow) that the clarifier will be subjected to. This is a function of the clarifier’s volume.

• Effective sludge removal for the entire bottom of the secondary clarifier. This typically includes a sludge scraper mechanism that sweeps the bottom of the clarifier and moves settled sludge toward the RAS pump inlet box.

• Accurate control of the RAS pumping rate. This is critical for ensuring that the sludge is removed at the proper rate. Some form of RAS pump control and flow measurement should be provided.

• Drains should be provided for each clarifier so that they can be taken down for service and inspection.

3.4.3.2 RAS Flow Rate

The sludge blanket depth in an activated sludge secondary clarifier should be determined at least twice a day by actually measuring the blanket at about the middle of the clarifier bridge. In general, the RAS pumps should be run just fast enough to maintain the smallest sludge blanket in the clarifier possible.

If sludge settles well but is not removed from the secondary clarifier fast enough, biological activity will continue in the sludge, resulting in the formation of nitrogen gas bubbles. These nitrogen gas bubbles will cause particles and even clumps of sludge to float to the surface of the secondary clarifier (this process is known as denitrification). Whenever this type of “rising sludge” is observed in an activated sludge secondary clarifier, it is a sign that RAS pumping rate should be increased.

3.5 	Control Strategies

3.5.1	MLSS and MLVSS Concentration

Though maintaining the proper F:M ratio in the system is essential for good treatment yet activated sludge plants are not operated on a day to day basis based on the F:M ratio. A system’s F:M ratio is really just a way of assessing the treatment process, not a way of controlling it. Part of the reason for this is that the information concerning the influent BOD loading used to calculate the F:M ratio is already 5 days old when an operator receives it because the BOD test takes 5 days to conduct. Decisions about changes to the wasting rate of a system must often be made on a daily basis and the information included in the F:M ratio is already at least 5 days old before it can be applied. Hence instead of the F:M ratio, judgments about the waste rate are based on the concentration of the mixed liquor in the aeration basin. This is measured using the total suspended solids (TSS) test on a sample of mixed liquor drawn from the end of the aeration basin, just before entering the secondary clarifier. When the TSS test is used to measure the concentration of mixed liquor, the result is reported as the mixed liquor suspended solids, or MLSS. If the volatile fraction is also measured, it is reported as the mixed liquor volatile suspended solids concentration, or MLVSS. Most activated sludge processes operate at a MLSS concentration of between 1,000 and 5,000 mg/L. Often, it will be discovered that a particular wastewater plant operates very well at say 2,500 mg/L and so the  wasting can be increased or decreased in order to maintain a MLSS concentration of 2,500 mg/L. In effect, this is nothing but maintaining the same overall mass of microorganisms by holding the concentration constant (because the volume of the aeration basin does not change). This has the effect of maintaining the correct F:M ratio. The percentage of MLSS that is volatile will vary depending upon the rate that solids are digested within an aeration basin. Typically, activated sludge systems operate with a MLVSS concentration that is about 70% of the total MLSS. For systems that operate at high F:M conditions, the percentage is more like 80%. For systems operating under low F:M conditions, the volatile percentage can be as low as 60%. The MLVSS represents the living fraction of the mixed liquor solids. The rest of the MLSS is just inert matter that is trapped in the system, but not providing any treatment to the incoming wastes. Systems operating under high F:M conditions do not have as much time to digest the incoming wastes as effectively as systems that operate under low F:M conditions. This is why the percentage of the MLSS that is volatile is higher for high F:M systems. Although the activated sludge process can be operated based upon the MLSS and MLVSS concentrations alone, it is not always a good idea to do so. This is because this approach does not take into account all of the solids that are entering and exiting the system on a daily basis. The reason is that the influent hydraulic and organic loading to the system does actually vary from day to day.

3.5.2	Sludge Volume Index (SVI)

When an activated sludge process is operating well, it will primarily contain a mixture of simple round and rod shaped bacteria, an assortment of higher life forms known as protozoa, and a few long, hair-like filamentous bacteria that add strength to the bio-flocculated structure (known as floc). If the right conditions cannot be maintained in the system, this balance of microorganisms in the floc will change. For systems operating at very high F:M ratios and low SRTs, the organisms do not remain in the system long enough for the slower growing protozoa to appear. For this reason, this condition is referred to as “young sludge”. The settling characteristics of young sludge are slow, and a cloudy supernatant, laden with large straggler floc particles is left behind. If the system is operating at a very low F:M ratio and a high SRT, larger, slow growing organisms such as rotifers and sludge worms will begin to appear. This condition is often referred to as “old sludge”. Old sludge tends to settle very rapidly but leaves pin floc in the supernatant and a surface material known as “ashing”. Ashing appears just as though ashes were scattered on the surface of secondary clarifier. One of the most common problems that arise in the activated sludge process is the proliferation of excessive amounts of filamentous type bacteria. The problem has many causes, including septic conditions, low D.O. conditions and operating the system at the wrong F:M ratio. The growth of excessive numbers of filamentous bacteria results in a floc that cannot separate from liquid due to the hair-like projections of the filaments. This condition is know as “sludge bulking”, and it can lead to the total loss of the solids inventory in the treatment system as the sludge is washed out of the secondary clarifier. The MLSS test provides information about the concentration of solids in the aeration basin, but does not give insight into the settling characteristics of the sludge. In order to analyze the settling characteristics at a given MLSS concentration, it is necessary to calculate a value known as the sludge volume index, or SVI. The SVI of mixed liquor is determined by knowing both the sludge’s settling characteristics and its MLSS concentration. The SVI is an index of how well a sludge will settle at a given MLSS concentration. The SVI is most useful at identifying filamentous organism outbreaks, allowing for remedial actions before the system is out of control. For most activated sludge treatment plants, a SVI range of 80 – 120 signals good treatment. SVI values of <80 indicate older, fast settling sludge and the need to waste solids. SVI values over 150 almost always indicate a serious filamentous bacteria outbreak that must be dealt with before the entire solids inventor is lost from the system. Hence these ranges give a good indication of where most plants operate well and when most plants will get into trouble, but they are not hard and fast rules. This is because different systems have different secondary clarifiers. Shallow, poorly baffled secondary clarifiers do not respond well to bulking conditions, whereas deep, well baffled clarifiers can handle SVI values at or above 150 before loosing the sludge blanket to washout. If the equipment is available to measure the settleability and the MLSS concentration of a mixed liquor, the SVI value offers a powerful tool for assessing the condition of the biological process.

3.5.3	 Mean Cell Residence Time (MCRT)

Because of the time delay involved in generating the data used to determine the F:M ratio, it is not used to control the secondary treatment process, however, a similar approach, based on other information that can be collected in a timely manner, can be used. The mean cell residence time (MCRT) approach to balancing the solids in the activated sludge treatment system offers a simple and effective way to operate the activated sludge process ahead of the curve. What the MCRT approach attempts to do is account for all of the solids that are in the system as well as all of the solids that exit the system everyday. A system’s MCRT is a representation of the average time (in days) that a bacterial cell will remain in the system before being removed as WAS or leaving in the effluent. The calculation is made by dividing the total kilograms of MLSS in the aeration basin by the total kilograms wasted each day and the total kilograms that exit the in the effluent each day. A system’s MCRT is very similar to its SRT, except that the MCRT looks at what is leaving the system each day and the SRT looks at what is coming into the system each day. Typically, conventional activated sludge systems run at MCRTs of < 15 days. In order to use the MCRT approach, daily information about a system’s MLSS concentration, WAS concentration, WAS flow, effluent TSS concentration and effluent flow are needed. The MCRT approach to process control should be used based upon a seven-day running average. In other words, seven days worth of WAS pump adjustments are averaged, and that average is what the pump is actually set to run each day. Using a seven-day running average prevents large changes to the wasting rate at any one time. It is very important that large changes are not made if the system is to operate as a stable process. Even if the seven-day running average is not used, a good rule of thumb to follow is “never change the waste rate by more than 10% a week”. The MCRT approach offers a valuable method of balancing the solids in an activated sludge system. It is particularly suited to plants that treat 1.0 MGD and more, because these treatment facilities have the necessary in-house laboratory capability to generate the needed data. It must be applied to a treatment plant in a consistent manner and is only as good as the laboratory sampling and analysis. Any error introduced through non-representative sampling or inaccurate flow measurements will be magnified as errors in the MCRT calculation.

3.6	Typical Activated Sludge Wastewater Treatment 	Plant

The first unit operation generally encountered in waste water treatment plants is screening. A screen is used to retain solids found in the influent waste water to the treatment plant. The principle role of screening is to remove coarse materials from the flow stream that could (1) damage subsequent process equipment, (2) reduce overall treatment process reliability and effectiveness, or (3) contaminate waterways.

Grit chambers are designed to remove grit, consisting of sand, gravel, cinders or other heavy solid materials. Grit chambers are provided to (1) protect moving mechanical equipment from abrasion and accompanying abnormal wear, (2) reduce formation of heavy deposits in pipelines, channels and conduits and (3) reduce the frequency of digester cleaning caused by excessive accumulation of grit.

The objective of Primary Clarifier is to remove readily settleable solids and floating material and thus reduce the suspended solids content. The efficiency of sedimentation basin  with respect to the removal of BOD and TSS is reduced by (1) eddy currents formed by the inertia of the incoming fluid, (2) wind induced circulation cells formed in uncovered tanks, (3) thermal convection currents, (4) cold or warm water causing the formation of density currents that move along the bottom of the basin and warm water rising and flowing across the top of the tank, and (5) thermal stratification in hot and climates (Fair and Geyer, 1954)

An aeration tank is a reactor where the biological reactions occur. It provides oxygen and mixing.

Secondary clarifier is a sedimentation tank where the solids settle and are separated.

Chapter    4

METHODOLOGY FOR PERFORMANCE EVALUATION OF SEWAGE TREATMENT PLANTS

4.1	Performance evaluation

The evaluation of performance efficiency of a treatment plant or unit process operation for percent removal of the organics is an important exercise in the operation of the systems. The results can be compared with those listed in the plant’s operation and maintenance manual (O&M) to determine whether the facility is performing as expected. The equation used to determine plant performance and efficiency, is given by,

[Influent concentration – Effluent concentration] x 100

% Removal =                        	Influent concentration

The concentration may be either SS, BOD, COD or any other constituents. The concentration entering the unit and the concentration leaving the unit (i.e. primary clarifier, secondary clarifier etc.) are used to determine the unit performance.

  - Methodology

During the preliminary visits, the routine operation of the plant is observed critically to plan the evaluation and to decide the sampling locations, the frequency of the sampling and parameters to be analyzed for evaluation.

An activated sludge process sewage treatment plant generally comprises of flow measuring devices, mechanical bar screens, grit chambers, primary settling tanks, aeration tanks, secondary settling tanks, digesters, gas holders and sludge drying beds.

A typical flow diagram for planning the evaluation of an activated sludge process plant is shown on the next page.

    - Collection of plant data, Raw sewage characteristics and Desired effluent quality

First step in evaluation procedure is to collect all the relevant data concerning the plant such as capacity, treatment process, various units and their functions. Basic design criteria will include daily flow, peak hourly flow, lean flow, raw sewage characteristics and

--contd.

--from pre-page

Flow Chart for Evaluation Planning

treated effluent characteristics.

Raw sewage characteristics of importance are temperature, BOD, COD, SS, total solids, volatile solids, chlorides, total alkalinity and pH etc. Desired effluent quality is generally defined by BOD and SS.

Design data in respect of mechanical bar screens, grit chambers, primary settling tanks, aeration tanks and secondary settling tanks are also studied.

    - Monitoring of Inflow

Raw sewage flow monitoring is generally done by Electromagnetic flow meter at and Parshall flume after the grit chamber. The plant inflow is measured at every two hours or earlier depending upon the fluctuations in the flow pattern. It is ascertained if the plant is under loaded or overloaded hydraulically. Fluctuations in the inflow is also noted.

4.2.3	Collection of sample

The collection of a representative sample is the most important. Two types of samples are collected and analyzed to determine the characteristics of raw sewage and treatment system effluent: grab samples and composite samples.  A grab sample is one that is taken to represent one moment in time and is not mixed with any other samples.  A grab sample is sometimes called an individual or discrete sample and will only represent sample conditions at the exact moment it is collected. Grab samples are typically used for unstable parameters such as temperature, dissolved oxygen or pH.  A composite sample is prepared by combining a series of grab (individual / discrete) samples over known time or flow intervals.  A composite sample shows the average composition of a flow stream over a set time or flow period if the sample is collected proportional to flow.

The primary use of an effluent sampling is to evaluate treatment system performance in order to verify compliance with specific discharge limits, or to compare the performance of individual systems.

The common sampling locations, parameters to be analyzed and nature of samples for performance evaluation are given in Table-4.1.

Table–4.1 Sampling locations, parameters and nature of samples for performance evaluation

| Sampling location | Type of sample | Parameters to be analyzed |
| --- | --- | --- |
| Grit chamber | Composite | BOD, COD, TS, TSS, TKN, total phosphorous |
|  | Grab | pH, temperature |
| Primary sedimentation tank | Composite | BOD, COD, TS, TSS, DO |
|  | Grab | pH |
| PST sludge | Grab | pH, TS, VS, % solids |
| Aeration tank | Grab | DO, TS, TSS, TKN, total phosphorous |
| Secondary sedimentation tank | Composite | BOD, TSS, DO, TKN |
|  | Grab | pH |
| SST Sludge | Grab | pH, TSS, VS, SVI |
| Anaerobic digester | Grab | pH, VA, Alkalinity, TS, VS |

    - Analysis of samples

Analytical methods used for testing of samples are given in Table-4.2.

Table-4.2  Analytical Methods for Analysis of  Sewage Samples

| Sr. No. | Parameters | Analytical methods for analysis of wastewater Standard methods (1985) 16th Edition. |
| --- | --- | --- |
| 1 | Total Solids | 209 A Total solids dried at 103 o C – 105 o C |
| 2 | Dissolved Solids | 209 B Dissolved Solids dried at 180 o C |
| 3 | Suspended Solids | 209 C Suspended Solids dried at 103 o C – 105 o C |
| 4 | Volatile / fixed | 209 D fixed and volatile solids dried at 550 o C |
| 5 | PH value | pH meter |
| 6 | BOD5 | Biological Oxygen Demand ( 5 days at 20o C ) |
| 7 | COD | 508 B Closed reflux method |
| 8 | Chlorides | 407 A Argentometric titration method |
| 9 | Oil & grease | 503 A Partition gravimetric method |
| 10 | Phosphate | Colorimetric test (by spectrophotometer) |

    - Study Performance of Units

      - Screen

Performance of screen is studied to find out whether it is meeting the design criteria. In case of deviation from the design, the screen is checked for hydraulic loading rate and velocity through the screen. Frequency of removal of screenings is also noted.

      - Grit Chamber (Detritus Tank)

Performance of grit chamber is adjudged for the quantity and quality of the grit removed. If it is as per design then performance is good otherwise check the hydraulic flow and horizontal velocity in the grit chamber. Frequency of removal of grit is also noted.

      - Primary Sedimentation Tank

Study the residual BOD, COD, TS and TSS as well as DO in the effluent from the primary sedimentation tank. If the percentage removals are as per design then performance be considered as good otherwise check the reasons for under performance such as hydraulic/organic loading rate, sludge draw off and scum removal.

      - Aeration Tank

Study MLSS, DO and SV % in the mixed liquor if it is not as per design then adjust the quantity of return sludge to correct the MLSS and SV% and modify the aerator capacity to correct the DO.

      - Secondary Sedimentation Tank

Study the quality of effluent from the secondary sedimentation tank with respect to BOD, TSS, DO, TKN and pH. If the effluent meets the desired quality then it can be considered that the secondary sedimentation tank is performing to the desired level. If quality of effluent is lower than the desired quality then check hydraulic/ organic loading rate, recirculation of return activated sludge, detention time, DO, SVI and MLSS to improve the performance.

      - Effluent Quality

If effluent meets the laid down standards thjen overall performance of the sewage treatment plant can be considered as satisfactory.

  - Performance Evaluation Report

After studying the results of various treatment units their performance is recorded. The overall performance of the treatment plant is the sum total of the performance of individual treatment units which is expressed in terms of percentage removal of BOD, COD and SS etc.

Chapter    5

EVALUATION OF PERFORMANCE OF 16 MGD SEWAGE TREATMENT PLANT

  - General

Delhi is situated at longitude 77o13’16. 08”E & latitude 28o37’58. 55” and altitude of 220m above MSL. The total area of NCT of Delhi is 1484 sq.km. Delhi is situated on the banks of the river Yamuna. The river Yamuna flows from north to south. A hard rocky ridge running from the Southern border of NCT in the south west in a north easterly direction to the western banks of the river Yamuna near Wazirabad barrage forms the main watershed in NCT of Delhi. The topography created a drainage system that carries rain and storm water from the higher elevations of the West to the Yamuna. The eastern low-lying side was originally part of the flood plain of the river and considered inhabitable. Today however this Eastern wing, also known as the Trans Yamuna area, houses about 20 % of the total population of Delhi.

Delhi started as a small city, with a population of approximately 410,000 in 1911 and grew steadily to reach a population of 920,000 in 1941 with the decadal growth rate averaging approximately 30%. Following independence, the sudden influx of migrants raised the population from 920,000 in 1941 to 1.74 million in 1951, registering a decadal growth of approximately 90%. In the next four decades the population growth has been above 50%. The total present population of Delhi is around 15 million.

The estimated wastewater generation from the DJB supply and ground water extraction is about 800 MGD. To provide treatment to the wastewater generated, Delhi has been divided into six sewerage zones namely Okhla, Keshopur, Shahdara, Coronation Pillar, Rithala-Rohini and outer Delhi. There are 30 wastewater treatment modules at 17 locations in Delhi with a total nominal (design) capacity of 512 MGD (2330 MLD). Most of the STPs use conventional activated sludge process (ASP) for wastewater treatment but a few operate on extended aeration and waste stabilization ponds.

The first sewage treatment plant in Delhi was constructed at Okhla in the year 1938. Presently Okhla STP has 5 modules of 30 MGD, 12 MGD, 45 MGD, 37 MGD and 16 MGD sewage treatment capacity with the combined treatment capacity of 140 MGD, the largest in Delhi. These plants treat the majority of the sewage generated in this zone. Most of the sewage generated from this catchment is conveyed through trunk or main sewers to six major pumping stations (Ring Road, Pargati Vihar, Kilokri, Andrews Ganj, Sarita Vihar and Tughlakabad) which discharge to Okhla STPs.

Under this project , study of the performance of 16 MGD STP has been done. The 16 MGD plant was constructed and commissioned in 2001.  This STP receives sewage from Sarita Vihar, Tigri, Deoli, Tughlakabad village, areas along M.B. Road, Badarpur Road and Mathura Road etc.

  - 5.2		Description of 16 MGD Sewage Treatment Plant

The treatment process followed at the plant is the Conventional Activated Sludge Process. The typical units are as follows:

- 2 mechanical bar screens

- 2 grit chambers

- Parshall flume with ultrasound-type flow meter

- 2 primary settling tanks with central drive mechanical sludge rakes

- Raw sludge pump house

- Aeration tank with 20 nos. surface aerators, each 40 hp (30 kW)

- 2 secondary settling tanks

- Return sludge pumping house

- 6 digesters provided with MS dome and gas mixing

- 2 gas holders

- 18 sludge drying beds

5.2.1 	Bar Screen

The raw sewage first enters ‘Bar Screen’. The screen arrests large floating objectionable matter. The screens used are ‘S’ type screens. These are Hindustan Dorr Oliver’s screens. These have reciprocating rake mechanism and are angled into the channel with a slight bent invert at the bottom to facilitate easy collection and withdrawal of screenings. The raking mechanism meshes with the bars which are spaced at suitable spacing. The rake runs in a track and is pulled up the slope by two cables which automatically reverse direction at the top of stroke. At this point the toggle rake shaft, which is attached to the track, pulls it and rake away from bars for the descending stroke. When the rake reaches bottom, the toggle shaft pushes it against the bar and the raking operation is repeated. The rake scraper is raised and lowered by the action of rake, pushing the screening for disposal. The drive consists of gear suitable for such application. One of the prominent advantages of Door Bar Screen is that it has no revolving, rotating, drive portion below water level. Thus the chances of mechanical failure due to chokage, rusting, wearing are minimized.

5.2.2	Grit Chamber (Detritor)

This has been designed to remove grit consisting of sand, gravel, cinders or other heavy solid materials that have subsiding velocities or specific gravities substantially greater than those of the organic putrescible solids in waste water. By providing detritors, the moving mechanical equipments further downstream in the plant are protected to a great extent from abrasion and accompanying abnormal wear. Such degritting devices also reduce the formation of heavy deposition in pipe-lines, launders and conduits and reduce frequency of cleaning of the tanks that may be otherwise required due to excessive accumulation of grit in such units.

5.2.3	Primary Clarifier

The Primary Clarifier of fixed bridge type has been provided to enable settlement of suspended solids in raw sewage. The settled solids is raked to the central discharge cone from where it is taken by gravity to a raw sludge pump house for further pumping to the digester.

The primary clarifier is also equipped with a skimmer scum trough and scum baffle to remove all floating suspension present in raw sewage. The primary clarifier aids settlement of suspension and reduce the BOD in raw sewage by about 40% before it is conveyed to the aeration tank for biological oxidation.

5.2.4	Aeration Tank

For the oxidation of organics (BOD) by aerobic biological treatment, conical type of slow speed surface aerators have been used in the aeration tank. The aerator ensures that the biomass developed in the tank remains in suspension and is uniformly distributed throughout the tank for optimum stabilization of sewage. Further, it also ensures that the maximum oxygen is transferred to liquid phase for utilization by micro-organism developed in the tank.

5.2.5	Secondary Clarifier

The aeration tank contents (MLSS) are settled in secondary clarifiers. The clarifier is a circular R.C.C. tank with bottom feed entry and comprises a feed well. The clarifier mechanism is centrally driven and consists of rake arms and squeegees to scrape the settled sludge to the control discharge cone. Settled sludge from the secondary clarifier is conveyed to a return sludge sump for recycle to the aeration tanks. The overflow represents treated sewage conforming to desired limits.

5.2.6	Return Sludge Pumps

Return sludge pumps of the horizontal, centrifugal, non clog type are being used to pump return sludge collected in the sludge sump.

5.2.7	Raw Sludge Pumps

Raw sludge pumps of the Cl. horizontal, centrifugal, non-clog type are being used to pump sludge collected in the sludge sump. These pumps have been designed for pumping raw sludge in 3-4 hrs/day to the digester.

5.2.8	Digester

The mixed sludge (primary + excess secondary) is being digested in digesters with concrete tank and mild steel dome. The digesters work on gas mixing system.

Anaerobic Digester performance is achieved by efficient mixing system by recycled digester gas injection. The benefits of this system are:

- Maintenance of even sludge temperature providing physical, chemical and biological uniformity throughout the digester.

- Elimination of sludge/water bonding.

- Rapid distribution of raw feed, reducing risk of short circuiting to discharge.

- Maximum prevention of scum/crust formation on the surface which inhibits gas rise 	in the operation of digester.

- Minimizes grit and heavy particle settlement.

- The recycled gas is injected through a series of strategically positioned distribution 	pipes with special Helixor mixers (which induce adequate velocities so as to keep the 	contents in a completely mixed state) along the digester floor and feeding the has 	continuously into the base of each of the Helixor Mixing Unit (HMU).

The sludge is retained in the digester for a period of about 30 days during which it undergoes anaerobic digestion. The digested sludge is settled at the bottom which is collected by the sludge draw off pipe. The scum floating at the top is skimmed off. The clear supernatant is removed and recycled to the inlet of the primary clarifier under gravity. The gas produced is collected at the top of the digester and conveyed to the ‘Gas Holder’

5.2.9	Sludge Drying Beds

The digested sludge from the digester is applied on the sludge drying beds with filter media comprising fine sand of 100 mm, coarse sand 100 mm, and gravel of 150 mm. The filtrate from the sludge drying beds is pumped back to primary clarifier. The dry cake formed on the top of the media is raked off periodically and is disposed off suitably.

5.3	Basic Design Criteria

5.3.1	Flows

| Daily Flow | 3,033 m3/hr | 16 MGD |
| --- | --- | --- |
| Peak Flow Hourly | 6,067 m3/hr | 32 MGD |
| Lean/Minimum Flow | 1,517 m3/hr | 8 MGD |

5.3.2	Raw Sewage Characteristics

The Plant has been designed on the basis of the following:

| Temperature Sewage | Maximum Minimum Average | 35 o C 18 o C 25 o C |
| --- | --- | --- |
| BOD (5 days at 20O C) |  | 200 mg/l |
| COD |  | 450 mg/l |
| Suspended Solids |  | 400 mg/l |
| Total Solids |  | 1600 mg/l |
| Volatile Solids |  | 200 mg/l |
| Chlorides |  | 180 mg/l |
| Total alkalinity as CaCO3 |  | 390 mg/l |
| pH |  | Approx. 7.5 |

    - Treated Sewage (Effluent) Characteristics

| BOD (5 day at 20 oC) | 20 mg/l |
| --- | --- |
| Suspended Solids | 30 mg/l |
| pH | 6.5 to 8.0 |

    - Hydraulic Levels

| TWL in Inlet Chamber | 212.5 m RL |
| --- | --- |
| TWL of Treated Effluent at Outfall | m RL |
| Finished Ground Level | To be within levels of 208.0 to 210.0 |

  - Basis of Unit Sizing

    - Mechanically Cleaned Bar Screen

| Numbers | 2 nos. Each designed for peak flow |
| --- | --- |
| Spacing between Bars | 20 mm |
| Approach Velocity in Channel | > 0.4 m/sec |
| Velocity through Screen | 0.75 to 1.2 m/sec |
| Free Board | 0.45 m |
| Screen Flats | 50mm x 10mm tapered |
| Drop at Screen Bed | 150 mm |

    - Grit Removal

| Number | 2 Nos. Each designed for Daily Average Flow (16 mgd) |
| --- | --- |
| Surface Loading at 18 Deg.C | 1100 m3/d/m2 |
| Particle Size for Removal | 0.15 mm |
| Sp. Gravity of Particles | 2.65 |
| Free Board | 0.3 m |

5.4.3	Primary Clarifiers

| Number | 2 Nos. each designed for half daily Average Flow (8mgd) plus filtrate + Excess Sludge etc. |
| --- | --- |
| Surface Loading at Average Flow | 34 m3/d/m2 or less |
| Weir loading | 372 m3/d/m or less |
| Detention Period | 2.5 hrs |
| Side Water depth | 3.0 m (more than) |
| BOD Removal | 40 % |
| Suspended Solid Removal | 60 % |
| Solid Concentration in Sludge | 4 % |
| Free Board | 0.3 m |

5.4.4	Aeration Tank

| Number | 2 Nos. each designed for half daily Average Flow (8 mgd) plus return Sludge |
| --- | --- |
| BODin | 120 mg/l |
| MLSS | 2000 mg/l |
| MLVSS/MLSS ratio | 0.8 |
| F/M ratio | 0.2 to 0.4 |
| Volumetric Loading | 0.32 to 0.64 kg BOD/m3 tank volume |
| HRT considering Qd+25 Return Sludge | 6 hrs |
| Kg O2/Kg BOD removed | 0.8 |
| Field Correction Factor | 0.7 (or as calculated if less) |
| DO in tank | 1.5 mg/l |
| Power For Mixing | 20 Watt/m3 at shaft |
| Free Board | 0.60 m |

Higher of Oxygenation and Mixing requirement is adopted for design. Number of aerators to be even number per tank. HP of Aerators not to exceed 40 HP.

    - Secondary Clarifiers

| Number | 2 Nos. each designed for half daily Average Flow (8 mgd) plus return Sludge |
| --- | --- |
| Surface Loading at Average Flow | 32 m3/d/m2 or less |
| Weir loading | 185 m3/d/m or less |
| Detention Period | 2.0 hrs |
| Free Board | 0.3 m |

5.4.6	Digesters

| No. of Units | 6 |
| --- | --- |
| Volume of Each Unit | 3,200 m3 |
| Feed | Raw Primary + Secondary Sludge |
| Feed Solids Concentration | 4% |
| Volatile Solids in Feed | 50% |
| Specific Gravity of Sludge | 1.01 |
| Volatile Solids Destroyed in digestion | 60% |
| Temperature of Digester | 300C |
| Digester Retention Period | 30 days |
| Hopper Bottom | 1.4 |
| Mixing in Digester | Gas Mixing |

Digester effective capacity to be calculated up to bottom of ring beam.

    - Gas Holder

| Number of Units | 2 |
| --- | --- |
| Volume of Each Unit | 4,000 m3 |
| Gas Production | 0.9 m3/Kg of VSS destroyed |
| Gas Storage | 1 day |
| Gas Burner | Provision for 100% capacity |

5.4.8	Sludge Drying Beds

| Number of Units/Beds | 18 |
| --- | --- |
| Depth of Sludge application on Beds | 0.25 m |
| Sludge Dewatering / removal cycle | 21 days |
| Feed Sludge Concentration | 8% |
| Moisture in dewatered Sludge | approx 40 % |

    - Raw Sludge Sump cum Pump House

| Retention Period in Sump | 4 hours |
| --- | --- |
| Solid Concentration in Sludge | 4 % |
| Specific Gravity of Sludge | 1.07 |
| Pumping | Batch |
| Pumping Hours per Day (Actual) | 3 hrs. per day |
| Capacity of pumps | As per calculations |
| Number of Pumps | 4 |
| Working | 1 |
| Stand by | 3 |
| Type of Pumps | Horizontal Centrifugal Non Clog |

    - Return Sludge Sump cum Pump House

| Retention Period in Sump | 15 minutes of RS quantity |
| --- | --- |
| Return Sludge Quantity | 75% of average sewage flow |
| Solid Concentration in Sludge | 1 % |
| Specific Gravity of Sludge | 1.02 |
| Pumping | Continuously |
| Capacity of pump | As per calculations |
| Number of pumps | 2 |
| Working | 2 |
| Stand by | 2 |
| Type of Pumps | Horizontal Centrifugal Non Clog |

5.4.11	 Filtrate Sump cum Pump House

| Retention period in sump | 8 hrs of daily filtrate quantity |
| --- | --- |
| Filtrate Quantity | As per Calculations |
| Solid Concentration in filtrate | Less than 500 mg/l |
| Pumping | Batch |
| Capacity of pumps | As per calculations |
| Number of Pumps | 3 |
| Working | 1 |
| Stand by | 2 |
| Type of Pumps | Vertical Centrifugal |

    - Channels

All channels have been designed for peak flow and have a free board of 0.45 m. The Channels are:

- Channel Treated Effluent from Final Clarifier to Main / Final Effluent Channel.

- Channel Inlet Chamber to Screen Chamber.

- Channel Screen Chamber to Grit removal unit.

- Channel Grit Chamber to Parshall Flume.

- Channel Parshall Flume to Manually Cleaned Bar Screen.

- Channel Manually Cleaned Bar Screen to Primary Clarifier Feed Chamber.

- Channel Primary Clarifier to Aeration Tank Feed Chamber.

- Channel Aeration Tank to Secondary Clarifier.

- Channel Final / Main Effluent.

5.4.13	 Bye Passes from Various Plant Units

All Bye pass of plant units have been designed for peak flow conditions:

- Bye pass from Inlet Chamber to Main Effluent Channel – Bye pass taken by RCC Pipe from Inlet Chamber to Main Effluent Channel to have clear over ground approach to the units, as the units and channels are elevated.

- Bye pass from Distribution Chamber ahead of Primary Clarifier to Main / Final Effluent Channel – Bye pass taken by RCC Pipe from Chamber to Main Effluent Channel to have clear over ground approach to the units, as the units and channels are elevated.

- Bye pass from Distribution Chamber ahead of Aeration Tank to Main / Final Effluent Channel – Bye pass taken by RCC Pipe from Chamber to Main Effluent Channel to have clear over ground approach to the units, as the units and channels are elevated.

Sizes of the units worked out on the basis of unit sizing criteria, are given in

Table-5.1.

### Table- 5.1  Sizes of Units and Details of Components

| 1 | Inlet Works |  |
| --- | --- | --- |
|  | Number, type and size of screens | 2, mechanical, 2x6x0.95 m + 0.45m FB |
|  | Number, type and size of grit removal units | 2 , one each for half flow (1.5 mm grit) |
| 2 | Primary settling tanks |  |
|  | Number of tanks in stage | 2 |
|  | Length, width or diameter of sedimentation tank, | 37.5 m dia |
|  | Design tank depth and detention period | 3 m, 2.5 hrs |
|  | Method of sludge removal, rated and actual | gravity/pumping |
|  | Capacity per unit; | 8 mgd |
|  | Volume of sludge withdrawn per unit and per day. | 550 m3 |
| 3 | Aeration |  |
|  | Type of process | conventional aeration |
|  | Number, length, width and depth of each tank | 2 , 85.5 m x 35m 4.45 m |
|  | Detention period. | 6 hrs |
|  | Total number of aerators installed / operational capacity; | 20 , 40 HP motor |
|  | Type and Capacity of aerators | propeller type, 22.750 m3 |
|  | Make of aerators | M/s HDO |
|  | Number of aerators in normal operation, | 20 |
|  | at peak flow and at minimum flow; | 20 |
|  | Nominal and actual oxygen transfer capacity of each aerator | 1.8 kg O2 per hour |
|  | MLSS in tank | 2 kg per m3 |
| 4 | Sludge pumping stations |  |
|  | - Raw sludge |  |
|  | Percentage solids of sludge | 4% |
|  | - Return sludge |  |
|  | Percentage solids of sludge | 4% |
|  | Percentage sludge returned | 80% |
| 5 | Final Settling tanks |  |
|  | Number of tanks in stage | 2 |
|  | Length/width or diameter of sedimentation tank, | 41.5 m diameter |
|  | Design tank depth and detention period | 4 m, 2 hours detention time |
|  | Method of sludge removal; rated and actual capacity per unit | electrical pump, 4 no (each of 760 m3 per hr) |
|  | Volume of sludge withdrawn per unit and per day. | 760 m3/ hr |
|  | Where is final effluent discharged to? | Agra canal |
| 6 | Sludge Digestion |  |
|  | Number of digestion tanks | 6 (all operational) |
|  | Length/width or diameter of digester tank, | 20 meter diameter |
|  | design tank depth and detention period, | 9.40 m, 30 days |
|  | Are sludge heaters fitted? | no |
|  | Method of sludge stirring, mechanical or gas injection | gas injection |
|  | Method of sludge removal; rated and actual capacity per unit | gravity flow |
|  | Whether Mechanical Mixing or Gas Mixing | gas mixing |
|  | Type of gas mixing | compressed gas injection system |
|  | Whether Low rate or high rate compressors | high rated |
|  | Number of gasholders with storage capacity | 2 no, 4000 m3each |
|  | How is gas used: flared, power generation, supply. | supply |
|  | Percentage solids in digested sludge | 8% |
|  | How are digesters controlled? | manually |
| 7 | Sludge beds |  |
|  | Total number of sludge beds available and size | 18 , (30 m X 30 m each, sludge depth 0.250 meter) |
|  | Total number of sludge beds in use | 18 |
|  | Average depth of wet sludge added | 0.250 m |
|  | Average depth of dry sludge removed | 0.2 m |
|  | Total volume of sludge per year | 6-7 trucks/day |
|  | Scheme for disposal of sludge | lifted by trucks |
|  | Filtrate returned to WWTP? | yes |

The Plant layout is shown in Fig.- 1. Hydraulic flow diagram of the plant is shown in Fig.- 2.

Plan and section of Primary clarifier are shown in Fig.– 3 and a picture of primary clarifier is presented in Picture – 1.

Plan and section of Aeration Tank are shown in Fig.– 4 and a picture of aeration tank is presented in Picture – 2.

Plan and section of Secondary clarifier are shown in Fig.– 5 and a picture of secondary clarifier is presented in Picture – 3.

Plan and section of Digester Tank are shown in Fig.– 6 and a picture of digester is presented in Picture – 4.

  - Methodology

The treatment plant was visited on several occasions to understand the working of various units. In order to evaluate the treatment efficiency of primary clarifiers performing primary treatment and aeration tanks and secondary clarifiers performing secondary treatment, sampling was required before and after each treatment unit. Also to evaluate the performance of anaerobic digesters, sampling was required for raw sludge and digested sludge. The samples were collected by the plant staff from the following locations:

- Raw sewage sample from channel feeding to primary clarifier, after grit chamber

- Primary effluent sample from launder of primary clarifier

- Aerated effluent sample from outlet channel of aeration tank

- Raw sludge sample from sump of raw sludge pump house

- Digested sludge sample from outlet valves in sludge drying beds

Laboratory testing followed the procedures outlined in Standard Methods for Examination of Water and Wastewater. Determination of Dissolved Oxygen (D.O.) level in mixed liquor was made in the aeration tank at the treatment plant using Beckman D.O. meter.

Physical tests carried out on raw sewage included temperature, total solids, suspended solids and dissolved solids. Chemical tests included pH, alkalinity, chloride, oxygen absorption, BOD5, COD, ammonia, oil and grease, detergents and phosphate.

Effluent from primary clarifier was tested for pH, alkalinity, chloride, total solids, suspended solids, dissolved solids, oxygen absorption, BOD5 and COD.

Effluent fro aeration tank was tested for pH, alkalinity, chloride, total solids, suspended solids, dissolved solids, oxygen absorption, S.V. % and dissolved oxygen.

Final effluent from secondary clarifier, to evaluate the efficiency of treatment process, was analyzed for temperature, pH, alkalinity, chloride, total solids, suspended solids, dissolved solids, oxygen absorption, BOD5, COD, DO, ammonia, phosphate, oil and grease and detergents.

Raw and digested sludges were tested for pH, alkalinity, total solids, fixed solids and volatile solids.

The analyzed performance parameters were evaluated for the months of December 2004 and June 2005 to assess the performance of the plant during winter and summer season respectively.

PRIMARY CLARIFIER 			 Picture-1

AERATION TANK  			Picture-2

SECONDARY CLARIFIER 		 Picture-3

DIGESTER  				Picture- 4

Chapter    6

RESULTS AND DISCUSSION

Once the sewage treatment plant is designed considering basic design criteria, the parameter of interest is its performance i.e. when the plant is in operation, its ability to achieve the required effluent standards.

Results of analysis of performance parameters for December 2004 (winter season) and June 2005 (summer season) are as follows:

6.1	Performance of 16 MGD Okhla STP during winter (December 2004)

6.1.1	Raw Sewage Characteristics

Raw sewage characteristics are given in Table-6.1. The Suspended Solids (SS) ranged from 208 to 370 mg/L, with a mean value of 249 mg/L, against the design value of 400 mg/L. Biochemical Oxygen Demand (BOD) ranged from 150 to 200 mg/L, with a mean value of 160 mg/L, against design value of 200 mg/L. The corresponding Chemical Oxygen Demand (COD) ranged between 340 to 472 mg/L, with a mean value of 390 mg/L, against the design value of 450 mg/L. Comparing the characteristics of raw sewage with the typical values cited by Peavy et al. (1985), it can be seen that the raw sewage is of medium concentration. Average BOD to COD ratio is 0.4 and the same does not change significantly that means raw sewage has consistent characteristics.

6.1.2	Primary Effluent

Analysis of primary effluent indicated a significant improvement in sewage quality as shown in Table-6.2. The mean residual SS, BOD and COD values were 92, 84 and 199 mg/L respectively. The corresponding average percentage removals were 61.5, 47.8 and 47.3 % as given in Table-6.3, Table-6.4 and Table-6.5 respectively.

Curves for SS in raw and primary treated sewage are presented in Fig. 7(a). Performance curve for % reduction in SS is plotted in Fig. 7(b). It can be seen that % reduction in SS is more than the theoretical minimum reduction (45%) and most of the time it is more than the theoretical maximum reduction (60%). Curves for BOD in raw and primary treated sewage are presented in Fig. 8(a). Performance curve Fig. 8(b), indicates that % reduction in BOD is more than or equal to the theoretical maximum reduction value of 45%. Curves for COD in raw sewage vis-à-vis primary effluent are plotted in Fig.  9(a).  Fig. 9(b) shows that % reduction in COD is always more than 40%.

6.1.3	Final Effluent

The results of the physicochemical analysis of the aerated sewage are presented in Table-6.6 and that of final effluent are given in Table-6.7. The residual SS in final effluent ranged from a minimum value of 9 mg/L to a maximum value of 26 mg/L, with a mean value of 17 mg/L. The BOD ranged from 5 to 15.3 mg/L, with a mean value of 10 mg/L. The residual COD was between 28 to 52 mg/L, with a mean value of 36 mg/L. The corresponding average percentage removals were 93.3, 93.7 and 90.7 % as shown in Table-6.8, Table-6.9 and Table-6.10 respectively.

Curves for SS in raw sewage vis-à-vis final effluent are plotted in Fig. 10(a). Performance curve, Fig. 10(b), indicates that % reduction in SS, except on two days, was always more than the theoretical maximum reduction value of 90%. Curves for BOD in raw and treated sewage are presented in Fig. 11(a). BOD reduction curve, Fig. 11(b) shows that % BOD removal was always within the theoretical minimum and maximum values of 85% and 95% respectively. Moreover, most of the time it was near to the maximum theoretical reduction. Curves for COD in raw and treated sewage are presented in Fig. 12(a). As per Fig. 12 (b), % reduction in COD was around 90% most of the time.

Average 10 mg/L ammonia was also found in the final effluent which is an indication that complete nitrification has not taken place.

The overall efficiency of the sewage treatment plant during winter season for removing the carbonaceous fraction was good. A removal of more than 90% was achieved for the three critical parameters i.e. SS, BOD and COD.

6.1.4	Characteristics of the Sludge

Percentages of total, fixed and volatile solids in raw and digested sludges have been depicted in Table-6.11. Percentages of Volatile Matter (VM) in raw and digested sludge are illustrated graphically in Fig. 13(a). Percentage reduction of VM during digestion has been plotted in Fig. 13(b). Volatile organic matter reduced between 18.9 to 25.4%, with an average of 22%.

6.2	Performance of 16 MGD Okhla STP during summer (June 2005)

6.2.1	Raw Sewage Characteristics

Raw sewage characteristics are given in Table-6.12. The Suspended Solids (SS) ranged from 250 to 504 mg/L, with a mean value of 314 mg/L, against the design value of 400 mg/L. Biochemical Oxygen Demand (BOD) ranged from 153 to 230 mg/L, with a mean value of 190 mg/L, against design value of 200 mg/L. The corresponding Chemical Oxygen Demand (COD) ranged between 320 to 520 mg/L, with a mean value of 420 mg/L, against the design value of 450 mg/L. Comparing the characteristics of raw sewage with the typical values cited by Peavy et al. (1985), it can be seen that the raw sewage is of medium concentration. Average BOD to COD ratio is 0.46 and the same does not change significantly that means raw sewage has consistent characteristics.

6.2.2	Primary Effluent

Analysis of primary effluent indicated a significant improvement in sewage quality as shown in Table-6.13. The mean residual SS, BOD and COD values were 103, 80 and 208 mg/L respectively. The corresponding average percentage removals were 65.9, 54.9 and 51.0 % as presented in Table-6.14, Table-6.15 and Table-6.16 respectively.

Curves for SS in raw and primary treated sewage are presented in Fig. 14(a). Performance curve for % reduction in SS is plotted in Fig. 14(b). It can be seen that % reduction in SS is more than the theoretical minimum reduction (45%) and most of the time it is more than the theoretical maximum reduction (60%). Curves for BOD in raw and primary treated sewage are presented in Fig. 15(a). Performance curve Fig. 15(b), indicates that % reduction in BOD is more than or equal to the theoretical maximum reduction value of 45%. Curves for COD in raw sewage vis-à-vis primary effluent are plotted in Fig.  16(a).  Fig. 16(b) shows that % reduction in COD is always more than 40%.

6.2.3	Final Effluent

The results of the physicochemical analysis of the aerated sewage are presented in Table-6.17 and that of final effluent are given in Table-6.18. The residual SS in final effluent ranged from a minimum value of 10 mg/L to a maximum value of 30 mg/L, with a mean value of 17 mg/L. The BOD ranged from 6 to 20 mg/L, with a mean value of 10 mg/L. The residual COD was between 23 to 52 mg/L, with a mean value of 41 mg/L. The corresponding average percentage removals were 94.3, 94.4 and 89.7 % as given in Table-6.19, Table-6.20 and Table-6.21 respectively.

Curves for SS in raw sewage vis-à-vis final effluent are plotted in Fig. 17(a). Performance curve, Fig. 17(b), indicates that % reduction in SS was always more than the theoretical maximum reduction value of 90%. Curves for BOD in raw and treated sewage are presented in Fig. 18(a). BOD reduction curve, Fig. 18(b) shows that % BOD removal was always within the theoretical minimum and maximum values of 85% and 95% respectively. Moreover, most of the time it was near to the maximum theoretical reduction. Curves for COD in raw and treated sewage are presented in Fig. 19(a). As per Fig. 19 (b), % reduction in COD was around 90% most of the time.

Average 14 mg/L ammonia was also found in the final effluent which is an indication that complete nitrification has not taken place.

The overall efficiency of the sewage treatment plant during summer season for removing the carbonaceous fraction was good. A removal of 94% was achieved for SS and BOD and 90% for COD.

6.2.4	Characteristics of the Sludge

Percentages of total, fixed and volatile solids in raw and digested sludges have been depicted in Table-6.22. Percentages of Volatile Matter (VM) in raw and digested sludge are illustrated graphically in Fig. 20(a). Percentage reduction of VM during digestion has been plotted in Fig. 20(b). Volatile organic matter reduced between 20.1 to 49.5%, with an average of 33.5%.

Chapter    7

CONCLUSIONS AND RECOMMENDATIONS

7.1	Conclusions

Activated sludge process (ASP) has a great potential in the field of wastewater treatment. In the present project, the performance of 16 MGD sewagw treatment plant at Okhla, Delhi has been studied. The 16 MGD plant was constructed and commissioned in 2001.  This plant receives sewage from Sarita Vihar, Tigri, Deoli, Tughlakabad village, areas along M.B. Road, Badarpur Road and Mathura Road etc.

The treatment process followed at the plant is the Conventional Activated Sludge Process. The typical units include mechanical bar screens, grit chambers, primary settling tanks, aeration tanks, secondary settling tanks, digesters, gas holders and sludge drying beds.

The plant has been designed for the treatment of domestic raw sewage of medium concentration having temperature between 18 o C to 35 o C, BOD (5 days at 20O C) - 200 mg/L, COD-450 mg/ L and suspended solids-400 mg/ L. The various units of the plant have been designed on the basis of design criteria given in Manual on sewerage and sewage treatment. The design MLSS in the aeration tank was considered as 2000 mg/ L.

The treatment was aimed at achieving the treated sewage (effluent) characteristics of BOD (5 day at 20 oC) - 20 mg/ L and suspended solids-30 mg/ L.

It was observed that raw sewage SS, BOD and COD during winter were between 208-370, 150-200 and 340-472 mg/ L respectively. During summer SS, BOD and COD were between 250-504, 153-230 and 320-520 mg/ L respectively. The raw sewage characteristics were well within the design values except a few scattered values. Moreover, sewage during summer was slightly more concentrated than that during winter season.

The mean residual SS, BOD and COD after primary clarification were 92, 84 and 199 mg/L respectively. The corresponding average percentage removals were 61.5, 47.8 and 47.3 % respectively which indicated that the primary clarifiers were performing well.

The residual SS, BOD and COD in final effluent ranged between 9-26, 5-15.3 and 28- 52 mg/L respectively. Corresponding mean values were 17, 10 and 36 mg/L respectively and average percentage removals were 93.3, 93.7 and 90.7 % respectively. The results show that efficiency of aeration tanks and secondary clarifiers were excellent and these units were treating the sewage near to the maximum theoretical limits. The overall efficiency of the sewage treatment plant during winter and summer seasons for removing the carbonaceous fraction was good as removal of 90% was achieved for SS, BOD and COD.

MLSS in the aeration tanks varied between 1277 to 2958 mg/L (except one scatter value of 486 mg/L) with a mean value of 1894 mg/L during winter and between 1340 to 2951 mg/l (except one scatter value of 712 mg/L) with a mean value of 1861 mg/L during summer against design value of 2000mg/L. Though mean values are near to the design value yet there is vast difference in the daily MLSS concentration. This shows that return sludge has not been pumped continuously and MLSS concentration could not be strictly maintained as per the design. If MLSS concentration was maintained as per design effluent quality would have improved further.

In digesters, volatile organic matter reduced between 18.9 to 25.4%, with an average of 22% during winter season. Corresponding figures during summer were 20.1 to 49.5% and 33.5%. This shows that percentage removal of volatile organic matter in digesters was 50% more in summer season as compared to winter season.

However, the sewage treatment plant was consistently meeting the required treated effluent characteristics of BOD20 mg/L and SS  30 mg/L.

7.2	Recommendations

- For better performance peripheral driven bridges with rakes mounted along the whole length is recommended instead of centrally driven rake mechanism.

- Presently fixed speed surface aerators have been provided at the STP. These aerators are to be operated throughout the day without any interruption resulting in huge consumption of energy. With use of fine bubble aeration system, energy savings of approximately 30% could be expected. For future plants, tanks can be designed with diffused aeration system. Further for the larger treatment plants (91 mld and above) with considerable fluctuations in the wastewater flow, variable speed aerators with high output efficiency should be used. These variable speed aerators enable considerable energy savings without compromising on the treatment efficiency of the wastewater.

- Mechanical sludge dewatering be gradually used at the larger STPs. This will release sludge-drying beds for future expansion of the STPs and permit construction of tertiary treatment units, if required. Mechanical dewatering options should be considered on priority where the risk due to ground water contamination is high.

- Future plants may treat the sewage to tertiary level. Treated wastewater having 10 mg/l BOD5@20 °C and 15 mg/l suspended solids can be in used in various industries as supplies for cooling water and boiler feed water.

- Installation of incinerators at STPs should be considered in future for proper disposal of screenings and grit. Even excess sludge can be incinerated to convert it into inert material.

Chapter    8

SUGGESTIONS FOR IMPROVEMENT IN THE EXISTING PLANT

8.1	Suggestions for Improvement

- Operation of the sewage treatment plant is totally manual. Grab and composite samples do not reflect the complete dynamics of a treatment process. Hence on-line process monitoring may be resorted to so that dose of return sludge, DO etc. can be changed quickly with the change in raw sewage characteristics. Automatic control systems not only reduce work load but also allow for more precise control of process parameters. A SCADA system may be installed at the plant.

- Collected material from screens is contaminated and at present disposed of within the STP site. It needs to be disposed of at proper sanitary landfill sites or alternatively, incinerated.

- Grit extracted at STP is currently disposed of in low-lying areas within the STP site. As it is contaminated with faecal matter, viruses, and other bacteria it is a health hazard to both the staff of DJB and the general public. It needs to be disposed of at proper sanitary landfill sites or alternatively, incinerated.

- The return sludge is not continuously fed into the aeration tank as per the design MLSS in the aeration tank. The return sludge must be fed continuously to the aeration tank as per the design. Regular monitoring of MLSS, MLVSS, SVI, DO in aeration tank, and concentration of return sludge should be done.

- Digester contents should be continuously mixed as a process requirement and for proper functioning of digesters. For best digestion of sludge, the temperature should be controlled at its optimum level. During winter season heating of sludge may be resorted to. It will increase the gas production and will give better quality digested sludge in term of stability and dewatering.

- Presently gas generated at the plant is supplied to the near by areas with negligible revenue generation. Gas generated at the plant may be gainfully utilized for power generation. Most of the electricity produced can be used in the treatment process and

any excess can be delivered to the grid.

- Sludge is not lifted from the drying beds due to various reasons. The use of the dried sludge as a soil conditioner is not recommended due to the high level of contamination. However, if the dried sludge is stored for a long period of time (one year), it could be very well used for horticulture. For quick disposal of sludge a sanitary landfill site must be identified. Alternatively, the sludge could be used as a sources material in a composting plant.

- As far as possible, the treated effluent must be used for horticulture and gardening purpose etc.

Table- 6.1  Characteristics of Raw sewage for the month of December 2004

| Parameter Date | Temp. | pH | Total Alkal- inity | Chloride Cl- | Total Solids | Susp. Solids | Dissolv. Solids | Oxygen Absorption (3Hrs) | BOD5 | COD | NH3 | Oil & Grease | Deter- gents | PO4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | oC |  | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L |
| 12/1/2004 | 22.5 | 7.3 | 508 | 248 | 1195 | 208 | 987 | 51.6 | 153.3 | 360 | 33 | - | - | - |
| 12/2/2004 | 22.0 | 7.3 | 508 | 264 | 1201 | 230 | 971 | 48.8 | 150.0 | - | - | - | - | - |
| 12/3/2004 | 22.5 | 7.4 | 496 | 236 | 1122 | 218 | 904 | 51.6 | 165.0 | 372 | 33 | - | - | - |
| 12/4/2004 | 22.0 | 7.3 | 476 | 220 | 1048 | 240 | 808 | 47.2 | 158.3 | - | - | - | - | - |
| 12/5/2004 | 22.0 | 7.3 | 496 | 228 | 1025 | 234 | 791 | 52.0 | 160.0 | - | - | - | - | - |
| 12/6/2004 | 21.5 | 7.4 | 488 | 228 | 1192 | 240 | 953 | 54.8 | 166.6 | 420 | 32 | - | - | - |
| 12/7/2004 | 21.5 | 7.4 | 512 | 252 | 1162 | 208 | 974 | 48.0 | 156.6 | - | - | - | - | - |
| 12/8/2004 | 22.0 | 7.5 | 424 | 244 | 942 | 225 | 722 | 46.8 | 159.0 | 340 | - | 9 | 0.7 | 3.5 |
| 12/9/2004 | 21.5 | 7.5 | 468 | 244 | 1202 | 208 | 994 | 49.6 | 160.0 | - | - | - | - | - |
| 12/10/2004 | 21.0 | 7.2 | 464 | 212 | 1195 | 228 | 967 | 49.6 | 169.1 | - | 38 | - | - | - |
| 12/11/2004 | 21.0 | 7.3 | 508 | 220 | 1188 | 286 | 902 | 52.0 | 161.0 | 428 | - | - | - | - |
| 12/12/2004 | 21.0 | 7.3 | 532 | 228 | 1040 | 254 | 786 | 52.8 | 175.0 | - | - | - | - | - |
| 12/13/2004 | 20.5 | 7.2 | 500 | 256 | 1047 | 220 | 827 | 52.8 | 158.0 | 400 | - | - | - | - |
| 12/14/2004 | 20.5 | 7.4 | 480 | 216 | 1083 | 254 | 829 | 54.8 | 165.0 | - | - | - | - | - |
| 12/15/2004 | 20.5 | 7.4 | 524 | 232 | 1128 | 268 | 860 | 52.8 | 152.0 | 440 | 50 | - | - | - |
| 12/16/2004 | 21.0 | 7.4 | 500 | 236 | 1093 | 224 | 869 | 54.8 | 166.0 | - | - | - | - | - |
| 12/17/2004 | 20.5 | 7.4 | 492 | 228 | 1161 | 280 | 881 | 54.0 | 166.0 | 388 | 48 | 8 | 1.0 | 3.5 |
| 12/18/2004 | 21.0 | 7.5 | 472 | 204 | 1075 | 298 | 777 | 54.0 | 172.0 | - | - | - | - | - |
| 12/19/2004 | 20.5 | 7.3 | 496 | 212 | 1090 | 280 | 810 | 55.2 | 162.0 | - | - | - | - | - |
| 12/20/2004 | 20.0 | 7.4 | 492 | 228 | 1415 | 270 | 1007 | 59.2 | 200 | - | 48 | - | - | - |
| 12/21/2004 | 20.0 | 7.3 | 500 | 244 | 1342 | 270 | 900 | 51.6 | 167.0 | 472 |  | - | - | - |
| 12/22/2004 | 20.0 | 7.3 | 492 | 192 | 1055 | 236 | 819 | 54.0 | 162.0 | - | 43 | - | - | - |
| 12/23/2004 | 19.5 | 7.4 | 480 | 208 | 1227 | 370 | 857 | 47.2 | 153.0 | 364 | - | - | - | - |
| 12/24/2004 | 19.5 | 7.4 | 516 | 224 | 1088 | 222 | 866 | 50.0 | 153.0 | - | 42 | 6 | 1.6 | 2.5 |
| 12/25/2004 | 19.0 | 7.4 | 500 | 216 | 1000 | 280 | 720 | 48.8 | 169.0 | 360 | - | - | - | - |
| 12/26/2004 | 19.0 | 7.4 | 492 | 228 | 993 | 264 | 729 | 54.0 | 167.0 | - | - | - | - | - |
| 12/27/2004 | 18.5 | 7.4 | 496 | 192 | 951 | 242 | 709 | 50.8 | 162.0 | - | 45 | - | - | - |
| 12/28/2004 | 18.5 | 7.3 | 544 | 196 | 1095 | 240 | 855 | 46.8 | 158.0 | 372 | - | - | - | - |
| 12/29/2004 | 18.5 | 7.3 | 544 | 196 | 1095 | 240 | 855 | 46.8 | 159.0 | 348 | 42 | 7 | 1.7 | 3.0 |
| 12/30/2004 | 18.5 | 7.4 | 460 | 200 | 1142 | 240 | 902 | 48.0 | 152.0 | - | - | - | - | - |
| 12/31/2004 | 19.0 | 7.4 | 460 | 212 | 1121 | 264 | 857 | 51.2 | 160.0 | 400 | - | - | - | - |
| Average | 20.5 | 7.4 | 494 | 224 | 1120 | 249 | 889 | 51.3 | 160.0 | 390 | 41 | 7.5 | 1.2 | 3.1 |

Table-6.2  Parameters of Primary treated sewage for the month of December 2004

| Parameter Date | pH | Total Alkalinity | Chloride | Total Solid | Suspended Solids | Dissolved Solids | Oxygen Absorption | BOD5 | COD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L |
| 12/1/2004 | 7.3 | 502 | 244 | 1020 | 90 | 930 | 30.4 | 85.5 | 200 |
| 12/2/2004 | 7.3 | 504 | 252 | 1040 | 88 | 952 | 28.4 | - | - |
| 12/3/2004 | 7.4 | 492 | 244 | 1006 | 90 | 916 | 28.8 | 85.5 | - |
| 12/4/2004 | 7.3 | 492 | 228 | 974 | 93 | 881 | 28.8 | - | - |
| 12/5/2004 | - | - | - | - | - | - | - | - | - |
| 12/6/2004 | 7.2 | 512 | 240 | 974 | 94 | 880 | 30.4 | 89.0 | 220 |
| 12/7/2004 | 7.3 | 488 | 224 | 1008 | 92 | 909 | 29.6 | 87 | - |
| 12/8/2004 | 7.5 | 464 | 212 | 1016 | 77 | 939 | 26.0 | - | - |
| 12/9/2004 | 7.3 | 480 | 224 | 1023 | 93 | 926 | 28.4 | 71 | - |
| 12/10/2004 | 7.3 | 444 | 224 | 1022 | 90 | 932 | 28.4 | - | - |
| 12/11/2004 | 7.4 | 464 | 248 | 1007 | 93 | 914 | 28.4 | 86 | - |
| 12/12/2004 | - | - | - | - | - | - | - | - | - |
| 12/13/2004 | 7.3 | 576 | 224 | 934 | 94 | 840 | 28.4 | 89 | 188 |
| 12/14/2004 | 7.4 | 540 | 216 | 1004 | 91 | 910 | 29.2 | 82 | - |
| 12/15/2004 | 7.4 | 516 | 212 | 996 | 95 | 901 | 31.2 | - | - |
| 12/16/2004 | 7.4 | 544 | 244 | 961 | 89 | 872 | 30.8 | - | - |
| 12/17/2004 | 7.4 | 508 | 212 | 949 | 93 | 856 | 31.2 | - | - |
| 12/18/2004 | - | - | - | - | - | - | - | - | - |
| 12/19/2004 | - | - | - | - | - | - | - | - | -- |
| 12/20/2004 | - | - | - | - | - | - | - | - | - |
| 12/21/2004 | 7.3 | 488 | 240 | 951 | 84 | 867 | 28.8 | 82.5 | - |
| 12/22/2004 | 7.2 | 528 | 236 | 1020 | 85 | 935 | 28.4 | - | - |
| 12/23/2004 | - | - | - | - | - | - | - | - | - |
| 12/24/2004 | 7.3 | 508 | 212 | 1006 | 95 | 911 | 28.8 | 73.5 | - |
| 12/25/2004 | 7.4 | 500 | 216 | 947 | 98 | 849 | 29.6 | 93 | 188 |
| 12/26/2004 | - | - | - | - | - | - | - | - | - |
| 12/27/2004 | 7.4 | 520 | 220 | 895 | 94 | 801 | 28.0 | - | - |
| 12/28/2004 | - | - | - | - | - | - | - | - | - |
| 12/29/2004 | 7.3 | 552 | 232 | 1009 | 100 | 909 | 28.0 | 85.5 | 196 |
| 12/30/2004 | 7.4 | 464 | 204 | 979 | 94 | 885 | 28.4 | - | - |
| 12/31/2004 | - | - | - | - | - | - | - | - | - |
| Average | 7.3 | 504 | 227 | 988 | 92 | 896 | 29.0 | 84.0 | 199 |

Table-6.3  % Reduction in  Suspended Solids in Primary Clarifier for the month of December 2004

| Parameter Date | Suspended solids | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Primary treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 12/1/2004 | 208 | 90 | 118 | 56.7 |
| 12/2/2004 | 230 | 88 | 142 | 61.7 |
| 12/3/2004 | 218 | 90 | 128 | 58.7 |
| 12/4/2004 | 240 | 93 | 147 | 61.2 |
| 12/5/2004 | 234 | - | - | - |
| 12/6/2004 | 240 | 94 | 146 | 60.8 |
| 12/7/2004 | 208 | 92 | 116 | 55.8 |
| 12/8/2004 | 225 | 77 | 148 | 65.8 |
| 12/9/2004 | 208 | 93 | 115 | 55.3 |
| 12/10/2004 | 228 | 90 | 138 | 60.5 |
| 12/11/2004 | 286 | 93 | 193 | 67.5 |
| 12/12/2004 | 254 | - | - | - |
| 12/13/2004 | 220 | 94 | 126 | 57.3 |
| 12/14/2004 | 254 | 91 | 163 | 64.2 |
| 12/15/2004 | 268 | 95 | 173 | 64.6 |
| 12/16/2004 | 224 | 89 | 135 | 60.3 |
| 12/17/2004 | 280 | 93 | 187 | 66.8 |
| 12/18/2004 | 298 | - | - | - |
| 12/19/2004 | 280 | - | - | - |
| 12/20/2004 | 270 | - | - | - |
| 12/21/2004 | 270 | 84 | 186 | 68.9 |
| 12/22/2004 | 236 | 85 | 151 | 64.0 |
| 12/23/2004 | 370 | - | - | - |
| 12/24/2004 | 222 | 95 | 127 | 57.2 |
| 12/25/2004 | 280 | 98 | 182 | 65.0 |
| 12/26/2004 | 264 | - | - | - |
| 12/27/2004 | 242 | 94 | 148 | 61.1 |
| 12/28/2004 | 240 | - | - | - |
| 12/29/2004 | 240 | 100 | 140 | 58.3 |
| 12/30/2004 | 240 | 94 | 146 | 60.8 |
| 12/31/2004 | 264 | - | - | - |
| Average | 249 | 92 | 148 | 61.5 |

Table-6.4  % Reduction in B.O.D. in Primary Clarifier for the month of December 2004

| Parameter Date | B. O. D. | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Primary treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 12/1/2004 | 153.3 | 85.5 | 67.8 | 44.2 |
| 12/2/2004 | 150.0 | - | - | - |
| 12/3/2004 | 165.0 | 85.5 | 79.5 | 48.2 |
| 12/4/2004 | 158.3 | - | - | - |
| 12/5/2004 | 160.0 | - | - | - |
| 12/6/2004 | 166.6 | 89.0 | 77.6 | 46.6 |
| 12/7/2004 | 156.6 | 87.0 | 69.6 | 44.4 |
| 12/8/2004 | 159.0 | - | - | - |
| 12/9/2004 | 160.0 | 71.0 | 89.0 | 55.6 |
| 12/10/2004 | 169.1 | - | - | - |
| 12/11/2004 | 161.0 | 86.0 | 75.0 | 46.6 |
| 12/12/2004 | 175.0 | - | - | - |
| 12/13/2004 | 158.0 | 89.0 | 69.0 | 43.7 |
| 12/14/2004 | 165.0 | 82.0 | 83.0 | 50.3 |
| 12/15/2004 | 152.0 | - | - | - |
| 12/16/2004 | 166.0 | - | - | - |
| 12/17/2004 | 166.0 | - | - | - |
| 12/18/2004 | 172.0 | - | - | - |
| 12/19/2004 | 162.0 | - | - | - |
| 12/20/2004 | 200.0 | - | - | - |
| 12/21/2004 | 167.0 | 82.5 | 84.5 | 50.6 |
| 12/22/2004 | 162.0 | - | - | - |
| 12/23/2004 | 153.0 | - | - | - |
| 12/24/2004 | 153.0 | 73.5 | 79.5 | 52.0 |
| 12/25/2004 | 169.0 | 93.0 | 76 | 45.0 |
| 12/26/2004 | 167.0 | - | - | - |
| 12/27/2004 | 162.0 | - | - | - |
| 12/28/2004 | 158.0 | - | - | - |
| 12/29/2004 | 159.0 | 85.5 | 73.5 | 46.2 |
| 12/30/2004 | 152.0 | - | - | - |
| 12/31/2004 | 160.0 | - | - | - |
| Average | 160.0 | 84.0 | 77 | 47.8 |

Table-6.5  % Reduction in C.O.D. in Primary Clarifier for  the month of December 2004

| Parameter Date | C. O. D. | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Primary treated sewage |  |  |
|  | mg/L | mg/L | mg/LL |  |
| 12/1/2004 | 360 | 200 | 160 | 44.4 |
| 12/2/2004 | - | - | - | - |
| 12/3/2004 | 372 | - | - | - |
| 12/4/2004 | - | - | - | - |
| 12/5/2004 | - | - | - | - |
| 12/6/2004 | 420 | 220 | 200 | 47.6 |
| 12/7/2004 | - | - | - | - |
| 12/8/2004 | 340 | - | - | - |
| 12/9/2004 | - | - | - | - |
| 12/10/2004 | - | - | - | - |
| 12/11/2004 | 428 | - | - | - |
| 12/12/2004 | - | - | - | - |
| 12/13/2004 | 400 | 188 | 212 | 53.0 |
| 12/14/2004 | - | - | - | - |
| 12/15/2004 | 440 | - | - | - |
| 12/16/2004 | - | - | - | - |
| 12/17/2004 | 388 | - | - | - |
| 12/18/2004 | - | - | - | - |
| 12/19/2004 | - | - | - | - |
| 12/20/2004 | - | - | - | - |
| 12/21/2004 | 472 | - | - | - |
| 12/22/2004 | - | - | - | - |
| 12/23/2004 | 364 | - | - | - |
| 12/24/2004 | - | - | - | - |
| 12/25/2004 | 360 | 188 | 172 | 47.8 |
| 12/26/2004 | - | - | - | - |
| 12/27/2004 | - | - | - | - |
| 12/28/2004 | 372 | - | - | - |
| 12/29/2004 | 348 | 196 | 152 | 43.7 |
| 12/30/2004 | - | - | - | - |
| 12/31/2004 | 400 | - | - | - |
| Average | 390 | 199 | 172 | 47.3 |

Table-6.6  Parameters of  Mixed Liquor for the month of December 2004

| Parameter Date | pH | Total Alkalinity | Chloride | Total Solids | Suspended Solids | Dissolved Solids | O.A | S.V.% | D.O. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L |  | mg/L |
| 12/1/2004 | 7.6 | 440 | 240 | 2408 | 1562 | 846 | 228.0 | 92 | 1.8 |
| 12/2/2004 | 7.7 | 456 | 248 | 2739 | 1819 | 920 | 230.4 | 93 | 1.5 |
| 12/3/2004 | 7.7 | 440 | 232 | 2617 | 1765 | 852 | 231.2 | 95 | 1.6 |
| 12/4/2004 | 7.6 | 424 | 236 | 2382 | 1537 | 845 | 231.2 | 97 | 1.2 |
| 12/5/2004 | - | - | - | - | - | - | - | - | - |
| 12/6/2004 | 7.6 | 336 | 252 | 2270 | 1374 | 896 | 160.0 | 45 | 1.5 |
| 12/7/2004 | 7.6 | 308 | 228 | 1404 | 486 | 918 | 89.6 | 19 | 2.8 |
| 12/8/2004 | 7.8 | 352 | 252 | 2670 | 1776 | 894 | 212.8 | 97 | 2.6 |
| 12/9/2004 | 7.6 | 440 | 208 | 2724 | 1863 | 861 | 224.8 | 98 | 1.7 |
| 12/10/2004 | 7.7 | 404 | 228 | 2764 | 1910 | 854 | 217.6 | 95 | 1.6 |
| 12/11/2004 | 7.8 | 424 | 232 | 3012 | 2111 | 901 | 308.0 | 97 | 1.8 |
| 12/12/2004 | - | - | - | - | - | - | - | - | - |
| 12/13/2004 | 7.6 | 376 | 228 | 2521 | 1646 | 875 | 228.8 | 95 | 1.7 |
| 12/14/2004 | 7.6 | 328 | 220 | 2751 | 1873 | 878 | 223.2 | 97 | 1.2 |
| 12/15/2004 | 7.7 | 400 | 208 | 3009 | 2104 | 905 | 152.8 | 94 | 1.7 |
| 12/16/2004 | 7.6 | 384 | 240 | 3040 | 2213 | 827 | 269.6 | 92 | 1.6 |
| 12/17/2004 | 7.6 | 376 | 216 | 3783 | 2958 | 856 | 288.0 | 98 | 1.5 |
| 12/18/2004 | - | - | - | - | - | - | - | - | - |
| 12/19/2004 | - | - | - | - | - | - | - | - | -- |
| 12/20/2004 | - | - | - | - | - | - | - | - | - |
| 12/21/2004 | 7.7 | 348 | 196 | 3238 | 2424 | 814 | 215.2 | 93 | 1.9 |
| 12/22/2004 | 7.6 | 364 | 216 | 3316 | 2501 | 815 | 220.8 | 96 | 1.7 |
| 12/23/2004 | - | - | - | - | - | - | - | - | - |
| 12/24/2004 | 7.6 | 420 | 208 | 3341 | 2503 | 838 | 231.2 | 94 | 1.7 |
| 12/25/2004 | 7.7 | 392 | 204 | 2469 | 1655 | 814 | 201.6 | 92 | 1.8 |
| 12/26/2004 | - | - | - | - | - | - | - | - | - |
| 12/27/2004 | 7.7 | 472 | 200 | 2038 | 1277 | 761 | 224 | 96 | 1.7 |
| 12/28/2004 | - | - | - | - | - | - | - | - | - |
| 12/29/2004 | 7.6 | 460 | 208 | 2989 | 2128 | 861 | 225.6 | 81 | 1.6 |
| 12/30/2004 | 7.7 | 392 | 208 | 3000 | 2182 | 818 | 230.4 | 89 | 2.3 |
| 12/31/2004 | - | - | - | - | - | - | - | - | - |
| Average |  |  |  | 1894 |  |  |  |  | 1.8 |

Table-6.7  Parameters of Final Effluent for the month of December 2004

| Parameter Date | Temp. | pH | Total Alkal- inity | Chloride Cl- | Total Solids | Susp. Solids | Dissolv. Solids | Oxygen Abs. | BOD5 | COD | DO | NH3 | PO4 | Oil & grease | Detergent |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0C |  | Mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L |
| 12/1/2004 | 22.0 | 7.6 | 396 | 232 | 852 | 19 | 833 | 6.8 | 11 | 36 | 2.4 | 10 |  |  |  |
| 12/2/2004 | 22.0 | 7.6 | 432 | 244 | 925 | 20 | 905 | 7.2 | 12 | - | 2.2 | 8 |  |  |  |
| 12/3/2004 | 22.0 | 7.7 | 424 | 228 | 873 | 16 | 857 | 6.4 | 10.8 | 40 | 2.2 | 8 |  |  |  |
| 12/4/2004 | 22.0 | 7.7 | 424 | 228 | 869 | 19 | 850 | 6.8 | 12.0 | - | 2.1 |  |  |  |  |
| 12/5/2004 | 21.5 | 7.8 | 436 | 224 | 844 | 20 | 824 | 6.8 | 12.5 | - | 2.3 | - |  |  |  |
| 12/6/2004 | 21.0 | 7.6 | 332 | 264 | 909 | 20 | 889 | 7.6 | 12.5 | 40 | 1.9 | 5 |  |  |  |
| 12/7/2004 | 21.0 | 7.7 | 296 | 225 | 940 | 24 | 916 | 8.0 | 16.3 | - | 2.1 |  |  |  |  |
| 12/8/2004 | 21.5 | 7.8 | 336 | 232 | 895 | 26 | 868 | 8.8 | 11.9 | 52 | 1.4 |  | 2.5 | 3 | 0.6 |
| 12/9/2004 | 21.0 | 7.5 | 380 | 220 | 746 | 12 | 734 | 5.6 | 6.0 | - | 1.9 |  |  |  |  |
| 12/10/2004 | 20.5 | 7.8 | 360 | 220 | 819 | 10 | 809 | 5.2 | 8.1 | - | 2.0 | 8 |  |  |  |
| 12/11/2004 | 20.5 | 7.8 | 380 | 228 | 847 | 15 | 834 | 5.2 | 10 | 36 | 2.2 |  |  |  |  |
| 12/12/2004 | 20.5 | 7.7 | 400 | 224 | 819 | 10 | 809 | 5.6 | 9 | - | 2.4 |  |  |  |  |
| 12/13/2004 | 20.5 | 7.8 | 332 | 240 | 860 | 9 | 851 | 52 | 8.5 | 28 | 2.5 |  |  |  |  |
| 12/14/2004 | 20 | 7.5 | 360 | 216 | 885 | 10 | 875 | 5.6 | 8.3 | - | 2.3 |  |  |  |  |
| 12/15/2004 | 20.0 | 7.6 | 368 | 212 | 869 | 17 | 852 | 6.4 | 11 | 36 | 2.0 | 5 |  |  |  |
| 12/16/2004 | 20.5 | 7.6 | 368 | 232 | 836 | 20 | 816 | 6.8 | 10 | - | 1.9 |  |  |  |  |
| 12/17/2004 | 20.0 | 7.7 | 416 | 208 | 855 | 19 | 836 | 6.8 | 12 | 32 | 2.0 | 8 | 2.5 | 7 | 0.5 |
| 12/18/2004 | 30.5 | 7.8 | 380 | 220 | 817 | 16 | 801 | 6.0 | 10 | - | 2.1 |  |  |  |  |
| 12/19/2004 | 20.0 | 8.0 | 400 | 224 | 829 | 16 | 813 | 6.0 | 10 | - | 2.6 |  |  |  |  |
| 12/20/2004 | 19.5 | 7.7 | 420 | 212 | 904 | 20 | 884 | 7.2 | 11 | - | 2.4 | 10 |  |  |  |
| 12/21/2004 | 19.5 | 7.6 | 460 | 232 | 841 | 16 | 825 | 5.6 | 10 | 28 | 2.8 |  |  |  |  |
| 12/22/2004 | 19.5 | 7.6 | 420 | 212 | 833 | 17 | 816 | 5.2 | 10 | - | 2.1 | 15 |  |  |  |
| 12/23/2004 | 19.0 | 7.7 | 400 | 204 | 852 | 19 | 833 | 5.2 | 7 | - | 22 |  |  |  |  |
| 12/24/2004 | 18.5 | 7.8 | 412 | 208 | 859 | 10 | 849 | 4.8 | 5 | - | 27 | 15 | 2.25 | 5 | 1.1 |
| 12/25/2004 | 18.5 | 7.7 | 408 | 200 | 790 | 16 | 774 | 5.6 | 10. | 32 | 2.4 |  |  |  |  |
| 12/26/2004 | 18.5 | 7.7 | 416 | 208 | 719 | 14 | 705 | 5.2 | 9.0 | - | 2.1 |  |  |  |  |
| 12/27/2004 | 18.0- | 7.8 | 468 | 220 | 775 | 13 | 762 | 5.6 | 10.3 | - | 2.3 | 12 |  |  |  |
| 12/28/2004 | 18.0 | 7.6 | 440 | 200 | 822 | 11 | 811 | 5.2 | 8.3 | 32 | 2.4 |  |  |  |  |
| 12/29/2004 | 18.0 | 7.7 | 464 | 208 | 836 | 20 | 816 | 6.8 | 10.8 | 40 | 2.3 | 15 | 2.25 | 3 | 1.2 |
| 12/30/2004 | 18.0 | 7.7 | 408 | 216 | 834 | 18 | 816 | 6.4 | 11.0 | - | 2.3 |  |  |  |  |
| 12/31/2004 | 18.5 | 7.8 | 392 | 192 | 819 | 19 | 860 | 6.0 | 10.6 | 36 | 2.2 |  |  |  |  |
| Average | 21.3 | 7.7 | 397 | 208 | 844 | 17 | 827 | 6.2 | 10 | 36 | 2.2 | 10 | 2.4 | 4.5 | 0.9 |

Table-6.8  % Reduction in Suspended Solids after treatment for the month of December 2004

| Parameter Date | Suspended solids | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Secondary Treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 12/1/2004 | 208 | 19 | 189 | 90.1 |
| 12/2/2004 | 230 | 20 | 210 | 91.3 |
| 12/3/2004 | 218 | 16 | 202 | 92.7 |
| 12/4/2004 | 240 | 19 | 221 | 92.1 |
| 12/5/2004 | 234 | 20 | 214 | 91.5 |
| 12/6/2004 | 240 | 20 | 220 | 91.7 |
| 12/7/2004 | 208 | 24 | 184 | 88.5 |
| 12/8/2004 | 225 | 26 | 199 | 88.4 |
| 12/9/2004 | 208 | 12 | 196 | 94.2 |
| 12/10/2004 | 228 | 10 | 218 | 95.6 |
| 12/11/2004 | 286 | 15 | 271 | 94.7 |
| 12/12/2004 | 254 | 10 | 244 | 96.1 |
| 12/13/2004 | 220 | 9 | 211 | 95.9 |
| 12/14/2004 | 254 | 10 | 244 | 96.1 |
| 12/15/2004 | 268 | 17 | 251 | 93.7 |
| 12/16/2004 | 224 | 20 | 204 | 91.1 |
| 12/17/2004 | 280 | 19 | 261 | 93.2 |
| 12/18/2004 | 298 | 16 | 282 | 94.6 |
| 12/19/2004 | 280 | 16 | 264 | 94.3 |
| 12/20/2004 | 270 | 20 | 250 | 92.6 |
| 12/21/2004 | 270 | 16 | 254 | 94.1 |
| 12/22/2004 | 236 | 17 | 219 | 92.8 |
| 12/23/2004 | 370 | 19 | 351 | 94.9 |
| 12/24/2004 | 222 | 10 | 212 | 95.5 |
| 12/25/2004 | 280 | 16 | 264 | 94.3 |
| 12/26/2004 | 264 | 14 | 250 | 94.7 |
| 12/27/2004 | 242 | 13 | 229 | 94.6 |
| 12/28/2004 | 240 | 11 | 229 | 95.4 |
| 12/29/2004 | 240 | 20 | 220 | 91.7 |
| 12/30/2004 | 240 | 18 | 222 | 92.5 |
| 12/31/2004 | 264 | 19 | 245 | 92.8 |
| Average | 249 | 17 | 233 | 93.3 |

Table-6.9  % Reduction in B. O. D. after treatment for the month of December 2004

| Parameter Date | B. O. D. | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Secondary treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 12/1/2004 | 153.3 | 11.0 | 142.3 | 92.8 |
| 12/2/2004 | 150.0 | 12.0 | 138.0 | 92.0 |
| 12/3/2004 | 165.0 | 10.8 | 154.2 | 93.4 |
| 12/4/2004 | 158.3 | 12.0 | 146.3 | 92.4 |
| 12/5/2004 | 160.0 | 12.5 | 147.5 | 92.2 |
| 12/6/2004 | 166.6 | 12.5 | 154.1 | 92.5 |
| 12/7/2004 | 156.6 | 16.3 | 140.3 | 89.6 |
| 12/8/2004 | 159.0 | 11.9 | 147.1 | 92.5 |
| 12/9/2004 | 160.0 | 6.0 | 154.0 | 96.3 |
| 12/10/2004 | 169.1 | 8.1 | 161.0 | 95.2 |
| 12/11/2004 | 161.0 | 10.0 | 151.0 | 93.8 |
| 12/12/2004 | 175.0 | 9.0 | 166.0 | 94.9 |
| 12/13/2004 | 158.0 | 8.5 | 149.5 | 94.6 |
| 12/14/2004 | 165.0 | 8.3 | 156.7 | 95.0 |
| 12/15/2004 | 152.0 | 11.0 | 141.0 | 92.8 |
| 12/16/2004 | 166.0 | 10.0 | 156.0 | 94.0 |
| 12/17/2004 | 166.0 | 12.0 | 154.0 | 92.8 |
| 12/18/2004 | 172.0 | 10.0 | 162.0 | 94.2 |
| 12/19/2004 | 162.0 | 10.0 | 152.0 | 93.8 |
| 12/20/2004 | 200.0 | 11.0 | 189.0 | 94.5 |
| 12/21/2004 | 167.0 | 10.0 | 157.0 | 94.0 |
| 12/22/2004 | 162.0 | 10.0 | 152.0 | 93.8 |
| 12/23/2004 | 153.0 | 7.0 | 146.0 | 95.4 |
| 12/24/2004 | 153.0 | 5.0 | 148.0 | 96.7 |
| 12/25/2004 | 169.0 | 10.0 | 159.0 | 94.1 |
| 12/26/2004 | 167.0 | 9.0 | 158.0 | 94.6 |
| 12/27/2004 | 162.0 | 10.3 | 151.7 | 93.6 |
| 12/28/2004 | 158.0 | 8.3 | 149.7 | 94.7 |
| 12/29/2004 | 159.0 | 10.8 | 148.2 | 93.2 |
| 12/30/2004 | 152.0 | 11.0 | 141.0 | 92.8 |
| 12/31/2004 | 160.0 | 10.6 | 149.4 | 93.4 |
| Average | 160.0 | 10.0 | 152.3 | 93.7 |

Table-6.10  % Reduction in C. O. D. after treatment for the month of December 2004

| Parameter Date | C. O. D. | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Secondary treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 12/1/2004 | 360 | 36 | 324 | 90.0 |
| 12/2/2004 | - | - | - | - |
| 12/3/2004 | 372 | 40 | 332 | 89.2 |
| 12/4/2004 | - | - | - | - |
| 12/5/2004 | - | - | - | - |
| 12/6/2004 | 420 | 40 | 380 | 90.5 |
| 12/7/2004 | - | - | - | - |
| 12/8/2004 | 340 | 52 | 288 | 84.7 |
| 12/9/2004 | - | - | - | - |
| 12/10/2004 | - | - | - | - |
| 12/11/2004 | 428 | 36 | 392 | 91.6 |
| 12/12/2004 | - | - | - | - |
| 12/13/2004 | 400 | 28 | 372 | 93.0 |
| 12/14/2004 | - | - | - | - |
| 12/15/2004 | 440 | 36 | 404 | 91.8 |
| 12/16/2004 | - | - | - | - |
| 12/17/2004 | 388 | 32 | 356 | 91.8 |
| 12/18/2004 | - | - | - | - |
| 12/19/2004 | - | - | - | - |
| 12/20/2004 | - | - | - | - |
| 12/21/2004 | 472 | 28 | 444 | 94.1 |
| 12/22/2004 | - | - | - | - |
| 12/23/2004 | 364 | - | - | - |
| 12/24/2004 | - | - | - | - |
| 12/25/2004 | 360 | 32 | 328 | 91.1 |
| 12/26/2004 | - | - | - | - |
| 12/27/2004 | - | - | - | - |
| 12/28/2004 | 372 | 32 | 340 | 91.4 |
| 12/29/2004 | 348 | 40 | 308 | 88.5 |
| 12/30/2004 | - | - | - | - |
| 12/31/2004 | 400 | 36 | 364 | 91.0 |
| Average | 390 | 36 | 356 | 90.7 |

Table-6.11  Characteristics of Raw Sludge & Digested Sludge for the month of December 2004

| Date | Raw Sludge | Digested Sludge |
| --- | --- | --- |
|  | pH | Total Alkalinity | Solids % | % Volatile Matter | pH | Total Alkalinity | Solids % | % Volatile Matter | % Reduction in Volatile Matter |
|  |  |  | Total | Fixed | Volatile |  |  |  | Total | Fixed | Volatile |  |  |
| 12/1/2004 | 7.5 | 940 | 4.76 | 2.32 | 2.44 | 51.3 | 7.6 | 3040 | 1.54 | 0.93 | 0.61 | 39.6 | 22.8 |
| 12/4/2004 | 7.5 | 1490 | 9.87 | 4.84 | 5.03 | 51.0 | 8.0 | 3160 | 5.51 | 3.23 | 2.28 | 41.37 | 18.9 |
| 12/7/2004 | 7.4 | 990 | 6.28 | 3.09 | 3.19 | 50.8 | 8.1 | 2830 | 5.08 | 3.09 | 1.99 | 39.2 | 22.8 |
| 12/8/2004 | 7.5 | 870 | 6.39 | 3.16 | 3.23 | 50.5 | 8.1 | 3360 | 5.39 | 3.32 | 2.07 | 38.4 | 24.0 |
| 12/11/2004 | 7.4 | 970 | 5.07 | 2.44 | 2.63 | 51.9 | 8.0 | 3010 | 4.84 | 2.89 | 1.95 | 40.3 | 22.4 |
| 12/14/2004 | 7.4 | 840 | 6.66 | 3.22 | 3.44 | 51.7 | 8.0 | 2790 | 3.82 | 2.32 | 1.50 | 39.3 | 24.0 |
| 12/15/2004 | 7.4 | 950 | 5.64 | 2.70 | 2.94 | 52.1 | 8.0 | 2820 | 8.04 | 4.79 | 3.25 | 40.4 | 22.5 |
| 12/17/2004 | 7.5 | 1540 | 10.1 | 4.87 | 5.19 | 51.6 | 8.1 | 3170 | 2.70 | 1.66 | 1.04 | 38.5 | 25.4 |
| 12/18/2004 | 7.6 | 1070 | 8.22 | 4.03 | 4.19 | 50.9 | 8.2 | 3420 | 5.17 | 3.13 | 2.04 | 39.5 | 22.4 |
| 12/20/2004 | 7.6 | 1230 | 3.73 | 1.81 | 1.92 | 51.5 | 8.1 | 3170 | 5.82 | 3.51 | 2.31 | 39.7 | 22.9 |
| 12/22/2004 | 7.4 | 910 | 3.43 | 1.71 | 1.72 | 50.1 | 8.2 | 3470 | 4.06 | 2.44 | 1.62 | 39.9 | 20.4 |
| 12/23/2004 | 7.6 | 1020 | 8.47 | 4.21 | 4.26 | 50.3 | 8.1 | 3040 | 4.56 | 2.73 | 1.83 | 40.1 | 20.3 |
| 12/25/2004 | 7.5 | 1080 | 2.39 | 1.18 | 1.21 | 50.6 | 8.0 | 3230 | 2.10 | 1.25 | 0.85 | 40.5 | 20.0 |
| 12/26/2004 | 7.2 | 900 | 5.36 | 2.64 | 2.72 | 50.7 | 7.9 | 3000 | 4.07 | 2.44 | 1.63 | 40.0 | 21.1 |
| 12/27/2004 | 7.2 | 1140 | 4.13 | 2.03 | 2.10 | 50.8 | 8.4 | 2850 | 7.30 | 4.32 | 2.98 | 40.8 | 19.7 |
| Average |  |  |  |  |  | 51.1 |  |  |  |  |  | 39.8 | 22.0 |

Table-6.12  Characteristics of Raw Sewage for the month of June 2005

| Parameter Date | Temp. | pH | Total Alkal- inity | Chloride Cl- | Total Solids | Susp. Solids | Dissolv. Solids | Oxygen Absorption (3Hrs) | BOD5 | COD | NH3 | Oil & Grease | Deter- gents | PO4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | oC |  | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L |
| 6/1/2005 | 31.5 | 7.4 | 444 | 244 | 1078 | 286 | 792 | 64.8 | 218 | 500 | 33 | - | - | - |
| 6/2/2005 | 31.5 | 7.4 | 452 | 224 | 1078 | 272 | 806 | 59.6 | 200 | - | - | 7 | - | 2.25 |
| 6/3/2005 | 31.5 | 7.4 | 456 | 232 | 1178 | 456 | 722 | 62.0 | 210 | 520 | 35 | - | - | - |
| 6/4/2005 | 32.0 | 7.4 | 452 | 228 | 1185 | 302 | 883 | 60.8 | 195 | - | - | - | - | - |
| 6/5/2005 | 32.5 | 7.4 | 480 | 232 | 1175 | 308 | 867 | 60.0 | 200 | - | - | - | - | - |
| 6/6/2005 | 31.0 | 7.4 | 464 | 236 | 1197 | 330 | 867 | 63.2 | 215 | 400 | 35 | - | - | - |
| 6/7/2005 | 30.0 | 7.4 | 272 | 208 | 1091 | 410 | 681 | 52.0 | 160 | - | - | - | - | - |
| 6/8/2005 | 31.0 | 7.5 | 428 | 240 | 1054 | 250 | 804 | 48.8 | 153 | 320 | 38 | - | - | - |
| 6/9/2005 | 31.0 | 7.4 | 528 | 248 | 1675 | 468 | 1207 | 64.8 | 225 | 480 | - | - | - | - |
| 6/10/2005 | 31.0 | 7.5 | 480 | 240 | 1022 | 248 | 774 | 54.4 | 165 | 360 | 36 | 11 | - | - |
| 6/11/2005 | 31.5 | 7.4 | 504 | 248 | 1142 | 250 | 892 | 56.0 | 185 | - | - | - | - | - |
| 6/12/2005 | 32.0 | 7.5 | 480 | 232 | 1265 | 282 | 983 | 56.8 | 180 | - | - | - | - | - |
| 6/13/2005 | 31.5 | 7.4 | 512 | 256 | 1154 | 324 | 830 | 63.6 | 230 | 480 | - | - | - | - |
| 6/14/2005 | 31.5 | 7.4 | 448 | 240 | 1098 | 300 | 798 | 58.8 | 210 | 480 | 33 | - | - | - |
| 6/15/2005 | 31.5 | 7.4 | 508 | 240 | 1148 | 264 | 884 | 58.4 | 180 | 440 | - | - | - | - |
| 6/16/2005 | 32.0 | 7.4 | 500 | 248 | 1056 | 280 | 776 | 55.2 | 185 | 360 | - | - | - | - |
| 6/17/2005 | 32.0 | 7.4 | 456 | 248 | 1082 | 260 | 822 | 53.6 | 175 | - | - | - | - | - |
| 6/18/2005 | 32.0 | 7.4 | 472 | 244 | 988 | 278 | 710 | 51.2 | 165 | - | - | - | - | - |
| 6/19/2005 | 32.0 | 7.4 | 492 | 248 | 1039 | 264 | 775 | 53.6 | 173 | - | - | 13 | - | - |
| 6/20/2005 | 32.0 | 7.4 | 500 | 248 | 1215 | 354 | 861 | 60.0 | 220 | 440 | - | - | - | - |
| 6/21/2005 | 33.0 | 7.5 | 528 | 320 | 1130 | 278 | 859 | 54.0 | 180 | 360 | 43 | - | - | - |
| 6/22/2005 | 33.0 | 7.4 | 516 | 248 | 1118 | 278 | 840 | 56.8 | 190 | 360 | - | - | 0.8 | 4.0 |
| 6/23/2005 | 32.5 | 7.3 | 524 | 276 | 1070 | 266 | 804 | 60.0 | 210 | - | - | - | - | - |
| 6/24/2005 | 33.0 | 7.4 | 468 | 248 | 1205 | 454 | 751 | 57.2 | 185 | 468 | - | - | - | - |
| 6/25/2005 | Plant closed due to repair of gravity duct. |
| 6/26/2005 |  |
| 6/27/2005 | 31.0 | 7.5 | 448 | 224 | 1159 | 288 | 871 | 54.4 | 175 | 400 | 40 | - | - | - |
| 6/28/2005 | 30.5 | 7.4 | 460 | 244 | 907 | 256 | 651 | 52.8 | 165 | 340 | - | - | - | - |
| 6/29/2005 | 31.0 | 7.4 | 460 | 244 | 1032 | 274 | 758 | 48.0 | 158 | 380 | - | - | - | - |
| 6/30/2005 | 31.0 | 7.5 | 408 | 196 | 1834 | 504 | 1330 | 62.0 | 225 | 480 | 38 | 9 | - | 4.25 |
| Average | 31.6 | 7.4 | 469 | 242 | 1156 | 314 | 842 | 57.0 | 190 | 420 | 37 | 10 | 0.8 | 3.5 |

Table-6.13  Parameters of Primary treated sewage for the month of June 2005

| Parameter Date | pH | Total Alkalinity | Chloride | Total Solids | Suspended Solids | Dissolved Solids | Oxygen Absorption | BOD5 | COD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L |
| 1.6.2005 | 7.4 | 456 | 232 | 840 | 126 | 714 | 33.6 | 107 | 220 |
| 2.6.2005 | 7.4 | 448 | 220 | 922 | 101 | 821 | 30.8 | - | - |
| 3.6.2005 | 7.4 | 452 | 224 | 854 | 108 | 746 | 31.6 | 74 | 220 |
| 4.6.2005 | 7.3 | 448 | 224 | 948 | 105 | 843 | 30.4 | - | - |
| 5.6.2005 | - | - | - | - | - | - | - | - | - |
| 6.6.2005 | 7.3 | 456 | 228 | 992 | 120 | 872 | 33.2 | 88 | 212 |
| 7.6.2005 | 7.4 | 360 | 192 | 814 | 98 | 716 | 28.4 | - | - |
| 8.6.2005 | 7.4 | 360 | 240 | 843 | 107 | 736 | 32.4 | 83 | - |
| 9.6.2005 | 7.4 | 512 | 240 | 922 | 100 | 822 | 30.0 | 75 | 200 |
| 10.6.2005 | 7.4 | 476 | 232 | 944 | 105 | 839 | 31.2 | - | - |
| 11.6.2005 | 7.3 | 496 | 232 | 962 | 105 | 857 | 32.0 | 77 | - |
| 12.6.2005 | - | - | - | - | - | - | - | - | - |
| 13.6.2005 | 7.3 | 512 | 248 | 981 | 103 | 878 | 32.4 | 90 | 200 |
| 14.6.2005 | 7.4 | 460 | 240 | 916 | 101 | 815 | 31.2 | - | - |
| 15.6.2005 | 7.4 | 438 | 220 | 923 | 101 | 822 | 30.8 | 98 | 188 |
| 16.6.2005 | 7.4 | 512 | 260 | 951 | 116 | 835 | 32.8 | - | - |
| 17.6.2005 | 7.4 | 460 | 232 | 882 | 119 | 763 | 32.4 | 78 | - |
| 18.6.2005 | 7.4 | 480 | 232 | 892 | 103 | 789 | 29.6 | - | - |
| 19.6.2005 | - | - | - | - | - | - | - | - | -- |
| 20.6.2005 | 7.4 | 488 | 240 | 932 | 99 | 833 | 30.0 | 88 | 220 |
| 21.6.2005 | 7.4 | 504 | 236 | 819 | 96 | 723 | 28.8 | - | - |
| 22.6.2005 | 7.4 | 516 | 248 | 974 | 102 | 872 | 30.0 | - | 220 |
| 23.6.2005 | 7.4 | 504 | 260 | 947 | 96 | 851 | 29.6 | - | - |
| 24.6.2005 | 7.4 | 516 | 260 | 879 | 90 | 789 | 29.6 | - | - |
| 25.6.2005 | - | - | - | - | - | - | - | - | - |
| 26.6.2005 | - | - | - | - | - | - | - | - | - |
| 27.6.2005 | 7.5 | 440 | 220 | 876 | 80 | 796 | 26.8 | - | 200 |
| 28.6.2005 | 7.4 | 476 | 272 | 839 | 110 | 729 | 32.0 | 93 | 208 |
| 29.6.2005 | 7.3 | 488 | 252 | 943 | 94 | 849 | 28.8 | 82 | 196 |
| 30.6.2005 | 7.4 | 392 | 204 | 911 | 85 | 826 | 28.4 | - | - |
| Average | 7.4 | 468 | 236 | 908 | 103 | 805 | 31 | 80 | 208 |

Table-6.14  % Reduction in Suspended Solids in Primary Clarifier for the month of June 2005

| Parameter Date | Suspended solids | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Primary treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 6/1/2005 | 286 | 126 | 160 | 55.9 |
| 6/2/2005 | 272 | 101 | 171 | 62.9 |
| 6/3/2005 | 456 | 108 | 348 | 76.3 |
| 6/4/2005 | 302 | 105 | 197 | 65.2 |
| 6/5/2005 | 308 | - | - | - |
| 6/6/2005 | 330 | 120 | 210 | 63.6 |
| 6/7/2005 | 410 | 98 | 312 | 76.1 |
| 6/8/2005 | 250 | 107 | 143 | 57.2 |
| 6/9/2005 | 468 | 100 | 368 | 78.6 |
| 6/10/2005 | 248 | 105 | 143 | 57.7 |
| 6/11/2005 | 250 | 105 | 145 | 58.0 |
| 6/12/2005 | 282 | - | - | - |
| 6/13/2005 | 324 | 103 | 221 | 68.2 |
| 6/14/2005 | 300 | 101 | 199 | 66.3 |
| 6/15/2005 | 264 | 101 | 163 | 61.7 |
| 6/16/2005 | 280 | 116 | 164 | 58.6 |
| 6/17/2005 | 260 | 119 | 141 | 54.2 |
| 6/18/2005 | 278 | 103 | 175 | 62.9 |
| 6/19/2005 | 264 | - | - | - |
| 6/20/2005 | 354 | 99 | 255 | 72.0 |
| 6/21/2005 | 278 | 96 | 182 | 65.5 |
| 6/22/2005 | 278 | 102 | 176 | 63.3 |
| 6/23/2005 | 266 | 96 | 170 | 63.9 |
| 6/24/2005 | 454 | 90 | 364 | 80.2 |
| 6/25/2005 | Plant closed due to repair of gravity duct. |
| 6/26/2005 |  |
| 6/27/2005 | 288 | 80 | 208 | 72.2 |
| 6/28/2005 | 256 | 110 | 146 | 57.0 |
| 6/29/2005 | 274 | 94 | 180 | 65.7 |
| 6/30/2005 | 504 | 85 | 419 | 83.1 |
| Average | 314 | 103 | 214 | 65.9 |

Table-6.15  % Reduction in B. O. D. in Primary Clarifier for the month of June 2005

| Parameter Date | B. O. D. | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Primary treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 6/1/2005 | 218 | 107 | 111 | 50.9 |
| 6/2/2005 | 200 | - | - | - |
| 6/3/2005 | 210 | 74 | 136 | 64.8 |
| 6/4/2005 | 195 | - | - | - |
| 6/5/2005 | 200 | - | - | - |
| 6/6/2005 | 215 | 88 | 127 | 59.1 |
| 6/7/2005 | 160 | - | - | - |
| 6/8/2005 | 153 | 83 | 70 | 45.8 |
| 6/9/2005 | 225 | 75 | 150 | 66.7 |
| 6/10/2005 | 165 | - | - | - |
| 6/11/2005 | 185 | 77 | 108 | 58.4 |
| 6/12/2005 | 180 | - | - | - |
| 6/13/2005 | 230 | 90 | 140 | 60.9 |
| 6/14/2005 | 210 | - | - | - |
| 6/15/2005 | 180 | 98 | 82 | 45.6 |
| 6/16/2005 | 185 | - | - | - |
| 6/17/2005 | 175 | 78 | 97 | 55.4 |
| 6/18/2005 | 165 | - | - | - |
| 6/19/2005 | 173 | - | - | - |
| 6/20/2005 | 220 | 88 | 132 | 60.0 |
| 6/21/2005 | 180 | - | - | - |
| 6/22/2005 | 190 | - | - | - |
| 6/23/2005 | 210 | - | - | - |
| 6/24/2005 | 185 | - | - | - |
| 6/25/2005 | Plant closed due to repair of gravity duct. |
| 6/26/2005 |  |
| 6/27/2005 | 175 | - | - | - |
| 6/28/2005 | 165 | 93 | 72 | 43.6 |
| 6/29/2005 | 158 | 82 | 76 | 48.1 |
| 6/30/2005 | 225 | - | - | - |
| Average | 190 | 80 | 108 | 54.9 |

Table-6.16  % Reduction in C. O. D. in Primary Clarifier for the month of June 2005

| Parameter Date | C. O. D. | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Primary treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 6/1/2005 | 500 | 220 | 280 | 56.0 |
| 6/2/2005 | - | - | - | - |
| 6/3/2005 | 520 | 220 | 300 | 57.7 |
| 6/4/2005 | - | - | - | - |
| 6/5/2005 | - | - | - | - |
| 6/6/2005 | 400 | 212 | 188 | 47.0 |
| 6/7/2005 | - | - | - | - |
| 6/8/2005 | 320 | - | - | - |
| 6/9/2005 | 480 | 200 | 280 | 58.3 |
| 6/10/2005 | 360 | - | - | - |
| 6/11/2005 | - | - | - | - |
| 6/12/2005 | - | - | - | - |
| 6/13/2005 | 480 | 200 | 280 | 58.3 |
| 6/14/2005 | 480 | - | - | - |
| 6/15/2005 | 440 | 188 | 252 | 57.3 |
| 6/16/2005 | 360 | - | - | - |
| 6/17/2005 | - | - | - | - |
| 6/18/2005 | - | - | - | - |
| 6/19/2005 | - | - | - | - |
| 6/20/2005 | 440 | 220 | 220 | 50.0 |
| 6/21/2005 | 360 | - | - | - |
| 6/22/2005 | 360 | 220 | 140 | 38.9 |
| 6/23/2005 | - | - | - | - |
| 6/24/2005 | 468 | - | - | - |
| 6/25/2005 | Plant closed due to repair of gravity duct. |
| 6/26/2005 |  |
| 6/27/2005 | 400 | 200 | 200 | 50.0 |
| 6/28/2005 | 340 | 208 | 132 | 38.8 |
| 6/29/2005 | 380 | 196 | 184 | 48.4 |
| 6/30/2005 | 480 | - | - | - |
| Average | 420 | 208 | 217 | 51.0 |

Table- 6.17  Parameters of  Mixed Liquor for the month of June 2005

| Parameter Date | pH | Total Alkalinity | Chloride | Total Solids | Suspended Solids | Dissolved Solids | O.A | S.V.% | D.O. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L |  | mg/L |
| 1.6.2005 | 8.1 | 388 | 232 | 3519 | 2755 | 764 | 206.4 | 94 | 1.4 |
| 2.6.2005 | 8.0 | 342 | 224 | 2874 | 2113 | 761 | 300.8 | 90 | 1.2 |
| 3.6.2005 | 7.8 | 420 | 228 | 2484 | 1741 | 743 | 280.8 | 78 | 1.3 |
| 4.6.2005 | 8.0 | 440 | 220 | 2624 | 1734 | 890 | 304.0 | 90 | 1.0 |
| 5.6.2005 | - | - | - | - | - | - | - | - | - |
| 6.6.2005 | 7.6 | 448 | 224 | 2608 | 1755 | 853 | 294.4 | 90 | 0.6 |
| 7.6.2005 | 8.0 | 364 | 220 | 2161 | 1358 | 803 | 185.6 | 96 | 1.2 |
| 8.6.2005 | 7.5 | 320 | 208 | 2331 | 1729 | 602 | 213.6 | 95 | 1.0 |
| 9.6.2005 | 7.8 | 440 | 232 | 2555 | 1800 | 755 | 291.2 | 91 | 0.6 |
| 10.6.2005 | 7.9 | 448 | 224 | 2586 | 1880 | 706 | 292.0 | 93 | 0.5 |
| 11.6.2005 | 7.8 | 508 | 228 | 2589 | 1879 | 710 | 296.8 | 94 | 0.7 |
| 12.6.2005 | - | - | - | - | - | - | - | - | - |
| 13.6.2005 | 7.7 | 408 | 252 | 2290 | 1466 | 824 | 224.0 | 75 | 0.5 |
| 14.6.2005 | 7.6 | 288 | 220 | 2090 | 1340 | 750 | 188.8 | 70 | 0.8 |
| 15.6.2005 | - | - | - | Power | Failure | - | - | - | - |
| 16.6.2005 | - | - | - | - | - | - | - | - | - |
| 17.6.2005 | 7.6 | 444 | 240 | 2375 | 1585 | 790 | 160,0 | 31 | 1.1 |
| 18.6.2005 | 7.6 | 352 | 228 | 1485 | 712 | 773 | 99.2 | 23 | 1.4 |
| 19.6.2005 | - | - | - | - | - | - | - | - | -- |
| 20.6.2005 | 7.6 | 448 | 232 | 3735 | 2951 | 784 | 298.4 | 93 | 1.5 |
| 21.6.2005 | - | - | - | - | - | - | - | - | - |
| 22.6.2005 | 7.6 | 360 | 240 | 3442 | 2687 | 755 | 288.0 | 93 | 1.4 |
| 23.6.2005 | 7.8 | 448 | 248 | 2432 | 1665 | 767 | 222.4 | 78 | 1.5 |
| 24.6.2005 | 7.8 | 392 | 264 | 3450 | 2654 | 796 | 288.0 | 90 | 1.6 |
| 25.6.2005 | - | - | - | - | - | - | - | - | - |
| 26.6.2005 | - | - | - | - | - | - | - | - | - |
| 27.6.2005 | 7.9 | 368 | 232 | 3445 | 2657 | 788 | 286.4 | 92 | 1.6 |
| 28.6.2005 | 7.7 | 396 | 244 | 3473 | 2700 | 773 | 201.6 | 97 | 2.0 |
| 29.6.2005 | 7.6 | 440 | 248 | 272.3 | 1880 | 843 | 236.0 | 90 | 2.5 |
| 30.6.2005 | 7.8 | 356 | 192 | 2543 | 1753 | 790 | 272.0 | 90 | 2.1 |
| Average |  |  |  |  | 1861 |  |  | 84 | 1.3 |

Table-6.18  Parameters of Final Effluent for the month of June 2005

| Parameter Date | Temp. | pH | Total Alkal- inity | Chloride Cl- | Total Solids | Susp. Solids | Dissolv. Solids | Oxygen Abs. | BOD5 | COD | DO | NH3 | Oil & grease | Detergent | PO4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0C |  | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L | mg/L |
| 1.6.2005 | 31.0 | 7.8 | 392 | 236 | 797 | 25 | 772 | 8.0 | 13 | 44 | 1.2 | 20 |  |  |  |
| 2.6.2005 | 31.5 | 7.8 | 424 | 220 | 780 | 20 | 760 | 7.2 | 13 | - | 1.4 | - | 2 | 2.0 | N.D |
| 3.6.2005 | 31.0 | 7.9 | 412 | 224 | 770 | 20 | 750 | 7.6 | 12 | 44 | 1.5 | 15 |  |  |  |
| 4.6.2005 | 31.5 | 7.9 | 428 | 216 | 880 | 25 | 855 | 8.4 | 13 | - | 1.3 | - |  |  |  |
| 5.6.2005 | 32.0 | 7.9 | 448 | 224 | 742 | 25 | 717 | 7.6 | 10 | - | 1.4 | - |  |  |  |
| 6.6.2005 | 30.5 | 7.6 | 440 | 232 | 857 | 30 | 827 | 11.2 | 20 | 52 | 1.1 | 18 |  |  |  |
| 7.6.2005 | 29.5 | 7.8 | 396 | 212 | 801 | 15 | 786 | 7.2 | 11 | - | 1.0 |  |  |  |  |
| 8.6.2005 | 31.0 | 7.6 | 372 | 208 | 708 | 15 | 693 | 6.8 | 10 | 40 | 1.1 |  | - | - | - |
| 9.6.2005 | 31.0 | 8.0 | 392 | 220 | 718 | 12 | 706 | 6.8 | 10 | 40 | 1.6 | 20 |  |  |  |
| 10.6.2005 | 30.5 | 8.0 | 400 | 212 | 748 | 14 | 734 | 6.0 | 7 | 36 | 1.5 | - | 5 |  |  |
| 11.6.2005 | 31.0 | 7.8 | 420 | 216 | 755 | 18 | 737 | 6.4 | 11 | - | 1.5 | 15 |  |  |  |
| 12.6.2005 | 31.5 | 7.9 | 444 | 220 | 830 | 16 | 814 | 6.0 | 7 | - | 1.4 |  |  |  |  |
| 13.6.2005 | 31.0 | 7.9 | 400 | 240 | 846 | 17 | 829 | 6.8 | 9 | 44 | 1.6 | - |  |  |  |
| 14.6.2005 | 31.0 | 7.7 | 296 | 220 | 783 | 16 | 767 | 6.4 | 8 | 44 | 1.7 | 10 |  |  |  |
| 15.6.2005 | 31.0 | 8.0 | 428 | 212 | 821 | 16 | 805 | 7.2 | 12 | 44 | 1.6 |  |  |  |  |
| 16.6.2005 | 32.0 | 7.6 | 460 | 248 | 781 | 19 | 762 | 7.2 | 12 | 44 | - |  |  |  |  |
| 17.6.2005 | 31.5 | 8.0 | 432 | 232 | 803 | 15 | 788 | 7.6 | 11 | - | 1.5 |  |  |  |  |
| 18.6.2005 | 31.5 | 7.8 | 348 | 228 | 770 | 12 | 758 | 6.4 | 8 | - | - |  |  |  |  |
| 19.6.2005 | 31.5 | 7.7 | 380 | 232 | 753 | 14 | 739 | 6.0 | 9 | - | 1.5 |  |  |  |  |
| 20.6.2005 | 31.5 | 7.7 | 432 | 228 | 833 | 15 | 818 | 6.8 | 9 | 48 | 1.6 |  | 5 |  |  |
| 21.6.2005 | 32.5 | 7.9 | 420 | 244 | 756 | 15 | 741 | 6.8 | 9 | 40 | 1.2 | 20 |  |  |  |
| 22.6.2005 | 32.5 | 7.7 | 388 | 232 | 754 | 15 | 739 | 6.4 | 11 | 40 | 1.3 |  |  | 0.4 | 1.5 |
| 23.6.2005 | 32.0 | 7.9 | 412 | 240 | 739 | 10 | 729 | 6.0 | 7 | - | 1.4 |  |  |  |  |
| 24.6.2005 | 32.5 | 7.9 | 400 | 260 | 758 | 13 | 745 | 6.0 | 8 | 23 | 1.5 | - | - | - | - |
| 25.6.2005 | - | - | - | - | - | - | - | - | - | - | - |  |  |  |  |
| 26.6.2005 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - |
| 27.6.2005 | 30.5 | 8.0 | 328 | 224 | 805 | 20 | 785 | 6.8 | 10 | 40 | 1.4 | 5 |  |  |  |
| 28.6.2005 | 30.0 | 7.7 | 320 | 244 | 779 | 20 | 759 | 9.2 | 16 | 52 | 1.6 |  |  |  |  |
| 29.6.2005 | 30.5 | 7.7 | 392 | 244 | 873 | 15 | 858 | 5.6 | 11 | 32 | 1.9 | --- | - | - | - |
| 30.6.2005 | 30.5 | 8.2 | 352 | 200 | 832 | 13 | 819 | 5.6 | 6 | 28 | 1.8 | 5 | 3 |  | 2.7 |
| Average | 31.2 | 7.8 | 398 | 227 | 788 | 17 | 771 | 7 | 10 | 41 | 1.4 | 14 | 3.8 | 0.4 | 2.1 |

Table-6.19  % Reduction in Suspended Solids after treatment for the month of June 2005

| Parameter Date | Suspended solids | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Secondary Treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 6/1/2005 | 286 | 25 | 261 | 91.3 |
| 6/2/2005 | 272 | 20 | 252 | 92.6 |
| 6/3/2005 | 456 | 20 | 436 | 95.6 |
| 6/4/2005 | 302 | 25 | 277 | 91.7 |
| 6/5/2005 | 308 | 25 | 283 | 91.9 |
| 6/6/2005 | 330 | 30 | 300 | 90.9 |
| 6/7/2005 | 410 | 15 | 395 | 96.3 |
| 6/8/2005 | 250 | 15 | 235 | 94.0 |
| 6/9/2005 | 468 | 12 | 456 | 97.4 |
| 6/10/2005 | 248 | 14 | 234 | 94.3 |
| 6/11/2005 | 250 | 18 | 232 | 92.8 |
| 6/12/2005 | 282 | 16 | 266 | 94.3 |
| 6/13/2005 | 324 | 17 | 307 | 94.8 |
| 6/14/2005 | 300 | 16 | 284 | 94.7 |
| 6/15/2005 | 264 | 16 | 248 | 93.9 |
| 6/16/2005 | 280 | 19 | 261 | 93.2 |
| 6/17/2005 | 260 | 15 | 245 | 94.2 |
| 6/18/2005 | 278 | 12 | 266 | 95.7 |
| 6/19/2005 | 264 | 14 | 250 | 94.7 |
| 6/20/2005 | 354 | 15 | 339 | 95.8 |
| 6/21/2005 | 278 | 15 | 263 | 94.6 |
| 6/22/2005 | 278 | 15 | 263 | 94.6 |
| 6/23/2005 | 266 | 10 | 256 | 96.2 |
| 6/24/2005 | 454 | 13 | 441 | 97.1 |
| 6/25/2005 | Plant closed due to repair of gravity duct. |
| 6/26/2005 |  |
| 6/27/2005 | 288 | 20 | 268 | 93.1 |
| 6/28/2005 | 256 | 20 | 236 | 92.2 |
| 6/29/2005 | 274 | 15 | 259 | 94.5 |
| 6/30/2005 | 504 | 13 | 491 | 97.4 |
| Average | 314 | 17 | 297 | 94.3 |

Table-6.20  % Reduction in B.O.D. after treatment for the month of June 2005

| Parameter Date | B. O. D. | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Secondary Treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 6/1/2005 | 218 | 13 | 205 | 94.0 |
| 6/2/2005 | 200 | 13 | 187 | 93.5 |
| 6/3/2005 | 210 | 12 | 198 | 94.3 |
| 6/4/2005 | 195 | 13 | 182 | 93.3 |
| 6/5/2005 | 200 | 10 | 190 | 95.0 |
| 6/6/2005 | 215 | 20 | 195 | 90.7 |
| 6/7/2005 | 160 | 11 | 149 | 93.1 |
| 6/8/2005 | 153 | 10 | 143 | 93.5 |
| 6/9/2005 | 225 | 10 | 215 | 95.6 |
| 6/10/2005 | 165 | 7 | 158 | 95.6 |
| 6/11/2005 | 185 | 11 | 174 | 94.1 |
| 6/12/2005 | 180 | 7 | 173 | 96.1 |
| 6/13/2005 | 230 | 9 | 221 | 96.1 |
| 6/14/2005 | 210 | 8 | 202 | 96.2 |
| 6/15/2005 | 180 | 12 | 168 | 93.3 |
| 6/16/2005 | 185 | 12 | 173 | 93.5 |
| 6/17/2005 | 175 | 11 | 164 | 93.7 |
| 6/18/2005 | 165 | 8 | 157 | 95.2 |
| 6/19/2005 | 173 | 9 | 164 | 94.8 |
| 6/20/2005 | 220 | 9 | 211 | 95.9 |
| 6/21/2005 | 180 | 9 | 171 | 95.0 |
| 6/22/2005 | 190 | 11 | 179 | 94.2 |
| 6/23/2005 | 210 | 7 | 203 | 96.7 |
| 6/24/2005 | 185 | 8 | 177 | 95.7 |
| 6/25/2005 | Plant closed due to repair of gravity duct. |
| 6/26/2005 |  |
| 6/27/2005 | 175 | 10 | 165 | 94.3 |
| 6/28/2005 | 165 | 16 | 149 | 90.3 |
| 6/29/2005 | 158 | 11 | 147 | 93.0 |
| 6/30/2005 | 225 | 6 | 219 | 97.3 |
| Average | 190 | 10 | 180 | 94.4 |

Table-6.21  % Reduction in C.O.D. after treatment for the month of June 2005

| Parameter Date | C. O. D. | Reduction | % Reduction |
| --- | --- | --- | --- |
|  | Raw sewage | Secondary Treated sewage |  |  |
|  | mg/L | mg/L | mg/L |  |
| 6/1/2005 | 500 | 44 | 456 | 91.2 |
| 6/2/2005 | - | - | - | - |
| 6/3/2005 | 520 | 44 | 476 | 91.5 |
| 6/4/2005 | - | - | - | - |
| 6/5/2005 | - | - | - | - |
| 6/6/2005 | 400 | 52 | 348 | 87.0 |
| 6/7/2005 | - | - | - | - |
| 6/8/2005 | 320 | 40 | 280 | 87.5 |
| 6/9/2005 | 480 | 40 | 440 | 91.7 |
| 6/10/2005 | 360 | 36 | 324 | 90.0 |
| 6/11/2005 | - | - | - | - |
| 6/12/2005 | - | - | - | - |
| 6/13/2005 | 480 | 44 | 436 | 90.8 |
| 6/14/2005 | 480 | 44 | 436 | 90.8 |
| 6/15/2005 | 440 | 44 | 396 | 90.0 |
| 6/16/2005 | 360 | 44 | 316 | 87.8 |
| 6/17/2005 | - | - | - | - |
| 6/18/2005 | - | - | - | - |
| 6/19/2005 | - | - | - | - |
| 6/20/2005 | 440 | 48 | 392 | 89.1 |
| 6/21/2005 | 360 | 40 | 320 | 88.9 |
| 6/22/2005 | 360 | 40 | 320 | 88.9 |
| 6/23/2005 | - | - | - | - |
| 6/24/2005 | 468 | 23 | - | - |
| 6/25/2005 | Plant closed due to repair of gravity duct. |
| 6/26/2005 |  |
| 6/27/2005 | 400 | 40 | 360 | 90.0 |
| 6/28/2005 | 340 | 52 | 288 | 84.7 |
| 6/29/2005 | 380 | 32 | 348 | 91.6 |
| 6/30/2005 | 480 | 28 | 452 | 94.2 |
| Average | 420 | 41 | 376 | 89.7 |

Table-6.22  Characteristics of Raw Sludge & Digested Sludge for the month of June 2005

| Date | Raw Sludge | Digested Sludge |
| --- | --- | --- |
|  | pH | Total Alkalinity | Solids % | % Volatile Matter | pH | Total Alkalinity | Solids % | % Volatile Matter | % Reduction in Volatile Matter |
|  |  |  | Total | Fixed | Volatile |  |  |  | Total | Fixed | Volatile |  |  |
| 6/3/2005 | 7.6 | 1010 | 5.03 | 2.40 | 2.63 | 52.2 | 8.3 | 2560 | 14.63 | 9.70 | 4.93 | 33.6 | 35.6 |
| 6/4/2005 | 7.6 | 1080 | 10.49 | 5.01 | 5.48 | 52.2 | 8.2 | 2870 | 1.97 | 1.40 | 0.57 | 28.9 | 44.6 |
| 6/5/2005 | 7.5 | 960 | 6.38 | 2.90 | 3.48 | 54.5 | 8.0 | 2470 | 1.92 | 1.33 | 0.55 | 41.3 | 24.2 |
| 6/6/2005 | 7.6 | 1030 | 11.68 | 5.15 | 6.53 | 55.9 | 8.3 | 3180 | 2.60 | 1.60 | 1.00 | 38.4 | 31.3 |
| 6/7/2005 | 7.6 | 930 | 7.32 | 3.24 | 4.08 | 55.7 | 8.1 | 2980 | 5.11 | 3.40 | 1.71 | 33.4 | 40.0 |
| 6/8/2005 | 7.5 | 780 | 6.21 | 2.85 | 3.36 | 54.1 | 8.3 | 3240 | 3.79 | 2.24 | 1.55 | 40.8 | 24.6 |
| 6/11/2005 | 7.6 | 820 | 6.79 | 3.02 | 3.77 | 55.5 | 8.1 | 3120 | 3.75 | 2.70 | 1.05 | 28.0 | 49.5 |
| 6/12/2005 | 7.6 | 940 | 3.37 | 1.50 | 1.87 | 55.4 | 8.3 | 3180 | 2.04 | 1.41 | 0.63 | 30.8 | 44.4 |
| 6/13/2005 | 7.6 | 1020 | 8.45 | 4.00 | 4.45 | 52.6 | 8.1 | 3060 | 2.00 | 1.40 | 0.60 | 30.0 | 43.0 |
| 6/14/2005 | 7.6 | 980 | 9.96 | 4.24 | 5.72 | 57.4 | 8.0 | 3110 | 12.14 | 7.47 | 4.67 | 38.4 | 33.1 |
| 6/15/2005 | 7.6 | 970 | 9.22 | 4.72 | 4.50 | 48.8 | 8.2 | 3230 | 9.28 | 5.66 | 3.62 | 39.0 | 20.1 |
| 6/18/2005 | 8.0 | 890 | 6.80 | 3.33 | 3.47 | 51.0 | 8.2 | 2770 | 5.59 | 3.56 | 2.03 | 36.3 | 28.8 |
| 6/19/2005 | 7.9 | 960 | 3.15 | 1.51 | 1.64 | 52.1 | 8.2 | 2420 | 1.38 | 0.86 | 0.52 | 37.7 | 27.6 |
| 6/20/2005 | 7.9 | 930 | 3.68 | 1.81 | 1.87 | 50.8 | 8.1 | 2520 | 2.53 | 1.51 | 1.02 | 40.3 | 20.7 |
| 6/22/2005 | 7.8 | 920 | 9.00 | 4.39 | 4.61 | 51.2 | 8.2 | 3180 | 5.84 | 3.89 | 1.95 | 33.4 | 34.8 |
| 6/24/2005 | 7.5 | 940 | 9.93 | 4.20 | 5.73 | 57.7 | 8.2 | 2190 | 8.54 | 5.04 | 3.50 | 41.0 | 28.9 |
| 6/27/2005 | 7.6 | 980 | 4.13 | 2.10 | 2.03 | 49.2 | 8.1 | 3050 | 2.77 | 1.80 | 0.97 | 35.0 | 28.9 |
| 6/28/2005 | 7.6 | 960 | 6.40 | 3.00 | 3.40 | 53.1 | 8.1 | 3210 | 10.20 | 6.70 | 3.50 | 34.3 | 35.4 |
| 6/29/2005 | 7.7 | 990 | 3.33 | 1.50 | 1.83 | 55.0 | 8.0 | 2970 | 1.00 | 0.62 | 0.34 | 33.8 | 38.5 |
| Average |  |  |  |  |  | 53.4 |  |  |  |  |  | 35.5 | 33.4 |

REFERENCES

- Anaerobic Sludge Digestion-Operation Manual, U.S. Environmental Protection Agency, MO-11.

- Babbitt, H.E. and Baumann, E.R. Sewerage and sewage treatment, 8th Edition, John Wiley & Sons.

- Balm’er, P. (1994). Chemical treatment; Consequences for sludge biosolids handling. Chemical water and wastewater treatment, 3rd Edition, R. Klute and H.H. Hahn, eds., Springer, New York.

- Bartlett, R.E. (1970). Sewerage, Elsevier Publishing Co.

- Basic Engineering Document-Okhla 16 MGD sewage treatment plant (1995), Delhi Water Supply & Sewage Disposal Undertaking.

- Benatti, Tavares, Filho and Moitinho (2002). Operation of a slow rate anaerobic digester treating municipal secondary sludge, Electronic J. Biotech. 5 (3), 216-227.

- Blais, Meunier, Mercier, Drogui and Tyagi. Pilot Plant Study of Simultaneous Sewage Sludge Digestion and Metal Leaching, J. Environ. Eng., 130 (5), 516-525.

- Cater, J.L. and Barry, W.F. (1975). Effects of shock temperature in biological systems, J. Environ. Eng., 101(2), 229-243.

- Cetin, F.D. and Surucu, G. (1990). Effects of temperature and pH on settleability of activated sludge flocs, Water Sci. Technol., 22(9), 249-254.

- Cheunbarn and Pagilla. Aerobic Thermophilic and Anaerobic Mesophilic Treatment of Sludge, J. Environ. Eng., 126 (9), 790-795.

- Chudoba, J. (1985). Control of activated sludge filamentous bulking-VI: Formulation of basic principles, Water Res., 19(8), 1017-1022.

- Chudoba, P., Morel, A. and Capedeville, b. (1992). The case of both energetic uncoupling and metabolic selection of micro-organisms in the OSA activated sludge system, Environ. Technol., 13, 761-770.

- Daigger, G.T. and Roper, Jr., R.E. (1985). The relationship between SVI and activated sludge settling characteristics, J. Water Pollut. Control Fed., 57(8), 859-866.

- Draft Final Report-Okhla Drainage Zone (2000), TCE Consulting Engineers.

- Eckenfelder, W.W. and Grau, P. (1992). Activated sludge process design and control theory and practice, Water quality management library Vol.I, Technomic, Lancaster, Pa., 170.

- EL-Gohary, F.A., Nasr, F.A. and EL-Hawaary, S. (1998). Performance assessment of a wastewater treatment plant producing effluent for irrigation in Egypt, The Environmentalist 18, 87-93.

- Evans, B. (1989). Getting a handle on sludge handling costs, Water Pollution Control, 127(3), 24.

- Fair, G.M., Geyer, J.C. and Okun, D.A. (1981). Water and Wastewater Engineering, Vol. II – Water Purification and Wastewater Treatment and Disposal, Wiley & Toppan.

- Final Report-Delhi Water Supply and sewerage Project (2005), PricewaterHouseCoopers Ltd.

- Fouad, M. and Bhargava, R. (2005). Sludge Production and Settleability in Biofilm-Activated Sludge Process, J. Environ. Eng., 417-424.

- Fouad, M. and Bhargava, R. (2005). Mathematical Model for the Biofilm-Activated Sludge Reactor, J. Environ. Eng., 557-562.

- Ghose, D.N. (1991). Operation and Maintenance of sewage treatment plants, CBS Publishers and Distributors.

- Gunnerson, C.G. and Stuckley, D.C. Integrated Resource Recovery Anaerobic Digestion, World Bank Technical Paper Number 49 (WTP-49).

- Henze, M., Grady, C.P.L., Gujer, W., Marais, G.V.R. and Matsuo, T. (1987). Activated sludge model No. 1, Scientific and Technical Rep. No.1, International Association of Water Quality, London.

- Hing, Zeng and Kuchenrither. (1991). Municipal Sewage Sludge Management: Processing, Utilization and Disposal, Technomic Publishing Co.

- Horan, N.J. (1990). Biological wastewater systems, 1st Ed., Wiley, Chichester.

- Iranpour, R., Straub, B. and Jugo, T. (1997). Real Time BOD Monitoring for Wastewater Process Control, J. Environ. Eng., 154-159.

- Jenkins, D., Richard, M.G. and Daigger, G.T. (1993). Manual on the causes and control of activated sludge bulking and foaming, 2nd Ed., Lewis, Boca Raton, Fla.

- Jonsson, K., Grunditz, C., Dalhammer, G. and La Cour, J.J. (2000). Occurrence of nitrification inhibition in Swedish municipal wastewater, Water Res., 34(9), 2455-2462.

- Journey, W.K. and McNiven, S. (1996). Anaerobic Enhanced Treatment of Wastewater and Options for Further Treatment, ACDI/VOCA.

- Kapur, A., Kansal, A., Prasad, R.K. and Gupta, S. Performance Evaluation of Sewage Treatment Plant and Sludge Bio-methanation, Indian JEP 19(2), 96-100.

- Kim, Bae and Speece (2004). Improved Anaerobic Process Efficiency Using Mesophilic and Thermophilic Elutriated Phased Treatment, J. Environ. Eng., 130 (9), 960-966.

- Kiracofe, B.D. (2000). Performance Evaluation of the Town of Monterey Wastewater Treatment Plant Utilizing Subsurface Flow Constructed Wetlands. M. Sc. Thesis, Virginia Polytechnic Institute and State University.

- Lapinski, J. and Tunnacliffe, A. (2003). Reduction of suspended biomass in municipal wastewater using Bdelloid rotifers, water Res., 37, 2027-2034.

- Lawrence, A.W. and McCarty, P.L. (1970). Unified basis for biological treatment design and operation, J. Sanit. Eng., 96(3), 757-779.

- Lee, N.M. and Welander, T. (1996a). Use of protozoa and metazoa for decreasing sludge production in aerobic wastewater treatment, Biotechnol. Lett., 18(4), 429-434.

- Lee, N.M. and Welander, T. (1996b). Reducing the sludge production in aerobic wastewater treatment through manipulation of the ecosystem, Water Res., 30(8), 1781-1790.

- Malina and Pohland (1992). Design of Anaerobic Processes for the Treatment of Industrial and Municipal Wastes, Technomic Publishing Co.

- Manual on Sewerage and Sewage Treatment (1993). 2nd Edition, CPHEEO, Govt. of India.

- Meeroff, D.E., Waite, T.D., Kazumi, J. and Kurucz, C.N. (2004). Radiation-Assisted Process Enhancement in Wastewater Treatment, J. Environ. Eng., 155-166.

- Metcalf and Eddy Inc. (2003). Wastewater Engineering – Treatment, Disposal and Reuse, 4th Edition, Tata McGraw Hill.

- Mueller, J.A., Kim, Y.W., Krupa, J.J., Shkreli, F., Nasr, S. and Fitzpatrick, B. (2000). Full-Scale Demonstration of Improvement in Aeration Efficiency, J. Environ. Eng., 549-555.

- Peavy, H.S., Rowe, D.R. and Tchobanoglous, G. (1985).  Environmental Engineering, McGraw Hill.

- Performance evaluation of sewage treatment plants in India. (1994), NEERI.

- Ponugoti, P.R., Dahab, M.F., and Surampalli, R. (1997). Effects of different biosolids treatment systems on pathogen and pathogen indicator reduction, Water Environ. Res., 69(7), 1195-1206.

- Quasim, S.R. (1999). Wastewater Treatment Plants: Planning, Design and Operation, 2nd Edition, CRC Press.

- Quesnel, D. and Nakhla, G. (2005). Utilization of an Activated Sludge for the Improvement of an Existing Thermophilic Wastewater Treatment System, J. Environ. Eng., 570-578.

- Ramalho, R.S. (1977). Introduction to Wastewater Treatment Processes, Academic Press.

- Ravindra, P.N. (2004). Handbook of Terminologies-Water and Wastewater, Indian Water Works Association, Bangalore Centre.

- Rebollo, B. Technology portfolio of urban wastewater treatment and sludge management, Institute for Prospective Technological Studies (ITPS).

- Reddy, R.C., Rao, R.R. and Andey, S.P. (1999). Evaluation of Sewage Treatment Plant-A case study, Indian J. Enviuron Hlth. 41(4), 346-355.

- Ren, S. and Frymeir, P.D. (2004). Statistical Comparison of Bioassays for Assessment of Toxicity of Organic Compounds of wastewater to Activated Sludge, J. Environ. Eng., 484-488.

- Sakai, Y., Tani, K. and Tkahashi, F. (1992). Sewage under conditions of balancing microbial growth and cell decay with a high concentration of activated sludge supplemented with ferromagnetic powder, J. Ferment. Bioeng., 76(6), 413-415.

- Sastry, Hashim and Agamuthu, (1995). Waste Treatment Plants, Narosa Publishing House.

- Saunamaki, R. (1988). Sludge handling and disposal at the Finnish activated sludge plants, water Sci Technol., 20, 171-182.

- Sincero and Sincero (2003). Physical-Chemical Treatment of Water and Wastewater, CRC Press.

- Snidaro, D., et al. (1997). Characterization of activated sludge flocs structure, Water Sci. Technol., 36, 313-320.

- Standard Methods for Examination of Water and Wastewater (1992), 18th Edition, American Public Health Association.

- Suidan, M.T., Wang, Y.T. and Kim, B.R. (1989). Performance evaluation of viofilm reactors using graphical techniques, Water Res., 23(7), 837-844.

- Tchobanoglous, G. and Burton, F.L. (1991). Wastewater engineering: Treatment, disposal and reuse, 3rd Ed., McGraw Hill, New York.

- Tugun, Loehr and Qui (2003), Natural Stabilization of Stored Industrial Sludges, J. Environ. Eng., 129 (3), 248-257.

- U.S. Environmental Protection Agency, Operations Manual: Anaerobic Sludge digestion, EPA 430/9-76-001, February 1976.

- Wanner, J. Beginning of the Activated Sludge Process, Prague Institute of Chemical Technology.

- Wanner, J., Kucman, K. and Grau, P. (1988). Activated sludge process combined with biofilm cultivation, Water Res., 22(2), 207-215.

- Westfall, B.A. (1981). Evaluation of An Activated Sludge Package Plant. M. Sc. Thesis, The University of Texas at El Paso.

- Wong, K.Y., Zhang, M.Q., Li, X.M. and Lo, W. (1997). A luminescence-based scanning respirometer for heavy metal toxicity monitoring, Biosens. Bioelectron., 12(2), 15-133.

- Several relevant websites on the internet.

# Text boxes

Primary sludge                  Excess sludge

Raw

sewage

Bar

Screen

Grit

Chamber

Return sludge

Aeration tank

Secondary

Clarifier

Primary

Clarifier

Biogas

Sludge

Drying

Bed

Sludge

Digester

Final treated

effluent

Sludge

disposal

DEFINE DESIRED EFFLUENT QUALITY

COLLECT PLANT DATA

DEFINE DESIGN AND PERFORMANCE CRITERIA

n

MEASURE PLANT FLOW

IS PLANT LOADED WITH RATED  CAPACITY

CHECK

- UNDER LOADED (HYDRAULIC)

- OVER LOADED (HYDRAULIC

- FLOW FLUCTUATION

n

STUDY PERFORMANCE OF SCREENS

DO THEY MEET  DESIGN & PERFORMANCE CRITERIA

n

CHECK

- LOADING RATE  (HYDRAULIC)

- FREQUENCY OF SCREENING REMOVAL

- VELOCITY THROUGH SCREENS

STUDY PERFORMANCE OF DETRITUS TANK

DOES IT MEET  DESIGN & PERFORMANCE CRITERIA

CHECK

- LOADING RATE  (HYDRAULIC)

- FREQUENCY OF GRIT REMOVAL

- HORIZONTAL VELOCITY

n

STUDY PERFORMANCE OF PRIMARY SEDIMENTATION TANK

DOES IT MEET  DESIGN & PERFORMANCE CRITERIA

CHECK

- LOADING RATE  (HYDRAULIC /ORGANIC)

- SLUDGE DRAW OFF

- SCUM REMOVAL

n

DOES IT MEET  DESIGN & PERFORMANCE CRITERIA

CHECK

- LOADING RATE  (HYDRAULIC /ORGANIC)

- RECIRCULATION OF RETURN ACTIVATED SLUDGE / SUPERNATENT

- DETENTION TIME

- DO

- SVI, MLSS

n

STUDY EFFLUENT QUALITY

DOES IT MEET EFFLUENT DESIRED QUALITY

- APPRISE PLANT O&M PERSONNEL /AUTHORITIES OF THE DEFICIENCIES

- MOTIVATE  FOR CORRECTIVE MEASURES

n

SUCCESS

STUDY PERFORMANCE OF SECONDARY TREATMENT